| Instrumentation |
| --- |
| Primary Instrumentation |
| Type | Brand/Model | Accuracy | Range | References |
| Automatic Level | Leica DNA03 | Heights 0.3 mm SD / km (double leveling with invar; 1.0 mm without invar) | 1.8 m to 110 m (optically from 0.6 m) | Leica Product Page Leica Paper |
| Laser Tracker | FARO Xi | ADM: 10 μm + 0.4 μm/m Interferometer: 2 μm + 0.4 μm/m | 0 m to 35 m ±270° horz +75° to -50° vert | FARO Product Page FARO Techsheet |
| Gyrotheodolite | Gyromat 2000 | 1/1000 gon or 1.5 cm/km | 80° latitude | Leica Product Page |
| Accessories |
| Type | Brand/Model | Accuracy | Range | References |
| Survey Target | PLX FARO | 0.0001” for best type Sphericity < 0.00005” |  | PLX Info |
| Field Data Collector | Paravant RHC44E Allegro DOS Allegro CE,CX |  |  | Paravant Allegro DOS Allegro CE Allegro CX Product Page Allegro CX Brochure |
| Additional Equipment |
| Type | Brand/Model | Accuracy | Range | References |
| Total Station | Leica TC2002 | 1 mm + 1 ppm (0.25 mm with calibration/correction) 0.5 arcsecs |  | Wirth & Moritz Paper |
| Total Station | Leica TDA5005 | 1 mm + 2 ppm 0.5 arcsecs | Reflective tape: ± 0.5 mm at 100m Corner cube: ± 0.2 mm | Leica Product Page |
| Laser Scanner | Z+F Imager 5006 | 0.7 mm (from 0.4 mm rms @ 10 m white surface to 7.5 mm rms @ 50 m black surface) 0.007° rms horz & vert | 1.0 m to 79 m (ambiguity interval) | Z+F Product Page Z+F Datasheet |
| Optical Plummet | Wild NL Automatic Nadir Plummet | 1 : 20000 = 0.062mm (see NL Manual) |  | NL Manual Ref. Paper Ref. Paper |