Monumentation Drilling Specifications:

Floor Monuments:

- Floor is drilled using 1 3/4" core drill bit to a depth of  2” with a Hilti rotary hammer drill

- Quikrete is used to set monuments into the floor

- We generally allow 24 hours of curing time before starting any observations

- The lids of the monuments should be flush with the floor

Below is a floor Monument with a lid and 2 floor monuments with fixtures used for installation. The fixtures are marked with a cone for trip hazards and are removed once the Quikrete has set. The two fixtures shown below are interchangeable. Originally a limited number of the taller fixtures were purchased (far right of top picture). The T-shaped fixture (middle of picture) is our “in-house” version built so that more monuments can be installed at once.

Lid, Floor Monument and Two Installation Fixtures

Floor Monument Installed with Lid On and Off

Wall Monuments:

- Wall is drilled  with a 5/8” drill bit  to a depth of 2 1/8” with a Hilti rotary hammer drill

- Hilti  1/2-13 drop-in anchors are then installed

- Wall monument is screwed into anchor ( Loctite  may be used on threads )

- Monumentation is ready for use right away, no waiting time necessary, unlike the floor monuments

Hilti Anchor, Wall Monuments With and Without Lid

Installed Wall Monument

Brass Plugs:

- Floor is drilled using 1 1/2" drill bit to a depth of  1” with a Hilti rotary hammer drill

- A small amount of Duct Seal is used on the bottom of the Brass Plug

- 5 Minute Epoxy is poured into the hole and the Brass Plug is pushed down until it is flush with the floor

- We generally allow 24 hours of curing time before starting any observations

- The plugs are then cleaned off of any excess epoxy and are ready to mark

A Brass Plug with most of the equipment used for installation

A Brass Plug installed in floor

Rivets:

- Floor is drilled  with a 5/8” drill bit  to a depth of 2 1/8” with a Hilti rotary hammer drill

- 5 Minute Epoxy is used to set the rivets

- Generally wait 24 hours before using

Rivets before installation

Installed Rivet