Document Number NIF-000073966

WBS N.M.9.5.2

Step-by-Step Procedure for Adjustment Analysis Using Geonet/LEGO

For

By

Dorothy S. Ng

October 2002

Table of contents

1.0	Introduction 	4

2.0	Geonet/LEGO Program 	4

2.1	To create data structure and access path 	7

2.2	To create new jobs 	9

2.3	To upload field data into Geonet/LEGO 	11

2.4	To reduce data into distance and direction format 	14

2.5	To generate LEGO input file 	15

2.6	To execute LEGO Adjustment analysis 	21

3.0	Adjustment result evaluation 	26

3.1	Quality control of analysis 	26

3.2	To input the results into the Form B of the workbook 	26

4.0	Life Saving Tips 	27

References: 	29

Attachment 1	NIF component alignment verification data structure 	30

Attachment 2	Sample Field data file 	33

Attachment 3	Sample Tracker.res 	34

Attachment 4	Sample Level.res 	36

Attachment 5	Sample Redir.res 	37

Attachment 6	Sample Redisth.res 	38

Attachment 7	Sample Redists.res 	39

Attachment 8	Sample Zenith.res 	40

Attachment 9	Sample network file for Laser Bay 1 	41

Attachment 10	Sample input file (LM1LSC3A.inp) 	42

Attachment 11	Sample LM1LSC3A.SUM file 	46

Attachment 12	Sample LM1LSC3A.ORG file 	47

Attachment 13	Sample LM1LSC3A.PAR file 	49

Attachment 14	Sample output file (LM1LSC3A.out) 	50

Table of Figures

| Figure 1 Introduction of Geonet/LEGO | 5 |
| --- | --- |
| Figure 2 Geonet/LEGO Home Window | 5 |
| Figure 3 Geonet/LEGO pull down menu | 6 |
| Figure 4 Data structure setup and Adjustment analysis procedures | 7 |
| Figure 5 Edit Data Choice Window in Data Structure Function | 8 |
| Figure 6 Edit Data String Window (Location) in Data Structure Function | 8 |
| Figure 7 Edit Data Strings Window (Data Types) in Data Structure Function | 9 |
| Figure 8 Edit Data Strings Window (Epochs) in Data Structure Function | 9 |
| Figure 9 System Configuration Options Window in Create Job Function | 10 |
| Figure 10 System Configuration Window in Create Job Function | 10 |
| Figure 11 Select Survey to Add Window in Create Job Function | 11 |
| Figure 12 Upload Data Window | 12 |
| Figure 13 Upload Data From Window in Upload Field Data Function | 13 |
| Figure 14 Upload Data To Window in Upload Field Data Function | 13 |
| Figure 15 Data Reduction Window | 14 |
| Figure 16 Data Reduction Geonet/LEGO Window | 15 |
| Figure 17 LEGO Input File Creation Window | 17 |
| Figure 18 Observation Weights Window in LEGO Input File Creation Function | 17 |
| Figure 19 Input SMX Tracker Field Data From Window in LEGO Input File Creation Function | 18 |
| Figure 20 LEGO Input File Location Window in LEGO Input File Creation Function | 20 |
| Figure 21 Enter Input File Name Window in LEGO Input File Creation Function | 21 |
| Figure 22 Input File Creation Window in LEGO Input File Creation Function | 21 |
| Figure 23 Run Lego Window | 22 |
| Figure 24 LEGO Par File Editor Window | 23 |
| Figure 25 LEGO Completed Window | 24 |

# 1.0	Introduction

Adjustment analysis is one of the major processes in verification of component installation in the National Ignition Facility (NIF) Project. It analyzes high precision survey measurements at micron level. Multiple observations in local coordinate system are formed into a matrix and are fit to a network to solve for the adjusted coordinates and their associated uncertainties in global coordinate system. Adjustment analysis is performed using Geonet/LEGO Program.

Various types of survey instrument are used in NIF to accommodate the required tolerance: Laser Tracker for components that required stringent tolerance while Leica and Total Station for components that required loose tolerance. Geonet/LEGO is versatile and can accommodate various types of survey instruments as long as the data files are in the specific format.

Evaluation of component’s as-built positions is performed in two steps; namely, survey performance evaluation and design requirement verification. Survey performance is not in the scope of this document. The resulting coordinates from Adjustment analysis are the final as-built coordinates. Along with the uncertainties, they are used for verification against design requirements; namely: coordinates and tolerances. The Adjustment analysis procedure relevant to NIF component alignment verification is described in this document step-by-step.

# 2.0	Geonet/LEGO Program

Geonet/Lego (Ref. 1) is a software package developed for SLAC (Stanford Linear Accelerator Center). It applies the least-squares adjustment on real observations. An introduction picture of Geonet/LEGO Program appears when it is executed (as shown in Figure 1). Click the picture to initiate the program and reveal the Home Window.

Home Window (as shown in Figure 2) is constituted of a pull down menu located at the top of the window and 10 function icons at below. The pull down menu contains 4 functions as depicted in Figure 3. Some of these functions are also available in 10 function Icons.

Only a few functions in the pull down menu are commonly used for NIF component alignment verification. The Exit Icon is one of the File functions (as shown in canary boxes in Figure 3). To terminate the program, click the Exit Button or simply click the “X” on the right-top corner of the Home Window. Always return to Home Window to properly terminate the program.

The Data Structure Option, an Edit function, is for creating the data structure (as shown in green boxes). The data structure has to been setup before any job can be created. The Calibration Structures Option, another Edit function, is for calibration which is set at default values. The Path Type Option, an Option function, toggles between Geonet and Menu (as shown in blue boxes). It controls the format of text file for viewing.

Among 10 functions, only the following 8 functions are commonly used in NIF component installation verification:

- Create job

- Upload Field Data

- Data Reductions

- Create LEGO Input File

- LEGO Adjustment

- Access Subdirectories

- Exit

Figure 1	Introduction of Geonet/LEGO

Figure 2	Geonet/LEGO Home Window

Figure 3	Geonet/LEGO pull down menu

Figure 4 depicts the steps for Geonet/LEGO Program setup and for performing adjustment analysis. In program setup, the users are required to create data structure and access paths as shown in the light green boxes in Figure 4. Jobs can be created by adding the job description in the data structure. Geonet/LEGO inquires users to identify directories in Geonet/LEGO data structure for the storage of data file, reduction result file, input file, and output files.

The data structure composes of 3 layers; namely: Root, Location, and Epoch. There are 10 Roots, 16 Locations per Root, and 16 Epochs per Location. The NIF data structure configuration (as of September 2002) is given in Attachment 1.

The data file (as shown in yellow and canary boxes) is uploaded to the appropriate storage. The field coordinates are reduced into Geonet/LEGO recognizable format before the input file can be formulated (as shown in blue boxes). Then, adjustment analysis is performed to produce adjusted coordinates and uncertainties in the output file. LEGO performs the mathematics of the adjustment analysis.

Figure 4	Data structure setup and Adjustment analysis procedures

## 2.1	To create data structure and access path

As part of the program setup, the Data Structure is created in the following steps:

- Click Edit Key in the pull down menu to reveal options (as shown in Figure 3). Click Data Structure Button to open Edit Data Choice Window (as given in Figure 5) which shows the data structure.

- Select the first available number in the left column of the window and fill in the Path name and Path description. Note that the first several characters of the Path description are used for identification, not the Path name; thus, the description should be concise.

- Click OK Button to get Edit Data Strings Window (as given in Figure 6). There are 3 indexes in the window; namely: Locations, Data Types, and Epochs. The Edit Data Strings Window opens to Locations Index. Select the Path name in the Root to Edit Window and the number in the Locations Window. Fill in the location name and description. Always highlight the number in the left column to activate the row of boxes.

- Click the Data Types Index to get Data Types Window (as given in Figure7). Select the number, data type name (instrument type), and data type description (instrument manufacturer). The instrument type and manufacturer determine the calibration values used in the analysis.

Figure 5	Edit Data Choice Window in Data Structure Function

Figure 6	Edit Data String Window (Location) in Data Structure Function

- Click the Epochs Index to get Epochs Window (as given in Figure 8). Select the first available SRV number. There is no indication which SRV has been used in the Epoch column. It is up to the user to keep a record of the used SRV.

- Click OK Button to complete the data structure setup.

- Steps 4-6 may be repeated to create data structure for Total Station and Level. Laser Tracker is commonly used in NIF component alignment verification.

When the data structure is created 3 tracking files (name.his, name.pth, and name.str) are generated in the Init Directory. The path and location names in these three files have to be consistent. Since Geonet/LEGO does not update the new name properly changing the path and location names in the data structure is not recommended. It is better to create the path as needed and new path can be added later.

Figure 7	Edit Data Strings Window (Data Types) in Data Structure Function

Figure 8	Edit Data Strings Window (Epochs) in Data Structure Function

## 2.2	To create new jobs

After the data structure is created, new job can be added by identifying the location and labeling the Epoch (SRV#). The jobs are created in the following steps:

- Click Create Job(s) Icon to reveal System Configuration Options Window (as given in Figure 9).

- Select Data Configuration Button to bring in Data Configuration Window (as given in Figure 10).

Figure 9	System Configuration Options Window in Create Job Function

Figure 10	System Configuration Window in Create Job Function

- Scroll up and down to find the Path name and double click the Path name to get its Locations. Find and double click the Location to reveal Directories ADJUST, TOTAL, LEVEL, and TRAK.

- Click the + Add Button to get Select Survey to Add Window (as given in Figure 11). This window depicts layers of data structure; namely: Root. Location, Epoch.

- Select Root, Location, Data Type, and Epoch. Note that the occupied Epochs are not shown in the Epoch column. For example, in Figure 11, SRV1 has been used and is not shown in the Epoch Column. SRV2 is the first available SRV which has been activated in data structure process.

- Fill in the job name, component identification, and date in the History Window.

- Click OK Button to complete the create-job process. The program will respond by flashing a small window to indicate job added. If no response from the Program, the SRV number may not be activated in the data structure. Repeat the Data Structure setup to activate the SRV in Epoch.

Figure 11	Select Survey to Add Window in Create Job Function

## 2.3	To upload field data into Geonet/LEGO

Geonet/LEGO recognizes field data file in Cartesian coordinate system in text format with a file name extension of .ZXY (for example: LM1LSC31.zxy). Note that the coordinates must be in meters. The columns of coordinates have to be in an order of Z, X, and Y in floating point format as shown in Table 1. No title row is allowed at the beginning of the file (as shown in gray in Table 1) and no blank line is allowed at the end. Attachment 2 is a sample of a .ZXY file.

The source of field data in NIF can be either from SMXInsight Program (Ref. 2) or Excel Program. SMXInsight produces .ZXY files in Geonet/LEGO recognizable format. Ref. 3 provides step-by-step procedure for .ZXY files preparation from SMXInsight files. This .ZXY file should be placed in a source directory external to Geonet/LEGO data structure and will be uploaded onto Geonet/LEGO data structure afterward.

Table 1	.ZXY file format for laser tracker data

| Point name | Z-Horizontal axis | X-Horizontal axis | Vertical axis |
| --- | --- | --- | --- |
| CFB2SS1 | 2.0 | 2.0 | 4.0 |
| CFB2SS2 | 3.0 | 3.0 | 5.0 |
| CFB2SS3 | 3.0 | 4.0 | 5.0 |

Field data files are uploaded in the following steps.

- Click Upload Filed Data Icon in Home Window to get the Upload data Window (as given in Figure 12) in which there are a pull down menu and two browser windows. The pull down window contains 2 functions; namely: File for administration and Options for path type same as that in Home Window.

- Click Browser Button in the Upload From: Window (as given in Figure 13) to locate the source directory for the .ZXY files. Open the source directory to show the field data files and click Open Button to return to the Upload data Window.

- Click Browser Button in the Upload To: Window (as given in Figure 14). Find and double click the location to reveal the TRAK Directory. Select the Epoch SRV# for field data file storage. Click OK Button to return to the Upload data Window.

- Click Upload Filed Data Icon which has a picture of ‘computer and disk’ to upload. When a completion window appears click OK button to return to the Upload data Window.

- Steps 1-4 may be repeated to upload the data files from Total Station and Level. Make sure that they are placed in the appropriate directories.

Figure 12	Upload Data Window

Figure 13	Upload Data From Window in Upload Field Data Function

Figure 14	Upload Data To Window in Upload Field Data Function

This process copies the data files from the source directory into Geonet/LEGO directory (TRAK/SRV#). The original files remain in the source directory but their name extension has been changed from .ZXY to .999.

A record of field data file name is kept in SRV1.IDX file. The upload process may be repeated as necessary. SRV1.IDX file will be updated to include the newly added files. Only the files listed in SRV1.IDX file are forwarded to the next step. It is very important to maintain a consistent count between the data files and the list; otherwise, data may be missed.

## 2.4	To reduce data into distance and direction format

LEGO forms a matrix of coordinates in a format of distance and directions (distance-angle-angle). Geonet/LEGO reduces the Cartesian coordinate data from laser tracker into distance-angle-angle format for each point and then places them in a reduction result file called Tracker.res for Laser Tracker data as an example. Note that the reduced distance is in meter and the directions are in gon (400 gon in a circle).

The Data Reductions Icon is available in the Home Window and also in the Upload Data Window. Data is reduced in the following steps:

- Click Data Reductions Icon to reveal Data Reduction Directory Selection Window (as given in Figure 15). Scroll up and down to find the Location/Epoch and select the SRV#. If a Tracker.res file exists in the File Window as shown in Figure 15 an error message will appear. Rename old Tracker.res file to something other than Tracker.res.

- Click OK Button to get Data Reduction Menu Window (as given in Figure 16). Make sure the small box in the Reduction Result Files Window is empty.

Figure 15	Data Reduction Window

- Click the Data Reductions Icon which has a picture of ‘a compressor’ to initiate data reduction. When the completion window appears click OK Button to return to the Reduction Result Files Window. The small box in the Reduction Result Files Window is now filled with an ‘X’ indicating data reduction process complete.

- Click the View Button which has to a picture of pencil and papers to view the Tracker.res file. Geonet/LEGO sends the file to Kedit (a word processor) for viewing. Attachment 3 is a sample of a Tracker.res file. The data file name becomes the station name and is placed in the first left column. The point name is placed in the second left column followed by distance, horizontal, and vertical coordinates.

- Steps 1-3 may be repeated for Total Stations and Levels. The name of the reduction result file for Level is Level.res. For Total Station data, 4 reduction result files are generated; namely: Redir.res, Redisth.res, Redists.res, and Zenith.res. Samples are provided in Attachment 4 for Level and Attachments 5-8 for Total Station.

Figure 16	Data Reduction Menu Window for Data Reductions Function

## 2.5	To generate LEGO input file

The field data is recorded in local coordinates relative to the station. Adjustment analysis computes the coordinates into global system by fitting the data to a global network system. The analysis can also remain at the local coordinate system without bestfit. To take multiple observations, the instrument has to be moved around to obtain a strong geometry in the data set. Commonly the NIF survey data are taken in local coordinate system.

Two precision networks were established in the year of 2000 for NIF; namely: Laser Bay 1 and Laser Bay 2 Network. A network is constituted of an array of monuments located on the floors, walls, and pedestals. These monuments become the control network monuments (CNMs) and their coordinates are nominal. The network file containing the CNM nominal is stored in the TEMP Directory in Geonet/LEGO data structure and is used as the reference file for bestfit. New monuments were added to both networks. Laser Bay 2 network was extended to include monuments in switchyard area and also was densified by adding more monuments in the Cluster 3 area.

Many precision survey features (PSFs) are installed on NIF components. During the precision survey, the PSFs on a component along with the CNMs located in the vicinity of the component are measured at each station. The CNMs nominal are extracted from the reference (network) file and added into the input file for bestfit. Note that the order of coordinates in a reference file should be Z, X, and Y, consistent with those in field data files as shown in Table 2. Attachment 9 is a sample of a partial network file. In addition to fitting to a network, Adjustment analysis can also fit to some known points within the component as performed in CSP12 (Ref. 4).

Table 2	Reference file format (network nominal)

| Point name | Z-Horizontal axis | X-Horizontal axis | Vertical axis |
| --- | --- | --- | --- |
| 3LP01F01 | 2.0 | 2.0 | 4.0 |
| 3LP01F02 | 3.0 | 3.0 | 5.0 |
| 3LP01F03 | 3.0 | 4.0 | 5.0 |

The Create LEGO Input File Icon is available in the Home Window as well as in the Data Reduction Menu Window. An input file is generated in the following steps:

2.5.1	To select observation weights

- Click Create LEGO Input File Icon to reveal the LEGO Input File Creation Window (as given in Figure 17). There is a pull down menu in this window which contains File, Edit, and Option functions. The File Key is for administrative. Edit Key is for observation weights selection. Options Key is for path types.

- Click Edit Key to reveal the options and select Observation Weights Button to open the Observation Weights Window (as given in Figure 18). The observation weight is a priori mean square error which acts as scale factor for the observations.

- There are 7 types (indexes) of instruments in this window; namely: SMX Tracker, Leica Tracker, Total Station, Levels, Directions, TC2002 Distances, and Mekometer Distances. Select the SMX Tracker which is commonly used in NIF component alignment verification.

- For SMX Tracker data a value of 0.00003 meter is recommended for distance weights. For direction weight, it is recommended to calculate internally at the Horizontal and Zenith errors of 0.0001 gon.

- For Total Station data choose the recommended distance weight of 0.00015 meter and the same direction weight as for Laser Tracker data.

- For Level data select height weight of 0.00005 meter.

- Click OK Button to return to LEGO Input File Creation Window

Figure 17	LEGO Input File Creation Window

Figure 18	Observation Weights Window in LEGO Input File Creation Function

2.5.2	Access reduction results files

- Select type of instrument in the Data Type Window.

- Click the Browser Button to open the Input SMX Tracker field data from Window (as given in Figure 19). The Browser Button has a picture of indexed folder.

- Scroll up and down to locate the Root and Location in the File Window. Highlight the SRV# in TRAK, LEVEL, or TOTAL to access reduction result files. Click OK Button to return to the LEGO Input File Creation Window. The reduction results are copied into the input file leaving the origin reduction results file unchanged.

- In general, only Laser Tracker data is used in NIF evaluation with exception. In CSP-13 (Ref. 5), the submitted field data was taken with Total Station and was processed using Spatial Analyzer (SA). The submitted field data was identical to the Laser Tracker data and was added to the TRAK Epoch with prism adjustment added.

- Fill in the project and task descriptions.

- Select 3 Dimension in the Dimension Window (as shown in Figure 19).

Figure 19	Input SMX Tracker Field Data From Window in LEGO Input File Creation Function

2.5.3	Access reference file

- Select User Defined in the Coordinate Location Window and 3 Dimensional in the Coordinate Types Window by clicking the squares.

- Scroll up and down the User Database Files Window and click the square and highlight the appropriate bestfit reference (network) file. If the reference file is not available in the User Database Files Window click Browser Button to copy the file from TEMP Directory into the User Database Files Window which has limited capacity. When it is full, a warning message will appear. Use Del Key to delete the old files and repeat the browser process.

2.5.4	To generate input file

- Click Create LEGO Input File ' which has a picture of ‘writing on paper’ to open LEGO Input File Location Window (as given in Figure 20).

- Geonet/LEGO opens the folders leading to root and location where the reduction results file is located in TRAK Directory. Make sure that the folder leading to the Survey # under the ADJUST Directory is opened.

- Click the OK Button to open the Enter Input File Name Window (as given in 
Figure 21).

- Type in a file name and click the OK Button. If the file name has been used an error message will appear and provide choices to overwrite the existing file or not.

- When the small Input File Creation Window (as given in Figure 22) appears, click OK Button to complete the process and return to the LEGO Input File Creation Window.

- Click View Button to open the input file and look for the bestfit reference coordinates for confirmation. Attachment 10 is a sample of an input file.

2.5.5	The contents of an input file delimitated by an END line

- Job identification as provided in the LEGO Input File Creation Window.

- Station names

- Object Points (CNM nominal) copied from the reference file and followed by PSFs and common points in some cases. Common points are used to bridge the CNMs to PSFs when they are not visible at a station.

- Height differences (data from the Levels)

- Distances in 4 columns; namely: station name, point name, distance, and weight.

- Directions in 6 columns; namely: station name, point name, horizontal angle, horizontal weight, vertical angle, and vertical weight.

- Control information and fixed coordinates

- Relative error point pairs.

2.5.6	Additional procedure for data from a Total Station

When the Total Station data is uploaded and reduced in Geonet/LEGO the prism adjustment is made internally. When the Total Station data was processed using Spectral Analyzer, prism adjustment must be specified in the following two ways:

- Remove the ‘T’ next to the distance weight and raise the distance weight from 0.00003m to 0.00015m.

- The adjustment can be made in the parameter file (see Subsection 2.6.3 for detail) by adding the following at its end:

- Tacheo

- Set

- ID templ

- offset    u

- k        i

- Station SCBBAC30

- Station SCBBAC31

- Station SCBBAC32

- End

- End

Warning: Occasionally, Geonet fails to dump the buffer when asked to replace a file. When in doubt terminate Geonet/LEGO and restart. For example if new data files are added to the TRAK Directory and new Tracker.res file is generated. Do check the new Tracker.res and input file for fragment from last generation.

Figure 20	LEGO Input File Location Window in LEGO Input File Creation Function

Figure 21	Enter Input File Name Window in LEGO Input File Creation Function

Figure 22	Input File Creation Window in LEGO Input File Creation Function

Along with the input file, a summary file (XXXX.SUM) and an organization file (XXXX,ORG) are also generated. See Attachments 11 and 12 for sample of a .SUM and an .ORG files, respectively. The Summary File gives the number of observations for each survey target. To obtain realistic uncertainties, at least 3 observations per PSF are needed. The Organization File organizes the data in the following order: monument with bestfit reference coordinates, station names, survey target point name, and data set of station, point, and observations.

## 2.6	To execute LEGO Adjustment analysis

Before running the LEGO Adjustment analysis some parameters must be defined; namely: choices of stations and points for bestfit, earth model parameters, number of iterations, value to stop the iteration, adjustment type, and choices of station scale or offset. A Parameter (XXXX.PAR) File is created when the analysis is initiated. PAR file can be edited as necessary using Kedit; however, the Earth Model has to be defined interactively.

The datum is defined in Parameter File. In the case of NIF component installation, the NIF control network is the primary network. The observations at the CNMs and PSFs obtained in a component installation inspection survey form the secondary network. Both networks will be connected via points common to both networks (Ref. 1). The common pints are the CNMs. The variance and covariance values for these points are used to calculate weights for the connecting point of the secondary network.

The LEGO Adjustment Icon is in the Home Window as well as in the LEGO Input File Creation Window. LEGO adjustment analysis is processed in the following steps:

2.6.1	Access input file

- Click the LEGO Adjustment Icon to reveal the Run Lego Window (as given in 
Figure 23). There is a pull down menu in this window containing File (administrative functions), Options (choices of Geonet/LEGO Editor or Text Editor), and Export functions [Dbase Update (DBS Files), Shape (XYZ File), 9Par (INU File), and Sims (TRG File)]. 9Par file is for transformation while Sims is for simulation. None of these Export Options is commonly used for NIF component alignment verification; thus, will not be elaborated.

- Click the Browser Button to select input file.

Figure 23	Run Lego Window

2.6.2	To edit input file

- Often the analysis is aborted due to high variance. The input file may be edited to change the distance and direction weights.

- Click the square leading to Input file to view the Input file. Select the editor format in Options Function in the pull down menu to get the Manual Text Format for editing.

- Closing the Input file will return to the Run Lego Window.

2.6.3	To create PAR file

  - Click the square leading to Parameter File to open the LEGO PAR File Editor Window (as given in Figure 24). View the window in Geonet Editor Format.

  - This LEGO PAR File Editor Window contains various sizes of windows. The large window on the right has two indexes: Stations and Points. The LEGO Par File Editor Window opens to Station Index which contains 4 columns; namely: Station name, Use Z, Use X, and Use Y. The Use Z, Use X, and Use Y are the indicator for the coordinates. In general, the analysis does not fit to the stations; therefore, remove the red check marks in the squares by double clicking the indicators.

  - Click Points Index and double click the indicator Use Z, Use X, and Use Y to remove all the red check marks. Selectively double click the name of the CNMs to mark its 3 squares with red check marks for bestfit. Double click the individual squares to turn on and off the red check mark as needed.

  - The number of iterations is defaulted to a maximum value of 10 and can be increased. The stop value is set for 0.00001m.

  - In general, the network dimension is set to be 3-dimensional which determines the position and elevation in one step. Setting Free of constraint means the coordinates are free to be adjusted in matrix solving. Occasionally, Fix Option may be used to constraint 6 coordinates (datum) at 3 points for a 3-dimensional model. Attachment 13 is a sample of a .PAR file.

Figure 24	LEGO Par File Editor Window

  - In general there is no need to input earth model for component installation verification because the distances are so short that the earth curvature does not affect the height. The earth model must be input when the network is established due to its large area of interest. The earth model at NIF site is given below:

  - Earth radius = 6372699.265m

  - Z Bias = 0

  - X Bias = 0

  - Y Bias = 0

  - Height = 155.3296m

  - No station scaling is needed.

  - Select Inversion for matrix solving.

  - Click OK Button to return to the Run Lego Window.

2.6.4	To run Lego Adjustment analysis

- Click Lego Adjustment Icon to run the adjustment analysis.

- When the LEGO Completed Window (as given in Figure 25) appears, click OK Button to return to the Run Lego Window.

- If for any reasons the analysis is aborted inspect the output file for error messages which may provide debug clues. Attachment 14 is a sample of an output file.

Figure 25	LEGO Completed Window

2.6.5	Additional procedure for relative coordinate calculation

- Add the relative pair of point name at the end of the input file.

- Add the relative pair of point name at the end of the parameter file. In addition, the word ‘Relative’ must be added before the relative pairs.

2.6.6	To view output file

- Click the square leading to Output File to open the output file in Kedit.

- Output file from a normal completion gives summary of the matrix followed by the approximate coordinates.

- Output file from an abnormal completion may not give messages. See Subsection 2.6.9 and Section 4.0 for debug tips.

    - The contents of an output file

- Directory of the output file in data structure

- Matrix summary

- Approximate values of all observations

- Correction to coordinates (evaluate corrections over 300 microns-Subsection 2.6.10)

- Final results after # iterations (No convergence may be reported.)

- Statistic results (one and two-tailed tests, variances, sigma a priori, and sigma posteriori)

- Distance residuals (Station name, point name, estimated distance measurement, residual, and estimated mean square error)

- Histogram of distance residuals

- Horizontal residuals (Station name, point name, estimated horizontal measurement, residual, and the estimated mean square error)

- Histogram of direction residuals

- Chi2 goodness of fit test

- Vertical residuals (Station name, point name, estimated vertical measurement, residual, and the estimated mean square error)

- Histogram of direction residuals

- Chi2 goodness of fit test

- Histogram of all residuals

- Chi2 goodness of fit test

- Standard deviations (sigma a posteriori #)

- Standard point confidence ellipse (point name; Z, X, and Y uncertainties; major and minor radius; and phase)

- Relative standard ellipse (sigma, a posteriori #)

2.6.8	Frequently encountered error messages

- In output: Must deselect distance between JK032303 and SB2.

- In output: Must deselect height difference between 3LD02F03 and 3LD03F02.

- In output: Must deselect horizontal direction between JK032303 and SB2.

- In output: Must deselect vertical angle between JK022808 and SB1.

- In Tracker.res: Data file cannot be found.

- In input generation: Overwritten the existing file or not.

2.6.9	To debug the model

- Remove the data fragment when “Must deselect” message appears.

- When no message appears after the matrix information is reported it is possible that a negative direction is in the file.

- In case of no convergence in matrix solving it is possible the residual is too high. Look for the highest residual point in distance and set the distance weight to be 9 meter and the direction weight to be 9 gon. This is a flag to not use this bad point. Rerun the analysis. A new point name may be given to the bad point to separate them from the observation set. This procedure reduces the total number of observations at a point.

- If the matrix converges, but does not pass the numerical tests increase the distance weight at the high residual points. Distance weight is more sensitive to the numerical test than the direction weights. Often, by changing the distance weight the direction residuals may reduce. After rerun always check the residual against the weight for improvement.

- Raising the distance weight across all points by a small amount (from 0.00003 meter to 0.0005 meter) may help passing the one-tailed test.

- Check the correction of coordinates and remove the high correction CNMs from bestfit by either edit the Parameter File or double click the indicator interactively in the LEGO Par File Editor.

# 3.0	Adjustment result evaluation

Resulting coordinates in Z, X, and Y orientation are printed in the output along with statistical data. It estimates the coordinates and their corresponding uncertainties at 1-sigma standard deviation.

## 3.1	Quality control of analysis

The following procedures are performed to ensure quality results:

- Inspect bestfit reference coordinate corrections for good fit to references. Low values reflect good fit to network and high values indicate poor fit.

- Ensure that either one- or two-tailed test on the estimated variance factor is passed. Adjust the default weights as needed.

- The quality of the survey is showed by the variance factor of each component which is the ratio of the mean square error a priori to the mean square error a posteriori. It should be close to one for an acceptable adjustment.

- Check residual to the weight ratio. Adjusting the coordinate weights is an iterative process. It is important to check for comparable residual and weight ratios after each rerun. Some high residuals may drop significantly after a rerun.

- Ensure acceptable distribution histogram of residuals is obtained.

- Ensure that Chi2 goodness of fit testing is passed.

## 3.2	To input the results into the Form B of the workbook

- Copy the output file into the worksheet and keep the name of the worksheet the same as the output name for paper trail purpose.

- Sort the final coordinates in alphabetical order of the point names.

- Go to Form B and highlight the coordinate cell. Use the VLOOKUP option to extract the coordinates from the output file by the point names and to place them in the cell. Excel command: VLOOKUP (point name, file name containing the coordinate component, number of column in the file, FALSE).

- Copy the standard point confidence ellipse of the points to the end of the file and sort it in alphabetical order of the point names. This operation groups the first line of the ellipse (uncertainties) together.

- Go to Form B highlight the uncertainty cell. Use the VLOOKUP option to extract the uncertainties from the output file by the point names and scale them by 3 before input. Excel command: VLOOKUP (point name, file name containing the uncertainty component, number of column in the file, FALSE)*3. Note that the uncertainties must be scaled from 1-sigma to 3-sigma standard deviation.

- Look at the last 6 columns in Form C (specification margins) for negative number. The cells are programmed to show the margin in canary color when it is less than 0.0 which indicates out-of-specification.

- Report the PSF that has out-of-specification margin in the summary report and non-conformance report. Both documents must be signed by the responsible engineer and the Precision Survey Group Leader.

# 4.0	Lift Saving Tips

  - Always terminate the program in the Home Window.

  - Be sure that the order of coordinate is Z, X, and Y in the .ZXY files and no blank line at the end of the file. Data Reduction Function sends error message without specific description when a blank line exists at the end of the data file.

  - The unit of the Cartesian coordinates must be in meter.

  - Be sure that all .ZXY file name is less than 8 characters. Data Reduction Function ignores files with name longer than 8 characters.

  - Re-start Geonet when re-generate tracker.res after adding .ZXY files to avoid fragment data in Tracker.res and input files.

  - Lego extract the data files in accordance with the file list in the SRV1.IDX file and sends message on missing files. Make sure that all data files are listed in the SRV1.IDX file; otherwise, the data file will not be in the reduction result file and no message will be sent on this blunder.

  - Be sure no data set is missing by counting the data sets in the Tracker.res file.

  - Be sure to convert negative angles into positive angles in Tracker.res file. Remember the unit of the angle is gon, 400 gon in a circle.

  - Check the .SUM file for at least 3 observations per point. The single observation points are marked by an asterisk.

  - Be sure that the input has bestfit reference coordinates at the CNMs because there is no error message for missing bestfit reference coordinates.

  - Be sure that the distance weight is 0.00015m for Total Station measurements and is 0.00003m for Laser Tracker measurements. For Total Station measurement should not have a “T” in the column next to distance weight.

  - Be sure that there is no fragment data (distance or directions in reduction result files and station names in input files).

  - For relative coordinate calculation tabulate the master and slave point pairs at the end of the input file after ‘Relative error point pairs’ and ‘END’ and an END card to terminate the data pairs.

  - Check for iteration completion. Increase the maximum iteration number and hope for the best. A well behave matrix does not take more than 10 iteration to converge. Its time to check for bad observations and coordinate corrections in case of no convergence.

  - Check the approximate coordinates for bestfit specification in the output file. The coordinates chosen for bestfit should not have a circle next to it.

  - Remove bestfit specification from the questionable CNMs such as having large coordinate corrections.

  - Large coordinate correction values indicated bad observations. Separate the bad subset observations by giving it a new name or set its weight to 9.0000m and 9.0000gon.

  - In general, passing only the one-tailed test on the estimated variance factor is acceptable. It is desirable to achieve the estimated variance factor around 1.0.

  - Adjust the weight according to the residuals. ‘N’, ‘T’, and ‘*’ are indication of bad observations. ‘N*’ means that the Chi2 test exceeds 3 times of residual. ‘T*’ indicates the residual is larger than 3 times of weight. Increasing the weight can bring the variance down but will raise the uncertainties.

  - Check the histogram of the residuals for comparable distribution.

  - Be sure it passed the Chi2 goodness of fit test on all coordinate components.

  - Check the uncertainties. Large uncertainties are caused by large weights.

  - Remember to scale the uncertainties by 3 to obtain their 3-sigma standard deviation values when transfer them to the Form B of the worksheet. Scaling for the coordinates is not required.

  - The tooling offset should be applied to the final resulting coordinates in the appropriate coordinate components.

# References:

Ref. 1	SLAC-395, Stanford Linear Accelerator Center, “Geonet, Stanford Linear Accelerator Center Survey and Alignment Workshop on Data Processing Using Geonet for Accelerator Alignment,” prepared for the Department of Energy under contract number DE-AC03-76SF0015, Stanford Linear Accelerator Center, Stanford University, Stanford, California, February 20-25, 1992.

Ref. 2	SMX Corporations, “SMXInsight Laser Tracker Software,” Version 3.0, Kennett Squate, PA, 1994

Ref. 3	NIF-00xxxxx, Dorothy S. Ng, “Survey Data Evaluation Procedure,” National Ignition Facility Project, Lawrence Livermore National Laboratory, November 2002

Ref. 4	NIF-0073962, D. S. Ng and Precision Survey Group, “Precision Survey and Evaluation for CSP-12 Component Position,” National Ignition Facility Project, Lawrence Livermore National Laboratory, November 2001

Ref. 5	NIF-0072070, D. S. Ng and Precision Survey Group, “CSP-13 Component Position Verification Report,” National Ignition Facility Project, Lawrence Livermore National Laboratory, September 2002

# Attachment 1	NIF component alignment verification data structure

| Path name & description (10) | Locations & description(16) | Epochs (16) |
| --- | --- | --- |
| C_VESSEL-C type vessels | CSF-11, C sf1, cl1 (U5) | SRV1 |
|  | CSF-12, C sf1, cl2 (U6) | SRV1 |
|  | CSF-13, C sf1, cl3 (U2) | SRV2-3 |
|  | CSF-14, C sf1, cl4 (U1) | SRV1-3 |
|  | CSF-21, C sf2, cl1 (U7) | SRV1 |
|  | CSF-22, C sf2, cl2 (U8) | SRV1 |
|  | CSF-23, C sf2, cl3 (U3) | SRV1 |
|  | CSF-24, C sf2, cl4 (U4) | SRV1-2 |
|  | CSF-IDF, IDF sf1-4, c3 | SRV1-2 |
| T_VESSEL-T type vessels | TSF-31, T sf3, cl1 (U1) | SRV1 |
|  | TSF-32, T sf3, cl2 (U2) | SRV1 |
|  | TSF-33, T sf3, cl3 (U3) | SRV1 |
|  | TSF-34, T sf3, cl4 (U4) | SRV1 |
|  | TSF-41, T sf4, cl1 (U2) | SRV1-2 |
|  | TSF-42, T sf4, cl2 (U4) | SRV1-2 |
|  | TSF-43, T sf4, cl3 (U1) | SRV1 |
|  | TSF-44, T sf4, cl4 (U3) | SRV1-3 |
| PABTS_BB, PABTS breadboard | BB_AM_C3, PABTS BB amp c3 | SRV1 |
|  | BB_AM_C4, PABTS BB amp c4 | SRV1 |
|  | BB_TG_C3, PABTS BB tg c3 | SRV1 |
|  | BB_TG_C2, PABTS BB tg c2 | SRV1 |
|  | BB_TG_C1, PABTS BB tg c1 | SRV1 |
|  | BB_AM_C2, PABTS BB amp c2 | SRV1 |
|  | PRSCSP16, PERISCOPE | SRV1-10 |
| CENTERSF, Center sf vessels | CCSFC42, center sf c4u2 | SRV1-4 |
|  | CCSFC24, center sf c2u4 | SRV1-2 |
|  | CCSFC31, center sf c3u1 | SRV1-3 |
|  | CCSFC13, center sf c1u3 | SRV1-2 |
|  | CTSFC31, center tsf c3u1 | SRV1-4 |
|  | CTSFC13, center tsf c1u3 | SRV1-4 |
|  | CTSFC24, center tsf c2u4 | SRV1-2 |
|  | CTSFC42, center tsf c4u2 | SRV1-2 |

Attachment 1	NIF component alignment data structure (cont’d)

| Path name & description (10) | Locations & description(16) | Epochs (16) |
| --- | --- | --- |
| OPTABLE, optical table | OPTSF1, trans optical table1 | SRV1-2 |
|  | OPTSF2, trans optical table2 | SRV1-2 |
|  | OPTSF3, trans optical table3 | SRV1-2 |
|  | OPTSF4, trans optical table4 | SRV1-3 |
|  | OPCSF1, cavi optical table1 | SRV1-2 |
|  | OPCSF2, cavi optical table2 | SRV1-2 |
|  | OPCSF3, cavi optical table3 | SRV1-2 |
|  | OPCSF4, cavi optical table4 | SRV1 |
|  | OPCSF4N, cavi optical table4, new | SRV1-2 |
|  | OPTSF4N, trans optical table4, n | SRV1-2 |
| OPTABLE, optical table | RELOTC4, relay optics 4 | SRV1 |
|  | RELOTC3, relay optics 3 | SRV1 |
|  | RELOTC1, relay optics 1 | SRV1 |
|  | RELOTC2, relay optics 2 | SRV1 |
| LMIRROR, Laser mirror | LM1_C1, Lm1 cl1 | SRV1-3 |
|  | LM1_C2, Lm1 cl2 | SRV1-3 |
|  | LM1_C3, Lm1 cl3 | SRV1-2 |
|  | LM1_C4, Lm1 cl4 | SRV1-2 |
|  | MA_CSP16, Main amp | SRV1-13 |
|  | PA_CSP16, Power amp | SRV1-9 |
|  | VLM1_C3, vLm1 cl3 | SRV1 |
|  | VLM1_C4, vLm1 cl4 | SRV1 |
|  | CSP14, CSP14_PAM | SRV1-2 |
|  | SPW_L3LS, SPW_LM3_Lightsource | SRV1-2 |
|  | CSP15, CSP15_TCSS | SRV1 |
| VERIFCNT, verify center vessels | CSFCN1, cavity center c1 | SRV1 |
|  | CSFCN2, cavity center c2 | SRV1 |
|  | CSFCN3, cavity center c3 | SRV1 |
|  | CSFCN4, cavity center c4 | SRV1 |
|  | TSFCN1, transport center c1 | SRV1 |
|  | TSFCN2, transport center c2 | SRV1 |
|  | TSFCN3, transport center c3 | SRV1 |
|  | TSFCN4, transport center c4 | SRV1 |

Attachment 1	NIF component alignment data structure (cont’d)

| Path name & description (10) | Locations & description(16) | Epochs (16) |
| --- | --- | --- |
| VERIFTBL, verify table | TSFTB42, transp table 42 | SRV1-2 |
|  | TSFTB31, transp table 31 | SRV1-2 |
|  | CSFTB42, cavity table 42 | SRV1 |
|  | CSFTB31, cavity table 31 | SRV1 |
|  | TSFTB24, transp table 24 | SRV1 |
|  | TSFTB13, transp table 13 | SRV1 |
|  | CSFTB24, cavity table 24 | SRV1 |
|  | CSFTB13, cavity table 13 | SRV1 |
| VERIE1. verify lb1 end | SF243, SF243 end vessel | SRV1 |
|  | SF141, SF141 end vessel | SRV1 |
|  | SF132, SF132 end vessel | SRV1-2 |
|  | SF233, SF233 end vessel | SRV1 |
|  | SF113, SF113 end vessel | SRV1 |
|  | SF217, SF217 end vessel | SRV1 |
|  | SF126, SF126 end vessel | SRV1-2 |
|  | SF228, SF228 end vessel | SRV1-2 |
| VERIFCOM, verify com | SF431, sf431 end vessel | SRV1-3 |
|  | SF443, sf443 end vessel | SRV1-2 |
|  | SF332, sf332 end vessel | SRV1-2 |
|  | SF343, sf343 end vessel | SRV1-2 |
|  | SF424, sf424 end vessel | SRV1 |
|  | SF324, sf324 end vessel | SRV1 |
|  | SF311, sf324 end vessel | SRV1 |
|  | SF412, sf412 end vessel | SRV1 |

# Attachment 2	Sample Field data file

3LE01F01	-3.592496	-8.645098	-2.934105

3LE02W02	-7.414272	-17.977691	-0.647216

3LE02W31	-1.026242	-7.064920	-0.562781

3LE02W32	-0.043043	-7.792695	-0.555755

3LF01F01	-1.773523	-6.170362	-2.909483

3LF01W01	4.611787	1.697741	-0.457352

3LF02F01	4.012446	-4.586151	-2.886429

3LF02W01	4.947005	1.048490	-0.465050

3LF02W02	5.922280	0.326837	-0.454817

3LF02W03	6.582751	-0.853686	-0.500055

3LF02W04	5.697013	-2.056394	-0.494845

3LF02W15	1.273113	-8.072145	-0.584369

3LF02W16	2.202589	-6.820734	-0.564692

3LF02W17	2.779244	-6.580212	-0.503974

3LG01F01	3.812655	1.421393	-2.829056

L1B31GS1	4.778804	0.207609	2.364782

L1B31GS2	4.423232	-0.275659	2.359887

L1B31GS3	4.138697	-0.662210	2.355997

L1B31GS4	4.782423	0.214318	1.419774

L1B31GS5	4.426911	-0.268985	1.414905

L1B31GS6	4.142402	-0.655563	1.411018

# Attachment 3	Sample Tracker.res

LM1LSC31 3LE01F01  225.07275 119.33511    9.81085

LM1LSC31 3LE02W02  224.90221 102.11800   19.45733

LM1LSC31 3LE02W31  209.18323 105.00819    7.16121

LM1LSC31 3LE02W32  200.35164 104.53247    7.81261

LM1LSC31 3LF01F01  217.81781 127.08774    7.04868

LM1LSC31 3LF01W01   77.54420 105.90765    4.93559

LM1LSC31 3LF02F01  154.24129 128.16213    6.74270

LM1LSC31 3LF02W01   86.70396 105.83816    5.07823

LM1LSC31 3LF02W02   96.49020 104.87213    5.94870

LM1LSC31 3LF02W03  108.21020 104.78684    6.65668

LM1LSC31 3LF02W04  122.05284 105.18971    6.07697

LM1LSC31 3LF02W15  190.04147 104.54469    8.19279

LM1LSC31 3LF02W16  180.11490 105.00524    7.18976

LM1LSC31 3LF02W17  174.55840 104.48420    7.16082

LM1LSC31 3LG01F01   77.28231 138.67756    4.95583

LM1LSC31 L1B31GS1   97.23603  70.77005    5.33594

LM1LSC31 L1B31GS2  103.96234  68.85027    5.02096

LM1LSC31 L1B31GS3  110.10058  67.39911    4.80812

LM1LSC31 L1B31GS4   97.14898  81.64547    4.99332

LM1LSC31 L1B31GS5  103.86344  80.33995    4.65530

LM1LSC31 L1B31GS6  109.99207  79.33884    4.42496

LM1LSC32 3LE02W31  147.32666  99.43903    9.39426

LM1LSC32 3LF01F01  154.35021 116.03126    9.08610

LM1LSC32 3LF02F01  106.76103 119.76548    7.24627

LM1LSC32 3LF02W02   51.56528  96.60253    4.51128

LM1LSC32 3LF02W15  131.29150  99.57444   10.00374

LM1LSC32 3LF02W17  120.54744  98.82880    8.57087

LM1LSC32 3LG01F01   43.12741 149.54288    3.04584

LM1LSC32 L1B31GS1   61.18805  54.40642    4.65422

LM1LSC32 L1B31GS2   72.10678  54.29476    4.63304

LM1LSC32 L1B31GS3   80.73896  54.86618    4.67180

LM1LSC32 L1B31GS4   60.97062  65.55308    4.09764

LM1LSC32 L1B31GS5   71.88656  65.46936    4.07372

LM1LSC32 L1B31GS6   80.52482  65.99059    4.11784

LM1LSC33 3LE02W31  132.44427  94.95599   11.41411

LM1LSC33 3LF01F01  138.51793 108.38547   11.00470

LM1LSC33 3LF01W01   66.39068  76.31658    2.40278

LM1LSC33 3LF02F01  102.09985 111.54267    8.25576

LM1LSC33 3LF02W04   81.42429  90.97677    6.11036

LM1LSC33 3LF02W16  114.36956  94.65767   10.38855

LM1LSC33 3LG01F01   91.76540 138.58452    2.61287

LM1LSC33 L1B31GS1   79.50170  48.99492    5.16368

LM1LSC33 L1B31GS2   88.14121  51.67291    5.39228

LM1LSC33 L1B31GS3   94.03007  53.98931    5.61474

LM1LSC33 L1B31GS5   88.22625  60.82119    4.79205

LM1LSC33 L1B31GS6   94.10615  62.98217    5.04113

# Attachment 4	Sample Level.res

3LG01F01  3LF01F01       -0.00514

3LF01F01  3LD01F01        0.00523

3LD01F01  3LD02F02       -0.00932

3LD02F02  3LD03F03        0.00524

3LD03F03  3LE03F02       -0.01102

3LE03F02  3LG03F01        0.00570

3LG03F01  3LG02F01        0.01091

3LG02F01  3LG01F01       -0.00155

3LG03F01  3LE03F02       -0.00567

3LE03F02  3LD03F03        0.01103

3LD03F03  3LD04F04       -0.00301

3LD04F04  3LE04F02       -0.00860

3LE04F02  3LG04F02        0.00825

3LG04F02  3LG03F01       -0.00196

3LG04F02  3LE04F02       -0.00820

3LE04F02  3LD04F04        0.00862

3LD04F04  3LD06F03        0.00382

3LD06F03  3LE06F01       -0.01689

3LE06F01  3LG06F01        0.00721

3LG06F01  3LG04F02        0.00553

3LG06F01  3LE06F01       -0.00717

3LE06F01  3LD06F03        0.01691

3LD06F03  3LD07F06       -0.01716

3LD07F06  3LE07F02        0.00214

3LE07F02  3LG07F02        0.00682

3LG07F02  3LG06F01       -0.00153

3LG07F02  3LE07F02       -0.00685

3LE07F02  3LD07F06       -0.00211

3LD07F06  3LD08F03        0.00623

3LD08F03  3LD09F02        0.00169

3LD09F02  3LF09F02       -0.00422

3LF09F02  3LG09F02        0.00643

3LG09F02  3LG08F02        0.00399

3LG08F02  3LG07F02       -0.00508

3LG09F02  3LF09F02       -0.00641

3LF09F02  3LD09F02        0.00426

# Attachment 5	Sample Redir.res

0215009A

3LL00F03        0.00000

L228F002      255.78581

3LD01F01      248.44053

3LE01F01      245.32189

3LF01F01      243.23528

3LF02F02      226.53634

3LF02F01      208.95835

3LG01F01      205.02786

3LG02F01      162.79743

L228F001      155.36117

3LG02F02      157.89100

3LG03F01      156.16202

3LG03F02      155.55385

L225F001      153.56650

L222F001      153.31931

L218F001      153.25694

L215F001      153.26605

3LG14F01      153.54448

QUIT

0215009B

3LL00F03        0.00000

3LE02F02      249.60295

3LF02F02      250.94110

3LF01F01      293.67873

3LG01F01       13.65711

3LG02F01       47.66573

L228F001       48.80584

3LG02F02       90.66592

3LG03F03      114.39322

3LF03F02      142.74675

3LF03F01      140.37066

3LF03F03      172.91357

AB30W002        4.39143

QUIT

# Attachment 6	Sample Redisth.res

0215009A  3LL00F03    18.81121  0.00006

0215009A  L228F002    25.50507  0.00006

0215009A  3LD01F01    24.05961  0.00006

0215009A  3LE01F01    14.56697  0.00006

0215009A  3LF01F01    11.54531  0.00006

0215009A  3LF02F02    12.37044  0.00000

0215009A  3LF02F01     8.72441  0.00006

0215009A  3LG01F01     2.99124  0.00000

0215009A  3LG02F01     5.32727  0.00006

0215009A  L228F001     5.39234  0.00000

0215009A  3LG02F02    10.45994  0.00000

0215009A  3LG03F01    16.46711  0.00006

0215009A  3LG03F02    20.69501  0.00006

0215009A  L225F001    22.29234  0.00000

0215009A  L222F001    48.25981  0.00006

0215009A  L218F001    75.19640  0.00015

0215009A  L215F001    98.09940  0.00006

0215009A  3LG14F01   125.83877  0.00006

0215009B  3LL00F03    27.64485  0.00000

0215009B  3LE02F02     7.14278  0.00012

0215009B  3LF02F02     4.10848  0.00006

0215009B  3LF01F01     5.36118  0.00006

0215009B  3LG01F01     6.63504  0.00000

0215009B  3LG02F01     6.80194  0.00000

0215009B  L228F001     7.38081  0.00006

0215009B  3LG02F02     8.55794  0.00000

0215009B  3LG03F03    11.11795  0.00000

0215009B  3LF03F02    10.20794  0.00000

0215009B  3LF03F01    15.56558  0.00006

0215009B  3LF03F03    10.31434  0.00000

0215009B  AB30W002    36.71679  0.00012

# Attachment 7	Sample Redists.res

0215009A  3LL00F03    18.81121  0.00006

0215009A  L228F002    25.50507  0.00006

0215009A  3LD01F01    24.05961  0.00006

0215009A  3LE01F01    14.56697  0.00006

0215009A  3LF01F01    11.54531  0.00006

0215009A  3LF02F02    12.37044  0.00000

0215009A  3LF02F01     8.72441  0.00006

0215009A  3LG01F01     2.99124  0.00000

0215009A  3LG02F01     5.32727  0.00006

0215009A  L228F001     5.39234  0.00000

0215009A  3LG02F02    10.45994  0.00000

0215009A  3LG03F01    16.46711  0.00006

0215009A  3LG03F02    20.69501  0.00006

0215009A  L225F001    22.29234  0.00000

0215009A  L222F001    48.25981  0.00006

0215009A  L218F001    75.19641  0.00015

0215009A  L215F001    98.09941  0.00006

0215009A  3LG14F01   125.83877  0.00006

0215009B  3LL00F03    27.64485  0.00000

0215009B  3LE02F02     7.14278  0.00012

0215009B  3LF02F02     4.10848  0.00006

0215009B  3LF01F01     5.36118  0.00006

0215009B  3LG01F01     6.63504  0.00000

0215009B  3LG02F01     6.80194  0.00000

0215009B  L228F001     7.38081  0.00006

0215009B  3LG02F02     8.55794  0.00000

0215009B  3LG03F03    11.11795  0.00000

0215009B  3LF03F02    10.20795  0.00000

0215009B  3LF03F01    15.56558  0.00006

0215009B  3LF03F03    10.31435  0.00000

0215009B  AB30W002    36.71679  0.00012

0215009C  3LD02F03    18.19509  0.00006

# Attachment 8	Sample Zenith.res

0215009A

3LL00F03      105.13333

L228F002      103.75058

3LD01F01      103.97012

3LE01F01      106.58745

3LF01F01      108.32026

3LF02F02      107.91461

3LF02F01      111.12257

3LG01F01      133.42601

3LG02F01      118.14478

L228F001      117.95596

3LG02F02      109.23700

3LG03F01      105.84154

3LG03F02      104.64326

L225F001      104.32824

L222F001      101.99743

L218F001      101.27392

L215F001      100.98721

3LG14F01      100.77234

QUIT

0215009B

3LL00F03      103.47916

3LE02F02      113.63528

3LF02F02      124.27465

3LF01F01      118.04669

3LG01F01      114.46305

3LG02F01      114.08705

L228F001      112.99188

3LG02F02      111.27165

3LG03F03      108.69696

3LF03F02      109.45778

3LF03F01      106.18059

3LF03F03      109.35731

AB30W002      100.72034

# Attachment 9	Sample network file for Laser Bay 1

3LP01F01    19.54943    33.34407    0.02689

3LQ01F01    19.55190    42.71110    0.02455

3LN01F01    19.55748    30.13341    0.02125

3LM01F01    19.56152    20.73276    0.02254

3LN01W02    19.96062    31.07985    2.37237

3LN01W01    19.96231    32.42639    2.36164

3LP02W01    19.96476    43.39339    2.43717

3LN02W01    19.96572    20.11475    2.42358

3LM02W01    20.13346    19.79529    1.94199

3LQ02W01    20.13924    43.71856    1.99118

3LN02W02    20.41813    20.44584    2.44285

3LP02W02    20.43532    43.07263    2.42856

3LP02W15    20.44190    32.99343    2.42526

3LN02W15    20.44859    30.51487    2.42791

3LP02W16    21.82033    32.99623    2.42012

3LN02W16    21.82436    30.51581    2.43095

3LN02W03    21.82608    20.44179    2.44092

3LP02W03    21.84197    43.07792    2.43462

3LQ02W02    22.14159    43.72745    1.98015

3LM02W02    22.15531    19.79377    1.94774

3LP02F02    22.65488    33.31177    0.00067

3LQ02F01    22.68242    43.79864    0.01312

3LN02F01    22.71114    30.16161    0.00239

3LM02F02    22.71969    19.72507    0.02730

L127F002    22.91725    44.47587    0.01439

L127F001    22.98775    19.06040    0.01140

3LP02W04    23.05397    42.49981    2.42254

3LN02W17    23.06215    29.98403    2.41465

3LP02W05    23.06260    40.99981    2.42795

3LN02W04    23.06263    20.96978    2.41868

# Attachment 10	Sample input file (LM1LSC3A.inp)

SLAC   3 D C D   -   ORIENTATION DATA CAPTURE

PROJECT =

TASK =

DATE = 9/5/2002 1:31:47 PM

LISTING = STATS

Theodolite Stations

LM1LSC31

LM1LSC32

LM1LSC33

END

Object Points

3LE01F01       19.48947      -33.32545        0.01616

1.00E+03       1.00E+03       1.00E+03

3LE02W02       21.94122      -43.08753        2.38588

1.00E+03       1.00E+03       1.00E+03

3LE02W31       20.61697      -30.51231        2.36635

1.00E+03       1.00E+03       1.00E+03

3LE02W32       21.84043      -30.51562        2.37473

1.00E+03       1.00E+03       1.00E+03

3LF01F01       19.48759      -30.25390        0.01603

1.00E+03       1.00E+03       1.00E+03

3LF01W01       19.96380      -20.11367        2.38758

1.00E+03       1.00E+03       1.00E+03

3LF02F01       23.20845      -25.54827        0.00465

1.00E+03       1.00E+03       1.00E+03

3LF02W01       20.61874      -20.43795        2.38302

1.00E+03       1.00E+03       1.00E+03

3LF02W02       21.83216      -20.44098        2.39449

1.00E+03       1.00E+03       1.00E+03

3LF02W03       23.06321      -20.99994        2.35499

1.00E+03       1.00E+03       1.00E+03

3LF02W04       23.06313      -22.49378        2.37205

1.00E+03       1.00E+03       1.00E+03

3LF02W15       23.06568      -29.96068        2.34300

1.00E+03       1.00E+03       1.00E+03

3LF02W16       23.07272      -28.40143        2.35002

1.00E+03       1.00E+03       1.00E+03

3LF02W17       23.39465      -27.86533        2.40664

1.00E+03       1.00E+03       1.00E+03

3LG01F01       19.48667      -20.82814        0.02071

1.00E+03       1.00E+03       1.00E+03

L1B31GS1

L1B31GS2

L1B31GS3

L1B31GS4

L1B31GS5

L1B31GS6

END

Distances

LM1LSC31  3LE01F01        9.81085   0.00003   T

LM1LSC31  3LE02W02       19.45733   0.00003   T

LM1LSC31  3LE02W31        7.16121   0.00003   T

LM1LSC31  3LE02W32        7.81261   0.00003   T

LM1LSC31  3LF01F01        7.04868   0.00003   T

LM1LSC31  3LF01W01        4.93559   0.00003   T

LM1LSC31  3LF02F01        6.74270   0.00003   T

LM1LSC31  3LF02W01        5.07823   0.00003   T

LM1LSC31  3LF02W02        5.94870   0.00003   T

LM1LSC31  3LF02W03        6.65668   0.00003   T

LM1LSC31  3LF02W04        6.07697   0.00003   T

LM1LSC31  3LF02W15        8.19279   0.00003   T

LM1LSC31  3LF02W16        7.18976   0.00003   T

LM1LSC31  3LF02W17        7.16082   0.00003   T

LM1LSC31  3LG01F01        4.95583   0.00003   T

LM1LSC31  L1B31GS1        5.33594   0.00003   T

LM1LSC31  L1B31GS2        5.02096   0.00003   T

LM1LSC31  L1B31GS3        4.80812   0.00003   T

LM1LSC31  L1B31GS4        4.99332   0.00003   T

LM1LSC31  L1B31GS5        4.65530   0.00003   T

LM1LSC31  L1B31GS6        4.42496   0.00003   T

LM1LSC32  3LE02W31        9.39426   0.00003   T

LM1LSC32  3LF01F01        9.08610   0.00003   T

LM1LSC32  3LF02F01        7.24627   0.00003   T

LM1LSC32  3LF02W02        4.51128   0.00003   T

LM1LSC32  3LF02W15       10.00374   0.00003   T

LM1LSC32  3LF02W17        8.57087   0.00003   T

LM1LSC32  3LG01F01        3.04584   0.00003   T

LM1LSC32  L1B31GS1        4.65422   0.00003   T

LM1LSC32  L1B31GS2        4.63304   0.00003   T

LM1LSC32  L1B31GS3        4.67180   0.00003   T

LM1LSC32  L1B31GS4        4.09764   0.00003   T

LM1LSC32  L1B31GS5        4.07372   0.00003   T

LM1LSC32  L1B31GS6        4.11784   0.00003   T

LM1LSC33  3LE02W31       11.41411   0.00003   T

LM1LSC33  3LF01F01       11.00470   0.00003   T

LM1LSC33  3LF01W01        2.40278   0.00003   T

LM1LSC33  3LF02F01        8.25576   0.00003   T

LM1LSC33  3LF02W04        6.11036   0.00003   T

LM1LSC33  3LF02W16       10.38855   0.00003   T

LM1LSC33  3LG01F01        2.61287   0.00003   T

LM1LSC33  L1B31GS1        5.16368   0.00003   T

LM1LSC33  L1B31GS2        5.39228   0.00003   T

LM1LSC33  L1B31GS3        5.61474   0.00003   T

LM1LSC33  L1B31GS5        4.79205   0.00003   T

LM1LSC33  L1B31GS6        5.04113   0.00003   T

END

Height differences

END

Observations

LM1LSC31  3LE01F01  225.07275  119.33511 0.00065 0.00065

LM1LSC31  3LE02W02  224.90221  102.11800 0.00033 0.00033

LM1LSC31  3LE02W31  209.18323  105.00819 0.00089 0.00089

LM1LSC31  3LE02W32  200.35164  104.53247 0.00081 0.00081

LM1LSC31  3LF01F01  217.81781  127.08774 0.00090 0.00090

LM1LSC31  3LF01W01   77.54420  105.90765 0.00129 0.00129

LM1LSC31  3LF02F01  154.24129  128.16213 0.00094 0.00094

LM1LSC31  3LF02W01   86.70396  105.83816 0.00125 0.00125

LM1LSC31  3LF02W02   96.49020  104.87213 0.00107 0.00107

LM1LSC31  3LF02W03  108.21020  104.78684 0.00096 0.00096

LM1LSC31  3LF02W04  122.05284  105.18971 0.00105 0.00105

LM1LSC31  3LF02W15  190.04147  104.54469 0.00078 0.00078

LM1LSC31  3LF02W16  180.11490  105.00524 0.00089 0.00089

LM1LSC31  3LF02W17  174.55840  104.48420 0.00089 0.00089

LM1LSC31  3LG01F01   77.28231  138.67756 0.00128 0.00128

LM1LSC31  L1B31GS1   97.23603   70.77005 0.00119 0.00119

LM1LSC31  L1B31GS2  103.96234   68.85027 0.00127 0.00127

LM1LSC31  L1B31GS3  110.10058   67.39911 0.00132 0.00132

LM1LSC31  L1B31GS4   97.14898   81.64547 0.00127 0.00127

LM1LSC31  L1B31GS5  103.86344   80.33995 0.00137 0.00137

LM1LSC31  L1B31GS6  109.99207   79.33884 0.00144 0.00144

LM1LSC32  3LE02W31  147.32666   99.43903 0.00068 0.00068

LM1LSC32  3LF01F01  154.35021  116.03126 0.00070 0.00070

LM1LSC32  3LF02F01  106.76103  119.76548 0.00088 0.00088

LM1LSC32  3LF02W02   51.56528   96.60253 0.00141 0.00141

LM1LSC32  3LF02W15  131.29150   99.57444 0.00064 0.00064

LM1LSC32  3LF02W17  120.54744   98.82880 0.00074 0.00074

LM1LSC32  3LG01F01   43.12741  149.54288 0.00209 0.00209

LM1LSC32  L1B31GS1   61.18805   54.40642 0.00137 0.00137

LM1LSC32  L1B31GS2   72.10678   54.29476 0.00137 0.00137

LM1LSC32  L1B31GS3   80.73896   54.86618 0.00136 0.00136

LM1LSC32  L1B31GS4   60.97062   65.55308 0.00155 0.00155

LM1LSC32  L1B31GS5   71.88656   65.46936 0.00156 0.00156

LM1LSC32  L1B31GS6   80.52482   65.99059 0.00155 0.00155

LM1LSC33  3LE02W31  132.44427   94.95599 0.00056 0.00056

LM1LSC33  3LF01F01  138.51793  108.38547 0.00058 0.00058

LM1LSC33  3LF01W01   66.39068   76.31658 0.00265 0.00265

LM1LSC33  3LF02F01  102.09985  111.54267 0.00077 0.00077

LM1LSC33  3LF02W04   81.42429   90.97677 0.00104 0.00104

LM1LSC33  3LF02W16  114.36956   94.65767 0.00061 0.00061

LM1LSC33  3LG01F01   91.76540  138.58452 0.00244 0.00244

LM1LSC33  L1B31GS1   79.50170   48.99492 0.00123 0.00123

LM1LSC33  L1B31GS2   88.14121   51.67291 0.00118 0.00118

LM1LSC33  L1B31GS3   94.03007   53.98931 0.00113 0.00113

LM1LSC33  L1B31GS5   88.22625   60.82119 0.00133 0.00133

LM1LSC33  L1B31GS6   94.10615   62.98217 0.00126 0.00126

END

Control Information

Fixed Coordinates

END

Relative error point pairs

END

# Attachment 11	Sample LM1LSC3A.SUM file

PROJECT = NIF verification of component installation

TASK = Verification of LM1 light source, Cluster 3, 09/05/02

DATE = 9/5/2002 1:31:47 PM

Number of observations to each point in : c:\GEONET\LMIRROR\SPW_L3LS\ADJUST\SRV2\LM1LSC3A.INP

Name           Hang  Zang  Sdst  Lhgt

3LE01F01          1     1     1       *

3LE02W02          1     1     1       *

3LE02W31          3     3     3

3LE02W32          1     1     1       *

3LF01F01          3     3     3

3LF01W01          2     2     2

3LF02F01          3     3     3

3LF02W01          1     1     1       *

3LF02W02          2     2     2

3LF02W03          1     1     1       *

3LF02W04          2     2     2

3LF02W15          2     2     2

3LF02W16          2     2     2

3LF02W17          2     2     2

3LG01F01          3     3     3

L1B31GS1          3     3     3

L1B31GS2          3     3     3

L1B31GS3          3     3     3

L1B31GS4          2     2     2

L1B31GS5          3     3     3

L1B31GS6          3     3     3

# Attachment 12	Sample LM1LSC3A.ORG file

SLAC   3 D C D   -   ORIENTATION DATA CAPTURE

PROJECT =

TASK =

DATE = 9/5/2002 1:31:47 PM

LISTING = STATS

STA LM1LSC31

STA LM1LSC32

STA LM1LSC33

PTS 3LE01F01        19.48947      -33.32545        0.01616

PTS 3LE02W02        21.94122      -43.08753        2.38588

PTS 3LE02W31        20.61697      -30.51231        2.36635

PTS 3LE02W32        21.84043      -30.51562        2.37473

PTS 3LF01F01        19.48759      -30.25390        0.01603

PTS 3LF01W01        19.96380      -20.11367        2.38758

PTS 3LF02F01        23.20845      -25.54827        0.00465

PTS 3LF02W01        20.61874      -20.43795        2.38302

PTS 3LF02W02        21.83216      -20.44098        2.39449

PTS 3LF02W03        23.06321      -20.99994        2.35499

PTS 3LF02W04        23.06313      -22.49378        2.37205

PTS 3LF02W15        23.06568      -29.96068        2.34300

PTS 3LF02W16        23.07272      -28.40143        2.35002

PTS 3LF02W17        23.39465      -27.86533        2.40664

PTS 3LG01F01        19.48667      -20.82814        0.02071

PTS L1B31GS1

PTS L1B31GS2

PTS L1B31GS3

PTS L1B31GS4

PTS L1B31GS5

PTS L1B31GS6

TRK LM1LSC31   3LE01F01  225.07275  0.00065 119.33511   0.00065      9.81085   0.00003

TRK LM1LSC31   3LE02W02  224.90221  0.00033 102.11800   0.00033     19.45733   0.00003

TRK LM1LSC31   3LE02W31  209.18323  0.00089 105.00819   0.00089      7.16121   0.00003

TRK LM1LSC31   3LE02W32  200.35164  0.00081 104.53247   0.00081      7.81261   0.00003

TRK LM1LSC31   3LF01F01  217.81781  0.00090 127.08774   0.00090      7.04868   0.00003

TRK LM1LSC31   3LF01W01   77.54420  0.00129 105.90765   0.00129      4.93559   0.00003

TRK LM1LSC31   3LF02F01  154.24129  0.00094 128.16213   0.00094      6.74270   0.00003

TRK LM1LSC31   3LF02W01   86.70396  0.00125 105.83816   0.00125      5.07823   0.00003

TRK LM1LSC31   3LF02W02   96.49020  0.00107 104.87213   0.00107      5.94870   0.00003

TRK LM1LSC31   3LF02W03  108.21020  0.00096 104.78684   0.00096      6.65668   0.00003

TRK LM1LSC31   3LF02W04  122.05284  0.00105 105.18971   0.00105      6.07697   0.00003

TRK LM1LSC31   3LF02W15  190.04147  0.00078 104.54469   0.00078      8.19279   0.00003

TRK LM1LSC31   3LF02W16  180.11490  0.00089 105.00524   0.00089      7.18976   0.00003

TRK LM1LSC31   3LF02W17  174.55840  0.00089 104.48420   0.00089      7.16082   0.00003

TRK LM1LSC31   3LG01F01   77.28231  0.00128 138.67756   0.00128      4.95583   0.00003

TRK LM1LSC31   L1B31GS1   97.23603  0.00119  70.77005   0.00119      5.33594   0.00003

TRK LM1LSC31   L1B31GS2  103.96234  0.00127  68.85027   0.00127      5.02096   0.00003

TRK LM1LSC31   L1B31GS3  110.10058  0.00132  67.39911   0.00132      4.80812   0.00003

TRK LM1LSC31   L1B31GS4   97.14898  0.00127  81.64547   0.00127      4.99332   0.00003

TRK LM1LSC31   L1B31GS5  103.86344  0.00137  80.33995   0.00137      4.65530   0.00003

TRK LM1LSC31   L1B31GS6  109.99207  0.00144  79.33884   0.00144      4.42496   0.00003

TRK LM1LSC32   3LE02W31  147.32666  0.00068  99.43903   0.00068      9.39426   0.00003

TRK LM1LSC32   3LF01F01  154.35021  0.00070 116.03126   0.00070      9.08610   0.00003

TRK LM1LSC32   3LF02F01  106.76103  0.00088 119.76548   0.00088      7.24627   0.00003

TRK LM1LSC32   3LF02W02   51.56528  0.00141  96.60253   0.00141      4.51128   0.00003

TRK LM1LSC32   3LF02W15  131.29150  0.00064  99.57444   0.00064     10.00374   0.00003

TRK LM1LSC32   3LF02W17  120.54744  0.00074  98.82880   0.00074      8.57087   0.00003

TRK LM1LSC32   3LG01F01   43.12741  0.00209 149.54288   0.00209      3.04584   0.00003

TRK LM1LSC32   L1B31GS1   61.18805  0.00137  54.40642   0.00137      4.65422   0.00003

TRK LM1LSC32   L1B31GS2   72.10678  0.00137  54.29476   0.00137      4.63304   0.00003

TRK LM1LSC32   L1B31GS3   80.73896  0.00136  54.86618   0.00136      4.67180   0.00003

TRK LM1LSC32   L1B31GS4   60.97062  0.00155  65.55308   0.00155      4.09764   0.00003

TRK LM1LSC32   L1B31GS5   71.88656  0.00156  65.46936   0.00156      4.07372   0.00003

TRK LM1LSC32   L1B31GS6   80.52482  0.00155  65.99059   0.00155      4.11784   0.00003

TRK LM1LSC33   3LE02W31  132.44427  0.00056  94.95599   0.00056     11.41411   0.00003

TRK LM1LSC33   3LF01F01  138.51793  0.00058 108.38547   0.00058     11.00470   0.00003

TRK LM1LSC33   3LF01W01   66.39068  0.00265  76.31658   0.00265      2.40278   0.00003

TRK LM1LSC33   3LF02F01  102.09985  0.00077 111.54267   0.00077      8.25576   0.00003

TRK LM1LSC33   3LF02W04   81.42429  0.00104  90.97677   0.00104      6.11036   0.00003

TRK LM1LSC33   3LF02W16  114.36956  0.00061  94.65767   0.00061     10.38855   0.00003

TRK LM1LSC33   3LG01F01   91.76540  0.00244 138.58452   0.00244      2.61287   0.00003

TRK LM1LSC33   L1B31GS1   79.50170  0.00123  48.99492   0.00123      5.16368   0.00003

TRK LM1LSC33   L1B31GS2   88.14121  0.00118  51.67291   0.00118      5.39228   0.00003

TRK LM1LSC33   L1B31GS3   94.03007  0.00113  53.98931   0.00113      5.61474   0.00003

TRK LM1LSC33   L1B31GS5   88.22625  0.00133  60.82119   0.00133      4.79205   0.00003

TRK LM1LSC33   L1B31GS6   94.10615  0.00126  62.98217   0.00126      5.04113   0.00003

END

# Attachment 13	Sample LM1LSC3A.PAR file

Itermax       10

Valstop       0.00001

Dimension     3

Not in Datum

LM1LSC31   0 0 0

LM1LSC32   0 0 0

LM1LSC33   0 0 0

3LE01F01   1 1 1

3LE02W02   1 0 0

3LE02W31   1 0 1

3LE02W32   1 1 1

3LF01F01   1 1 1

3LF01W01   1 0 0

3LF02F01   1 1 0

3LF02W01   1 0 1

3LF02W02   0 0 1

3LF02W03   1 1 1

3LF02W04   1 1 1

3LF02W15   0 1 1

3LF02W16   1 0 1

3LF02W17   1 0 1

3LG01F01   1 1 1

L1B31GS1   0 0 0

L1B31GS2   0 0 0

L1B31GS3   0 0 0

L1B31GS4   0 0 0

L1B31GS5   0 0 0

L1B31GS6   0 0 0

End

# Attachment 14	Sample output file (LM1LSC3A.out)

File: c:\GEONET\LMIRROR\SPW_L3LS\ADJUST\SRV2\LM1LSC3A.out

Summary

3D problem

number of instruments                3

number of points                    21

number of distances                 46

number of horizontal directions     46

number of vertical directions       46

number of coordinates unknowns      72

number of nuisance parameters        9

number of datum parameters           6

Approximate values

LM1LSC31             17.254880o     -24.209958o       2.874147o

0.008088        0.001188       -2.205280

LM1LSC32             17.493015o     -21.654884o       2.169687o

0.012876       -0.000108       -1.082397

LM1LSC33             17.817705o     -19.479852o       1.512026o

-0.005051        0.002307       -0.758379

3LE01F01             19.489470      -33.325450        0.016160

3LE02W02             21.941220      -43.087530o       2.385880o

3LE02W31             20.616970      -30.512310o       2.366350

3LE02W32             21.840430      -30.515620        2.374730

3LF01F01             19.487590      -30.253900        0.016030

3LF01W01             19.963800      -20.113670o       2.387580o

3LF02F01             23.208450      -25.548270        0.004650o

3LF02W01             20.618740      -20.437950o       2.383020

3LF02W02             21.832160o     -20.440980o       2.394490

3LF02W03             23.063210      -20.999940        2.354990

3LF02W04             23.063130      -22.493780        2.372050

3LF02W15             23.065680o     -29.960680        2.343000

3LF02W16             23.072720      -28.401430o       2.350020

3LF02W17             23.394650      -27.865330o       2.406640

3LG01F01             19.486670      -20.828140        0.020710

L1B31GS1             20.978221o     -21.191337o       5.219265o

L1B31GS2             20.978265o     -21.791323o       5.219148o

L1B31GS3             20.978214o     -22.271322o       5.219085o

L1B31GS4             20.978088o     -21.191316o       4.274188o

L1B31GS5             20.978340o     -21.791439o       4.274174o

L1B31GS6             20.978329o     -22.271437o       4.274145o

Compact storage solution

Version 0.0

Corrections to coordinates

LM1LSC31              0.000431       -0.000091        0.000584

LM1LSC32             -0.000015       -0.000358        0.000343

LM1LSC33             -0.000495       -0.000417        0.000121

3LE01F01              0.000134        0.000019        0.000154

3LE02W02             -0.000022       -0.000810       -0.001369

3LE02W31              0.000197       -0.000306       -0.000055

3LE02W32              0.000018       -0.000243       -0.000108

3LF01F01              0.000009       -0.000178        0.000224

3LF01W01             -0.000119        0.000843       -0.000295

3LF02F01             -0.000059       -0.000100        0.000603

3LF02W01             -0.000235        0.000885       -0.000154

3LF02W02             -0.000427        0.000910       -0.000103

3LF02W03              0.000261        0.000271        0.000006

3LF02W04             -0.000093        0.000525        0.000150

3LF02W15              0.000449       -0.000301       -0.000133

3LF02W16              0.000183       -0.000607       -0.000061

3LF02W17              0.000030       -0.000719        0.000061

3LG01F01             -0.000304        0.000008        0.000019

L1B31GS1              0.000243        0.000153        0.000013

L1B31GS2              0.000287        0.000148        0.000061

L1B31GS3              0.000325        0.000138        0.000094

L1B31GS4              0.000288        0.000099        0.000025

L1B31GS5              0.000217        0.000197        0.000044

L1B31GS6              0.000271        0.000181        0.000071

Final results after 2 iterations

LM1LSC31

RxRyRz :              0.008053        0.001065       -2.205280

xyz   :             17.255311      -24.210050        2.874731

LM1LSC32

RxRyRz :              0.012869       -0.000162       -1.082434

xyz   :             17.493000      -21.655243        2.170030

LM1LSC33

RxRyRz :             -0.005046        0.002295       -0.758452

xyz   :             17.817210      -19.480269        1.512146

3LE01F01             19.489604      -33.325431        0.016314

3LE02W02             21.941198      -43.088340        2.384511

3LE02W31             20.617167      -30.512616        2.366295

3LE02W32             21.840448      -30.515863        2.374622

3LF01F01             19.487599      -30.254078        0.016254

3LF01W01             19.963681      -20.112827        2.387285

3LF02F01             23.208391      -25.548370        0.005253

3LF02W01             20.618505      -20.437065        2.382866

3LF02W02             21.831733      -20.440070        2.394387

3LF02W03             23.063471      -20.999669        2.354996

3LF02W04             23.063037      -22.493255        2.372200

3LF02W15             23.066129      -29.960981        2.342867

3LF02W16             23.072903      -28.402037        2.349959

3LF02W17             23.394680      -27.866049        2.406701

3LG01F01             19.486366      -20.828132        0.020729

L1B31GS1             20.978464      -21.191183        5.219278

L1B31GS2             20.978553      -21.791174        5.219209

L1B31GS3             20.978539      -22.271184        5.219179

L1B31GS4             20.978376      -21.191217        4.274213

L1B31GS5             20.978557      -21.791242        4.274217

L1B31GS6             20.978600      -22.271256        4.274217

Pass the one-tailed test on the estimated variance factor

Fail the two-tailed test on the estimated variance factor

degree of freedom =     63

variance          =      0.176105

sig a priori      =      1.000000

sig a posteriori  =      0.419649

variance component for distances         0.261555

sigma a priori                           1.000000

sigma a posteriori for distances         0.511424

variance component for horizontal        0.105115

sigma a priori                           1.000000

sigma a posteriori for horizontal        0.324215

variance component for vertical          0.207317

sigma a priori                           1.000000

sigma a posteriori for vertical          0.455321

distance residuals

LM1LSC31 3LE01F01        9.810850        0.000000   0.000000

LM1LSC31 3LE02W02       19.457330       -0.000000   0.000000

LM1LSC31 3LE02W31        7.161210       -0.000000   0.000020

LM1LSC31 3LE02W32        7.812610       -0.000000   0.000000

LM1LSC31 3LF01F01        7.048680       -0.000028   0.000020              T *

LM1LSC31 3LF01W01        4.935590       -0.000006   0.000009

LM1LSC31 3LF02F01        6.742700       -0.000013   0.000018

LM1LSC31 3LF02W01        5.078230       -0.000000   0.000000

LM1LSC31 3LF02W02        5.948700       -0.000007   0.000016

LM1LSC31 3LF02W03        6.656680        0.000000   0.000000

LM1LSC31 3LF02W04        6.076970       -0.000003   0.000011

LM1LSC31 3LF02W15        8.192790        0.000006   0.000018

LM1LSC31 3LF02W16        7.189760        0.000009   0.000016

LM1LSC31 3LF02W17        7.160820        0.000008   0.000018

LM1LSC31 3LG01F01        4.955830       -0.000006   0.000014

LM1LSC31 L1B31GS1        5.335940       -0.000006   0.000018

LM1LSC31 L1B31GS2        5.020960       -0.000002   0.000018

LM1LSC31 L1B31GS3        4.808120       -0.000005   0.000017

LM1LSC31 L1B31GS4        4.993320        0.000013   0.000015              T

LM1LSC31 L1B31GS5        4.655300        0.000007   0.000017

LM1LSC31 L1B31GS6        4.424960       -0.000011   0.000017

LM1LSC32 3LE02W31        9.394260        0.000006   0.000021

LM1LSC32 3LF01F01        9.086100        0.000003   0.000021

LM1LSC32 3LF02F01        7.246270        0.000002   0.000021

LM1LSC32 3LF02W02        4.511280        0.000006   0.000015

LM1LSC32 3LF02W15       10.003740       -0.000006   0.000018

LM1LSC32 3LF02W17        8.570870       -0.000008   0.000018

LM1LSC32 3LG01F01        3.045840        0.000004   0.000014

LM1LSC32 L1B31GS1        4.654220        0.000004   0.000021

LM1LSC32 L1B31GS2        4.633040        0.000001   0.000021

LM1LSC32 L1B31GS3        4.671800        0.000004   0.000021

LM1LSC32 L1B31GS4        4.097640       -0.000012   0.000015              T

LM1LSC32 L1B31GS5        4.073720       -0.000002   0.000021

LM1LSC32 L1B31GS6        4.117840        0.000015   0.000021

LM1LSC33 3LE02W31       11.414110       -0.000005   0.000020

LM1LSC33 3LF01F01       11.004700        0.000025   0.000019              T

LM1LSC33 3LF01W01        2.402780        0.000003   0.000009

LM1LSC33 3LF02F01        8.255760        0.000009   0.000018

LM1LSC33 3LF02W04        6.110360        0.000002   0.000011

LM1LSC33 3LF02W16       10.388550       -0.000010   0.000016

LM1LSC33 3LG01F01        2.612870       -0.000010   0.000012              T

LM1LSC33 L1B31GS1        5.163680        0.000002   0.000017

LM1LSC33 L1B31GS2        5.392280        0.000000   0.000018

LM1LSC33 L1B31GS3        5.614740        0.000001   0.000018

LM1LSC33 L1B31GS5        4.792050       -0.000001   0.000017

LM1LSC33 L1B31GS6        5.041130       -0.000004   0.000018

histogram of distance residuals

0   0   0   1  24  20   1   0   0   0

histogram of normal distribution

0   0   1   6  16  16   6   1   0   0

Pass the Chi2 goodness of fit test

horizontal direction residuals

LM1LSC31 3LE01F01      225.072750       -0.000000   0.000000

LM1LSC31 3LE02W02      224.902210        0.000000   0.000000

LM1LSC31 3LE02W31      209.183230       -0.000434   0.000697

LM1LSC31 3LE02W32      200.351640       -0.000000   0.000000

LM1LSC31 3LF01F01      217.817810       -0.000318   0.000666

LM1LSC31 3LF01W01       77.544200       -0.000108   0.001131

LM1LSC31 3LF02F01      154.241290       -0.000161   0.000771

LM1LSC31 3LF02W01       86.703960        0.000000   0.000000

LM1LSC31 3LF02W02       96.490200       -0.000060   0.000818

LM1LSC31 3LF02W03      108.210200        0.000000   0.000000

LM1LSC31 3LF02W04      122.052840       -0.000126   0.000894

LM1LSC31 3LF02W15      190.041470        0.000080   0.000535

LM1LSC31 3LF02W16      180.114900        0.000266   0.000678

LM1LSC31 3LF02W17      174.558400        0.000099   0.000644

LM1LSC31 3LG01F01       77.282310        0.000799   0.001027

LM1LSC31 L1B31GS1       97.236030       -0.000025   0.001002

LM1LSC31 L1B31GS2      103.962340        0.000171   0.001077

LM1LSC31 L1B31GS3      110.100580       -0.000062   0.001123

LM1LSC31 L1B31GS4       97.148980        0.000530   0.001005

LM1LSC31 L1B31GS5      103.863440        0.000070   0.001214

LM1LSC31 L1B31GS6      109.992070       -0.000298   0.001284

LM1LSC32 3LE02W31      147.326660        0.000151   0.000508

LM1LSC32 3LF01F01      154.350210       -0.000089   0.000511

LM1LSC32 3LF02F01      106.761030       -0.000246   0.000703

LM1LSC32 3LF02W02       51.565280       -0.000377   0.001105

LM1LSC32 3LF02W15      131.291500        0.000026   0.000426

LM1LSC32 3LF02W17      120.547440        0.000099   0.000522

LM1LSC32 3LG01F01       43.127410        0.000537   0.001720

LM1LSC32 L1B31GS1       61.188050       -0.000160   0.001135

LM1LSC32 L1B31GS2       72.106780       -0.000037   0.001140

LM1LSC32 L1B31GS3       80.738960       -0.000195   0.001135

LM1LSC32 L1B31GS4       60.970620        0.000470   0.001206

LM1LSC32 L1B31GS5       71.886560        0.000252   0.001371

LM1LSC32 L1B31GS6       80.524820       -0.000224   0.001369

LM1LSC33 3LE02W31      132.444270        0.000172   0.000398

LM1LSC33 3LF01F01      138.517930       -0.000046   0.000410

LM1LSC33 3LF01W01       66.390680       -0.001532   0.002376

LM1LSC33 3LF02F01      102.099850       -0.000079   0.000612

LM1LSC33 3LF02W04       81.424290       -0.000137   0.000894

LM1LSC33 3LF02W16      114.369560        0.000091   0.000439

LM1LSC33 3LG01F01       91.765400       -0.001734   0.001886              T

LM1LSC33 L1B31GS1       79.501700       -0.000109   0.001007

LM1LSC33 L1B31GS2       88.141210       -0.000126   0.000970

LM1LSC33 L1B31GS3       94.030070       -0.000033   0.000930

LM1LSC33 L1B31GS5       88.226250        0.000512   0.001174

LM1LSC33 L1B31GS6       94.106150        0.000018   0.001113

histogram of horizontal direction residuals

0   0   0   0  29  17   0   0   0   0

histogram of normal distribution

0   0   1   6  16  16   6   1   0   0

Pass the Chi2 goodness of fit test

vertical direction residuals

LM1LSC31 3LE01F01      119.335110       -0.000000   0.000000

LM1LSC31 3LE02W02      102.118000       -0.000000   0.000000

LM1LSC31 3LE02W31      105.008190        0.000243   0.000648

LM1LSC31 3LE02W32      104.532470        0.000000   0.000000

LM1LSC31 3LF01F01      127.087740        0.000642   0.000660              T

LM1LSC31 3LF01W01      105.907650        0.000388   0.000925

LM1LSC31 3LF02F01      128.162130       -0.000701   0.000709              T

LM1LSC31 3LF02W01      105.838160        0.000000   0.000000

LM1LSC31 3LF02W02      104.872130       -0.000309   0.000715

LM1LSC31 3LF02W03      104.786840       -0.000000   0.000000

LM1LSC31 3LF02W04      105.189710       -0.000344   0.000705

LM1LSC31 3LF02W15      104.544690        0.000158   0.000491

LM1LSC31 3LF02W16      105.005240       -0.000159   0.000579

LM1LSC31 3LF02W17      104.484200       -0.000203   0.000582

LM1LSC31 3LG01F01      138.677560        0.000107   0.001050

LM1LSC31 L1B31GS1       70.770050        0.000369   0.000974

LM1LSC31 L1B31GS2       68.850270        0.000342   0.001042

LM1LSC31 L1B31GS3       67.399110        0.000300   0.001079

LM1LSC31 L1B31GS4       81.645470        0.000115   0.000907

LM1LSC31 L1B31GS5       80.339950        0.000702   0.001121

LM1LSC31 L1B31GS6       79.338840        0.000940   0.001175

LM1LSC32 3LE02W31       99.439030       -0.000016   0.000486

LM1LSC32 3LF01F01      116.031260        0.000110   0.000500

LM1LSC32 3LF02F01      119.765480        0.000451   0.000665

LM1LSC32 3LF02W02       96.602530        0.000544   0.000945

LM1LSC32 3LF02W15       99.574440       -0.000167   0.000404

LM1LSC32 3LF02W17       98.828800        0.000108   0.000481

LM1LSC32 3LG01F01      149.542880        0.001608   0.001668              T

LM1LSC32 L1B31GS1       54.406420       -0.000096   0.001072

LM1LSC32 L1B31GS2       54.294760       -0.000318   0.001069

LM1LSC32 L1B31GS3       54.866180       -0.000240   0.001064

LM1LSC32 L1B31GS4       65.553080       -0.000695   0.001072

LM1LSC32 L1B31GS5       65.469360       -0.000356   0.001231

LM1LSC32 L1B31GS6       65.990590       -0.000303   0.001225

LM1LSC33 3LE02W31       94.955990       -0.000155   0.000393

LM1LSC33 3LF01F01      108.385470       -0.000020   0.000411

LM1LSC33 3LF01W01       76.316580       -0.000306   0.001814

LM1LSC33 3LF02F01      111.542670        0.000416   0.000589

LM1LSC33 3LF02W04       90.976770        0.000406   0.000700

LM1LSC33 3LF02W16       94.657670        0.000009   0.000393

LM1LSC33 3LG01F01      138.584520        0.000348   0.002090

LM1LSC33 L1B31GS1       48.994920       -0.000150   0.000965

LM1LSC33 L1B31GS2       51.672910       -0.000113   0.000933

LM1LSC33 L1B31GS3       53.989310        0.000030   0.000897

LM1LSC33 L1B31GS5       60.821190       -0.000358   0.001048

LM1LSC33 L1B31GS6       62.982170       -0.000340   0.000993

histogram of vertical direction residuals

0   0   0   0  25  21   0   0   0   0

histogram of normal distribution

0   0   1   6  16  16   6   1   0   0

Pass the Chi2 goodness of fit test

histogram of all observations residuals

0   0   0   1  78  58   1   0   0   0

histogram of normal distribution

0   0   3  19  47  47  19   3   0   0

Pass the Chi2 goodness of fit test

Standard deviations (sigma a posteriori    0.420)

Standard point confidence ellipse

LM1LSC31       0.000009       0.000008       0.000020

0.000010       0.000008     170.5

LM1LSC32       0.000013       0.000011       0.000019

0.000014       0.000009     166.7

LM1LSC33       0.000019       0.000012       0.000021

0.000020       0.000009     170.1

3LE01F01       0.000030       0.000019       0.000031

0.000032       0.000015     175.5

3LE02W02       0.000052       0.000019       0.000061

0.000053       0.000015     185.9

3LE02W31       0.000024       0.000013       0.000028

0.000025       0.000010     176.9

3LE02W32       0.000031       0.000025       0.000037

0.000037       0.000013     159.0

3LF01F01       0.000023       0.000013       0.000026

0.000024       0.000012     187.0

3LF01W01       0.000020       0.000017       0.000029

0.000022       0.000014      37.7

3LF02F01       0.000016       0.000018       0.000025

0.000021       0.000013     141.0

3LF02W01       0.000033       0.000030       0.000039

0.000042       0.000015      46.0

3LF02W02       0.000020       0.000024       0.000032

0.000029       0.000013      60.0

3LF02W03       0.000019       0.000033       0.000033

0.000035       0.000014      73.0

3LF02W04       0.000013       0.000020       0.000027

0.000020       0.000013      93.8

3LF02W15       0.000024       0.000020       0.000029

0.000029       0.000011     159.1

3LF02W16       0.000020       0.000021       0.000029

0.000027       0.000011     147.9

3LF02W17       0.000019       0.000025       0.000028

0.000029       0.000012     138.4

3LG01F01       0.000018       0.000014       0.000018

0.000018       0.000014       7.9

L1B31GS1       0.000025       0.000019       0.000023

0.000026       0.000019      14.6

L1B31GS2       0.000025       0.000019       0.000023

0.000025       0.000019      13.5

L1B31GS3       0.000024       0.000019       0.000022

0.000024       0.000019      11.4

L1B31GS4       0.000024       0.000023       0.000030

0.000027       0.000019      46.1

L1B31GS5       0.000021       0.000018       0.000024

0.000022       0.000017      31.4

L1B31GS6       0.000020       0.000018       0.000024

0.000021       0.000017      32.5

Standard error on stations parameters

LM1LSC31       0.000002       0.000005       0.000002

0.000000       0.000000

LM1LSC32       0.000004       0.000005       0.000003

0.000000       0.000000

LM1LSC33       0.000004       0.000006       0.000003

0.000000       0.000000

# Text boxes

Job Directory

Output Generation

Adjustment Analysis

Input File Generation

Data Reduction

ZXY file from Excel File

ZXY file from Insight File

Data File Upload

Geonet/LEGO Program

Index

Contents

Help

Manual

Geonet

Path Type

Option

Error Log

Bios Values

Calibration Structures

Data Structures

Main

Input

Geonet

Down Load

Data Type

Init Files

Edit

Exit

File

Specification Evaluation
 in Form C

Adjustment Analysis

Insight File

Insigh File

Printer setup

Data Configuration

Data Structure