|  | NONCONFORMANCE REPORT (NCR) |  |
| --- | --- | --- |
| SUBSYSTEM MFD 28932-15 | DESCRIPTION OF ITEM BASE | DATE 11/16/12 |
| ORIGINATOR K. Caban | PART NO. & REV. PF-380-805-01 R2 | SERIAL NO.(s) 101 |
| NONCONFORMANCE DESCRIPTION |
| Nonconformance Description (Describe the nonconformance; ensure the applicable requirements, planned activities, procedures, specifications, drawing, standards, serial numbers, etc. are noted. Indicate who documented the nonconformance.). Parallelism .0002 of distance .2299 to Datum –A- measures 0.00022 (+0.00002” out of parallel). Distance 1.3390 ± 0.0002 measures 1.33958 (+0.00038” out of tolerance). Parallelism .0002 of distance 1.3390 to Datum –A- 0.00021 (+0.00001” out of parallel). 2X Distance .9522 +0.0002/-0.0000 measures 0.95179 (-0.00041” out of tolerance). 2X Position of 0.0002 of 2X R 1.4119 measures 0.00091 (+0.00071” out of position). Distance 2X 3.087 ± 0.001 measures 3.08470 (-0.00130” out of tolerance). Distance 2X 3.538 ± 0.001 measures 3.53569 (-0.00131” out of tolerance). Iris diameter 1.0319 +0.0002/-0.0000 measures 1.03161 (-0.00029” out of tolerance). Position of 0.0002 of Iris diameter 1.0319 measures 0.00032 (+0.00012” out of position). Profile 0.0002 X-Y is out of surface profile (see attached profile plot, also has plots of cavity and cover-lid where near top of the part, where top of cavity and lid profiles “spring” inward, bottom of cavity is okay). R. .012 ± 0.001 measures 0.0172 (+0.0042” out of tolerance). See next page for more info… |
| DISPOSITION |
| Disposition: (Describe for each cause what action(s) will be taken with the item or process, including, as applicable, the completion dates, disposition of material, and responsible staff for each action. The completion dates, disposition of material, and responsible staff for each action. |
| CORRECTIVE/PREVENTIVE ACTION ¦ ASSIGNED TO: |
| Corrective/Preventive Action: Describe, as applicable, what actions are needed to prevent recurrence of the identified nonconformance, such as process improvement, procedure revisions, training plan, etc., and include completion dates and responsible staff for each action.). |
| FOLLOW-UP REQUIRED: ( Yes ( No |
| NCR CLOSEOUT APPROVALS |
| LCLS-II TECHNICAL REPRESENTATIVE | DATE | LCLS-II QUALITY ASSURANCE | DATE |
| FOLLOW UP EFFECTIVE ( Yes ( No | FOLLOW UP BY: | DATE |