|  | NONCONFORMANCE REPORT (NCR) |  |
| --- | --- | --- |
| SUBSYSTEM MFD 28932-28 | DESCRIPTION OF ITEM CUP 4A/4B | DATE 11/07/12 |
| ORIGINATOR K. Caban | PART NO. & REV. PF-380-805-11 R2 | SERIAL NO.(s) 101 |
| NONCONFORMANCE DESCRIPTION |
| Nonconformance Description (Describe the nonconformance; ensure the applicable requirements, planned activities, procedures, specifications, drawing, standards, serial numbers, etc. are noted. Indicate who documented the nonconformance.). Diameter 3.2812 ±0.0003 measures 3.28078 (-0.00012” undersized). Diameter 3.4865 +0.0005/-0.0000 measures 3.48630 (-0.00020” undersized). Parallelism .0002 of distance 1.1466 measures 0.00024 (+0.00004” out of parallel). Position of 0.0002 of Diameter 3.4860 measures 0.00027 (+0.00007” out of position). Position of 0.0002 of Diameter 3.2818 measures 0.00025 (+0.00005” out of position). Radius .0527 ±0.0005 measures 0.05110 (-0.00110” undersized). Profile 0.0002 X-Y is out of surface profile (see attached profile plot). |
| DISPOSITION |
| Disposition: (Describe for each cause what action(s) will be taken with the item or process, including, as applicable, the completion dates, disposition of material, and responsible staff for each action. The completion dates, disposition of material, and responsible staff for each action. |
| CORRECTIVE/PREVENTIVE ACTION ¦ ASSIGNED TO: |
| Corrective/Preventive Action: Describe, as applicable, what actions are needed to prevent recurrence of the identified nonconformance, such as process improvement, procedure revisions, training plan, etc., and include completion dates and responsible staff for each action.). |
| FOLLOW-UP REQUIRED: ( Yes ( No |
| NCR CLOSEOUT APPROVALS |
| LCLS-II TECHNICAL REPRESENTATIVE | DATE | LCLS-II QUALITY ASSURANCE | DATE |
| FOLLOW UP EFFECTIVE ( Yes ( No | FOLLOW UP BY: | DATE |