## Slide 1: Magnetic tuning set-up for DELTA undulator
Y. Levashov
FDR, Dec. 11, 2013

## Slide 2: Outline
The undulator can not be tuned when assembled. Each quadrant will be tuned individually to tight tolerances.
We use existing LCLS-1 fixtures as much as possible for set-up and measurements.
Tuning procedure for 3.2m long quadrants is the same as for the prototype. A few things will be done differently:
A special fixture designed to allow a quick accurate quadrant set-up on the measurement bench, magnets facing up.
Optical tools replaced by more accurate Keyence sensors for Hall probe positioning in vertical direction.
Stretched wire technique will be used for measuring field integrals.

## Slide 3: Tuning tolerances
Magnet centers’ deviations (magnet blocks’ deflections) from a nominal center line < ± 100m in X, <+50m in Y, and <+100m in Z (phase error < 1°).
Parameter | Assembled Undulator | Quadrant
K | >3.4853 (Slot 33) | >1.2323 (± 1.510-4 )
Phase error R.M.S. | <10° | < 4°
First field Integrals | < 40 Tm (40 G-cm) | < 20Tm (20 G-cm)
Second field Integrals | < 50 Tm2 (5000 G-cm2) | < 25Tm2 (2500 G-cm2)

## Slide 4: Set-up on LCLS-1 girder
Cam movers
Kinematic supports
LCLS-1 girder
The quadrant tuning fixture will have kinematic supports. It will be mounted on existing LCLS-1 girder with cam movers.
The same set-up is used on magnet gap tuning stand, transport carts and on CMM.
3.4m
Stages
Use existing LCLS-1 undulator tuning set-up on Kugler measurement bench.

## Slide 5: Tuning fixture
Coordinate system: Z- along the beam axis, Y – up, X – makes right-hand system
Three 1m long magnet arrays will be assembled on the tuning fixture with rails attached to make 3.2m quadrant with entrance and exit sections.
Existing cam movers
Reference surface for roll measurements
Kinematic support fixture. Lifting at the same points as supports.
Mounting surfaces for rails
Y
X
Z
3.39m

## Slide 6: Tuning set-up on Kugler bench
Granite
Z-Stage
Bracket
Keyence sensor :
Working distance 80 mm,
Range ± 15mm,
Accuracy 3mK
1m long removable bracket with mounting holes.
Reference surface for Keyence and CMM
Pitch and Y will be set to ±5m using Keyence measurements.
Yaw and X will be set to ±30m using optical tools.
Second Keyence sensor will be used to control magnet motions.
Reference surface for Optical measurements
Y
X

## Slide 7: Positioning Hall probe in X and Y direction
Fiducialization magnet
Tooling ball
Gauge block
Keyence
Hall probe sensitive area is small and covered inside a plastic package. Location is known to ±100m.
We will use LCLS-1 fiducialization magnets to find Hall probe center location w.r.t. outside fiducials.

## Slide 8: Field integral measurements
Moving wires
Fixed wires
Moving end
fixed end
Field integrals and trajectories will be initially tuned using Hall probe measurements.
We will use a single stretched wire and LCLS-1 stages to do accurate
(±20G·cm /2000G·cm2) measurements and do final corrections to field integrals by
moving magnets at entrance and exit.
It will have small effect on trajectories.

## Slide 9: Tuning procedure
Initially align 1m long sections of magnets using CMM with ±50m accuracy.
Mount 3 sections of the magnets on the tuning fixture to make a quadrant.
Align the quadrant on Kugler bench.
  Do Hall probe and stretched wire measurements and tune the quadrant using virtual shimming (re-positioning the magnets w.r.t. magnetic axis).
  Tuning procedure is the same as for the prototype.
Round 1:
Tune trajectories, field integrals and phase errors with the use of CMM data.
Measure K
- Check magnet positions w.r.t the quadrant references on CMM.
Round 2:
- Correct magnet positions to be within ±100m in X and < +50m in Y from the beam line.
Continue tuning trajectories , field integrals and phase errors with the use of CMM data.
Set K-value as close as possible to the average from Round 1.
Check magnet positions on CMM.
Round 3 ….

## Slide 10: Summary
Tuning procedure for DELTA quadrants has been developed and tested on the prototype.
The quadrant tuning set-up utilizes existing LCLS-1 fixtures.
A new tuning fixture with kinematic supports has been designed.
High accuracy non-contact Keyence sensors are used for magnet positioning.
Field integrals are measured using stretched wire technique.

## Slide 11: Back-up slides
Hall probe
(±2m)
Known from calibration (±5m)
Optical measurement (±25m)
Keyence measurement (±3m)
Reference on tuning fixture
Keyence measurement (±3m)
Cam mover adjustment
Positioning Hall probe in X and Y direction

## Slide 12: Alignment to the bench (X & yaw)
Chart: By vs probe X position
Do Hall probe scan in X at each pole location
Truncate data ± 3mm from center
Fit parabola, find center
Fit a straight line through all pole centers, find x and yaw, correct yaw
if necessary.

## Slide 13: Second tuning fixture
A
B
D
C
B
Second (mirror) fixture will be made for quadrants B & D.
Magnet assembly, CMM checking and quadrant tuning will be done in parallel.

## Slide 14: Tuning set-up on Kugler bench
Granite
Z-Stage
Bracket
Keyence sensor :
Working distance 80 mm,
Range ± 15mm,
Accuracy 3mK
1m long removable bracket with mounting holes.
Reference surface for Keyence and CMM
Pitch and Y will be set to ±5m using Keyence measurements.
Yaw and X will be set to ±30m using optical tools.
Second Keyence sensor will be used to control magnet motions.
Reference surface for Optical measurements
Y
X