SLAC Magnetic Measurements
Date: 07-10-1995
Time: 12:48:56

Magnet Name (Serial #): 011
Bar Code Number: 006
Project: PEP II High Energy Ring Sextupoles
Test Stand: IR8, S1
Measurement Coil: # 1
Operator: bmd
Run Number: 1
Comment: 

Standardization Currents (A):
   250.0    10.0   200.0    10.0   200.0    10.0   200.0
    10.0

Test Currents (A):
    25.0    50.0   100.0   125.0   150.0   175.0   200.0
   150.0   100.0    50.0    25.0

12:49:44  Magnet Current, Imag = -.000044  A

12:49:44  Magnet Current Ramping to  150  A...

12:51:04  Magnet Current, Imag =  150.5452  A

12:51:06  Temperature: Channel  1 , T =  15.69147  deg C

12:51:09  Temperature: Channel  2 , T =  22.66962  deg C

12:51:11  Temperature: Channel  3 , T =  18.08655  deg C

12:51:14  Temperature: Channel  4 , T =  20.87283  deg C

12:51:16  Temperature: Channel  5 , T =  23.37454  deg C

12:51:17  Magnet Current, Imag =  150.5528  A

12:51:19  Magnet Voltage, Vmag =  7.52134  V

12:52:06  Temperature: Channel  1 , T =  15.71805  deg C

12:52:09  Temperature: Channel  2 , T =  24.97489  deg C

12:52:11  Temperature: Channel  3 , T =  18.64761  deg C

12:52:14  Temperature: Channel  4 , T =  20.85464  deg C

12:52:16  Temperature: Channel  5 , T =  23.34009  deg C

12:52:17  Magnet Current, Imag =  150.5424  A

12:52:19  Magnet Voltage, Vmag =  7.57058  V

12:53:06  Temperature: Channel  1 , T =  15.71423  deg C

12:53:09  Temperature: Channel  2 , T =  27.03519  deg C

12:53:11  Temperature: Channel  3 , T =  19.28937  deg C

12:53:14  Temperature: Channel  4 , T =  20.8446  deg C

12:53:16  Temperature: Channel  5 , T =  23.39804  deg C

12:53:17  Magnet Current, Imag =  150.5472  A

12:53:19  Magnet Voltage, Vmag =  7.61118  V

12:54:06  Temperature: Channel  1 , T =  15.70761  deg C

12:54:09  Temperature: Channel  2 , T =  28.87839  deg C

12:54:11  Temperature: Channel  3 , T =  19.81058  deg C

12:54:14  Temperature: Channel  4 , T =  20.83447  deg C

12:54:16  Temperature: Channel  5 , T =  23.73685  deg C

12:54:18  Magnet Current, Imag =  150.5602  A

12:54:19  Magnet Voltage, Vmag =  7.64325  V

12:55:06  Temperature: Channel  1 , T =  15.73016  deg C

12:55:09  Temperature: Channel  2 , T =  30.66537  deg C

12:55:11  Temperature: Channel  3 , T =  20.17966  deg C

12:55:14  Temperature: Channel  4 , T =  20.82837  deg C

12:55:16  Temperature: Channel  5 , T =  23.75717  deg C

12:55:18  Magnet Current, Imag =  150.547  A

12:55:19  Magnet Voltage, Vmag =  7.66871  V

12:56:06  Temperature: Channel  1 , T =  15.79672  deg C

12:56:09  Temperature: Channel  2 , T =  32.43997  deg C

12:56:11  Temperature: Channel  3 , T =  20.44125  deg C

12:56:14  Temperature: Channel  4 , T =  20.81851  deg C

12:56:16  Temperature: Channel  5 , T =  23.59735  deg C

12:56:18  Magnet Current, Imag =  150.547  A

12:56:19  Magnet Voltage, Vmag =  7.68825  V

12:57:07  Temperature: Channel  1 , T =  15.90408  deg C

12:57:09  Temperature: Channel  2 , T =  34.13104  deg C

12:57:11  Temperature: Channel  3 , T =  20.62003  deg C

12:57:14  Temperature: Channel  4 , T =  20.81528  deg C

12:57:16  Temperature: Channel  5 , T =  23.7601  deg C

12:57:18  Magnet Current, Imag =  150.5448  A

12:57:19  Magnet Voltage, Vmag =  7.70131  V

12:58:07  Temperature: Channel  1 , T =  16.05957  deg C

12:58:09  Temperature: Channel  2 , T =  35.56442  deg C

12:58:12  Temperature: Channel  3 , T =  20.77014  deg C

12:58:14  Temperature: Channel  4 , T =  20.81573  deg C

12:58:16  Temperature: Channel  5 , T =  23.65747  deg C

12:58:18  Magnet Current, Imag =  150.5416  A

12:58:19  Magnet Voltage, Vmag =  7.71042  V

12:59:07  Temperature: Channel  1 , T =  16.23785  deg C

12:59:09  Temperature: Channel  2 , T =  36.65033  deg C

12:59:11  Temperature: Channel  3 , T =  20.88904  deg C

12:59:14  Temperature: Channel  4 , T =  20.80844  deg C

12:59:16  Temperature: Channel  5 , T =  23.48755  deg C

12:59:18  Magnet Current, Imag =  150.5446  A

12:59:19  Magnet Voltage, Vmag =  7.71582  V

13:00:07  Temperature: Channel  1 , T =  16.42615  deg C

13:00:09  Temperature: Channel  2 , T =  37.37451  deg C

13:00:11  Temperature: Channel  3 , T =  20.99762  deg C

13:00:14  Temperature: Channel  4 , T =  20.80649  deg C

13:00:16  Temperature: Channel  5 , T =  23.28781  deg C

13:00:18  Magnet Current, Imag =  150.5452  A

13:00:19  Magnet Voltage, Vmag =  7.7207  V

13:01:07  Temperature: Channel  1 , T =  16.62775  deg C

13:01:09  Temperature: Channel  2 , T =  37.78571  deg C

13:01:11  Temperature: Channel  3 , T =  21.11719  deg C

13:01:14  Temperature: Channel  4 , T =  20.81763  deg C

13:01:16  Temperature: Channel  5 , T =  23.38684  deg C

13:01:18  Magnet Current, Imag =  150.5506  A

13:01:19  Magnet Voltage, Vmag =  7.72513  V

13:02:05  Magnet Current, Imag =  150.5464  A

13:02:05  Magnet Current Ramping to  0  A...

13:03:25  Magnet Current, Imag =  .595366  A

13:03:27  Magnet Current, Imag =  .5962321  A

13:03:27  Magnet Current Ramping to  250  A...

13:05:18  Magnet Current, Imag =  250.504  A

13:05:20  Magnet Current, Imag =  250.5048  A

13:05:20  Magnet Current Ramping to  10  A...

13:07:08  Magnet Current, Imag =  10.59384  A

13:07:09  Magnet Current, Imag =  10.59206  A

13:07:09  Magnet Current Ramping to  200  A...

13:08:42  Magnet Current, Imag =  200.5716  A

13:08:44  Magnet Current, Imag =  200.588  A

13:08:44  Magnet Current Ramping to  10  A...

13:10:16  Magnet Current, Imag =  10.5932  A

13:10:18  Magnet Current, Imag =  10.5905  A

13:10:18  Magnet Current Ramping to  200  A...

13:11:50  Magnet Current, Imag =  200.5474  A

13:11:52  Magnet Current, Imag =  200.5554  A

13:11:52  Magnet Current Ramping to  10  A...

13:13:24  Magnet Current, Imag =  10.5913  A

13:13:26  Magnet Current, Imag =  10.58772  A

13:13:26  Magnet Current Ramping to  200  A...

13:14:58  Magnet Current, Imag =  200.5334  A

13:15:00  Magnet Current, Imag =  200.556  A

13:15:00  Magnet Current Ramping to  10  A...

13:16:32  Magnet Current, Imag =  10.5888  A

13:16:34  Magnet Current, Imag =  10.5895  A

13:16:34  Magnet Current Ramping to  25  A...

13:17:13  Magnet Current, Imag =  25.58092  A

13:17:15  Magnet Current, Imag =  25.58182  A

13:17:17  Magnet Current, Imag =  25.58298  A

13:17:19  Magnet Current, Imag =  25.58374  A

13:17:21  Magnet Current, Imag =  25.58596  A

13:17:21  Average Magnet Current:
Imag =  25.58363  +-  1.512528E-03  A

13:17:24  Coil Rotation Frequency, Fcoil =  4.058711  Hz

13:17:28  Coil Rotation Frequency, Fcoil =  4.058738  Hz

13:17:57  Coil Voltage Measurement #  1  Made, Stored in RAWFILE

13:17:57  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1201289  V, Vp main =  89.70302  deg

13:17:57  Coil Voltage Fit: 
Vfit(i) =  0.1201289 V * cos(3*2pi*i/ns +   89.70 deg)
        = -0.1201273 V * sin(3*2pi*i/ns) +  0.0006226 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015840 V

13:18:01  Coil Rotation Frequency, Fcoil =  4.060836  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.059428 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00101340   115.24   0.00004426  -115.24
  2   0.00194503   -67.32   0.00008495    33.66
  3   0.12012889    89.70   0.00524687   -29.90
  4   0.00013226  -138.92   0.00000578    34.73
  5   0.00013028   -90.50   0.00000569    18.10
  6   0.00001884  -170.81   0.00000082    28.47
  7   0.00003602   -86.35   0.00000157    12.34
  8   0.00002764   130.29   0.00000121   -16.29
  9   0.00040368   -91.10   0.00001763    10.12
 10   0.00000144  -176.22   0.00000006    17.62
 11   0.00000752   -83.07   0.00000033     7.55
 12   0.00000702   137.03   0.00000031   -11.42
 13   0.00000132  -158.25   0.00000006    12.17
 14   0.00000884   131.31   0.00000039    -9.38
 15   0.00008807   -94.99   0.00000385     6.33
 16   0.00000533  -140.23   0.00000023     8.76

13:18:04  Coil Rotation Frequency, Fcoil =  4.059815  Hz

13:18:08  Coil Rotation Frequency, Fcoil =  4.059323  Hz

13:18:36  Coil Voltage Measurement #  2  Made, Stored in RAWFILE

13:18:36  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1202656  V, Vp main =  89.70165  deg

13:18:36  Coil Voltage Fit: 
Vfit(i) =  0.1202656 V * cos(3*2pi*i/ns +   89.70 deg)
        = -0.1202640 V * sin(3*2pi*i/ns) +  0.0006262 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015830 V

13:18:40  Coil Rotation Frequency, Fcoil =  4.061876  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.060338 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00100853   115.18   0.00004404  -115.18
  2   0.00194770   -67.36   0.00008505    33.68
  3   0.12026564    89.70   0.00525167   -29.90
  4   0.00012412  -141.99   0.00000542    35.50
  5   0.00012903   -89.88   0.00000563    17.98
  6   0.00002965   150.41   0.00000129   -25.07
  7   0.00003326   -84.37   0.00000145    12.05
  8   0.00003261   127.40   0.00000142   -15.93
  9   0.00039725   -90.73   0.00001735    10.08
 10   0.00000154    25.74   0.00000007    -2.57
 11   0.00000417  -123.76   0.00000018    11.25
 12   0.00000764  -143.52   0.00000033    11.96
 13   0.00000156   171.63   0.00000007   -13.20
 14   0.00000909   132.45   0.00000040    -9.46
 15   0.00008641   -92.00   0.00000377     6.13
 16   0.00000450   -37.65   0.00000020     2.35

13:18:43  Coil Rotation Frequency, Fcoil =  4.059192  Hz

13:18:47  Coil Rotation Frequency, Fcoil =  4.059061  Hz

13:19:16  Coil Voltage Measurement #  3  Made, Stored in RAWFILE

13:19:16  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .120213  V, Vp main =  89.70553  deg

13:19:16  Coil Voltage Fit: 
Vfit(i) =  0.1202130 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.1202114 V * sin(3*2pi*i/ns) +  0.0006178 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015925 V

13:19:20  Coil Rotation Frequency, Fcoil =  4.059364  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.059206 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00101015   115.40   0.00004412  -115.40
  2   0.00196111   -67.40   0.00008566    33.70
  3   0.12021299    89.71   0.00525083   -29.90
  4   0.00013957  -126.66   0.00000610    31.66
  5   0.00013541   -91.57   0.00000591    18.31
  6   0.00002299  -105.81   0.00000100    17.64
  7   0.00002862  -101.48   0.00000125    14.50
  8   0.00001763   133.22   0.00000077   -16.65
  9   0.00039808   -91.65   0.00001739    10.18
 10   0.00000276   -66.74   0.00000012     6.67
 11   0.00001693  -146.22   0.00000074    13.29
 12   0.00000677  -172.64   0.00000030    14.39
 13   0.00001156   126.76   0.00000050    -9.75
 14   0.00001253   106.25   0.00000055    -7.59
 15   0.00008442   -94.96   0.00000369     6.33
 16   0.00000124  -106.10   0.00000005     6.63

13:19:23  Coil Rotation Frequency, Fcoil =  4.059804  Hz

13:19:27  Coil Rotation Frequency, Fcoil =  4.06049  Hz

13:19:55  Coil Voltage Measurement #  4  Made, Stored in RAWFILE

13:19:56  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1201883  V, Vp main =  89.7046  deg

13:19:56  Coil Voltage Fit: 
Vfit(i) =  0.1201883 V * cos(3*2pi*i/ns +   89.70 deg)
        = -0.1201867 V * sin(3*2pi*i/ns) +  0.0006196 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015845 V

13:19:59  Coil Rotation Frequency, Fcoil =  4.061899  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.060731 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00101015   115.64   0.00004411  -115.64
  2   0.00195097   -67.20   0.00008519    33.60
  3   0.12018834    89.70   0.00524779   -29.90
  4   0.00011541  -140.31   0.00000504    35.08
  5   0.00013230   -89.07   0.00000578    17.81
  6   0.00001728   119.84   0.00000075   -19.97
  7   0.00003663   -85.35   0.00000160    12.19
  8   0.00002633   113.96   0.00000115   -14.24
  9   0.00039151   -91.03   0.00001709    10.11
 10   0.00000033  -165.36   0.00000001    16.54
 11   0.00000137  -161.29   0.00000006    14.66
 12   0.00000247  -151.90   0.00000011    12.66
 13   0.00000531   146.15   0.00000023   -11.24
 14   0.00000673   108.94   0.00000029    -7.78
 15   0.00008677   -93.22   0.00000379     6.21
 16   0.00000464   -64.47   0.00000020     4.03

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00004  0.00000   -115.37     0.18
  2   0.00009  0.00000     33.66     0.04
  3   0.00525  0.00000    -29.90     0.00
  4   0.00001  0.00000     34.24     1.51
  5   0.00001  0.00000     18.05     0.18
  6   0.00000  0.00000      0.27    23.18
  7   0.00000  0.00000     12.77     1.00
  8   0.00000  0.00000    -15.78     0.92
  9   0.00002  0.00000     10.13     0.04
 10   0.00000  0.00000      9.56     8.20
 11   0.00000  0.00000     11.69     2.68
 12   0.00000  0.00000      6.90    10.61
 13   0.00000  0.00000     -5.51    10.28
 14   0.00000  0.00000     -8.55     0.87
 15   0.00000  0.00000      6.25     0.08
 16   0.00000  0.00000      5.44     2.45

13:20:00  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  5.249291E-03  +-  2.009191E-06  Tm
Integrated Sextupole Strength, SL =  5.211782  +-  1.994835E-03  T/m

13:20:00            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00004  0.00000    0.8407   0.0016
  2   0.00009  0.00000    1.6233   0.0052
  3   0.00525  0.00000  100.0000   0.0541
  4   0.00001  0.00000    0.1064   0.0075
  5   0.00001  0.00000    0.1096   0.0020
  6   0.00000  0.00000    0.0185   0.0040
  7   0.00000  0.00000    0.0280   0.0026
  8   0.00000  0.00000    0.0217   0.0045
  9   0.00002  0.00000    0.3308   0.0036
 10   0.00000  0.00000    0.0013   0.0007
 11   0.00000  0.00000    0.0062   0.0049
 12   0.00000  0.00000    0.0050   0.0017
 13   0.00000  0.00000    0.0041   0.0034
 14   0.00000  0.00000    0.0077   0.0017
 15   0.00000  0.00000    0.0719   0.0011
 16   0.00000  0.00000    0.0033   0.0013

13:20:02  Magnet Current, Imag =  25.58218  A

13:20:02  Magnet Current Ramping to  50  A...

13:20:45  Magnet Current, Imag =  50.56484  A

13:20:47  Magnet Current, Imag =  50.56674  A

13:20:49  Magnet Current, Imag =  50.56622  A

13:20:50  Magnet Current, Imag =  50.56716  A

13:20:52  Magnet Current, Imag =  50.56742  A

13:20:52  Average Magnet Current:
Imag =  50.56689  +-  4.536965E-04  A

13:20:55  Coil Rotation Frequency, Fcoil =  4.060235  Hz

13:21:00  Coil Rotation Frequency, Fcoil =  4.060639  Hz

13:21:28  Coil Voltage Measurement #  5  Made, Stored in RAWFILE

13:21:28  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2349958  V, Vp main =  89.70481  deg

13:21:28  Coil Voltage Fit: 
Vfit(i) =  0.2349958 V * cos(3*2pi*i/ns +   89.70 deg)
        = -0.2349926 V * sin(3*2pi*i/ns) +  0.0012106 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028028 V

13:21:32  Coil Rotation Frequency, Fcoil =  4.059215  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.06003 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00069885   136.11   0.00003052  -136.11
  2   0.00380286   -67.32   0.00016607    33.66
  3   0.23499577    89.70   0.01026240   -29.90
  4   0.00023108  -136.79   0.00001009    34.20
  5   0.00028851   -91.21   0.00001260    18.24
  6   0.00001961  -167.56   0.00000086    27.93
  7   0.00006867   -86.85   0.00000300    12.41
  8   0.00004426   130.22   0.00000193   -16.28
  9   0.00076698   -91.06   0.00003349    10.12
 10   0.00000866  -116.56   0.00000038    11.66
 11   0.00000628   144.92   0.00000027   -13.17
 12   0.00000834  -147.33   0.00000036    12.28
 13   0.00000544    48.20   0.00000024    -3.71
 14   0.00001639   115.37   0.00000072    -8.24
 15   0.00016691   -94.42   0.00000729     6.29
 16   0.00000526  -176.24   0.00000023    11.01

13:21:35  Coil Rotation Frequency, Fcoil =  4.059373  Hz

13:21:39  Coil Rotation Frequency, Fcoil =  4.059296  Hz

13:22:08  Coil Voltage Measurement #  6  Made, Stored in RAWFILE

13:22:08  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2350376  V, Vp main =  89.70669  deg

13:22:08  Coil Voltage Fit: 
Vfit(i) =  0.2350375 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.2350345 V * sin(3*2pi*i/ns) +  0.0012031 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028078 V

13:22:12  Coil Rotation Frequency, Fcoil =  4.057772  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.058814 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00070486   135.86   0.00003079  -135.86
  2   0.00380836   -67.22   0.00016636    33.61
  3   0.23503758    89.71   0.01026730   -29.90
  4   0.00023547  -132.32   0.00001029    33.08
  5   0.00028505   -90.83   0.00001245    18.17
  6   0.00002585  -144.16   0.00000113    24.03
  7   0.00006533   -85.35   0.00000285    12.19
  8   0.00004022   126.23   0.00000176   -15.78
  9   0.00076918   -91.20   0.00003360    10.13
 10   0.00000746    12.03   0.00000033    -1.20
 11   0.00000897   110.24   0.00000039   -10.02
 12   0.00000567  -110.87   0.00000025     9.24
 13   0.00000329  -109.21   0.00000014     8.40
 14   0.00001937   111.06   0.00000085    -7.93
 15   0.00017608   -93.82   0.00000769     6.25
 16   0.00000710    66.93   0.00000031    -4.18

13:22:15  Coil Rotation Frequency, Fcoil =  4.057853  Hz

13:22:19  Coil Rotation Frequency, Fcoil =  4.060575  Hz

13:22:47  Coil Voltage Measurement #  7  Made, Stored in RAWFILE

13:22:47  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2350547  V, Vp main =  89.70386  deg

13:22:47  Coil Voltage Fit: 
Vfit(i) =  0.2350546 V * cos(3*2pi*i/ns +   89.70 deg)
        = -0.2350515 V * sin(3*2pi*i/ns) +  0.0012148 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028112 V

13:22:51  Coil Rotation Frequency, Fcoil =  4.059434  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.059288 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00070600   136.00   0.00003084  -136.00
  2   0.00381153   -67.38   0.00016648    33.69
  3   0.23505466    89.70   0.01026685   -29.90
  4   0.00023176  -127.44   0.00001012    31.86
  5   0.00029448   -90.55   0.00001286    18.11
  6   0.00002891   -98.65   0.00000126    16.44
  7   0.00006865   -90.26   0.00000300    12.89
  8   0.00003523   125.25   0.00000154   -15.66
  9   0.00077707   -90.79   0.00003394    10.09
 10   0.00001396   -13.57   0.00000061     1.36
 11   0.00000090    67.53   0.00000004    -6.14
 12   0.00000656  -116.03   0.00000029     9.67
 13   0.00000279  -172.38   0.00000012    13.26
 14   0.00002144   155.69   0.00000094   -11.12
 15   0.00016538   -93.67   0.00000722     6.24
 16   0.00001429  -146.87   0.00000062     9.18

13:22:55  Coil Rotation Frequency, Fcoil =  4.060616  Hz

13:22:59  Coil Rotation Frequency, Fcoil =  4.060851  Hz

13:23:27  Coil Voltage Measurement #  8  Made, Stored in RAWFILE

13:23:27  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2351363  V, Vp main =  89.70554  deg

13:23:27  Coil Voltage Fit: 
Vfit(i) =  0.2351363 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.2351332 V * sin(3*2pi*i/ns) +  0.0012083 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028038 V

13:23:31  Coil Rotation Frequency, Fcoil =  4.058319  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.059929 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00070284   135.70   0.00003069  -135.70
  2   0.00380150   -67.48   0.00016602    33.74
  3   0.23513633    89.71   0.01026879   -29.90
  4   0.00024150  -143.36   0.00001055    35.84
  5   0.00028459   -90.70   0.00001243    18.14
  6   0.00005041   160.60   0.00000220   -26.77
  7   0.00006762   -85.85   0.00000295    12.26
  8   0.00005537   124.45   0.00000242   -15.56
  9   0.00077430   -91.01   0.00003382    10.11
 10   0.00000858   -66.38   0.00000037     6.64
 11   0.00001080  -140.58   0.00000047    12.78
 12   0.00000513   179.91   0.00000022   -14.99
 13   0.00000731  -105.63   0.00000032     8.13
 14   0.00001563   102.92   0.00000068    -7.35
 15   0.00016411   -94.95   0.00000717     6.33
 16   0.00000146  -123.59   0.00000006     7.72

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00003  0.00000   -135.92     0.15
  2   0.00017  0.00000     33.67     0.05
  3   0.01027  0.00000    -29.90     0.00
  4   0.00001  0.00000     33.74     1.46
  5   0.00001  0.00000     18.16     0.05
  6   0.00000  0.00000     10.41    21.86
  7   0.00000  0.00000     12.44     0.27
  8   0.00000  0.00000    -15.82     0.28
  9   0.00003  0.00000     10.11     0.02
 10   0.00000  0.00000      4.61     4.95
 11   0.00000  0.00000     -4.14    10.08
 12   0.00000  0.00000      4.05    11.05
 13   0.00000  0.00000      6.52     6.25
 14   0.00000  0.00000     -8.66     1.46
 15   0.00001  0.00000      6.28     0.03
 16   0.00000  0.00000      5.93     5.96

13:23:31  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  1.026633E-02  +-  2.383639E-06  Tm
Integrated Sextupole Strength, SL =  10.19297  +-  2.366606E-03  T/m

13:23:31            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00003  0.00000    0.2991   0.0012
  2   0.00017  0.00000    1.6192   0.0019
  3   0.01027  0.00000  100.0000   0.0328
  4   0.00001  0.00000    0.1000   0.0018
  5   0.00001  0.00000    0.1226   0.0017
  6   0.00000  0.00000    0.0133   0.0049
  7   0.00000  0.00000    0.0287   0.0006
  8   0.00000  0.00000    0.0186   0.0032
  9   0.00003  0.00000    0.3284   0.0017
 10   0.00000  0.00000    0.0041   0.0011
 11   0.00000  0.00000    0.0029   0.0016
 12   0.00000  0.00000    0.0027   0.0005
 13   0.00000  0.00000    0.0020   0.0008
 14   0.00000  0.00000    0.0077   0.0010
 15   0.00001  0.00000    0.0715   0.0020
 16   0.00000  0.00000    0.0030   0.0020

13:23:34  Magnet Current, Imag =  50.56504  A

13:23:34  Magnet Current Ramping to  100  A...

13:24:23  Magnet Current, Imag =  100.561  A

13:24:24  Magnet Current, Imag =  100.5592  A

13:24:26  Magnet Current, Imag =  100.558  A

13:24:27  Magnet Current, Imag =  100.5588  A

13:24:29  Magnet Current, Imag =  100.5644  A

13:24:29  Average Magnet Current:
Imag =  100.5601  +-  2.518766E-03  A

13:24:32  Coil Rotation Frequency, Fcoil =  4.062285  Hz

13:24:36  Coil Rotation Frequency, Fcoil =  4.063306  Hz

13:25:04  Coil Voltage Measurement #  9  Made, Stored in RAWFILE

13:25:04  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4670343  V, Vp main =  89.71495  deg

13:25:04  Coil Voltage Fit: 
Vfit(i) =  0.4670343 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.4670285 V * sin(3*2pi*i/ns) +  0.0023233 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055080 V

13:25:08  Coil Rotation Frequency, Fcoil =  4.057137  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.06091 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00075108  -150.62   0.00003279   150.62
  2   0.00754914   -67.48   0.00032960    33.74
  3   0.46703431    89.71   0.02039123   -29.90
  4   0.00043151  -132.64   0.00001884    33.16
  5   0.00061181   -89.75   0.00002671    17.95
  6   0.00008962  -144.55   0.00000391    24.09
  7   0.00014290   -85.45   0.00000624    12.21
  8   0.00009408   127.26   0.00000411   -15.91
  9   0.00154990   -90.78   0.00006767    10.09
 10   0.00000928    22.99   0.00000041    -2.30
 11   0.00001794   -24.79   0.00000078     2.25
 12   0.00003683   -36.36   0.00000161     3.03
 13   0.00000920    64.38   0.00000040    -4.95
 14   0.00004303   136.84   0.00000188    -9.77
 15   0.00033930   -92.42   0.00001481     6.16
 16   0.00000425    53.97   0.00000019    -3.37

13:25:11  Coil Rotation Frequency, Fcoil =  4.057442  Hz

13:25:15  Coil Rotation Frequency, Fcoil =  4.057165  Hz

13:25:44  Coil Voltage Measurement #  10  Made, Stored in RAWFILE

13:25:44  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4671029  V, Vp main =  89.71478  deg

13:25:44  Coil Voltage Fit: 
Vfit(i) =  0.4671029 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.4670971 V * sin(3*2pi*i/ns) +  0.0023250 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055142 V

13:25:48  Coil Rotation Frequency, Fcoil =  4.058634  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057747 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00075736  -151.28   0.00003309   151.28
  2   0.00755209   -67.58   0.00032999    33.79
  3   0.46710289    89.71   0.02041012   -29.90
  4   0.00047411  -134.34   0.00002072    33.58
  5   0.00060101   -90.20   0.00002626    18.04
  6   0.00011147  -159.99   0.00000487    26.67
  7   0.00012655   -93.02   0.00000553    13.29
  8   0.00008833   128.94   0.00000386   -16.12
  9   0.00157074   -90.90   0.00006863    10.10
 10   0.00003174  -102.77   0.00000139    10.28
 11   0.00002522  -110.17   0.00000110    10.02
 12   0.00002998   -16.42   0.00000131     1.37
 13   0.00000485   131.71   0.00000021   -10.13
 14   0.00003406   113.34   0.00000149    -8.10
 15   0.00032954   -92.02   0.00001440     6.13
 16   0.00000923  -151.70   0.00000040     9.48

13:25:51  Coil Rotation Frequency, Fcoil =  4.059793  Hz

13:25:55  Coil Rotation Frequency, Fcoil =  4.061144  Hz

13:26:23  Coil Voltage Measurement #  11  Made, Stored in RAWFILE

13:26:24  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4672138  V, Vp main =  89.71545  deg

13:26:24  Coil Voltage Fit: 
Vfit(i) =  0.4672137 V * cos(3*2pi*i/ns +   89.72 deg)
        = -0.4672080 V * sin(3*2pi*i/ns) +  0.0023201 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0054970 V

13:26:27  Coil Rotation Frequency, Fcoil =  4.059985  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.060308 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00075642  -149.85   0.00003303   149.85
  2   0.00753398   -67.79   0.00032899    33.89
  3   0.46721378    89.72   0.02040209   -29.91
  4   0.00047553  -139.53   0.00002077    34.88
  5   0.00059286   -89.12   0.00002589    17.82
  6   0.00013348  -172.85   0.00000583    28.81
  7   0.00013158   -87.01   0.00000575    12.43
  8   0.00009127   132.55   0.00000399   -16.57
  9   0.00153422   -91.38   0.00006700    10.15
 10   0.00000974  -106.79   0.00000043    10.68
 11   0.00001544   169.45   0.00000067   -15.40
 12   0.00003013    -3.94   0.00000132     0.33
 13   0.00001435   142.15   0.00000063   -10.93
 14   0.00004423   102.51   0.00000193    -7.32
 15   0.00034519   -92.48   0.00001507     6.17
 16   0.00001078    73.15   0.00000047    -4.57

13:26:31  Coil Rotation Frequency, Fcoil =  4.061075  Hz

13:26:35  Coil Rotation Frequency, Fcoil =  4.06109  Hz

13:27:03  Coil Voltage Measurement #  12  Made, Stored in RAWFILE

13:27:03  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4670761  V, Vp main =  89.71358  deg

13:27:03  Coil Voltage Fit: 
Vfit(i) =  0.4670760 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.4670702 V * sin(3*2pi*i/ns) +  0.0023347 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0054868 V

13:27:07  Coil Rotation Frequency, Fcoil =  4.060428  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.060864 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00074781  -151.42   0.00003265   151.42
  2   0.00751738   -67.54   0.00032822    33.77
  3   0.46707612    89.71   0.02039328   -29.90
  4   0.00040591  -146.67   0.00001772    36.67
  5   0.00060770   -88.96   0.00002653    17.79
  6   0.00011634   147.77   0.00000508   -24.63
  7   0.00014945   -89.10   0.00000653    12.73
  8   0.00010838   121.56   0.00000473   -15.19
  9   0.00155882   -90.23   0.00006806    10.03
 10   0.00001597  -149.66   0.00000070    14.97
 11   0.00002312   -60.29   0.00000101     5.48
 12   0.00002065   -18.16   0.00000090     1.51
 13   0.00000841  -150.82   0.00000037    11.60
 14   0.00003136   133.07   0.00000137    -9.51
 15   0.00035302   -92.82   0.00001541     6.19
 16   0.00000435   -68.95   0.00000019     4.31

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00003  0.00000    150.79     0.62
  2   0.00033  0.00000     33.80     0.06
  3   0.02040  0.00001    -29.90     0.00
  4   0.00002  0.00000     34.57     1.36
  5   0.00003  0.00000     17.90     0.10
  6   0.00000  0.00000     13.73    22.21
  7   0.00001  0.00000     12.66     0.41
  8   0.00000  0.00000    -15.95     0.50
  9   0.00007  0.00000     10.09     0.05
 10   0.00000  0.00000      8.41     6.45
 11   0.00000  0.00000      0.59     9.64
 12   0.00000  0.00000      1.56     0.96
 13   0.00000  0.00000     -3.60     9.07
 14   0.00000  0.00000     -8.67     1.01
 15   0.00001  0.00000      6.16     0.02
 16   0.00000  0.00000      1.46     5.75

13:27:07  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  2.039918E-02  +-  7.519311E-06  Tm
Integrated Sextupole Strength, SL =  20.25342  +-  7.465582E-03  T/m

13:27:07            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00003  0.00000    0.1612   0.0009
  2   0.00033  0.00000    1.6138   0.0033
  3   0.02040  0.00001  100.0000   0.0521
  4   0.00002  0.00000    0.0956   0.0063
  5   0.00003  0.00000    0.1292   0.0015
  6   0.00000  0.00000    0.0241   0.0033
  7   0.00001  0.00000    0.0295   0.0019
  8   0.00000  0.00000    0.0204   0.0016
  9   0.00007  0.00000    0.3326   0.0029
 10   0.00000  0.00000    0.0036   0.0019
 11   0.00000  0.00000    0.0044   0.0008
 12   0.00000  0.00000    0.0063   0.0012
 13   0.00000  0.00000    0.0020   0.0007
 14   0.00000  0.00000    0.0082   0.0012
 15   0.00001  0.00000    0.0732   0.0018
 16   0.00000  0.00000    0.0015   0.0006

13:27:09  Magnet Current, Imag =  100.56  A

13:27:09  Magnet Current Ramping to  125  A...

13:27:52  Magnet Current, Imag =  125.5434  A

13:27:53  Magnet Current, Imag =  125.5424  A

13:27:54  Magnet Current, Imag =  125.5462  A

13:27:56  Magnet Current, Imag =  125.5386  A

13:27:57  Magnet Current, Imag =  125.5394  A

13:27:57  Average Magnet Current:
Imag =  125.5417  +-  2.988223E-03  A

13:28:00  Coil Rotation Frequency, Fcoil =  4.058873  Hz

13:28:04  Coil Rotation Frequency, Fcoil =  4.058942  Hz

13:28:33  Coil Voltage Measurement #  13  Made, Stored in RAWFILE

13:28:33  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .5823922  V, Vp main =  89.71298  deg

13:28:33  Coil Voltage Fit: 
Vfit(i) =  0.5823920 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.5823846 V * sin(3*2pi*i/ns) +  0.0029171 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0068690 V

13:28:37  Coil Rotation Frequency, Fcoil =  4.060863  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.059559 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00110612  -131.30   0.00004831   131.30
  2   0.00940477   -67.50   0.00041076    33.75
  3   0.58239216    89.71   0.02543634   -29.90
  4   0.00052329  -141.93   0.00002285    35.48
  5   0.00077190   -89.92   0.00003371    17.98
  6   0.00011955   161.44   0.00000522   -26.91
  7   0.00017610   -81.46   0.00000769    11.64
  8   0.00012529   125.13   0.00000547   -15.64
  9   0.00188694   -91.03   0.00008241    10.11
 10   0.00001332    53.66   0.00000058    -5.37
 11   0.00000630   -81.79   0.00000028     7.44
 12   0.00002295  -171.21   0.00000100    14.27
 13   0.00002956    45.25   0.00000129    -3.48
 14   0.00004460   144.50   0.00000195   -10.32
 15   0.00043599   -92.96   0.00001904     6.20
 16   0.00001973  -100.95   0.00000086     6.31

13:28:40  Coil Rotation Frequency, Fcoil =  4.061402  Hz

13:28:44  Coil Rotation Frequency, Fcoil =  4.062196  Hz

13:29:12  Coil Voltage Measurement #  14  Made, Stored in RAWFILE

13:29:12  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .5829472  V, Vp main =  89.71516  deg

13:29:12  Coil Voltage Fit: 
Vfit(i) =  0.5829471 V * cos(3*2pi*i/ns +   89.72 deg)
        = -0.5829399 V * sin(3*2pi*i/ns) +  0.0028978 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0068860 V

13:29:16  Coil Rotation Frequency, Fcoil =  4.060312  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.061304 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00110349  -131.25   0.00004817   131.25
  2   0.00942531   -67.69   0.00041148    33.84
  3   0.58294719    89.72   0.02544964   -29.91
  4   0.00052184  -139.34   0.00002278    34.83
  5   0.00076762   -90.09   0.00003351    18.02
  6   0.00010803   169.35   0.00000472   -28.22
  7   0.00016613   -88.30   0.00000725    12.61
  8   0.00012345   130.94   0.00000539   -16.37
  9   0.00191680   -91.51   0.00008368    10.17
 10   0.00002372   -40.28   0.00000104     4.03
 11   0.00001191  -121.66   0.00000052    11.06
 12   0.00002839  -177.41   0.00000124    14.78
 13   0.00000767   -10.39   0.00000033     0.80
 14   0.00005479   134.22   0.00000239    -9.59
 15   0.00042661   -92.15   0.00001862     6.14
 16   0.00000769   -26.61   0.00000034     1.66

13:29:20  Coil Rotation Frequency, Fcoil =  4.061541  Hz

13:29:24  Coil Rotation Frequency, Fcoil =  4.060883  Hz

13:29:52  Coil Voltage Measurement #  15  Made, Stored in RAWFILE

13:29:52  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .5823983  V, Vp main =  89.71355  deg

13:29:52  Coil Voltage Fit: 
Vfit(i) =  0.5823982 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.5823909 V * sin(3*2pi*i/ns) +  0.0029115 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0068674 V

13:29:56  Coil Rotation Frequency, Fcoil =  4.058603  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.060342 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00110322  -130.82   0.00004817   130.82
  2   0.00939777   -67.60   0.00041037    33.80
  3   0.58239830    89.71   0.02543170   -29.90
  4   0.00054715  -141.94   0.00002389    35.48
  5   0.00077734   -90.84   0.00003394    18.17
  6   0.00013750   161.30   0.00000600   -26.88
  7   0.00017250   -85.89   0.00000753    12.27
  8   0.00012137   130.44   0.00000530   -16.30
  9   0.00190548   -90.49   0.00008321    10.05
 10   0.00000795    -3.86   0.00000035     0.39
 11   0.00000947   -96.52   0.00000041     8.77
 12   0.00001384   153.39   0.00000060   -12.78
 13   0.00000734  -151.85   0.00000032    11.68
 14   0.00003947   136.88   0.00000172    -9.78
 15   0.00042570   -92.10   0.00001859     6.14
 16   0.00002669  -110.56   0.00000117     6.91

13:29:59  Coil Rotation Frequency, Fcoil =  4.059658  Hz

13:30:03  Coil Rotation Frequency, Fcoil =  4.060023  Hz

13:30:32  Coil Voltage Measurement #  16  Made, Stored in RAWFILE

13:30:32  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .5826418  V, Vp main =  89.71402  deg

13:30:32  Coil Voltage Fit: 
Vfit(i) =  0.5826417 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.5826344 V * sin(3*2pi*i/ns) +  0.0029079 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0068835 V

13:30:36  Coil Rotation Frequency, Fcoil =  4.061769  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.060483 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00110966  -131.47   0.00004845   131.47
  2   0.00942254   -67.76   0.00041144    33.88
  3   0.58264184    89.71   0.02544145   -29.90
  4   0.00058104  -136.96   0.00002537    34.24
  5   0.00076045   -90.36   0.00003321    18.07
  6   0.00014355  -177.74   0.00000627    29.62
  7   0.00015010   -87.32   0.00000655    12.47
  8   0.00012525   131.21   0.00000547   -16.40
  9   0.00189384   -91.45   0.00008270    10.16
 10   0.00002491   -24.57   0.00000109     2.46
 11   0.00003643   155.47   0.00000159   -14.13
 12   0.00001655  -177.17   0.00000072    14.76
 13   0.00002123    47.04   0.00000093    -3.62
 14   0.00004746   107.25   0.00000207    -7.66
 15   0.00042246   -94.28   0.00001845     6.29
 16   0.00000473   -97.69   0.00000021     6.11

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00005  0.00000    131.21     0.24
  2   0.00041  0.00000     33.82     0.05
  3   0.02544  0.00001    -29.90     0.00
  4   0.00002  0.00000     35.01     0.52
  5   0.00003  0.00000     18.06     0.07
  6   0.00001  0.00000    -13.10    24.67
  7   0.00001  0.00000     12.25     0.37
  8   0.00001  0.00000    -16.18     0.31
  9   0.00008  0.00000     10.12     0.05
 10   0.00000  0.00000      0.38     3.56
 11   0.00000  0.00000      3.28    10.14
 12   0.00000  0.00000      7.76    11.86
 13   0.00000  0.00000      1.35     6.23
 14   0.00000  0.00000     -9.34     1.00
 15   0.00002  0.00000      6.19     0.06
 16   0.00000  0.00000      5.25     2.09

13:30:36  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  2.543978E-02  +-  6.656784E-06  Tm
Integrated Sextupole Strength, SL =  25.258  +-  6.609217E-03  T/m

13:30:37  Magnet Current, Imag =  125.5376  A

13:30:37  Magnet Current Ramping to  150  A...

13:31:20  Magnet Current, Imag =  150.5416  A

13:31:21  Magnet Current, Imag =  150.5572  A

13:31:22  Magnet Current, Imag =  150.545  A

13:31:24  Magnet Current, Imag =  150.5404  A

13:31:25  Magnet Current, Imag =  150.5476  A

13:31:25  Average Magnet Current:
Imag =  150.5475  +-  6.139734E-03  A

13:31:28  Coil Rotation Frequency, Fcoil =  4.060833  Hz

13:31:32  Coil Rotation Frequency, Fcoil =  4.06074  Hz

13:32:01  Coil Voltage Measurement #  17  Made, Stored in RAWFILE

13:32:01  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .6975193  V, Vp main =  89.71144  deg

13:32:01  Coil Voltage Fit: 
Vfit(i) =  0.6975191 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.6975103 V * sin(3*2pi*i/ns) +  0.0035126 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0082528 V

13:32:05  Coil Rotation Frequency, Fcoil =  4.060625  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.060732 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00150254  -122.89   0.00006561   122.89
  2   0.01127356   -67.47   0.00049224    33.74
  3   0.69751930    89.71   0.03045579   -29.90
  4   0.00064430  -138.17   0.00002813    34.54
  5   0.00092997   -89.44   0.00004061    17.89
  6   0.00005212   151.45   0.00000228   -25.24
  7   0.00021133   -83.32   0.00000923    11.90
  8   0.00013738   121.72   0.00000600   -15.21
  9   0.00229573   -90.07   0.00010024    10.01
 10   0.00003220  -106.39   0.00000141    10.64
 11   0.00000561   -39.63   0.00000025     3.60
 12   0.00002664  -170.50   0.00000116    14.21
 13   0.00001480    49.06   0.00000065    -3.77
 14   0.00005110   102.53   0.00000223    -7.32
 15   0.00049227   -92.24   0.00002149     6.15
 16   0.00001032   -88.27   0.00000045     5.52

13:32:08  Coil Rotation Frequency, Fcoil =  4.061156  Hz

13:32:12  Coil Rotation Frequency, Fcoil =  4.060662  Hz

13:32:40  Coil Voltage Measurement #  18  Made, Stored in RAWFILE

13:32:40  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .6977677  V, Vp main =  89.71405  deg

13:32:40  Coil Voltage Fit: 
Vfit(i) =  0.6977675 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.6977588 V * sin(3*2pi*i/ns) +  0.0034821 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0082496 V

13:32:44  Coil Rotation Frequency, Fcoil =  4.05643  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.059416 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00151866  -122.97   0.00006633   122.97
  2   0.01126481   -67.45   0.00049201    33.73
  3   0.69776773    89.71   0.03047651   -29.90
  4   0.00060962  -141.84   0.00002663    35.46
  5   0.00093264   -90.67   0.00004073    18.13
  6   0.00007979   117.36   0.00000349   -19.56
  7   0.00019938   -87.18   0.00000871    12.45
  8   0.00015710   118.58   0.00000686   -14.82
  9   0.00231228   -91.22   0.00010099    10.14
 10   0.00001289   120.02   0.00000056   -12.00
 11   0.00003132  -152.77   0.00000137    13.89
 12   0.00003701   179.27   0.00000162   -14.94
 13   0.00004217   152.39   0.00000184   -11.72
 14   0.00004709   125.85   0.00000206    -8.99
 15   0.00049059   -92.55   0.00002143     6.17
 16   0.00002268  -150.25   0.00000099     9.39

13:32:47  Coil Rotation Frequency, Fcoil =  4.057234  Hz

13:32:52  Coil Rotation Frequency, Fcoil =  4.058711  Hz

13:33:20  Coil Voltage Measurement #  19  Made, Stored in RAWFILE

13:33:20  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .6975012  V, Vp main =  89.71181  deg

13:33:20  Coil Voltage Fit: 
Vfit(i) =  0.6975012 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.6974924 V * sin(3*2pi*i/ns) +  0.0035080 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0082587 V

13:33:24  Coil Rotation Frequency, Fcoil =  4.057957  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057967 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00150000  -122.57   0.00006554   122.57
  2   0.01127678   -67.50   0.00049271    33.75
  3   0.69750124    89.71   0.03047575   -29.90
  4   0.00065493  -138.52   0.00002862    34.63
  5   0.00093202   -89.36   0.00004072    17.87
  6   0.00005439   164.98   0.00000238   -27.50
  7   0.00020838   -81.84   0.00000910    11.69
  8   0.00013275   122.44   0.00000580   -15.30
  9   0.00232132   -90.72   0.00010142    10.08
 10   0.00002563   -40.33   0.00000112     4.03
 11   0.00000325    54.89   0.00000014    -4.99
 12   0.00002694  -159.65   0.00000118    13.30
 13   0.00000695   127.39   0.00000030    -9.80
 14   0.00003107    97.73   0.00000136    -6.98
 15   0.00048742   -92.52   0.00002130     6.17
 16   0.00002376   -35.37   0.00000104     2.21

13:33:27  Coil Rotation Frequency, Fcoil =  4.058868  Hz

13:33:31  Coil Rotation Frequency, Fcoil =  4.059388  Hz

13:34:00  Coil Voltage Measurement #  20  Made, Stored in RAWFILE

13:34:00  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .6976199  V, Vp main =  89.71307  deg

13:34:00  Coil Voltage Fit: 
Vfit(i) =  0.6976199 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.6976111 V * sin(3*2pi*i/ns) +  0.0034933 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0082539 V

13:34:04  Coil Rotation Frequency, Fcoil =  4.05532  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057859 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00151337  -123.13   0.00006613   123.13
  2   0.01126454   -67.54   0.00049219    33.77
  3   0.69761986    89.71   0.03048175   -29.90
  4   0.00065770  -141.63   0.00002874    35.41
  5   0.00093191   -89.83   0.00004072    17.97
  6   0.00009439   167.25   0.00000412   -27.87
  7   0.00020072   -84.35   0.00000877    12.05
  8   0.00014471   123.27   0.00000632   -15.41
  9   0.00233439   -90.69   0.00010200    10.08
 10   0.00002470   -81.69   0.00000108     8.17
 11   0.00002318  -126.05   0.00000101    11.46
 12   0.00004835  -168.10   0.00000211    14.01
 13   0.00000675   -54.73   0.00000030     4.21
 14   0.00004254    97.07   0.00000186    -6.93
 15   0.00049117   -92.32   0.00002146     6.15
 16   0.00003282   -88.36   0.00000143     5.52

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00007  0.00000    122.89     0.20
  2   0.00049  0.00000     33.75     0.02
  3   0.03047  0.00001    -29.90     0.00
  4   0.00003  0.00000     35.01     0.43
  5   0.00004  0.00000     17.97     0.10
  6   0.00000  0.00000    -25.04     3.32
  7   0.00001  0.00000     12.02     0.28
  8   0.00001  0.00000    -15.19     0.22
  9   0.00010  0.00000     10.08     0.05
 10   0.00000  0.00000      2.71     8.82
 11   0.00000  0.00000      5.99     7.39
 12   0.00000  0.00000      6.65    12.47
 13   0.00000  0.00000     -5.27     6.21
 14   0.00000  0.00000     -7.56     0.84
 15   0.00002  0.00000      6.16     0.01
 16   0.00000  0.00000      5.66     2.54

13:34:04  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  3.047245E-02  +-  9.892793E-06  Tm
Integrated Sextupole Strength, SL =  30.25471  +-  9.822104E-03  T/m

13:34:04            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00007  0.00000    0.2163   0.0011
  2   0.00049  0.00000    1.6155   0.0010
  3   0.03047  0.00001  100.0000   0.0459
  4   0.00003  0.00000    0.0920   0.0028
  5   0.00004  0.00000    0.1335   0.0002
  6   0.00000  0.00000    0.0101   0.0025
  7   0.00001  0.00000    0.0294   0.0007
  8   0.00001  0.00000    0.0205   0.0013
  9   0.00010  0.00000    0.3320   0.0021
 10   0.00000  0.00000    0.0034   0.0010
 11   0.00000  0.00000    0.0023   0.0017
 12   0.00000  0.00000    0.0050   0.0013
 13   0.00000  0.00000    0.0025   0.0021
 14   0.00000  0.00000    0.0062   0.0011
 15   0.00002  0.00000    0.0703   0.0002
 16   0.00000  0.00000    0.0032   0.0011

13:34:06  Magnet Current, Imag =  150.55  A

13:34:06  Magnet Current Ramping to  175  A...

13:34:48  Magnet Current, Imag =  175.5296  A

13:34:49  Magnet Current, Imag =  175.5246  A

13:34:50  Magnet Current, Imag =  175.5284  A

13:34:52  Magnet Current, Imag =  175.5306  A

13:34:53  Magnet Current, Imag =  175.529  A

13:34:53  Average Magnet Current:
Imag =  175.5282  +-  2.19982E-03  A

13:34:56  Coil Rotation Frequency, Fcoil =  4.058026  Hz

13:35:00  Coil Rotation Frequency, Fcoil =  4.057984  Hz

13:35:29  Coil Voltage Measurement #  21  Made, Stored in RAWFILE

13:35:29  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .811937  V, Vp main =  89.71192  deg

13:35:29  Coil Voltage Fit: 
Vfit(i) =  0.8119369 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.8119267 V * sin(3*2pi*i/ns) +  0.0040821 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0096235 V

13:35:33  Coil Rotation Frequency, Fcoil =  4.055408  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057139 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00188227  -117.97   0.00008226   117.97
  2   0.01312282   -67.48   0.00057349    33.74
  3   0.81193697    89.71   0.03548300   -29.90
  4   0.00075218  -141.46   0.00003287    35.36
  5   0.00108687   -89.66   0.00004750    17.93
  6   0.00009541   160.86   0.00000417   -26.81
  7   0.00024415   -84.01   0.00001067    12.00
  8   0.00016746   122.99   0.00000732   -15.37
  9   0.00270126   -90.75   0.00011805    10.08
 10   0.00002472  -130.36   0.00000108    13.04
 11   0.00002597  -155.80   0.00000113    14.16
 12   0.00003710  -178.59   0.00000162    14.88
 13   0.00002020    -9.37   0.00000088     0.72
 14   0.00006498   135.04   0.00000284    -9.65
 15   0.00056745   -90.84   0.00002480     6.06
 16   0.00001254   108.89   0.00000055    -6.81

13:35:36  Coil Rotation Frequency, Fcoil =  4.056592  Hz

13:35:40  Coil Rotation Frequency, Fcoil =  4.055601  Hz

13:36:08  Coil Voltage Measurement #  22  Made, Stored in RAWFILE

13:36:09  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .8117416  V, Vp main =  89.71066  deg

13:36:09  Coil Voltage Fit: 
Vfit(i) =  0.8117414 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.8117310 V * sin(3*2pi*i/ns) +  0.0040989 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0096136 V

13:36:13  Coil Rotation Frequency, Fcoil =  4.057649  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.056614 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00187802  -117.31   0.00008208   117.31
  2   0.01311050   -67.40   0.00057302    33.70
  3   0.81174159    89.71   0.03547906   -29.90
  4   0.00077991  -141.81   0.00003409    35.45
  5   0.00107691   -89.50   0.00004707    17.90
  6   0.00011419   170.76   0.00000499   -28.46
  7   0.00023954   -84.01   0.00001047    12.00
  8   0.00016518   124.95   0.00000722   -15.62
  9   0.00268683   -90.38   0.00011743    10.04
 10   0.00000556    39.62   0.00000024    -3.96
 11   0.00002602  -151.45   0.00000114    13.77
 12   0.00003472  -174.00   0.00000152    14.50
 13   0.00001941    57.73   0.00000085    -4.44
 14   0.00007577   127.63   0.00000331    -9.12
 15   0.00057730   -93.88   0.00002523     6.26
 16   0.00000504  -150.23   0.00000022     9.39

13:36:16  Coil Rotation Frequency, Fcoil =  4.059096  Hz

13:36:20  Coil Rotation Frequency, Fcoil =  4.059639  Hz

13:36:48  Coil Voltage Measurement #  23  Made, Stored in RAWFILE

13:36:48  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .812773  V, Vp main =  89.71088  deg

13:36:48  Coil Voltage Fit: 
Vfit(i) =  0.8127729 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.8127625 V * sin(3*2pi*i/ns) +  0.0041011 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0096022 V

13:36:52  Coil Rotation Frequency, Fcoil =  4.058384  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.05904 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00186306  -117.39   0.00008138   117.39
  2   0.01309708   -67.55   0.00057210    33.77
  3   0.81277305    89.71   0.03550291   -29.90
  4   0.00077787  -143.95   0.00003398    35.99
  5   0.00105669   -88.96   0.00004616    17.79
  6   0.00016543   163.91   0.00000723   -27.32
  7   0.00024805   -79.87   0.00001084    11.41
  8   0.00016147   129.10   0.00000705   -16.14
  9   0.00268637   -90.63   0.00011734    10.07
 10   0.00002802   -28.81   0.00000122     2.88
 11   0.00002774    61.02   0.00000121    -5.55
 12   0.00002381  -178.90   0.00000104    14.91
 13   0.00001183   109.49   0.00000052    -8.42
 14   0.00006400   118.56   0.00000280    -8.47
 15   0.00057972   -92.35   0.00002532     6.16
 16   0.00002392  -160.13   0.00000105    10.01

13:36:55  Coil Rotation Frequency, Fcoil =  4.058611  Hz

13:36:59  Coil Rotation Frequency, Fcoil =  4.057638  Hz

13:37:28  Coil Voltage Measurement #  24  Made, Stored in RAWFILE

13:37:28  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .8120438  V, Vp main =  89.71064  deg

13:37:28  Coil Voltage Fit: 
Vfit(i) =  0.8120437 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.8120334 V * sin(3*2pi*i/ns) +  0.0041007 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0096076 V

13:37:32  Coil Rotation Frequency, Fcoil =  4.059893  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.058714 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00187414  -117.52   0.00008187   117.52
  2   0.01310042   -67.34   0.00057229    33.67
  3   0.81204379    89.71   0.03547390   -29.90
  4   0.00076335  -141.07   0.00003335    35.27
  5   0.00107247   -89.98   0.00004685    18.00
  6   0.00008810   168.85   0.00000385   -28.14
  7   0.00022448   -81.79   0.00000981    11.68
  8   0.00016885   122.18   0.00000738   -15.27
  9   0.00270581   -91.20   0.00011820    10.13
 10   0.00002261   -22.66   0.00000099     2.27
 11   0.00000575  -137.55   0.00000025    12.50
 12   0.00001484   174.88   0.00000065   -14.57
 13   0.00001986   164.68   0.00000087   -12.67
 14   0.00006668   133.40   0.00000291    -9.53
 15   0.00057243   -92.95   0.00002501     6.20
 16   0.00000799    30.60   0.00000035    -1.91

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00008  0.00000    117.55     0.26
  2   0.00057  0.00000     33.72     0.04
  3   0.03548  0.00001    -29.90     0.00
  4   0.00003  0.00000     35.52     0.28
  5   0.00005  0.00000     17.91     0.07
  6   0.00001  0.00000    -27.68     0.65
  7   0.00001  0.00000     11.77     0.25
  8   0.00001  0.00000    -15.60     0.33
  9   0.00012  0.00000     10.08     0.03
 10   0.00000  0.00000      3.56     6.09
 11   0.00000  0.00000      8.72     8.26
 12   0.00000  0.00000      7.43    12.70
 13   0.00000  0.00000     -6.20     4.94
 14   0.00000  0.00000     -9.19     0.46
 15   0.00003  0.00000      6.17     0.07
 16   0.00000  0.00000      2.67     7.24

13:37:32  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  3.548472E-02  +-  1.0988E-05  Tm
Integrated Sextupole Strength, SL =  35.23116  +-  1.090949E-02  T/m

13:37:33  Magnet Current, Imag =  175.5392  A

13:37:33  Magnet Current Ramping to  200  A...

13:38:16  Magnet Current, Imag =  200.5432  A

13:38:17  Magnet Current, Imag =  200.5474  A

13:38:18  Magnet Current, Imag =  200.553  A

13:38:20  Magnet Current, Imag =  200.5488  A

13:38:21  Magnet Current, Imag =  200.5424  A

13:38:21  Average Magnet Current:
Imag =  200.5479  +-  3.786594E-03  A

13:38:24  Coil Rotation Frequency, Fcoil =  4.057364  Hz

13:38:28  Coil Rotation Frequency, Fcoil =  4.057222  Hz

13:38:57  Coil Voltage Measurement #  25  Made, Stored in RAWFILE

13:38:57  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .9258915  V, Vp main =  89.70937  deg

13:38:57  Coil Voltage Fit: 
Vfit(i) =  0.9258915 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.9258795 V * sin(3*2pi*i/ns) +  0.0046962 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0109457 V

13:39:01  Coil Rotation Frequency, Fcoil =  4.059315  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057967 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00222366  -115.03   0.00009716   115.03
  2   0.01491225   -67.43   0.00065156    33.72
  3   0.92589152    89.71   0.04045475   -29.90
  4   0.00084124  -142.41   0.00003676    35.60
  5   0.00121745   -89.49   0.00005319    17.90
  6   0.00008031   164.97   0.00000351   -27.49
  7   0.00026082   -87.72   0.00001140    12.53
  8   0.00017060   128.62   0.00000745   -16.08
  9   0.00309031   -90.68   0.00013502    10.08
 10   0.00001769   -98.47   0.00000077     9.85
 11   0.00001384   -96.88   0.00000060     8.81
 12   0.00000699   150.80   0.00000031   -12.57
 13   0.00001597  -122.31   0.00000070     9.41
 14   0.00008375   132.86   0.00000366    -9.49
 15   0.00065888   -91.05   0.00002879     6.07
 16   0.00004348   177.52   0.00000190   -11.10

13:39:04  Coil Rotation Frequency, Fcoil =  4.057338  Hz

13:39:08  Coil Rotation Frequency, Fcoil =  4.057087  Hz

13:39:36  Coil Voltage Measurement #  26  Made, Stored in RAWFILE

13:39:36  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .9262417  V, Vp main =  89.71174  deg

13:39:37  Coil Voltage Fit: 
Vfit(i) =  0.9262415 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.9262298 V * sin(3*2pi*i/ns) +  0.0046596 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0109806 V

13:39:40  Coil Rotation Frequency, Fcoil =  4.05968  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.058035 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00225086  -115.40   0.00009834   115.40
  2   0.01496137   -67.48   0.00065369    33.74
  3   0.92624170    89.71   0.04046937   -29.90
  4   0.00085201  -138.58   0.00003723    34.64
  5   0.00124964   -88.22   0.00005460    17.64
  6   0.00006453   171.62   0.00000282   -28.60
  7   0.00028082   -88.71   0.00001227    12.67
  8   0.00016627   126.25   0.00000726   -15.78
  9   0.00306791   -90.83   0.00013404    10.09
 10   0.00005628  -135.07   0.00000246    13.51
 11   0.00001359  -122.69   0.00000059    11.15
 12   0.00001073    98.57   0.00000047    -8.21
 13   0.00003200    73.49   0.00000140    -5.65
 14   0.00007008   118.11   0.00000306    -8.44
 15   0.00063408   -94.68   0.00002770     6.31
 16   0.00004419   171.87   0.00000193   -10.74

13:39:44  Coil Rotation Frequency, Fcoil =  4.058507  Hz

13:39:48  Coil Rotation Frequency, Fcoil =  4.058442  Hz

13:40:16  Coil Voltage Measurement #  27  Made, Stored in RAWFILE

13:40:16  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .9263449  V, Vp main =  89.71181  deg

13:40:16  Coil Voltage Fit: 
Vfit(i) =  0.9263448 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.9263330 V * sin(3*2pi*i/ns) +  0.0046590 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0109733 V

13:40:20  Coil Rotation Frequency, Fcoil =  4.05673  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057893 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00224103  -115.12   0.00009792   115.12
  2   0.01495795   -67.38   0.00065357    33.69
  3   0.92634487    89.71   0.04047530   -29.90
  4   0.00085094  -141.58   0.00003718    35.40
  5   0.00120452   -89.84   0.00005263    17.97
  6   0.00005804   157.70   0.00000254   -26.28
  7   0.00023821   -84.79   0.00001041    12.11
  8   0.00017574   124.12   0.00000768   -15.51
  9   0.00305783   -90.85   0.00013361    10.09
 10   0.00003341  -159.08   0.00000146    15.91
 11   0.00004301  -141.53   0.00000188    12.87
 12   0.00002486   168.02   0.00000109   -14.00
 13   0.00000681   -79.27   0.00000030     6.10
 14   0.00008778   134.88   0.00000384    -9.63
 15   0.00064897   -93.15   0.00002836     6.21
 16   0.00005283  -153.29   0.00000231     9.58

13:40:23  Coil Rotation Frequency, Fcoil =  4.056607  Hz

13:40:28  Coil Rotation Frequency, Fcoil =  4.057707  Hz

13:40:56  Coil Voltage Measurement #  28  Made, Stored in RAWFILE

13:40:56  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .9263357  V, Vp main =  89.71219  deg

13:40:56  Coil Voltage Fit: 
Vfit(i) =  0.9263355 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.9263238 V * sin(3*2pi*i/ns) +  0.0046527 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0109739 V

13:41:00  Coil Rotation Frequency, Fcoil =  4.059327  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.05788 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00223485  -115.31   0.00009765   115.31
  2   0.01494417   -67.50   0.00065297    33.75
  3   0.92633569    89.71   0.04047503   -29.90
  4   0.00089658  -142.16   0.00003917    35.54
  5   0.00123065   -90.12   0.00005377    18.02
  6   0.00009996   177.92   0.00000437   -29.65
  7   0.00027009   -83.17   0.00001180    11.88
  8   0.00018462   126.71   0.00000807   -15.84
  9   0.00310530   -91.18   0.00013568    10.13
 10   0.00001538  -123.03   0.00000067    12.30
 11   0.00001943  -123.95   0.00000085    11.27
 12   0.00003538   161.23   0.00000155   -13.44
 13   0.00005448   131.65   0.00000238   -10.13
 14   0.00007629   116.25   0.00000333    -8.30
 15   0.00065644   -91.94   0.00002868     6.13
 16   0.00005026  -146.40   0.00000220     9.15

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00010  0.00000    115.22     0.15
  2   0.00065  0.00000     33.72     0.02
  3   0.04047  0.00001    -29.90     0.00
  4   0.00004  0.00000     35.30     0.38
  5   0.00005  0.00000     17.88     0.15
  6   0.00000  0.00000    -28.01     1.25
  7   0.00001  0.00000     12.30     0.32
  8   0.00001  0.00000    -15.80     0.20
  9   0.00013  0.00000     10.10     0.02
 10   0.00000  0.00000     12.89     2.18
 11   0.00000  0.00000     11.02     1.45
 12   0.00000  0.00000    -12.05     2.28
 13   0.00000  0.00000     -0.07     8.07
 14   0.00000  0.00000     -8.97     0.60
 15   0.00003  0.00000      6.18     0.09
 16   0.00000  0.00000     -0.78    10.14

13:41:00  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  4.046861E-02  +-  8.344758E-06  Tm
Integrated Sextupole Strength, SL =  40.17944  +-  8.28513E-03  T/m

13:41:00            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00010  0.00000    0.2416   0.0011
  2   0.00065  0.00000    1.6135   0.0021
  3   0.04047  0.00001  100.0000   0.0292
  4   0.00004  0.00000    0.0929   0.0023
  5   0.00005  0.00000    0.1323   0.0018
  6   0.00000  0.00000    0.0082   0.0017
  7   0.00001  0.00000    0.0283   0.0017
  8   0.00001  0.00000    0.0188   0.0007
  9   0.00013  0.00000    0.3326   0.0020
 10   0.00000  0.00000    0.0033   0.0018
 11   0.00000  0.00000    0.0024   0.0013
 12   0.00000  0.00000    0.0021   0.0012
 13   0.00000  0.00000    0.0029   0.0020
 14   0.00000  0.00000    0.0086   0.0007
 15   0.00003  0.00000    0.0701   0.0010
 16   0.00000  0.00000    0.0051   0.0004

13:41:02  Magnet Current, Imag =  200.5406  A

13:41:02  Magnet Current Ramping to  150  A...

13:41:51  Magnet Current, Imag =  150.5482  A

13:41:52  Magnet Current, Imag =  150.554  A

13:41:53  Magnet Current, Imag =  150.554  A

13:41:55  Magnet Current, Imag =  150.551  A

13:41:56  Magnet Current, Imag =  150.5492  A

13:41:56  Average Magnet Current:
Imag =  150.552  +-  2.054249E-03  A

13:41:59  Coil Rotation Frequency, Fcoil =  4.057038  Hz

13:42:03  Coil Rotation Frequency, Fcoil =  4.057807  Hz

13:42:32  Coil Voltage Measurement #  29  Made, Stored in RAWFILE

13:42:32  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .702773  V, Vp main =  89.71394  deg

13:42:32  Coil Voltage Fit: 
Vfit(i) =  0.7027729 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.7027642 V * sin(3*2pi*i/ns) +  0.0035085 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0082820 V

13:42:36  Coil Rotation Frequency, Fcoil =  4.058261  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057702 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00141727  -124.10   0.00006193   124.10
  2   0.01132415   -67.72   0.00049482    33.86
  3   0.70277303    89.71   0.03070810   -29.90
  4   0.00062451  -138.85   0.00002729    34.71
  5   0.00093790   -90.10   0.00004098    18.02
  6   0.00005425   170.59   0.00000237   -28.43
  7   0.00020758   -86.29   0.00000907    12.33
  8   0.00014742   126.10   0.00000644   -15.76
  9   0.00231240   -91.09   0.00010104    10.12
 10   0.00001622  -171.72   0.00000071    17.17
 11   0.00002139  -168.11   0.00000093    15.28
 12   0.00004008  -163.63   0.00000175    13.64
 13   0.00001576  -150.96   0.00000069    11.61
 14   0.00004344   117.06   0.00000190    -8.36
 15   0.00048819   -93.56   0.00002133     6.24
 16   0.00002027   -72.95   0.00000089     4.56

13:42:39  Coil Rotation Frequency, Fcoil =  4.057707  Hz

13:42:43  Coil Rotation Frequency, Fcoil =  4.057565  Hz

13:43:12  Coil Voltage Measurement #  30  Made, Stored in RAWFILE

13:43:12  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .7029761  V, Vp main =  89.71385  deg

13:43:12  Coil Voltage Fit: 
Vfit(i) =  0.7029760 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.7029672 V * sin(3*2pi*i/ns) +  0.0035105 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0083096 V

13:43:16  Coil Rotation Frequency, Fcoil =  4.056834  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057368 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00144131  -123.28   0.00006298   123.28
  2   0.01135511   -67.77   0.00049621    33.89
  3   0.70297611    89.71   0.03071950   -29.90
  4   0.00062698  -136.28   0.00002740    34.07
  5   0.00093589   -90.24   0.00004090    18.05
  6   0.00006384   164.90   0.00000279   -27.48
  7   0.00020199   -86.67   0.00000883    12.38
  8   0.00013897   125.33   0.00000607   -15.67
  9   0.00234274   -91.23   0.00010238    10.14
 10   0.00001724    12.36   0.00000075    -1.24
 11   0.00001140  -138.75   0.00000050    12.61
 12   0.00004523   159.73   0.00000198   -13.31
 13   0.00003164  -156.46   0.00000138    12.04
 14   0.00004451   111.63   0.00000194    -7.97
 15   0.00050116   -92.85   0.00002190     6.19
 16   0.00002105   -71.82   0.00000092     4.49

13:43:19  Coil Rotation Frequency, Fcoil =  4.05529  Hz

13:43:23  Coil Rotation Frequency, Fcoil =  4.055136  Hz

13:43:51  Coil Voltage Measurement #  31  Made, Stored in RAWFILE

13:43:51  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .7031769  V, Vp main =  89.71389  deg

13:43:51  Coil Voltage Fit: 
Vfit(i) =  0.7031769 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.7031682 V * sin(3*2pi*i/ns) +  0.0035110 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0083093 V

13:43:55  Coil Rotation Frequency, Fcoil =  4.059384  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.056603 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00144578  -123.19   0.00006319   123.19
  2   0.01135710   -67.81   0.00049639    33.90
  3   0.70317692    89.71   0.03073407   -29.90
  4   0.00062323  -137.04   0.00002724    34.26
  5   0.00093345   -89.46   0.00004080    17.89
  6   0.00008845   159.55   0.00000387   -26.59
  7   0.00020855   -80.88   0.00000912    11.55
  8   0.00014596   123.52   0.00000638   -15.44
  9   0.00233103   -90.87   0.00010188    10.10
 10   0.00002877   -82.14   0.00000126     8.21
 11   0.00001701  -108.89   0.00000074     9.90
 12   0.00004264   168.49   0.00000186   -14.04
 13   0.00001754   -92.41   0.00000077     7.11
 14   0.00003936    79.82   0.00000172    -5.70
 15   0.00048607   -90.54   0.00002124     6.04
 16   0.00002531   -64.37   0.00000111     4.02

13:43:59  Coil Rotation Frequency, Fcoil =  4.058322  Hz

13:44:03  Coil Rotation Frequency, Fcoil =  4.059596  Hz

13:44:31  Coil Voltage Measurement #  32  Made, Stored in RAWFILE

13:44:31  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .7034445  V, Vp main =  89.71432  deg

13:44:31  Coil Voltage Fit: 
Vfit(i) =  0.7034444 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.7034356 V * sin(3*2pi*i/ns) +  0.0035071 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0083256 V

13:44:35  Coil Rotation Frequency, Fcoil =  4.058303  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.05874 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00144476  -124.19   0.00006311   124.19
  2   0.01137868   -67.97   0.00049707    33.99
  3   0.70344454    89.71   0.03072958   -29.90
  4   0.00069697  -135.93   0.00003045    33.98
  5   0.00092472   -89.80   0.00004040    17.96
  6   0.00012207  -170.12   0.00000533    28.35
  7   0.00019297   -80.60   0.00000843    11.51
  8   0.00013178   125.88   0.00000576   -15.73
  9   0.00232516   -91.20   0.00010157    10.13
 10   0.00000399   -74.23   0.00000017     7.42
 11   0.00004019   179.27   0.00000176   -16.30
 12   0.00004346   165.63   0.00000190   -13.80
 13   0.00002899   120.75   0.00000127    -9.29
 14   0.00005210   103.95   0.00000228    -7.43
 15   0.00048888   -94.04   0.00002136     6.27
 16   0.00001349   -13.38   0.00000059     0.84

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00006  0.00000    123.69     0.46
  2   0.00050  0.00000     33.91     0.05
  3   0.03072  0.00001    -29.90     0.00
  4   0.00003  0.00000     34.26     0.28
  5   0.00004  0.00000     17.98     0.06
  6   0.00000  0.00000    -13.54    24.20
  7   0.00001  0.00000     11.94     0.41
  8   0.00001  0.00000    -15.65     0.13
  9   0.00010  0.00000     10.12     0.02
 10   0.00000  0.00000      7.89     6.51
 11   0.00000  0.00000      5.37    12.66
 12   0.00000  0.00000     -6.88    11.85
 13   0.00000  0.00000      5.37     8.68
 14   0.00000  0.00000     -7.37     1.02
 15   0.00002  0.00000      6.18     0.09
 16   0.00000  0.00000      3.48     1.54

13:44:35  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  3.072281E-02  +-  9.999281E-06  Tm
Integrated Sextupole Strength, SL =  30.50328  +-  9.927832E-03  T/m

13:44:36  Magnet Current, Imag =  150.5552  A

13:44:36  Magnet Current Ramping to  100  A...

13:45:25  Magnet Current, Imag =  100.5644  A

13:45:26  Magnet Current, Imag =  100.564  A

13:45:28  Magnet Current, Imag =  100.5638  A

13:45:29  Magnet Current, Imag =  100.5648  A

13:45:31  Magnet Current, Imag =  100.5632  A

13:45:31  Average Magnet Current:
Imag =  100.564  +-  5.704344E-04  A

13:45:34  Coil Rotation Frequency, Fcoil =  4.058184  Hz

13:45:38  Coil Rotation Frequency, Fcoil =  4.058014  Hz

13:46:06  Coil Voltage Measurement #  33  Made, Stored in RAWFILE

13:46:06  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4719866  V, Vp main =  89.71386  deg

13:46:06  Coil Voltage Fit: 
Vfit(i) =  0.4719865 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.4719807 V * sin(3*2pi*i/ns) +  0.0023570 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055560 V

13:46:10  Coil Rotation Frequency, Fcoil =  4.058234  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.058144 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00066100  -159.48   0.00002888   159.48
  2   0.00762689   -67.89   0.00033323    33.94
  3   0.47198659    89.71   0.02062150   -29.90
  4   0.00043369  -138.97   0.00001895    34.74
  5   0.00059742   -88.34   0.00002610    17.67
  6   0.00010213   168.04   0.00000446   -28.01
  7   0.00014369   -78.08   0.00000628    11.15
  8   0.00010770   125.30   0.00000471   -15.66
  9   0.00155330   -90.75   0.00006786    10.08
 10   0.00002583  -133.50   0.00000113    13.35
 11   0.00001123   168.35   0.00000049   -15.30
 12   0.00001866    -9.28   0.00000082     0.77
 13   0.00003233   -26.30   0.00000141     2.02
 14   0.00004572   120.66   0.00000200    -8.62
 15   0.00035119   -89.63   0.00001534     5.98
 16   0.00001503    93.55   0.00000066    -5.85

13:46:14  Coil Rotation Frequency, Fcoil =  4.057515  Hz

13:46:18  Coil Rotation Frequency, Fcoil =  4.056711  Hz

13:46:46  Coil Voltage Measurement #  34  Made, Stored in RAWFILE

13:46:46  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4719459  V, Vp main =  89.71793  deg

13:46:46  Coil Voltage Fit: 
Vfit(i) =  0.4719459 V * cos(3*2pi*i/ns +   89.72 deg)
        = -0.4719402 V * sin(3*2pi*i/ns) +  0.0023231 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055537 V

13:46:50  Coil Rotation Frequency, Fcoil =  4.057723  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057316 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00069375  -159.33   0.00003032   159.33
  2   0.00762307   -67.83   0.00033313    33.92
  3   0.47194594    89.72   0.02062393   -29.91
  4   0.00045858  -137.65   0.00002004    34.41
  5   0.00059733   -90.40   0.00002610    18.08
  6   0.00011070   176.85   0.00000484   -29.48
  7   0.00014697   -83.81   0.00000642    11.97
  8   0.00008993   119.55   0.00000393   -14.94
  9   0.00153784   -90.56   0.00006720    10.06
 10   0.00000867   -88.64   0.00000038     8.86
 11   0.00000835   158.58   0.00000036   -14.42
 12   0.00003609     6.06   0.00000158    -0.50
 13   0.00000527  -158.47   0.00000023    12.19
 14   0.00003131    85.87   0.00000137    -6.13
 15   0.00034145   -92.61   0.00001492     6.17
 16   0.00001286    25.94   0.00000056    -1.62

13:46:53  Coil Rotation Frequency, Fcoil =  4.058064  Hz

13:46:57  Coil Rotation Frequency, Fcoil =  4.059504  Hz

13:47:26  Coil Voltage Measurement #  35  Made, Stored in RAWFILE

13:47:26  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4723339  V, Vp main =  89.71694  deg

13:47:26  Coil Voltage Fit: 
Vfit(i) =  0.4723338 V * cos(3*2pi*i/ns +   89.72 deg)
        = -0.4723281 V * sin(3*2pi*i/ns) +  0.0023333 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055584 V

13:47:30  Coil Rotation Frequency, Fcoil =  4.058026  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.058531 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00069137  -160.30   0.00003020   160.30
  2   0.00763296   -67.98   0.00033346    33.99
  3   0.47233394    89.72   0.02063470   -29.91
  4   0.00037261  -133.55   0.00001628    33.39
  5   0.00060023   -89.08   0.00002622    17.82
  6   0.00005249   160.71   0.00000229   -26.79
  7   0.00013160   -83.25   0.00000575    11.89
  8   0.00009839   116.95   0.00000430   -14.62
  9   0.00154913   -91.57   0.00006768    10.17
 10   0.00000646    -6.41   0.00000028     0.64
 11   0.00002997   163.83   0.00000131   -14.89
 12   0.00003335    -8.16   0.00000146     0.68
 13   0.00002696    76.37   0.00000118    -5.87
 14   0.00003264    98.75   0.00000143    -7.05
 15   0.00033748   -91.95   0.00001474     6.13
 16   0.00001503    -3.59   0.00000066     0.22

13:47:33  Coil Rotation Frequency, Fcoil =  4.056796  Hz

13:47:37  Coil Rotation Frequency, Fcoil =  4.057161  Hz

13:48:06  Coil Voltage Measurement #  36  Made, Stored in RAWFILE

13:48:06  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4717529  V, Vp main =  89.71622  deg

13:48:06  Coil Voltage Fit: 
Vfit(i) =  0.4717529 V * cos(3*2pi*i/ns +   89.72 deg)
        = -0.4717471 V * sin(3*2pi*i/ns) +  0.0023363 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055580 V

13:48:10  Coil Rotation Frequency, Fcoil =  4.058923  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057626 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00069069  -160.98   0.00003018   160.98
  2   0.00762520   -67.88   0.00033319    33.94
  3   0.47175294    89.72   0.02061392   -29.91
  4   0.00044273  -135.93   0.00001935    33.98
  5   0.00059840   -91.40   0.00002615    18.28
  6   0.00010733  -178.67   0.00000469    29.78
  7   0.00014854   -87.32   0.00000649    12.47
  8   0.00008667   120.39   0.00000379   -15.05
  9   0.00156293   -91.26   0.00006829    10.14
 10   0.00001022   -72.31   0.00000045     7.23
 11   0.00001465  -167.80   0.00000064    15.25
 12   0.00002799     8.41   0.00000122    -0.70
 13   0.00000688   -96.28   0.00000030     7.41
 14   0.00004342   109.80   0.00000190    -7.84
 15   0.00033918   -91.84   0.00001482     6.12
 16   0.00001440    40.58   0.00000063    -2.54

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00003  0.00000    160.02     0.66
  2   0.00033  0.00000     33.95     0.03
  3   0.02062  0.00001    -29.91     0.00
  4   0.00002  0.00000     34.13     0.51
  5   0.00003  0.00000     17.96     0.24
  6   0.00000  0.00000    -13.62    25.08
  7   0.00001  0.00000     11.87     0.47
  8   0.00000  0.00000    -15.07     0.38
  9   0.00007  0.00000     10.11     0.04
 10   0.00000  0.00000      7.52     4.56
 11   0.00000  0.00000     -7.34    13.05
 12   0.00000  0.00000      0.06     0.67
 13   0.00000  0.00000      3.94     6.71
 14   0.00000  0.00000     -7.41     0.92
 15   0.00001  0.00000      6.10     0.07
 16   0.00000  0.00000     -2.44     2.20

13:48:10  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  2.062351E-02  +-  7.44193E-06  Tm
Integrated Sextupole Strength, SL =  20.47614  +-  7.388754E-03  T/m

13:48:11  Magnet Current, Imag =  100.566  A

13:48:11  Magnet Current Ramping to  50  A...

13:49:00  Magnet Current, Imag =  50.56862  A

13:49:02  Magnet Current, Imag =  50.5641  A

13:49:03  Magnet Current, Imag =  50.56216  A

13:49:05  Magnet Current, Imag =  50.56876  A

13:49:07  Magnet Current, Imag =  50.56558  A

13:49:07  Average Magnet Current:
Imag =  50.56515  +-  2.411508E-03  A

13:49:10  Coil Rotation Frequency, Fcoil =  4.057477  Hz

13:49:14  Coil Rotation Frequency, Fcoil =  4.058773  Hz

13:49:43  Coil Voltage Measurement #  37  Made, Stored in RAWFILE

13:49:43  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2393169  V, Vp main =  89.70745  deg

13:49:43  Coil Voltage Fit: 
Vfit(i) =  0.2393168 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.2393137 V * sin(3*2pi*i/ns) +  0.0012218 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028552 V

13:49:47  Coil Rotation Frequency, Fcoil =  4.0594  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.058549 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00077105   130.30   0.00003368  -130.30
  2   0.00386175   -67.82   0.00016871    33.91
  3   0.23931685    89.71   0.01045491   -29.90
  4   0.00021881  -137.31   0.00000956    34.33
  5   0.00027925   -91.13   0.00001220    18.23
  6   0.00002591   179.03   0.00000113   -29.84
  7   0.00007623   -84.94   0.00000333    12.13
  8   0.00004562   128.63   0.00000199   -16.08
  9   0.00079403   -90.94   0.00003469    10.10
 10   0.00000908   -37.62   0.00000040     3.76
 11   0.00000316   -48.52   0.00000014     4.41
 12   0.00000394  -174.05   0.00000017    14.50
 13   0.00000944     7.97   0.00000041    -0.61
 14   0.00001590   112.85   0.00000069    -8.06
 15   0.00017465   -93.52   0.00000763     6.23
 16   0.00000425   178.78   0.00000019   -11.17

13:49:50  Coil Rotation Frequency, Fcoil =  4.057265  Hz

13:49:54  Coil Rotation Frequency, Fcoil =  4.057073  Hz

13:50:22  Coil Voltage Measurement #  38  Made, Stored in RAWFILE

13:50:23  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2394144  V, Vp main =  89.70959  deg

13:50:23  Coil Voltage Fit: 
Vfit(i) =  0.2394144 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.2394114 V * sin(3*2pi*i/ns) +  0.0012134 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028631 V

13:50:26  Coil Rotation Frequency, Fcoil =  4.059346  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057894 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00077561   130.76   0.00003389  -130.76
  2   0.00387147   -67.91   0.00016916    33.95
  3   0.23941444    89.71   0.01046086   -29.90
  4   0.00023861  -126.23   0.00001043    31.56
  5   0.00028037   -90.56   0.00001225    18.11
  6   0.00003660  -123.94   0.00000160    20.66
  7   0.00006567   -93.27   0.00000287    13.32
  8   0.00003605   130.35   0.00000158   -16.29
  9   0.00079447   -90.32   0.00003471    10.04
 10   0.00000676  -110.22   0.00000030    11.02
 11   0.00000957   -74.16   0.00000042     6.74
 12   0.00000490  -143.33   0.00000021    11.94
 13   0.00001202  -172.77   0.00000053    13.29
 14   0.00001747   130.28   0.00000076    -9.31
 15   0.00017349   -92.94   0.00000758     6.20
 16   0.00000724  -117.78   0.00000032     7.36

13:50:30  Coil Rotation Frequency, Fcoil =  4.057488  Hz

13:50:34  Coil Rotation Frequency, Fcoil =  4.055627  Hz

13:51:02  Coil Voltage Measurement #  39  Made, Stored in RAWFILE

13:51:02  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2392168  V, Vp main =  89.709  deg

13:51:02  Coil Voltage Fit: 
Vfit(i) =  0.2392167 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.2392136 V * sin(3*2pi*i/ns) +  0.0012148 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028569 V

13:51:06  Coil Rotation Frequency, Fcoil =  4.055977  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.056364 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00077111   130.79   0.00003371  -130.79
  2   0.00386644   -67.75   0.00016900    33.87
  3   0.23921676    89.71   0.01045617   -29.90
  4   0.00022318  -133.63   0.00000976    33.41
  5   0.00027512   -90.13   0.00001203    18.03
  6   0.00002063   169.51   0.00000090   -28.25
  7   0.00006679   -80.82   0.00000292    11.55
  8   0.00005021   123.53   0.00000219   -15.44
  9   0.00078372   -90.03   0.00003426    10.00
 10   0.00000543   126.53   0.00000024   -12.65
 11   0.00000333  -179.53   0.00000015    16.32
 12   0.00000599   135.90   0.00000026   -11.33
 13   0.00001258    95.45   0.00000055    -7.34
 14   0.00001420   114.69   0.00000062    -8.19
 15   0.00017666   -94.43   0.00000772     6.30
 16   0.00000805  -132.16   0.00000035     8.26

13:51:09  Coil Rotation Frequency, Fcoil =  4.058222  Hz

13:51:14  Coil Rotation Frequency, Fcoil =  4.058511  Hz

13:51:42  Coil Voltage Measurement #  40  Made, Stored in RAWFILE

13:51:42  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2391915  V, Vp main =  89.70874  deg

13:51:42  Coil Voltage Fit: 
Vfit(i) =  0.2391915 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.2391884 V * sin(3*2pi*i/ns) +  0.0012158 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028566 V

13:51:46  Coil Rotation Frequency, Fcoil =  4.059069  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.058601 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00077566   130.56   0.00003389  -130.56
  2   0.00386519   -67.83   0.00016885    33.92
  3   0.23919152    89.71   0.01044930   -29.90
  4   0.00022762  -133.68   0.00000994    33.42
  5   0.00028057   -89.88   0.00001226    17.98
  6   0.00002506  -179.56   0.00000109    29.93
  7   0.00006190   -87.44   0.00000270    12.49
  8   0.00004509   131.74   0.00000197   -16.47
  9   0.00078052   -91.57   0.00003410    10.17
 10   0.00000511  -124.77   0.00000022    12.48
 11   0.00000591  -164.94   0.00000026    14.99
 12   0.00000599    77.91   0.00000026    -6.49
 13   0.00001019   141.17   0.00000045   -10.86
 14   0.00002086   129.30   0.00000091    -9.24
 15   0.00017865   -94.04   0.00000780     6.27
 16   0.00000643  -133.62   0.00000028     8.35

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00003  0.00000   -130.60     0.19
  2   0.00017  0.00000     33.91     0.03
  3   0.01046  0.00000    -29.90     0.00
  4   0.00001  0.00000     33.18     1.01
  5   0.00001  0.00000     18.09     0.10
  6   0.00000  0.00000     -1.88    27.37
  7   0.00000  0.00000     12.37     0.64
  8   0.00000  0.00000    -16.07     0.39
  9   0.00003  0.00000     10.08     0.07
 10   0.00000  0.00000      3.65     9.98
 11   0.00000  0.00000     10.62     5.13
 12   0.00000  0.00000      2.16    11.23
 13   0.00000  0.00000     -1.38     9.24
 14   0.00000  0.00000     -8.70     0.57
 15   0.00001  0.00000      6.25     0.04
 16   0.00000  0.00000      3.20     8.31

13:51:46  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  1.045531E-02  +-  4.117697E-06  Tm
Integrated Sextupole Strength, SL =  10.3806  +-  4.088274E-03  T/m

13:51:48  Magnet Current, Imag =  50.56304  A

13:51:48  Magnet Current Ramping to  25  A...

13:52:30  Magnet Current, Imag =  25.58132  A

13:52:32  Magnet Current, Imag =  25.5782  A

13:52:34  Magnet Current, Imag =  25.57664  A

13:52:36  Magnet Current, Imag =  25.57564  A

13:52:38  Magnet Current, Imag =  25.5802  A

13:52:38  Average Magnet Current:
Imag =  25.57767  +-  1.721993E-03  A

13:52:41  Coil Rotation Frequency, Fcoil =  4.057569  Hz

13:52:45  Coil Rotation Frequency, Fcoil =  4.057753  Hz

13:53:13  Coil Voltage Measurement #  41  Made, Stored in RAWFILE

13:53:14  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1229693  V, Vp main =  89.71116  deg

13:53:14  Coil Voltage Fit: 
Vfit(i) =  0.1229693 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.1229677 V * sin(3*2pi*i/ns) +  0.0006199 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0016237 V

13:53:17  Coil Rotation Frequency, Fcoil =  4.058257  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.057859 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00105270   114.10   0.00004600  -114.10
  2   0.00198960   -68.07   0.00008693    34.04
  3   0.12296933    89.71   0.00537301   -29.90
  4   0.00011719  -133.91   0.00000512    33.48
  5   0.00012703   -90.78   0.00000555    18.16
  6   0.00001471   163.38   0.00000064   -27.23
  7   0.00003364   -79.47   0.00000147    11.35
  8   0.00002358   121.51   0.00000103   -15.19
  9   0.00040711   -90.77   0.00001779    10.09
 10   0.00000293   -35.94   0.00000013     3.59
 11   0.00000437   -86.59   0.00000019     7.87
 12   0.00001081   170.29   0.00000047   -14.19
 13   0.00000648   -55.58   0.00000028     4.28
 14   0.00001240   141.29   0.00000054   -10.09
 15   0.00008728   -92.49   0.00000381     6.17
 16   0.00000401   -64.63   0.00000018     4.04

13:53:21  Coil Rotation Frequency, Fcoil =  4.057934  Hz

13:53:25  Coil Rotation Frequency, Fcoil =  4.057392  Hz

13:53:53  Coil Voltage Measurement #  42  Made, Stored in RAWFILE

13:53:53  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1229434  V, Vp main =  89.70997  deg

13:53:53  Coil Voltage Fit: 
Vfit(i) =  0.1229434 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.1229418 V * sin(3*2pi*i/ns) +  0.0006223 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0016234 V

13:53:57  Coil Rotation Frequency, Fcoil =  4.05552  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.056949 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00104998   114.17   0.00004589  -114.17
  2   0.00199085   -68.17   0.00008701    34.09
  3   0.12294339    89.71   0.00537308   -29.90
  4   0.00011983  -128.94   0.00000524    32.24
  5   0.00012542   -90.76   0.00000548    18.15
  6   0.00000889  -163.23   0.00000039    27.20
  7   0.00003435   -96.72   0.00000150    13.82
  8   0.00001882   116.13   0.00000082   -14.52
  9   0.00040645   -91.85   0.00001776    10.21
 10   0.00000329    37.53   0.00000014    -3.75
 11   0.00000824  -124.72   0.00000036    11.34
 12   0.00000412   158.63   0.00000018   -13.22
 13   0.00000586   171.07   0.00000026   -13.16
 14   0.00000688   130.02   0.00000030    -9.29
 15   0.00008683   -92.39   0.00000379     6.16
 16   0.00000285   124.75   0.00000012    -7.80

13:54:01  Coil Rotation Frequency, Fcoil =  4.054456  Hz

13:54:05  Coil Rotation Frequency, Fcoil =  4.055089  Hz

13:54:33  Coil Voltage Measurement #  43  Made, Stored in RAWFILE

13:54:33  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1229709  V, Vp main =  89.70937  deg

13:54:33  Coil Voltage Fit: 
Vfit(i) =  0.1229709 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.1229693 V * sin(3*2pi*i/ns) +  0.0006237 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0016238 V

13:54:37  Coil Rotation Frequency, Fcoil =  4.057123  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.055556 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00106659   113.38   0.00004663  -113.38
  2   0.00198309   -68.00   0.00008670    34.00
  3   0.12297094    89.71   0.00537613   -29.90
  4   0.00010441  -133.57   0.00000456    33.39
  5   0.00012816   -89.78   0.00000560    17.96
  6   0.00001067   110.30   0.00000047   -18.38
  7   0.00003078   -88.77   0.00000135    12.68
  8   0.00002337   115.79   0.00000102   -14.47
  9   0.00040771   -91.19   0.00001782    10.13
 10   0.00000683   -46.50   0.00000030     4.65
 11   0.00000475  -119.47   0.00000021    10.86
 12   0.00000431   177.77   0.00000019   -14.81
 13   0.00000614    19.94   0.00000027    -1.53
 14   0.00001285   155.11   0.00000056   -11.08
 15   0.00008508   -91.24   0.00000372     6.08
 16   0.00000876  -124.09   0.00000038     7.76

13:54:40  Coil Rotation Frequency, Fcoil =  4.055985  Hz

13:54:45  Coil Rotation Frequency, Fcoil =  4.055754  Hz

13:55:13  Coil Voltage Measurement #  44  Made, Stored in RAWFILE

13:55:13  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1229501  V, Vp main =  89.71152  deg

13:55:13  Coil Voltage Fit: 
Vfit(i) =  0.1229500 V * cos(3*2pi*i/ns +   89.71 deg)
        = -0.1229485 V * sin(3*2pi*i/ns) +  0.0006190 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0016238 V

13:55:17  Coil Rotation Frequency, Fcoil =  4.053469  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.055069 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00107544   114.20   0.00004702  -114.20
  2   0.00197927   -68.22   0.00008654    34.11
  3   0.12295007    89.71   0.00537587   -29.90
  4   0.00011501  -133.98   0.00000503    33.50
  5   0.00012585   -90.03   0.00000550    18.01
  6   0.00001220   170.32   0.00000053   -28.39
  7   0.00003259   -92.02   0.00000142    13.15
  8   0.00002570   127.06   0.00000112   -15.88
  9   0.00040068   -91.09   0.00001752    10.12
 10   0.00000188  -177.50   0.00000008    17.75
 11   0.00000244  -122.57   0.00000011    11.14
 12   0.00000292  -136.14   0.00000013    11.34
 13   0.00000106   137.41   0.00000005   -10.57
 14   0.00001258   103.71   0.00000055    -7.41
 15   0.00008709   -94.12   0.00000381     6.27
 16   0.00000670    -6.70   0.00000029     0.42

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00005  0.00000   -113.96     0.34
  2   0.00009  0.00000     34.06     0.04
  3   0.00537  0.00000    -29.90     0.00
  4   0.00000  0.00000     33.15     0.53
  5   0.00001  0.00000     18.07     0.09
  6   0.00000  0.00000    -11.70    22.79
  7   0.00000  0.00000     12.75     0.90
  8   0.00000  0.00000    -15.02     0.58
  9   0.00002  0.00000     10.14     0.04
 10   0.00000  0.00000      5.56     7.75
 11   0.00000  0.00000     10.30     1.41
 12   0.00000  0.00000     -7.72    11.02
 13   0.00000  0.00000     -5.25     6.99
 14   0.00000  0.00000     -9.47     1.35
 15   0.00000  0.00000      6.17     0.07
 16   0.00000  0.00000      1.10     5.76

13:55:17  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  5.374524E-03  +-  1.479391E-06  Tm
Integrated Sextupole Strength, SL =  5.33612  +-  1.46882E-03  T/m

13:55:19  Magnet Current, Imag =  25.58046  A

13:55:19  Magnet Current Ramping to  0  A...

13:56:02  Magnet Current, Imag =  .596984  A