Magnet Measurement Test Plan

Fill

Logistic Info

| Person Responsible | Domenico Dell’Orco – Robert DiMattia (x5457) |
| --- | --- |
| Phone # | 650-926-8683 (cell. 510-219-0378) |
| Start Date | 06-12-2006 |
| Finish Date | 08-12-2006 |
| Acct # for alignment | 92-2121-1 |

Magnet Designation and Type

| Project Name | Spear 3 Chicane project |
| --- | --- |
| Magnet Type | Dipole |
| Magnet Name/Number | Chicane dipole prototype |
| Serial # / PC # |  |
| Trim Coils | Yes | Trim Types | Solid/ indirectly cooled |
| Magnet gap or diameter (mm) | 44.7 mm |

Alignment

| Precision (0.05 mm) |
| --- |
| Has the magnet been fiducialized | It will be fiducialized on 6/9/06 |
| If it has not been fiducialized, what is origin point of the magnet, what is its coordinate system and what surfaces should be used for alignment? | The magnet origin is the center of the pole gap (when chamfer plates are installed) or 2.726” from vertical face of pole. |
| + Z direction of magnet (Please provide drawing) | Z is the same as beam direction |

Special Alignment Tolerances

| X | 200 um |
| --- | --- |
| Y | 200 um |
| Pitch | 1000 urad |
| Yaw | 500 urad |
| Roll | 1000 urad |

Water and Power.

| Water Pressure | 180 psi DP (2 water circuits in paralles) | PSI |
| --- | --- | --- |
| Water Flow | 1.2 GPM @ 150 psi DP | Gpm |
| Maximum Current Main | 300 | Amps |
| Max Current Trims | 30 | Amps |

Polarity

| Main Coil Polarity. (Nearest North pole to Horizontal look in +z direction) | Power leads are marked. B field downward with coils in the backleg. B field upward with coils on the pole. |
| --- | --- |
| 1st Trim Polarity (Nearest North pole to Horizontal look in +z direction) | N/A |
| 2nd Trim Polarity (Nearest North pole to Horizontal look in +z direction) | N/A |

Temperature Tests

| Temperature and Resistance Test | No, Protect magnet using thermostats |
| --- | --- |
| Areas to be measured |  |
| Currents (Amps) |  |
| Check water flow | Yes |

Standardization

| Magnet warm up. ? time (mins) @ ? current (Amps) | 300 A |
| --- | --- |
| Conditioning Standardization Cycles Performed before measurements: |  |
| Number of Stdz cycles | 3 |
| Ramp Rate (A/s) | 10 A/s | Minimum Current (A) | 0 |
| Settle Time (sec) | 300 s | Maximum Current (A) | 300 |
| Ramp Type (Linear or Three Linear or Cosine | Linear |

Measurements

| Integrated Strength | Main | Yes | Trims | Yes |
| --- | --- | --- | --- | --- |
| Currents: | 0-280 A in steps of 20A | 20 A |
| Harmonics | Main | No | Trims | N/A |
| Currents: |  |  |

Harmonic Tolerances (as % of main, Main =100 %)

| Dipole n = 1 | Quadrupole n = 2 | Sextupole n = 3 | Octupole n =4 |
| --- | --- | --- | --- |

Field Map

| Type of map? (Transverse, axial, 3D, Locate Center) | Transverse: IntBydz vs x Beam is located at center of pole (when chamfered plates are installed) See #2 |
| --- | --- |
| Dimensions ( X, Y, Z) -50 mm < x < 50 mm |  |
| Spacing between step (X, Y, Z) Dx = 1mm |  |

Notes and Additional Tests:

- Based on these measurements we will chamfer the chamfer plates and repeat the measurements until field uniformity is met. The chamfer plates are removable.

- For the coil in the backleg the 3 currents (3GeV) are:

  - CD1: 23.47 A

  - CD2: 57.69 A

  - CD4: 116.43 A

(for the records I'm counting on loosing 5% of integrated field because of chamfering). Please perform the full scan (+/- 50 mm) at these 3 currents.