## Traveler for the Fast-Feedback Corrector Magnets

Aug. 11, 2008

This traveler is intended to cover magnetic measurements for the fast-feedback corrector dipole magnets.  There are at least four such air-core magnets.

Receiving:

The following information is to be noted upon receipt of the magnets by the SLAC MFD group:

| Received by (initials): |  |
| --- | --- |
| Date of magnetic measurements (mmm-dd-yyyy): | 8/29/2208 |
| SLAC barcode number: | 000614 |

| Place a barcode sticker on the magnet and also duplicate the barcode sticker here ( |  |
| --- | --- |

Preparation:

A beam direction arrow, with text “beam direction”, is to be applied to the top and/or connector side of the magnet, preferably by stenciling or rubber stamp, or by sticker supplied by LCLS.  Place the beam direction arrow pointing as shown in Fig. 1.

| Beam-direction arrow in place (initials): |  |
| --- | --- |

Fiducialization:

No fiducialization needs to be done for these steering coil magnets.

Magnetic Measurements:

Enter URL of on-line magnetic measurements data (please modify or correct if necessary):

http://www-group.slac.stanford.edu/met/MagMeas/MAGDATA/LCLS/Corr/

- Determine connection polarities (with power supply outputting positive current) for both the coils, which produce a “positive” field polarity as shown below:

Figure 1.  All steering coils are defined as “positive” and are powered by bipolar supplies.

- Mark the polarities near both pairs of magnet leads with clear “+” and “” labels as shown above.

| Labels and polarities have been marked (initials): |  |
| --- | --- |

- Connect the magnet terminals, in the correct polarity as established above, to a bipolar power supply with maximum current I ( (6 A.

- Run the coil up to 4.2 A for ~30 minutes to warm it up (record temperature).  Please also try to determine the current at which the temperature rise is 20ºC (Can it run at 6 A after full warm-up?). This test only needs to be done for one of these fast-feedback magnets.

| Ambient temperature (°C): | 28.52 °C |
| --- | --- |
| Final magnet temperature at 4.2 A (°C): | 31.81 °C |
| Magnet current at a temperature rise of 20 °C (A): | N/A |

- Measure the length-integrated dipole field, (Bydl, from 4.2 to +4.2 A in 0.6-A steps, including zero (15 ‘up’ measurements), and then back down from +4.2 A to 4.2 in 0.6-A steps, including zero (15 ‘down’ measurements).

| Filename & run number of (Bydl data: | Wiredat.ru2 |
| --- | --- |

- Measure the field harmonics at I = +4.2 A with a probe radius of about 0.5 inch (1-inch diameter) and at least twice the length of the magnet, in order to include the fringe fields.  This test only needs to be done for one of these fast-feedback magnets.

| Rotating coil designation (coil name): | DC34 |
| --- | --- |
| Rotating coil radius: | 0.0082083 m |
| Data file name of harmonics (file-name & run #): | Hardat.ru3 |

- Measure the inductance and resistance of each of the two coils on this magnet:

| Inductance of coils (mH): | 42.136 mH |
| --- | --- |
| Resistance of coils (Ohms): | 1.178 Ohm |

- Upon completion of tests, send traveler to Paul Emma at mailstop 103.

This section is to be completed by P. Emma.

| Magnet accepted (signed): |  |
| --- | --- |
| Assigned beamline location (MAD-deck name): |  |

- Upon full completion, send this traveler to Kathleen Ratcliffe at mailstop 18.