SLAC Magnetic Measurements
Date: 07-07-1995
Time: 06:12:14

Magnet Name (Serial #): 104
Bar Code Number: 012
Project: PEP II High Energy Ring Sextupoles
Test Stand: IR8, S1
Measurement Coil: # 1
Operator: bmd
Run Number: 2
Comment: std run

Standardization Currents (A):
   250.0    10.0   200.0    10.0   200.0    10.0   200.0
    10.0

Test Currents (A):
    25.0    50.0   100.0   125.0   150.0   175.0   200.0
   150.0   100.0    50.0    25.0

06:12:28  Magnet Current, Imag = -.000484  A

06:12:28  Magnet Current Ramping to  150  A...

06:13:48  Magnet Current, Imag =  150.5916  A

06:13:51  Temperature: Channel  1 , T =  14.6492  deg C

06:13:53  Temperature: Channel  2 , T =  17.51999  deg C

06:13:56  Temperature: Channel  3 , T =  16.3497  deg C

06:13:58  Temperature: Channel  4 , T =  19.43573  deg C

06:14:01  Temperature: Channel  5 , T =  19.82813  deg C

06:14:02  Magnet Current, Imag =  150.5816  A

06:14:04  Magnet Voltage, Vmag =  7.42213  V

06:14:51  Temperature: Channel  1 , T =  14.83862  deg C

06:14:53  Temperature: Channel  2 , T =  20.09021  deg C

06:14:56  Temperature: Channel  3 , T =  17.13293  deg C

06:14:58  Temperature: Channel  4 , T =  19.49582  deg C

06:15:01  Temperature: Channel  5 , T =  19.78558  deg C

06:15:02  Magnet Current, Imag =  150.5944  A

06:15:04  Magnet Voltage, Vmag =  7.48187  V

06:15:51  Temperature: Channel  1 , T =  15.02322  deg C

06:15:53  Temperature: Channel  2 , T =  22.62015  deg C

06:15:56  Temperature: Channel  3 , T =  18.28732  deg C

06:15:58  Temperature: Channel  4 , T =  19.55185  deg C

06:16:01  Temperature: Channel  5 , T =  19.70047  deg C

06:16:02  Magnet Current, Imag =  150.596  A

06:16:04  Magnet Voltage, Vmag =  7.53205  V

06:16:51  Temperature: Channel  1 , T =  15.18552  deg C

06:16:53  Temperature: Channel  2 , T =  25.06693  deg C

06:16:56  Temperature: Channel  3 , T =  19.67041  deg C

06:16:58  Temperature: Channel  4 , T =  19.56201  deg C

06:17:01  Temperature: Channel  5 , T =  19.85052  deg C

06:17:02  Magnet Current, Imag =  150.5968  A

06:17:04  Magnet Voltage, Vmag =  7.57185  V

06:17:51  Temperature: Channel  1 , T =  15.31726  deg C

06:17:54  Temperature: Channel  2 , T =  27.40906  deg C

06:17:56  Temperature: Channel  3 , T =  21.18506  deg C

06:17:58  Temperature: Channel  4 , T =  19.50177  deg C

06:18:01  Temperature: Channel  5 , T =  19.78952  deg C

06:18:02  Magnet Current, Imag =  150.596  A

06:18:04  Magnet Voltage, Vmag =  7.60367  V

06:18:51  Temperature: Channel  1 , T =  15.42468  deg C

06:18:54  Temperature: Channel  2 , T =  29.59042  deg C

06:18:56  Temperature: Channel  3 , T =  22.75021  deg C

06:18:58  Temperature: Channel  4 , T =  19.4079  deg C

06:19:01  Temperature: Channel  5 , T =  19.76953  deg C

06:19:02  Magnet Current, Imag =  150.5954  A

06:19:04  Magnet Voltage, Vmag =  7.62786  V

06:19:51  Temperature: Channel  1 , T =  15.526  deg C

06:19:54  Temperature: Channel  2 , T =  31.55179  deg C

06:19:56  Temperature: Channel  3 , T =  24.28223  deg C

06:19:58  Temperature: Channel  4 , T =  19.39713  deg C

06:20:01  Temperature: Channel  5 , T =  19.8732  deg C

06:20:02  Magnet Current, Imag =  150.6014  A

06:20:04  Magnet Voltage, Vmag =  7.64428  V

06:20:51  Temperature: Channel  1 , T =  15.63681  deg C

06:20:54  Temperature: Channel  2 , T =  33.18457  deg C

06:20:56  Temperature: Channel  3 , T =  25.70859  deg C

06:20:58  Temperature: Channel  4 , T =  19.40189  deg C

06:21:01  Temperature: Channel  5 , T =  19.81201  deg C

06:21:02  Magnet Current, Imag =  150.61  A

06:21:04  Magnet Voltage, Vmag =  7.657  V

06:21:51  Temperature: Channel  1 , T =  15.74435  deg C

06:21:54  Temperature: Channel  2 , T =  34.4357  deg C

06:21:56  Temperature: Channel  3 , T =  26.96308  deg C

06:21:58  Temperature: Channel  4 , T =  19.43362  deg C

06:22:01  Temperature: Channel  5 , T =  19.87979  deg C

06:22:02  Magnet Current, Imag =  150.5992  A

06:22:04  Magnet Voltage, Vmag =  7.66336  V

06:22:51  Temperature: Channel  1 , T =  15.86172  deg C

06:22:54  Temperature: Channel  2 , T =  35.32584  deg C

06:22:56  Temperature: Channel  3 , T =  28.02881  deg C

06:22:58  Temperature: Channel  4 , T =  19.45911  deg C

06:23:01  Temperature: Channel  5 , T =  19.80698  deg C

06:23:02  Magnet Current, Imag =  150.593  A

06:23:04  Magnet Voltage, Vmag =  7.67029  V

06:23:51  Temperature: Channel  1 , T =  16.00302  deg C

06:23:54  Temperature: Channel  2 , T =  35.92297  deg C

06:23:56  Temperature: Channel  3 , T =  28.87143  deg C

06:23:59  Temperature: Channel  4 , T =  19.48053  deg C

06:24:01  Temperature: Channel  5 , T =  19.84171  deg C

06:24:02  Magnet Current, Imag =  150.6044  A

06:24:04  Magnet Voltage, Vmag =  7.67473  V

06:24:50  Magnet Current, Imag =  150.6006  A

06:24:50  Magnet Current Ramping to  0  A...

06:26:10  Magnet Current, Imag =  .664948  A

06:26:12  Magnet Current, Imag =  .662264  A

06:26:12  Magnet Current Ramping to  250  A...

06:28:04  Magnet Current, Imag =  250.553  A

06:28:05  Magnet Current, Imag =  250.5538  A

06:28:05  Magnet Current Ramping to  10  A...

06:29:53  Magnet Current, Imag =  10.65688  A

06:29:55  Magnet Current, Imag =  10.65656  A

06:29:55  Magnet Current Ramping to  200  A...

06:31:28  Magnet Current, Imag =  200.5902  A

06:31:29  Magnet Current, Imag =  200.5864  A

06:31:29  Magnet Current Ramping to  10  A...

06:33:01  Magnet Current, Imag =  10.65882  A

06:33:03  Magnet Current, Imag =  10.6595  A

06:33:03  Magnet Current Ramping to  200  A...

06:34:36  Magnet Current, Imag =  200.5844  A

06:34:37  Magnet Current, Imag =  200.5936  A

06:34:37  Magnet Current Ramping to  10  A...

06:36:10  Magnet Current, Imag =  10.65466  A

06:36:12  Magnet Current, Imag =  10.65396  A

06:36:12  Magnet Current Ramping to  200  A...

06:37:45  Magnet Current, Imag =  200.5936  A

06:37:46  Magnet Current, Imag =  200.594  A

06:37:46  Magnet Current Ramping to  10  A...

06:39:18  Magnet Current, Imag =  10.6531  A

06:39:20  Magnet Current, Imag =  10.65514  A

06:39:20  Magnet Current Ramping to  25  A...

06:40:00  Magnet Current, Imag =  25.64264  A

06:40:02  Magnet Current, Imag =  25.64474  A

06:40:04  Magnet Current, Imag =  25.6438  A

06:40:06  Magnet Current, Imag =  25.64708  A

06:40:07  Magnet Current, Imag =  25.64716  A

06:40:07  Average Magnet Current:
Imag =  25.6457  +-  1.464418E-03  A

06:40:11  Coil Rotation Frequency, Fcoil =  4.049339  Hz

06:40:15  Coil Rotation Frequency, Fcoil =  4.050327  Hz

06:40:43  Coil Voltage Measurement #  1  Made, Stored in RAWFILE

06:40:43  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1204219  V, Vp main =  89.57342  deg

06:40:43  Coil Voltage Fit: 
Vfit(i) =  0.1204219 V * cos(3*2pi*i/ns +   89.57 deg)
        = -0.1204186 V * sin(3*2pi*i/ns) +  0.0008965 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015448 V

06:40:47  Coil Rotation Frequency, Fcoil =  4.04959  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049752 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00095881   110.61   0.00004198  -110.61
  2   0.00191066   -64.48   0.00008365    32.24
  3   0.12042190    89.57   0.00527224   -29.86
  4   0.00013634  -148.04   0.00000597    37.01
  5   0.00012188   -95.67   0.00000534    19.13
  6   0.00001935   170.72   0.00000085   -28.45
  7   0.00002888   -74.81   0.00000126    10.69
  8   0.00002890   129.68   0.00000127   -16.21
  9   0.00039863   -89.68   0.00001745     9.96
 10   0.00000501   123.91   0.00000022   -12.39
 11   0.00000532  -166.52   0.00000023    15.14
 12   0.00000691   140.38   0.00000030   -11.70
 13   0.00001250    85.63   0.00000055    -6.59
 14   0.00000746   131.12   0.00000033    -9.37
 15   0.00007943  -100.40   0.00000348     6.69
 16   0.00000963   149.35   0.00000042    -9.33

06:40:50  Coil Rotation Frequency, Fcoil =  4.04937  Hz

06:40:55  Coil Rotation Frequency, Fcoil =  4.047512  Hz

06:41:23  Coil Voltage Measurement #  2  Made, Stored in RAWFILE

06:41:23  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1204  V, Vp main =  89.5705  deg

06:41:23  Coil Voltage Fit: 
Vfit(i) =  0.1204000 V * cos(3*2pi*i/ns +   89.57 deg)
        = -0.1203966 V * sin(3*2pi*i/ns) +  0.0009025 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015428 V

06:41:27  Coil Rotation Frequency, Fcoil =  4.050663  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049181 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00095738   109.65   0.00004192  -109.65
  2   0.00190939   -64.44   0.00008361    32.22
  3   0.12040003    89.57   0.00527202   -29.86
  4   0.00012821  -155.88   0.00000561    38.97
  5   0.00012381   -98.90   0.00000542    19.78
  6   0.00001741   147.94   0.00000076   -24.66
  7   0.00002464   -86.28   0.00000108    12.33
  8   0.00002301   127.57   0.00000101   -15.95
  9   0.00039471   -90.46   0.00001728    10.05
 10   0.00000713  -139.45   0.00000031    13.95
 11   0.00000653  -126.93   0.00000029    11.54
 12   0.00000597  -141.19   0.00000026    11.77
 13   0.00000552    30.21   0.00000024    -2.32
 14   0.00000800   132.93   0.00000035    -9.50
 15   0.00008780   -92.77   0.00000384     6.18
 16   0.00000681  -136.86   0.00000030     8.55

06:41:30  Coil Rotation Frequency, Fcoil =  4.052374  Hz

06:41:34  Coil Rotation Frequency, Fcoil =  4.051594  Hz

06:42:03  Coil Voltage Measurement #  3  Made, Stored in RAWFILE

06:42:03  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1204195  V, Vp main =  89.57614  deg

06:42:03  Coil Voltage Fit: 
Vfit(i) =  0.1204195 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.1204162 V * sin(3*2pi*i/ns) +  0.0008908 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015441 V

06:42:07  Coil Rotation Frequency, Fcoil =  4.049478  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.051148 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00095184   110.37   0.00004166  -110.37
  2   0.00191345   -64.41   0.00008374    32.20
  3   0.12041946    89.58   0.00527031   -29.86
  4   0.00010702  -156.03   0.00000468    39.01
  5   0.00012727   -95.81   0.00000557    19.16
  6   0.00001273   100.13   0.00000056   -16.69
  7   0.00003091   -86.29   0.00000135    12.33
  8   0.00001444   114.44   0.00000063   -14.30
  9   0.00040242   -91.92   0.00001761    10.21
 10   0.00000851   -62.24   0.00000037     6.22
 11   0.00001016  -159.24   0.00000044    14.48
 12   0.00000319   -25.64   0.00000014     2.14
 13   0.00000399   160.87   0.00000017   -12.37
 14   0.00001399    72.18   0.00000061    -5.16
 15   0.00009178   -92.03   0.00000402     6.14
 16   0.00000647    -0.27   0.00000028     0.02

06:42:10  Coil Rotation Frequency, Fcoil =  4.049231  Hz

06:42:14  Coil Rotation Frequency, Fcoil =  4.051289  Hz

06:42:43  Coil Voltage Measurement #  4  Made, Stored in RAWFILE

06:42:43  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1204475  V, Vp main =  89.57338  deg

06:42:43  Coil Voltage Fit: 
Vfit(i) =  0.1204475 V * cos(3*2pi*i/ns +   89.57 deg)
        = -0.1204441 V * sin(3*2pi*i/ns) +  0.0008968 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015515 V

06:42:47  Coil Rotation Frequency, Fcoil =  4.053385  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.051301 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00095261   110.75   0.00004169  -110.75
  2   0.00192541   -64.37   0.00008427    32.19
  3   0.12044749    89.57   0.00527134   -29.86
  4   0.00013672  -145.76   0.00000598    36.44
  5   0.00012514   -97.91   0.00000548    19.58
  6   0.00001605   137.72   0.00000070   -22.95
  7   0.00002144  -109.84   0.00000094    15.69
  8   0.00003437   102.14   0.00000150   -12.77
  9   0.00039128   -91.79   0.00001712    10.20
 10   0.00000614   -14.31   0.00000027     1.43
 11   0.00001404   -99.76   0.00000061     9.07
 12   0.00000705    76.39   0.00000031    -6.37
 13   0.00001703   -55.39   0.00000075     4.26
 14   0.00001806   125.66   0.00000079    -8.98
 15   0.00008722   -91.57   0.00000382     6.10
 16   0.00000263  -135.52   0.00000012     8.47

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00004  0.00000   -110.35     0.42
  2   0.00008  0.00000     32.21     0.02
  3   0.00527  0.00000    -29.86     0.00
  4   0.00001  0.00000     37.86     1.15
  5   0.00001  0.00000     19.41     0.28
  6   0.00000  0.00000    -23.19     4.25
  7   0.00000  0.00000     12.76     1.82
  8   0.00000  0.00000    -14.81     1.39
  9   0.00002  0.00000     10.11     0.10
 10   0.00000  0.00000      2.30     9.59
 11   0.00000  0.00000     12.56     2.43
 12   0.00000  0.00000     -1.04     8.89
 13   0.00000  0.00000     -4.26     6.07
 14   0.00000  0.00000     -8.25     1.80
 15   0.00000  0.00000      6.28     0.24
 16   0.00000  0.00000      1.93     7.37

06:42:47  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  5.271479E-03  +-  7.496093E-07  Tm
Integrated Sextupole Strength, SL =  5.233811  +-  7.442529E-04  T/m

06:42:47            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00004  0.00000    0.7932   0.0026
  2   0.00008  0.00000    1.5900   0.0050
  3   0.00527  0.00000  100.0000   0.0201
  4   0.00001  0.00000    0.1055   0.0100
  5   0.00001  0.00000    0.1034   0.0016
  6   0.00000  0.00000    0.0136   0.0020
  7   0.00000  0.00000    0.0220   0.0031
  8   0.00000  0.00000    0.0209   0.0061
  9   0.00002  0.00000    0.3295   0.0035
 10   0.00000  0.00000    0.0056   0.0011
 11   0.00000  0.00000    0.0075   0.0028
 12   0.00000  0.00000    0.0048   0.0013
 13   0.00000  0.00000    0.0081   0.0044
 14   0.00000  0.00000    0.0099   0.0036
 15   0.00000  0.00000    0.0719   0.0037
 16   0.00000  0.00000    0.0053   0.0021

06:42:49  Magnet Current, Imag =  25.6384  A

06:42:49  Magnet Current Ramping to  50  A...

06:43:32  Magnet Current, Imag =  50.62422  A

06:43:34  Magnet Current, Imag =  50.62482  A

06:43:36  Magnet Current, Imag =  50.62268  A

06:43:38  Magnet Current, Imag =  50.62676  A

06:43:39  Magnet Current, Imag =  50.62022  A

06:43:39  Average Magnet Current:
Imag =  50.62362  +-  2.43528E-03  A

06:43:43  Coil Rotation Frequency, Fcoil =  4.051644  Hz

06:43:47  Coil Rotation Frequency, Fcoil =  4.053339  Hz

06:44:15  Coil Voltage Measurement #  5  Made, Stored in RAWFILE

06:44:15  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2348232  V, Vp main =  89.57349  deg

06:44:15  Coil Voltage Fit: 
Vfit(i) =  0.2348231 V * cos(3*2pi*i/ns +   89.57 deg)
        = -0.2348166 V * sin(3*2pi*i/ns) +  0.0017479 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0027488 V

06:44:19  Coil Rotation Frequency, Fcoil =  4.04639  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.050457 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00059162   125.27   0.00002590  -125.27
  2   0.00373623   -64.06   0.00016355    32.03
  3   0.23482318    89.57   0.01027909   -29.86
  4   0.00024219  -155.87   0.00001060    38.97
  5   0.00027608   -95.93   0.00001209    19.19
  6   0.00002825   155.76   0.00000124   -25.96
  7   0.00007728   -88.21   0.00000338    12.60
  8   0.00005125   160.39   0.00000224   -20.05
  9   0.00078858   -89.99   0.00003452    10.00
 10   0.00003680  -109.51   0.00000161    10.95
 11   0.00001057    52.50   0.00000046    -4.77
 12   0.00000968   -72.76   0.00000042     6.06
 13   0.00001302    33.95   0.00000057    -2.61
 14   0.00001266   126.34   0.00000055    -9.02
 15   0.00017537   -94.42   0.00000768     6.29
 16   0.00001136  -119.30   0.00000050     7.46

06:44:22  Coil Rotation Frequency, Fcoil =  4.048529  Hz

06:44:26  Coil Rotation Frequency, Fcoil =  4.050767  Hz

06:44:55  Coil Voltage Measurement #  6  Made, Stored in RAWFILE

06:44:55  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .234806  V, Vp main =  89.57106  deg

06:44:55  Coil Voltage Fit: 
Vfit(i) =  0.2348060 V * cos(3*2pi*i/ns +   89.57 deg)
        = -0.2347994 V * sin(3*2pi*i/ns) +  0.0017577 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0027419 V

06:44:59  Coil Rotation Frequency, Fcoil =  4.051845  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.05038 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00057306   125.16   0.00002509  -125.16
  2   0.00373314   -64.00   0.00016342    32.00
  3   0.23480600    89.57   0.01027854   -29.86
  4   0.00023258  -156.60   0.00001018    39.15
  5   0.00027120   -95.29   0.00001187    19.06
  6   0.00002857   138.41   0.00000125   -23.07
  7   0.00006924   -97.87   0.00000303    13.98
  8   0.00005489   106.56   0.00000240   -13.32
  9   0.00077591   -90.74   0.00003397    10.08
 10   0.00002524    37.33   0.00000110    -3.73
 11   0.00001138   178.29   0.00000050   -16.21
 12   0.00000611  -156.77   0.00000027    13.06
 13   0.00001869  -165.11   0.00000082    12.70
 14   0.00001678   154.18   0.00000073   -11.01
 15   0.00017242   -93.46   0.00000755     6.23
 16   0.00000888  -118.34   0.00000039     7.40

06:45:02  Coil Rotation Frequency, Fcoil =  4.050899  Hz

06:45:06  Coil Rotation Frequency, Fcoil =  4.049239  Hz

06:45:34  Coil Voltage Measurement #  7  Made, Stored in RAWFILE

06:45:34  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2348294  V, Vp main =  89.57204  deg

06:45:35  Coil Voltage Fit: 
Vfit(i) =  0.2348294 V * cos(3*2pi*i/ns +   89.57 deg)
        = -0.2348228 V * sin(3*2pi*i/ns) +  0.0017539 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0027449 V

06:45:38  Coil Rotation Frequency, Fcoil =  4.051308  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.050482 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00058254   123.83   0.00002550  -123.83
  2   0.00373531   -64.15   0.00016351    32.07
  3   0.23482937    89.57   0.01027930   -29.86
  4   0.00023853  -158.01   0.00001044    39.50
  5   0.00027538   -95.38   0.00001205    19.08
  6   0.00001450   124.40   0.00000063   -20.73
  7   0.00005400   -96.44   0.00000236    13.78
  8   0.00004704   108.11   0.00000206   -13.51
  9   0.00077735   -91.97   0.00003403    10.22
 10   0.00001773   146.98   0.00000078   -14.70
 11   0.00000513  -119.05   0.00000022    10.82
 12   0.00001574   145.59   0.00000069   -12.13
 13   0.00002048   -34.48   0.00000090     2.65
 14   0.00001964   137.82   0.00000086    -9.84
 15   0.00017820   -90.47   0.00000780     6.03
 16   0.00001363   162.51   0.00000060   -10.16

06:45:42  Coil Rotation Frequency, Fcoil =  4.051389  Hz

06:45:46  Coil Rotation Frequency, Fcoil =  4.049246  Hz

06:46:14  Coil Voltage Measurement #  8  Made, Stored in RAWFILE

06:46:14  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2348036  V, Vp main =  89.57349  deg

06:46:14  Coil Voltage Fit: 
Vfit(i) =  0.2348036 V * cos(3*2pi*i/ns +   89.57 deg)
        = -0.2347970 V * sin(3*2pi*i/ns) +  0.0017478 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0027448 V

06:46:18  Coil Rotation Frequency, Fcoil =  4.05025  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.050295 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00058458   125.79   0.00002559  -125.79
  2   0.00373602   -64.29   0.00016355    32.14
  3   0.23480362    89.57   0.01027865   -29.86
  4   0.00022140  -154.21   0.00000969    38.55
  5   0.00026098   -94.37   0.00001142    18.87
  6   0.00002140   139.25   0.00000094   -23.21
  7   0.00005761   -81.74   0.00000252    11.68
  8   0.00005034   146.88   0.00000220   -18.36
  9   0.00078406   -89.92   0.00003432     9.99
 10   0.00002171  -122.44   0.00000095    12.24
 11   0.00001019   -32.20   0.00000045     2.93
 12   0.00000861  -134.10   0.00000038    11.18
 13   0.00001036   143.61   0.00000045   -11.05
 14   0.00002215   127.05   0.00000097    -9.07
 15   0.00016147   -93.68   0.00000707     6.25
 16   0.00000407   -12.90   0.00000018     0.81

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00003  0.00000   -125.01     0.72
  2   0.00016  0.00000     32.06     0.05
  3   0.01028  0.00000    -29.86     0.00
  4   0.00001  0.00000     39.04     0.34
  5   0.00001  0.00000     19.05     0.11
  6   0.00000  0.00000    -23.24     1.85
  7   0.00000  0.00000     13.01     0.93
  8   0.00000  0.00000    -16.31     2.96
  9   0.00003  0.00000     10.07     0.09
 10   0.00000  0.00000      1.19    11.11
 11   0.00000  0.00000     -1.81     9.98
 12   0.00000  0.00000      4.54     9.96
 13   0.00000  0.00000      0.42     8.61
 14   0.00000  0.00000     -9.74     0.80
 15   0.00001  0.00000      6.20     0.10
 16   0.00000  0.00000      1.38     7.19

06:46:18  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  .0102789  +-  3.138498E-07  Tm
Integrated Sextupole Strength, SL =  10.20545  +-  3.116072E-04  T/m

06:46:18            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00003  0.00000    0.2483   0.0028
  2   0.00016  0.00000    1.5907   0.0005
  3   0.01028  0.00000  100.0000   0.0043
  4   0.00001  0.00000    0.0995   0.0034
  5   0.00001  0.00000    0.1154   0.0026
  6   0.00000  0.00000    0.0099   0.0025
  7   0.00000  0.00000    0.0275   0.0039
  8   0.00000  0.00000    0.0217   0.0012
  9   0.00003  0.00000    0.3328   0.0022
 10   0.00000  0.00000    0.0108   0.0030
 11   0.00000  0.00000    0.0040   0.0010
 12   0.00000  0.00000    0.0043   0.0015
 13   0.00000  0.00000    0.0067   0.0017
 14   0.00000  0.00000    0.0076   0.0015
 15   0.00001  0.00000    0.0732   0.0027
 16   0.00000  0.00000    0.0040   0.0015

06:46:21  Magnet Current, Imag =  50.62402  A

06:46:21  Magnet Current Ramping to  100  A...

06:47:10  Magnet Current, Imag =  100.6186  A

06:47:12  Magnet Current, Imag =  100.612  A

06:47:13  Magnet Current, Imag =  100.612  A

06:47:14  Magnet Current, Imag =  100.612  A

06:47:16  Magnet Current, Imag =  100.618  A

06:47:16  Average Magnet Current:
Imag =  100.6135  +-  2.599953E-03  A

06:47:19  Coil Rotation Frequency, Fcoil =  4.052953  Hz

06:47:23  Coil Rotation Frequency, Fcoil =  4.05249  Hz

06:47:51  Coil Voltage Measurement #  9  Made, Stored in RAWFILE

06:47:51  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4664013  V, Vp main =  89.58173  deg

06:47:51  Coil Voltage Fit: 
Vfit(i) =  0.4664012 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.4663888 V * sin(3*2pi*i/ns) +  0.0034045 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0054116 V

06:47:55  Coil Rotation Frequency, Fcoil =  4.050566  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.052003 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00052944  -126.11   0.00002317   126.11
  2   0.00742840   -64.04   0.00032505    32.02
  3   0.46640131    89.58   0.02040835   -29.86
  4   0.00049506  -157.89   0.00002166    39.47
  5   0.00058562   -96.07   0.00002562    19.21
  6   0.00008634   147.99   0.00000378   -24.66
  7   0.00011632   -90.69   0.00000509    12.96
  8   0.00008080    99.88   0.00000354   -12.48
  9   0.00153873   -90.88   0.00006733    10.10
 10   0.00002852   -75.27   0.00000125     7.53
 11   0.00001508    29.26   0.00000066    -2.66
 12   0.00004498    -2.38   0.00000197     0.20
 13   0.00003428    17.34   0.00000150    -1.33
 14   0.00003660   111.08   0.00000160    -7.93
 15   0.00034232   -93.62   0.00001498     6.24
 16   0.00001554    59.84   0.00000068    -3.74

06:47:58  Coil Rotation Frequency, Fcoil =  4.051528  Hz

06:48:03  Coil Rotation Frequency, Fcoil =  4.051091  Hz

06:48:31  Coil Voltage Measurement #  10  Made, Stored in RAWFILE

06:48:31  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4664865  V, Vp main =  89.58339  deg

06:48:31  Coil Voltage Fit: 
Vfit(i) =  0.4664865 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.4664741 V * sin(3*2pi*i/ns) +  0.0033917 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0054233 V

06:48:35  Coil Rotation Frequency, Fcoil =  4.050003  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.050874 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00052804  -126.97   0.00002311   126.97
  2   0.00744258   -63.99   0.00032576    31.99
  3   0.46648645    89.58   0.02041777   -29.86
  4   0.00046429  -156.21   0.00002032    39.05
  5   0.00059312   -96.78   0.00002596    19.36
  6   0.00010146   154.00   0.00000444   -25.67
  7   0.00013832   -91.17   0.00000605    13.02
  8   0.00007913   124.56   0.00000346   -15.57
  9   0.00155460   -90.73   0.00006804    10.08
 10   0.00002563   -89.46   0.00000112     8.95
 11   0.00001328   -85.63   0.00000058     7.78
 12   0.00002421     8.67   0.00000106    -0.72
 13   0.00002446   -50.78   0.00000107     3.91
 14   0.00003943   111.56   0.00000173    -7.97
 15   0.00034585   -94.01   0.00001514     6.27
 16   0.00001547   -46.64   0.00000068     2.91

06:48:38  Coil Rotation Frequency, Fcoil =  4.049876  Hz

06:48:42  Coil Rotation Frequency, Fcoil =  4.049976  Hz

06:49:11  Coil Voltage Measurement #  11  Made, Stored in RAWFILE

06:49:11  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4659211  V, Vp main =  89.58072  deg

06:49:11  Coil Voltage Fit: 
Vfit(i) =  0.4659211 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.4659086 V * sin(3*2pi*i/ns) +  0.0034093 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0054059 V

06:49:15  Coil Rotation Frequency, Fcoil =  4.049185  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049679 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00052674  -124.24   0.00002306   124.24
  2   0.00742072   -64.00   0.00032490    32.00
  3   0.46592113    89.58   0.02039904   -29.86
  4   0.00049387  -161.06   0.00002162    40.27
  5   0.00057211   -95.27   0.00002505    19.05
  6   0.00011460   151.00   0.00000502   -25.17
  7   0.00010702   -85.72   0.00000469    12.25
  8   0.00010111   109.22   0.00000443   -13.65
  9   0.00153810   -91.48   0.00006734    10.16
 10   0.00001197  -150.08   0.00000052    15.01
 11   0.00001448   155.15   0.00000063   -14.10
 12   0.00004849     8.70   0.00000212    -0.72
 13   0.00003104     9.86   0.00000136    -0.76
 14   0.00003574   107.61   0.00000156    -7.69
 15   0.00033360   -94.24   0.00001461     6.28
 16   0.00001157    91.53   0.00000051    -5.72

06:49:18  Coil Rotation Frequency, Fcoil =  4.050134  Hz

06:49:22  Coil Rotation Frequency, Fcoil =  4.050045  Hz

06:49:50  Coil Voltage Measurement #  12  Made, Stored in RAWFILE

06:49:51  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4662147  V, Vp main =  89.58066  deg

06:49:51  Coil Voltage Fit: 
Vfit(i) =  0.4662146 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.4662021 V * sin(3*2pi*i/ns) +  0.0034120 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0054180 V

06:49:54  Coil Rotation Frequency, Fcoil =  4.048148  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049442 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00051645  -125.88   0.00002261   125.88
  2   0.00744055   -64.14   0.00032578    32.07
  3   0.46621469    89.58   0.02041309   -29.86
  4   0.00047076  -156.30   0.00002061    39.07
  5   0.00059366   -94.62   0.00002599    18.92
  6   0.00009192   143.58   0.00000402   -23.93
  7   0.00012309   -97.51   0.00000539    13.93
  8   0.00011617   116.16   0.00000509   -14.52
  9   0.00153108   -91.84   0.00006704    10.20
 10   0.00002430   172.72   0.00000106   -17.27
 11   0.00002278   100.27   0.00000100    -9.12
 12   0.00003809    15.13   0.00000167    -1.26
 13   0.00002822    31.54   0.00000124    -2.43
 14   0.00003357   120.63   0.00000147    -8.62
 15   0.00034207   -93.24   0.00001498     6.22
 16   0.00001641   -72.25   0.00000072     4.52

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00002  0.00000    125.80     0.99
  2   0.00033  0.00000     32.02     0.03
  3   0.02041  0.00001    -29.86     0.00
  4   0.00002  0.00000     39.47     0.49
  5   0.00003  0.00000     19.14     0.16
  6   0.00000  0.00000    -24.86     0.64
  7   0.00001  0.00000     13.04     0.60
  8   0.00000  0.00000    -14.06     1.13
  9   0.00007  0.00000     10.14     0.05
 10   0.00000  0.00000      3.55    12.35
 11   0.00000  0.00000     -4.52     8.18
 12   0.00000  0.00000     -0.63     0.52
 13   0.00000  0.00000     -0.15     2.42
 14   0.00000  0.00000     -8.05     0.34
 15   0.00001  0.00000      6.25     0.03
 16   0.00000  0.00000     -0.51     4.32

06:49:55  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  2.040956E-02  +-  6.925514E-06  Tm
Integrated Sextupole Strength, SL =  20.26373  +-  6.876028E-03  T/m

06:49:55            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00002  0.00000    0.1126   0.0011
  2   0.00033  0.00000    1.5942   0.0020
  3   0.02041  0.00001  100.0000   0.0480
  4   0.00002  0.00000    0.1032   0.0029
  5   0.00003  0.00000    0.1257   0.0019
  6   0.00000  0.00000    0.0211   0.0023
  7   0.00001  0.00000    0.0260   0.0024
  8   0.00000  0.00000    0.0202   0.0033
  9   0.00007  0.00000    0.3304   0.0018
 10   0.00000  0.00000    0.0048   0.0014
 11   0.00000  0.00000    0.0035   0.0008
 12   0.00000  0.00000    0.0084   0.0020
 13   0.00000  0.00000    0.0063   0.0008
 14   0.00000  0.00000    0.0078   0.0004
 15   0.00001  0.00000    0.0731   0.0010
 16   0.00000  0.00000    0.0032   0.0004

06:49:57  Magnet Current, Imag =  100.615  A

06:49:57  Magnet Current Ramping to  125  A...

06:50:39  Magnet Current, Imag =  125.595  A

06:50:40  Magnet Current, Imag =  125.5944  A

06:50:42  Magnet Current, Imag =  125.5958  A

06:50:43  Magnet Current, Imag =  125.5972  A

06:50:44  Magnet Current, Imag =  125.5928  A

06:50:44  Average Magnet Current:
Imag =  125.5951  +-  1.633555E-03  A

06:50:48  Coil Rotation Frequency, Fcoil =  4.049035  Hz

06:50:52  Coil Rotation Frequency, Fcoil =  4.048745  Hz

06:51:20  Coil Voltage Measurement #  13  Made, Stored in RAWFILE

06:51:20  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .5813046  V, Vp main =  89.57761  deg

06:51:20  Coil Voltage Fit: 
Vfit(i) =  0.5813047 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.5812889 V * sin(3*2pi*i/ns) +  0.0042852 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0067835 V

06:51:24  Coil Rotation Frequency, Fcoil =  4.048776  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.048852 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00094044  -106.42   0.00004118   106.42
  2   0.00928860   -64.11   0.00040676    32.05
  3   0.58130461    89.58   0.02545598   -29.86
  4   0.00059168  -154.29   0.00002591    38.57
  5   0.00075249   -94.75   0.00003295    18.95
  6   0.00010161   154.79   0.00000445   -25.80
  7   0.00015704   -94.42   0.00000688    13.49
  8   0.00011649   110.03   0.00000510   -13.75
  9   0.00192650   -90.63   0.00008436    10.07
 10   0.00000693   -33.96   0.00000030     3.40
 11   0.00001597   -16.28   0.00000070     1.48
 12   0.00002710   165.88   0.00000119   -13.82
 13   0.00002869     7.52   0.00000126    -0.58
 14   0.00004830   132.37   0.00000212    -9.45
 15   0.00041590   -93.18   0.00001821     6.21
 16   0.00001317  -112.31   0.00000058     7.02

06:51:27  Coil Rotation Frequency, Fcoil =  4.049019  Hz

06:51:31  Coil Rotation Frequency, Fcoil =  4.048418  Hz

06:52:00  Coil Voltage Measurement #  14  Made, Stored in RAWFILE

06:52:00  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .5817945  V, Vp main =  89.57877  deg

06:52:00  Coil Voltage Fit: 
Vfit(i) =  0.5817944 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.5817787 V * sin(3*2pi*i/ns) +  0.0042770 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0067863 V

06:52:04  Coil Rotation Frequency, Fcoil =  4.050512  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049316 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00097673  -107.61   0.00004277   107.61
  2   0.00928998   -64.19   0.00040677    32.10
  3   0.58179450    89.58   0.02547451   -29.86
  4   0.00056150  -155.26   0.00002459    38.82
  5   0.00076273   -95.28   0.00003340    19.06
  6   0.00010394   147.65   0.00000455   -24.61
  7   0.00015647   -78.95   0.00000685    11.28
  8   0.00010655   122.47   0.00000467   -15.31
  9   0.00192607   -90.51   0.00008434    10.06
 10   0.00002969  -102.10   0.00000130    10.21
 11   0.00002224    27.08   0.00000097    -2.46
 12   0.00001399   175.55   0.00000061   -14.63
 13   0.00003029    52.79   0.00000133    -4.06
 14   0.00004912   140.75   0.00000215   -10.05
 15   0.00042739   -93.14   0.00001871     6.21
 16   0.00001729   -12.54   0.00000076     0.78

06:52:07  Coil Rotation Frequency, Fcoil =  4.049895  Hz

06:52:11  Coil Rotation Frequency, Fcoil =  4.047546  Hz

06:52:40  Coil Voltage Measurement #  15  Made, Stored in RAWFILE

06:52:40  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .5812599  V, Vp main =  89.57762  deg

06:52:40  Coil Voltage Fit: 
Vfit(i) =  0.5812597 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.5812439 V * sin(3*2pi*i/ns) +  0.0042847 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0067786 V

06:52:44  Coil Rotation Frequency, Fcoil =  4.051199  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049547 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00095214  -107.42   0.00004169   107.42
  2   0.00928149   -64.16   0.00040638    32.08
  3   0.58125991    89.58   0.02544966   -29.86
  4   0.00060021  -156.35   0.00002628    39.09
  5   0.00074400   -95.06   0.00003258    19.01
  6   0.00010558   162.82   0.00000462   -27.14
  7   0.00016928   -95.91   0.00000741    13.70
  8   0.00009998   127.36   0.00000438   -15.92
  9   0.00191002   -91.76   0.00008363    10.20
 10   0.00002083   -25.39   0.00000091     2.54
 11   0.00001543  -170.95   0.00000068    15.54
 12   0.00001887   144.82   0.00000083   -12.07
 13   0.00001351   -11.46   0.00000059     0.88
 14   0.00005548   135.71   0.00000243    -9.69
 15   0.00045839   -95.65   0.00002007     6.38
 16   0.00002629   -28.40   0.00000115     1.77

06:52:47  Coil Rotation Frequency, Fcoil =  4.05317  Hz

06:52:51  Coil Rotation Frequency, Fcoil =  4.051787  Hz

06:53:19  Coil Voltage Measurement #  16  Made, Stored in RAWFILE

06:53:19  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .5817345  V, Vp main =  89.58073  deg

06:53:20  Coil Voltage Fit: 
Vfit(i) =  0.5817344 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.5817189 V * sin(3*2pi*i/ns) +  0.0042566 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0067797 V

06:53:23  Coil Rotation Frequency, Fcoil =  4.048726  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.051228 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00098199  -109.06   0.00004298   109.06
  2   0.00928169   -64.14   0.00040622    32.07
  3   0.58173448    89.58   0.02545987   -29.86
  4   0.00058989  -155.25   0.00002582    38.81
  5   0.00077005   -96.13   0.00003370    19.23
  6   0.00010023   151.75   0.00000439   -25.29
  7   0.00015753   -93.36   0.00000689    13.34
  8   0.00012791   122.38   0.00000560   -15.30
  9   0.00190165   -90.95   0.00008323    10.11
 10   0.00004085  -147.52   0.00000179    14.75
 11   0.00002083    30.76   0.00000091    -2.80
 12   0.00004924   167.42   0.00000216   -13.95
 13   0.00003877    39.72   0.00000170    -3.06
 14   0.00007050   128.99   0.00000309    -9.21
 15   0.00042803   -93.78   0.00001873     6.25
 16   0.00003789   -54.74   0.00000166     3.42

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00004  0.00000    107.63     0.94
  2   0.00041  0.00000     32.08     0.02
  3   0.02546  0.00001    -29.86     0.00
  4   0.00003  0.00000     38.82     0.18
  5   0.00003  0.00000     19.06     0.10
  6   0.00000  0.00000    -25.71     0.93
  7   0.00001  0.00000     12.95     0.97
  8   0.00000  0.00000    -15.07     0.80
  9   0.00008  0.00000     10.11     0.05
 10   0.00000  0.00000      7.72     5.03
 11   0.00000  0.00000      2.94     7.47
 12   0.00000  0.00000    -13.62     0.95
 13   0.00000  0.00000     -1.70     1.96
 14   0.00000  0.00000     -9.60     0.31
 15   0.00002  0.00000      6.26     0.07
 16   0.00000  0.00000      3.25     2.37

06:53:24  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  .02546  +-  9.134441E-06  Tm
Integrated Sextupole Strength, SL =  25.27808  +-  9.069171E-03  T/m

06:53:25  Magnet Current, Imag =  125.5966  A

06:53:25  Magnet Current Ramping to  150  A...

06:54:07  Magnet Current, Imag =  150.59  A

06:54:08  Magnet Current, Imag =  150.5922  A

06:54:10  Magnet Current, Imag =  150.591  A

06:54:11  Magnet Current, Imag =  150.5944  A

06:54:12  Magnet Current, Imag =  150.5942  A

06:54:13  Average Magnet Current:
Imag =  150.593  +-  1.419826E-03  A

06:54:16  Coil Rotation Frequency, Fcoil =  4.05069  Hz

06:54:20  Coil Rotation Frequency, Fcoil =  4.049235  Hz

06:54:48  Coil Voltage Measurement #  17  Made, Stored in RAWFILE

06:54:48  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .6964974  V, Vp main =  89.57898  deg

06:54:48  Coil Voltage Fit: 
Vfit(i) =  0.6964973 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.6964785 V * sin(3*2pi*i/ns) +  0.0051177 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0081302 V

06:54:52  Coil Rotation Frequency, Fcoil =  4.047935  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049287 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00146799  -101.38   0.00006428   101.38
  2   0.01109355   -63.80   0.00048575    31.90
  3   0.69649738    89.58   0.03049713   -29.86
  4   0.00068088  -157.72   0.00002981    39.43
  5   0.00088528   -96.02   0.00003876    19.20
  6   0.00008431   126.55   0.00000369   -21.09
  7   0.00018489   -96.59   0.00000810    13.80
  8   0.00013379   112.71   0.00000586   -14.09
  9   0.00232457   -91.05   0.00010178    10.12
 10   0.00002374   -28.53   0.00000104     2.85
 11   0.00001713   167.77   0.00000075   -15.25
 12   0.00005578  -173.24   0.00000244    14.44
 13   0.00004219   -26.57   0.00000185     2.04
 14   0.00004462   129.41   0.00000195    -9.24
 15   0.00049611   -92.33   0.00002172     6.16
 16   0.00004251     1.69   0.00000186    -0.11

06:54:56  Coil Rotation Frequency, Fcoil =  4.049748  Hz

06:55:00  Coil Rotation Frequency, Fcoil =  4.050099  Hz

06:55:28  Coil Voltage Measurement #  18  Made, Stored in RAWFILE

06:55:28  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .6967384  V, Vp main =  89.57859  deg

06:55:28  Coil Voltage Fit: 
Vfit(i) =  0.6967383 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.6967195 V * sin(3*2pi*i/ns) +  0.0051242 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0081352 V

06:55:32  Coil Rotation Frequency, Fcoil =  4.047692  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.04918 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00144559  -101.04   0.00006330   101.04
  2   0.01110466   -64.26   0.00048625    32.13
  3   0.69673836    89.58   0.03050848   -29.86
  4   0.00072439  -156.52   0.00003172    39.13
  5   0.00091781   -95.82   0.00004019    19.16
  6   0.00007976   138.22   0.00000349   -23.04
  7   0.00017173   -92.15   0.00000752    13.16
  8   0.00010612   119.45   0.00000465   -14.93
  9   0.00230063   -90.96   0.00010074    10.11
 10   0.00002413   -61.97   0.00000106     6.20
 11   0.00001944    58.51   0.00000085    -5.32
 12   0.00005349   164.02   0.00000234   -13.67
 13   0.00003512    28.42   0.00000154    -2.19
 14   0.00003788   140.10   0.00000166   -10.01
 15   0.00047983   -94.76   0.00002101     6.32
 16   0.00001759    33.42   0.00000077    -2.09

06:55:35  Coil Rotation Frequency, Fcoil =  4.049582  Hz

06:55:39  Coil Rotation Frequency, Fcoil =  4.048263  Hz

06:56:08  Coil Voltage Measurement #  19  Made, Stored in RAWFILE

06:56:08  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .6964437  V, Vp main =  89.58  deg

06:56:08  Coil Voltage Fit: 
Vfit(i) =  0.6964436 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.6964248 V * sin(3*2pi*i/ns) +  0.0051048 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0081299 V

06:56:12  Coil Rotation Frequency, Fcoil =  4.049266  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049037 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00146805  -100.91   0.00006428   100.91
  2   0.01109600   -64.03   0.00048588    32.02
  3   0.69644368    89.58   0.03049666   -29.86
  4   0.00071265  -157.40   0.00003121    39.35
  5   0.00091326   -95.94   0.00003999    19.19
  6   0.00006060   138.89   0.00000265   -23.15
  7   0.00019728   -90.54   0.00000864    12.93
  8   0.00015139   111.00   0.00000663   -13.87
  9   0.00229320   -90.55   0.00010042    10.06
 10   0.00002859  -133.40   0.00000125    13.34
 11   0.00003168    90.23   0.00000139    -8.20
 12   0.00005376  -131.97   0.00000235    11.00
 13   0.00003075    37.43   0.00000135    -2.88
 14   0.00001138   115.00   0.00000050    -8.21
 15   0.00048139   -93.28   0.00002108     6.22
 16   0.00004115   -23.27   0.00000180     1.45

06:56:15  Coil Rotation Frequency, Fcoil =  4.051814  Hz

06:56:19  Coil Rotation Frequency, Fcoil =  4.051428  Hz

06:56:48  Coil Voltage Measurement #  20  Made, Stored in RAWFILE

06:56:48  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .6967305  V, Vp main =  89.58006  deg

06:56:48  Coil Voltage Fit: 
Vfit(i) =  0.6967307 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.6967120 V * sin(3*2pi*i/ns) +  0.0051063 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0081394 V

06:56:52  Coil Rotation Frequency, Fcoil =  4.047496  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.050246 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00148814  -101.78   0.00006514   101.78
  2   0.01110746   -64.03   0.00048624    32.02
  3   0.69673049    89.58   0.03050011   -29.86
  4   0.00068751  -157.42   0.00003010    39.35
  5   0.00088580   -95.96   0.00003878    19.19
  6   0.00007126   148.24   0.00000312   -24.71
  7   0.00019217   -91.59   0.00000841    13.08
  8   0.00010697   122.20   0.00000468   -15.27
  9   0.00231560   -90.76   0.00010137    10.08
 10   0.00004552   -49.80   0.00000199     4.98
 11   0.00000995   132.72   0.00000044   -12.07
 12   0.00004269  -152.37   0.00000187    12.70
 13   0.00001919    15.47   0.00000084    -1.19
 14   0.00001683  -177.54   0.00000074    12.68
 15   0.00046693   -91.99   0.00002044     6.13
 16   0.00000533   -69.47   0.00000023     4.34

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00006  0.00000    101.28     0.34
  2   0.00049  0.00000     32.02     0.08
  3   0.03050  0.00000    -29.86     0.00
  4   0.00003  0.00000     39.32     0.11
  5   0.00004  0.00000     19.19     0.01
  6   0.00000  0.00000    -23.00     1.28
  7   0.00001  0.00000     13.25     0.33
  8   0.00001  0.00000    -14.54     0.58
  9   0.00010  0.00000     10.09     0.02
 10   0.00000  0.00000      6.84     3.94
 11   0.00000  0.00000    -10.21     3.77
 12   0.00000  0.00000      6.12    11.49
 13   0.00000  0.00000     -1.05     1.89
 14   0.00000  0.00000     -3.70     9.48
 15   0.00002  0.00000      6.21     0.07
 16   0.00000  0.00000      0.90     2.35

06:56:52  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  3.050059E-02  +-  4.742858E-06  Tm
Integrated Sextupole Strength, SL =  30.28265  +-  4.708968E-03  T/m

06:56:52            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00006  0.00000    0.2107   0.0021
  2   0.00049  0.00000    1.5935   0.0008
  3   0.03050  0.00000  100.0000   0.0220
  4   0.00003  0.00000    0.1007   0.0026
  5   0.00004  0.00000    0.1293   0.0022
  6   0.00000  0.00000    0.0106   0.0013
  7   0.00001  0.00000    0.0268   0.0014
  8   0.00001  0.00000    0.0179   0.0027
  9   0.00010  0.00000    0.3314   0.0017
 10   0.00000  0.00000    0.0044   0.0013
 11   0.00000  0.00000    0.0028   0.0011
 12   0.00000  0.00000    0.0074   0.0007
 13   0.00000  0.00000    0.0046   0.0012
 14   0.00000  0.00000    0.0040   0.0020
 15   0.00002  0.00000    0.0691   0.0015
 16   0.00000  0.00000    0.0038   0.0023

06:56:54  Magnet Current, Imag =  150.5956  A

06:56:54  Magnet Current Ramping to  175  A...

06:57:36  Magnet Current, Imag =  175.58  A

06:57:37  Magnet Current, Imag =  175.573  A

06:57:38  Magnet Current, Imag =  175.5764  A

06:57:40  Magnet Current, Imag =  175.573  A

06:57:41  Magnet Current, Imag =  175.5732  A

06:57:41  Average Magnet Current:
Imag =  175.5739  +-  1.440461E-03  A

06:57:44  Coil Rotation Frequency, Fcoil =  4.052838  Hz

06:57:48  Coil Rotation Frequency, Fcoil =  4.05378  Hz

06:58:17  Coil Voltage Measurement #  21  Made, Stored in RAWFILE

06:58:17  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .8114127  V, Vp main =  89.58112  deg

06:58:17  Coil Voltage Fit: 
Vfit(i) =  0.8114126 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.8113909 V * sin(3*2pi*i/ns) +  0.0059318 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0094604 V

06:58:21  Coil Rotation Frequency, Fcoil =  4.050995  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.052537 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00191737   -98.19   0.00008389    98.19
  2   0.01287765   -64.13   0.00056341    32.07
  3   0.81141269    89.58   0.03550036   -29.86
  4   0.00085218  -159.38   0.00003728    39.85
  5   0.00104016   -96.47   0.00004551    19.29
  6   0.00009635   142.40   0.00000422   -23.73
  7   0.00022504   -85.48   0.00000985    12.21
  8   0.00018515   119.79   0.00000810   -14.97
  9   0.00268313   -91.13   0.00011739    10.13
 10   0.00002285  -109.12   0.00000100    10.91
 11   0.00003643  -156.89   0.00000159    14.26
 12   0.00002372   -86.29   0.00000104     7.19
 13   0.00004021   -86.67   0.00000176     6.67
 14   0.00003450   147.75   0.00000151   -10.55
 15   0.00059504  -100.03   0.00002603     6.67
 16   0.00003274   -13.24   0.00000143     0.83

06:58:24  Coil Rotation Frequency, Fcoil =  4.050582  Hz

06:58:28  Coil Rotation Frequency, Fcoil =  4.05118  Hz

06:58:56  Coil Voltage Measurement #  22  Made, Stored in RAWFILE

06:58:57  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .8115265  V, Vp main =  89.58001  deg

06:58:57  Coil Voltage Fit: 
Vfit(i) =  0.8115267 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.8115048 V * sin(3*2pi*i/ns) +  0.0059483 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0094912 V

06:59:00  Coil Rotation Frequency, Fcoil =  4.050196  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.050653 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00193970   -98.04   0.00008490    98.04
  2   0.01292647   -64.10   0.00056581    32.05
  3   0.81152654    89.58   0.03552186   -29.86
  4   0.00082560  -157.35   0.00003614    39.34
  5   0.00103969   -96.03   0.00004551    19.21
  6   0.00009701   128.46   0.00000425   -21.41
  7   0.00020287   -95.03   0.00000888    13.58
  8   0.00015556    83.25   0.00000681   -10.41
  9   0.00266796   -91.92   0.00011678    10.21
 10   0.00006717    13.13   0.00000294    -1.31
 11   0.00002409   118.56   0.00000105   -10.78
 12   0.00002528   159.76   0.00000111   -13.31
 13   0.00004584    33.12   0.00000201    -2.55
 14   0.00007283   125.69   0.00000319    -8.98
 15   0.00056735   -88.00   0.00002483     5.87
 16   0.00000859    19.11   0.00000038    -1.19

06:59:04  Coil Rotation Frequency, Fcoil =  4.049864  Hz

06:59:08  Coil Rotation Frequency, Fcoil =  4.047912  Hz

06:59:36  Coil Voltage Measurement #  23  Made, Stored in RAWFILE

06:59:36  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .8106922  V, Vp main =  89.57979  deg

06:59:36  Coil Voltage Fit: 
Vfit(i) =  0.8106923 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.8106704 V * sin(3*2pi*i/ns) +  0.0059453 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0094699 V

06:59:40  Coil Rotation Frequency, Fcoil =  4.049204  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.048993 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00194688   -99.87   0.00008525    99.87
  2   0.01288612   -64.17   0.00056428    32.09
  3   0.81069219    89.58   0.03549988   -29.86
  4   0.00083097  -158.28   0.00003639    39.57
  5   0.00105475   -95.11   0.00004619    19.02
  6   0.00009810   143.48   0.00000430   -23.91
  7   0.00023167   -94.80   0.00001014    13.54
  8   0.00012784   104.71   0.00000560   -13.09
  9   0.00269360   -90.76   0.00011795    10.08
 10   0.00004356   -54.42   0.00000191     5.44
 11   0.00003825   178.83   0.00000167   -16.26
 12   0.00002278  -158.34   0.00000100    13.20
 13   0.00001482  -153.71   0.00000065    11.82
 14   0.00005776   119.41   0.00000253    -8.53
 15   0.00058222   -93.67   0.00002550     6.24
 16   0.00004183    13.82   0.00000183    -0.86

06:59:43  Coil Rotation Frequency, Fcoil =  4.049382  Hz

06:59:48  Coil Rotation Frequency, Fcoil =  4.050211  Hz

07:00:16  Coil Voltage Measurement #  24  Made, Stored in RAWFILE

07:00:16  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .8110279  V, Vp main =  89.57845  deg

07:00:16  Coil Voltage Fit: 
Vfit(i) =  0.8110278 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.8110058 V * sin(3*2pi*i/ns) +  0.0059668 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0094754 V

07:00:20  Coil Rotation Frequency, Fcoil =  4.048707  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049433 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00193642   -98.21   0.00008479    98.21
  2   0.01289138   -64.15   0.00056445    32.07
  3   0.81102788    89.58   0.03551072   -29.86
  4   0.00080181  -154.40   0.00003511    38.60
  5   0.00108222   -96.76   0.00004738    19.35
  6   0.00004965   145.53   0.00000217   -24.25
  7   0.00023707   -89.98   0.00001038    12.85
  8   0.00016221   122.03   0.00000710   -15.25
  9   0.00271494   -90.87   0.00011887    10.10
 10   0.00003027    -4.32   0.00000133     0.43
 11   0.00003359  -176.78   0.00000147    16.07
 12   0.00004738   140.70   0.00000207   -11.72
 13   0.00002684   149.93   0.00000118   -11.53
 14   0.00007324   122.58   0.00000321    -8.76
 15   0.00057172   -95.51   0.00002503     6.37
 16   0.00002900    82.58   0.00000127    -5.16

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00008  0.00000     98.58     0.75
  2   0.00056  0.00000     32.07     0.01
  3   0.03551  0.00001    -29.86     0.00
  4   0.00004  0.00000     39.34     0.46
  5   0.00005  0.00000     19.22     0.12
  6   0.00000  0.00000    -23.33     1.12
  7   0.00001  0.00000     13.05     0.56
  8   0.00001  0.00000    -13.43     1.93
  9   0.00012  0.00000     10.13     0.05
 10   0.00000  0.00000      3.87     4.76
 11   0.00000  0.00000      0.82    14.49
 12   0.00000  0.00000     -1.16    11.57
 13   0.00000  0.00000      1.10     8.93
 14   0.00000  0.00000     -9.20     0.80
 15   0.00003  0.00000      6.29     0.29
 16   0.00000  0.00000     -1.60     2.20

07:00:20  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  .0355082  +-  8.995346E-06  Tm
Integrated Sextupole Strength, SL =  35.25448  +-  8.93107E-03  T/m

07:00:21  Magnet Current, Imag =  175.5814  A

07:00:21  Magnet Current Ramping to  200  A...

07:01:04  Magnet Current, Imag =  200.5864  A

07:01:05  Magnet Current, Imag =  200.5832  A

07:01:06  Magnet Current, Imag =  200.5824  A

07:01:08  Magnet Current, Imag =  200.5906  A

07:01:09  Magnet Current, Imag =  200.5918  A

07:01:09  Average Magnet Current:
Imag =  200.587  +-  4.234115E-03  A

07:01:12  Coil Rotation Frequency, Fcoil =  4.049629  Hz

07:01:16  Coil Rotation Frequency, Fcoil =  4.050103  Hz

07:01:45  Coil Voltage Measurement #  25  Made, Stored in RAWFILE

07:01:45  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .9242641  V, Vp main =  89.57808  deg

07:01:45  Coil Voltage Fit: 
Vfit(i) =  0.9242640 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.9242389 V * sin(3*2pi*i/ns) +  0.0068057 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0108317 V

07:01:49  Coil Rotation Frequency, Fcoil =  4.050779  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.05017 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00229545   -97.22   0.00010049    97.22
  2   0.01471744   -63.91   0.00064428    31.95
  3   0.92426407    89.58   0.04046138   -29.86
  4   0.00100620  -158.67   0.00004405    39.67
  5   0.00122048   -95.04   0.00005343    19.01
  6   0.00013324   156.45   0.00000583   -26.08
  7   0.00026849   -96.40   0.00001175    13.77
  8   0.00019222   114.67   0.00000841   -14.33
  9   0.00310783   -91.15   0.00013605    10.13
 10   0.00002126    -7.67   0.00000093     0.77
 11   0.00004637    -1.85   0.00000203     0.17
 12   0.00003477     9.14   0.00000152    -0.76
 13   0.00007170    -7.87   0.00000314     0.61
 14   0.00003783    76.96   0.00000166    -5.50
 15   0.00066580   -90.88   0.00002915     6.06
 16   0.00003689    27.23   0.00000161    -1.70

07:01:52  Coil Rotation Frequency, Fcoil =  4.049957  Hz

07:01:56  Coil Rotation Frequency, Fcoil =  4.05123  Hz

07:02:25  Coil Voltage Measurement #  26  Made, Stored in RAWFILE

07:02:25  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .9254183  V, Vp main =  89.57999  deg

07:02:25  Coil Voltage Fit: 
Vfit(i) =  0.9254182 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.9253933 V * sin(3*2pi*i/ns) +  0.0067833 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0108162 V

07:02:29  Coil Rotation Frequency, Fcoil =  4.050709  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.050632 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00229622   -96.75   0.00010051    96.75
  2   0.01471485   -64.06   0.00064410    32.03
  3   0.92541832    89.58   0.04050730   -29.86
  4   0.00092847  -157.13   0.00004064    39.28
  5   0.00120476   -95.65   0.00005273    19.13
  6   0.00007494   158.16   0.00000328   -26.36
  7   0.00019884  -103.26   0.00000870    14.75
  8   0.00017437   132.20   0.00000763   -16.52
  9   0.00305090   -91.49   0.00013354    10.17
 10   0.00005596   174.07   0.00000245   -17.41
 11   0.00004476   -46.30   0.00000196     4.21
 12   0.00004650   174.64   0.00000204   -14.55
 13   0.00003919     7.13   0.00000172    -0.55
 14   0.00005631   170.88   0.00000246   -12.21
 15   0.00066132   -90.60   0.00002895     6.04
 16   0.00000356    15.33   0.00000016    -0.96

07:02:32  Coil Rotation Frequency, Fcoil =  4.049606  Hz

07:02:36  Coil Rotation Frequency, Fcoil =  4.048426  Hz

07:03:04  Coil Voltage Measurement #  27  Made, Stored in RAWFILE

07:03:04  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .9254038  V, Vp main =  89.57965  deg

07:03:04  Coil Voltage Fit: 
Vfit(i) =  0.9254037 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.9253787 V * sin(3*2pi*i/ns) +  0.0067888 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0108611 V

07:03:08  Coil Rotation Frequency, Fcoil =  4.053646  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.050559 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00231577   -96.54   0.00010137    96.54
  2   0.01476995   -63.97   0.00064652    31.99
  3   0.92540383    89.58   0.04050739   -29.86
  4   0.00097609  -156.86   0.00004273    39.22
  5   0.00114102   -97.02   0.00004995    19.40
  6   0.00008060   144.56   0.00000353   -24.09
  7   0.00022824   -89.72   0.00000999    12.82
  8   0.00013507   122.98   0.00000591   -15.37
  9   0.00309559   -89.90   0.00013550     9.99
 10   0.00004576  -157.42   0.00000200    15.74
 11   0.00008872   158.84   0.00000388   -14.44
 12   0.00004058    41.92   0.00000178    -3.49
 13   0.00005911  -172.85   0.00000259    13.30
 14   0.00003996   121.61   0.00000175    -8.69
 15   0.00066848   -93.65   0.00002926     6.24
 16   0.00004694  -107.83   0.00000205     6.74

07:03:12  Coil Rotation Frequency, Fcoil =  4.053201  Hz

07:03:16  Coil Rotation Frequency, Fcoil =  4.051373  Hz

07:03:44  Coil Voltage Measurement #  28  Made, Stored in RAWFILE

07:03:44  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .925608  V, Vp main =  89.58218  deg

07:03:44  Coil Voltage Fit: 
Vfit(i) =  0.9256077 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.9255831 V * sin(3*2pi*i/ns) +  0.0067494 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0108504 V

07:03:48  Coil Rotation Frequency, Fcoil =  4.049258  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.051278 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00236934   -97.52   0.00010369    97.52
  2   0.01474309   -64.14   0.00064523    32.07
  3   0.92560798    89.58   0.04050914   -29.86
  4   0.00099209  -160.85   0.00004342    40.21
  5   0.00117717   -95.64   0.00005152    19.13
  6   0.00012686   121.75   0.00000555   -20.29
  7   0.00026954  -100.67   0.00001180    14.38
  8   0.00019694   108.17   0.00000862   -13.52
  9   0.00308160   -90.88   0.00013487    10.10
 10   0.00006566   -71.75   0.00000287     7.18
 11   0.00002636  -174.18   0.00000115    15.83
 12   0.00002018  -136.51   0.00000088    11.38
 13   0.00002110  -112.14   0.00000092     8.63
 14   0.00007841   150.92   0.00000343   -10.78
 15   0.00068556   -95.30   0.00003000     6.35
 16   0.00002285  -106.69   0.00000100     6.67

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00010  0.00000     97.01     0.39
  2   0.00065  0.00000     32.01     0.04
  3   0.04050  0.00002    -29.86     0.00
  4   0.00004  0.00000     39.60     0.40
  5   0.00005  0.00000     19.17     0.14
  6   0.00000  0.00000    -24.21     2.42
  7   0.00001  0.00000     13.93     0.73
  8   0.00001  0.00000    -14.94     1.13
  9   0.00013  0.00000     10.10     0.07
 10   0.00000  0.00000      1.57    12.18
 11   0.00000  0.00000      1.44    10.82
 12   0.00000  0.00000     -1.86     9.22
 13   0.00000  0.00000      5.49     5.72
 14   0.00000  0.00000     -9.29     2.52
 15   0.00003  0.00000      6.17     0.13
 16   0.00000  0.00000      2.69     4.03

07:03:48  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  .0404963  +-  2.017441E-05  Tm
Integrated Sextupole Strength, SL =  40.20694  +-  2.003026E-02  T/m

07:03:48            FIELD HARMONIC STRENGTH RATIOS
Nmain =  3 

 N     BLn     sigBLn   BLn/BLN  sBLn/BLN
       (Tm)     (Tm)      (%)      (%)   
---  --------+--------  --------+--------
  1   0.00010  0.00000    0.2507   0.0032
  2   0.00065  0.00000    1.5928   0.0025
  3   0.04050  0.00002  100.0000   0.0705
  4   0.00004  0.00000    0.1055   0.0032
  5   0.00005  0.00000    0.1282   0.0033
  6   0.00000  0.00000    0.0112   0.0028
  7   0.00001  0.00000    0.0261   0.0032
  8   0.00001  0.00000    0.0189   0.0026
  9   0.00013  0.00000    0.3333   0.0023
 10   0.00000  0.00000    0.0051   0.0018
 11   0.00000  0.00000    0.0056   0.0025
 12   0.00000  0.00000    0.0038   0.0011
 13   0.00000  0.00000    0.0052   0.0021
 14   0.00000  0.00000    0.0057   0.0018
 15   0.00003  0.00000    0.0725   0.0010
 16   0.00000  0.00000    0.0030   0.0018

07:03:50  Magnet Current, Imag =  200.594  A

07:03:50  Magnet Current Ramping to  150  A...

07:04:39  Magnet Current, Imag =  150.5936  A

07:04:40  Magnet Current, Imag =  150.5946  A

07:04:42  Magnet Current, Imag =  150.5936  A

07:04:43  Magnet Current, Imag =  150.5982  A

07:04:44  Magnet Current, Imag =  150.6012  A

07:04:44  Average Magnet Current:
Imag =  150.5969  +-  3.00992E-03  A

07:04:48  Coil Rotation Frequency, Fcoil =  4.05059  Hz

07:04:52  Coil Rotation Frequency, Fcoil =  4.049636  Hz

07:05:20  Coil Voltage Measurement #  29  Made, Stored in RAWFILE

07:05:20  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .7024164  V, Vp main =  89.5802  deg

07:05:20  Coil Voltage Fit: 
Vfit(i) =  0.7024164 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.7023975 V * sin(3*2pi*i/ns) +  0.0051462 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0081962 V

07:05:24  Coil Rotation Frequency, Fcoil =  4.049868  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.050031 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00144850  -100.05   0.00006341   100.05
  2   0.01119635   -64.30   0.00049016    32.15
  3   0.70241642    89.58   0.03075065   -29.86
  4   0.00070592  -156.80   0.00003090    39.20
  5   0.00087918   -97.34   0.00003849    19.47
  6   0.00005538   148.40   0.00000242   -24.73
  7   0.00016771   -94.78   0.00000734    13.54
  8   0.00011750   117.67   0.00000514   -14.71
  9   0.00231216   -91.17   0.00010122    10.13
 10   0.00000389   -61.31   0.00000017     6.13
 11   0.00000649  -150.24   0.00000028    13.66
 12   0.00002707   152.56   0.00000118   -12.71
 13   0.00002934    61.89   0.00000128    -4.76
 14   0.00004483   103.91   0.00000196    -7.42
 15   0.00046503   -92.90   0.00002036     6.19
 16   0.00002705   -56.29   0.00000118     3.52

07:05:27  Coil Rotation Frequency, Fcoil =  4.051412  Hz

07:05:31  Coil Rotation Frequency, Fcoil =  4.050073  Hz

07:06:00  Coil Voltage Measurement #  30  Made, Stored in RAWFILE

07:06:00  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .7027318  V, Vp main =  89.58246  deg

07:06:00  Coil Voltage Fit: 
Vfit(i) =  0.7027318 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.7027132 V * sin(3*2pi*i/ns) +  0.0051207 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0082125 V

07:06:04  Coil Rotation Frequency, Fcoil =  4.047562  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049682 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00144732  -102.81   0.00006337   102.81
  2   0.01121513   -64.20   0.00049102    32.10
  3   0.70273179    89.58   0.03076710   -29.86
  4   0.00068193  -154.58   0.00002986    38.64
  5   0.00090098   -96.24   0.00003945    19.25
  6   0.00005411   136.38   0.00000237   -22.73
  7   0.00019369  -102.56   0.00000848    14.65
  8   0.00013006    82.97   0.00000569   -10.37
  9   0.00232911   -91.39   0.00010197    10.15
 10   0.00003930   -20.09   0.00000172     2.01
 11   0.00001948  -111.18   0.00000085    10.11
 12   0.00005879  -171.44   0.00000257    14.29
 13   0.00004139   -20.23   0.00000181     1.56
 14   0.00003942   134.30   0.00000173    -9.59
 15   0.00046818   -88.51   0.00002050     5.90
 16   0.00003368   -62.95   0.00000147     3.93

07:06:07  Coil Rotation Frequency, Fcoil =  4.04753  Hz

07:06:11  Coil Rotation Frequency, Fcoil =  4.047785  Hz

07:06:40  Coil Voltage Measurement #  31  Made, Stored in RAWFILE

07:06:40  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .7025028  V, Vp main =  89.58442  deg

07:06:40  Coil Voltage Fit: 
Vfit(i) =  0.7025027 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.7024843 V * sin(3*2pi*i/ns) +  0.0050951 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0082256 V

07:06:44  Coil Rotation Frequency, Fcoil =  4.050605  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.04864 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00143327  -103.50   0.00006277   103.50
  2   0.01122788   -64.16   0.00049171    32.08
  3   0.70250285    89.58   0.03076500   -29.86
  4   0.00072239  -155.99   0.00003164    39.00
  5   0.00093472   -96.03   0.00004093    19.21
  6   0.00007918   135.74   0.00000347   -22.62
  7   0.00021001   -93.97   0.00000920    13.42
  8   0.00013778    99.10   0.00000603   -12.39
  9   0.00233744   -91.25   0.00010236    10.14
 10   0.00003446   -20.22   0.00000151     2.02
 11   0.00001613  -170.87   0.00000071    15.53
 12   0.00001578   167.61   0.00000069   -13.97
 13   0.00000177  -101.87   0.00000008     7.84
 14   0.00004388    60.56   0.00000192    -4.33
 15   0.00050036   -96.81   0.00002191     6.45
 16   0.00002912    -3.69   0.00000128     0.23

07:06:47  Coil Rotation Frequency, Fcoil =  4.050871  Hz

07:06:51  Coil Rotation Frequency, Fcoil =  4.049945  Hz

07:07:19  Coil Voltage Measurement #  32  Made, Stored in RAWFILE

07:07:19  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .7024769  V, Vp main =  89.58427  deg

07:07:19  Coil Voltage Fit: 
Vfit(i) =  0.7024768 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.7024583 V * sin(3*2pi*i/ns) +  0.0050967 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0082202 V

07:07:23  Coil Rotation Frequency, Fcoil =  4.047696  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049504 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00142484  -102.90   0.00006239   102.90
  2   0.01121799   -64.16   0.00049117    32.08
  3   0.70247686    89.58   0.03075729   -29.86
  4   0.00069367  -154.40   0.00003037    38.60
  5   0.00090733   -97.04   0.00003973    19.41
  6   0.00010278   141.88   0.00000450   -23.65
  7   0.00022518  -103.15   0.00000986    14.74
  8   0.00015233   118.42   0.00000667   -14.80
  9   0.00235903   -91.36   0.00010329    10.15
 10   0.00002015   -24.68   0.00000088     2.47
 11   0.00001846   -12.26   0.00000081     1.11
 12   0.00005406  -148.70   0.00000237    12.39
 13   0.00002301   -50.54   0.00000101     3.89
 14   0.00003087   160.69   0.00000135   -11.48
 15   0.00052156   -97.80   0.00002284     6.52
 16   0.00003027    11.31   0.00000133    -0.71

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00006  0.00000    102.32     1.34
  2   0.00049  0.00000     32.10     0.03
  3   0.03076  0.00001    -29.86     0.00
  4   0.00003  0.00000     38.86     0.25
  5   0.00004  0.00000     19.33     0.11
  6   0.00000  0.00000    -23.43     0.85
  7   0.00001  0.00000     14.09     0.61
  8   0.00001  0.00000    -13.07     1.83
  9   0.00010  0.00000     10.14     0.01
 10   0.00000  0.00000      3.16     1.73
 11   0.00000  0.00000     10.10     5.54
 12   0.00000  0.00000     -0.00    13.36
 13   0.00000  0.00000      2.13     4.57
 14   0.00000  0.00000     -8.20     2.66
 15   0.00002  0.00000      6.27     0.24
 16   0.00000  0.00000      1.74     2.01

07:07:23  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  3.076001E-02  +-  6.524043E-06  Tm
Integrated Sextupole Strength, SL =  30.54021  +-  6.477425E-03  T/m

07:07:25  Magnet Current, Imag =  150.6022  A

07:07:25  Magnet Current Ramping to  100  A...

07:08:14  Magnet Current, Imag =  100.6166  A

07:08:15  Magnet Current, Imag =  100.6188  A

07:08:16  Magnet Current, Imag =  100.6166  A

07:08:18  Magnet Current, Imag =  100.623  A

07:08:19  Magnet Current, Imag =  100.6202  A

07:08:19  Average Magnet Current:
Imag =  100.6197  +-  2.321098E-03  A

07:08:22  Coil Rotation Frequency, Fcoil =  4.049031  Hz

07:08:26  Coil Rotation Frequency, Fcoil =  4.049281  Hz

07:08:55  Coil Voltage Measurement #  33  Made, Stored in RAWFILE

07:08:55  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4720347  V, Vp main =  89.58936  deg

07:08:55  Coil Voltage Fit: 
Vfit(i) =  0.4720346 V * cos(3*2pi*i/ns +   89.59 deg)
        = -0.4720225 V * sin(3*2pi*i/ns) +  0.0033829 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055265 V

07:08:59  Coil Rotation Frequency, Fcoil =  4.050253  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.049522 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00047101  -130.15   0.00002062   130.15
  2   0.00760286   -64.43   0.00033288    32.22
  3   0.47203466    89.59   0.02066751   -29.86
  4   0.00046446  -154.30   0.00002034    38.57
  5   0.00057019   -94.82   0.00002496    18.96
  6   0.00006534  -175.15   0.00000286    29.19
  7   0.00010923   -81.75   0.00000478    11.68
  8   0.00010536    81.50   0.00000461   -10.19
  9   0.00152381   -90.62   0.00006672    10.07
 10   0.00007101    84.63   0.00000311    -8.46
 11   0.00001996   -30.34   0.00000087     2.76
 12   0.00001660    11.25   0.00000073    -0.94
 13   0.00004826     2.86   0.00000211    -0.22
 14   0.00004643   151.17   0.00000203   -10.80
 15   0.00035057   -95.26   0.00001535     6.35
 16   0.00007839   -35.59   0.00000343     2.22

07:09:02  Coil Rotation Frequency, Fcoil =  4.050084  Hz

07:09:06  Coil Rotation Frequency, Fcoil =  4.050702  Hz

07:09:34  Coil Voltage Measurement #  34  Made, Stored in RAWFILE

07:09:35  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .471605  V, Vp main =  89.58325  deg

07:09:35  Coil Voltage Fit: 
Vfit(i) =  0.4716049 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.4715924 V * sin(3*2pi*i/ns) +  0.0034301 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055170 V

07:09:38  Coil Rotation Frequency, Fcoil =  4.04558  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.048789 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00054785  -127.83   0.00002399   127.83
  2   0.00756913   -64.62   0.00033147    32.31
  3   0.47160497    89.58   0.02065243   -29.86
  4   0.00047569  -151.03   0.00002083    37.76
  5   0.00054217   -93.71   0.00002374    18.74
  6   0.00011781   160.02   0.00000516   -26.67
  7   0.00013315   -83.84   0.00000583    11.98
  8   0.00010188   132.61   0.00000446   -16.58
  9   0.00159801   -91.35   0.00006998    10.15
 10   0.00002828    -8.61   0.00000124     0.86
 11   0.00006024   153.56   0.00000264   -13.96
 12   0.00004613    18.83   0.00000202    -1.57
 13   0.00003205    91.19   0.00000140    -7.01
 14   0.00002012    48.74   0.00000088    -3.48
 15   0.00034953   -93.80   0.00001531     6.25
 16   0.00003876    54.51   0.00000170    -3.41

07:09:42  Coil Rotation Frequency, Fcoil =  4.045747  Hz

07:09:46  Coil Rotation Frequency, Fcoil =  4.047607  Hz

07:10:14  Coil Voltage Measurement #  35  Made, Stored in RAWFILE

07:10:14  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .471488  V, Vp main =  89.58888  deg

07:10:14  Coil Voltage Fit: 
Vfit(i) =  0.4714880 V * cos(3*2pi*i/ns +   89.59 deg)
        = -0.4714759 V * sin(3*2pi*i/ns) +  0.0033829 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055001 V

07:10:18  Coil Rotation Frequency, Fcoil =  4.050037  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.047797 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00046798  -131.04   0.00002050   131.04
  2   0.00755871   -64.51   0.00033109    32.26
  3   0.47148800    89.59   0.02065237   -29.86
  4   0.00047888  -153.55   0.00002098    38.39
  5   0.00062048   -98.11   0.00002718    19.62
  6   0.00006385   150.80   0.00000280   -25.13
  7   0.00014919   -93.67   0.00000653    13.38
  8   0.00010391   126.82   0.00000455   -15.85
  9   0.00153392   -91.33   0.00006719    10.15
 10   0.00004661   161.48   0.00000204   -16.15
 11   0.00006970    79.22   0.00000305    -7.20
 12   0.00003597   144.99   0.00000158   -12.08
 13   0.00010899    67.81   0.00000477    -5.22
 14   0.00007927   157.89   0.00000347   -11.28
 15   0.00027801   -82.87   0.00001218     5.52
 16   0.00005943   148.98   0.00000260    -9.31

07:10:21  Coil Rotation Frequency, Fcoil =  4.048421  Hz

07:10:26  Coil Rotation Frequency, Fcoil =  4.048903  Hz

07:10:54  Coil Voltage Measurement #  36  Made, Stored in RAWFILE

07:10:54  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .4715517  V, Vp main =  89.58826  deg

07:10:54  Coil Voltage Fit: 
Vfit(i) =  0.4715517 V * cos(3*2pi*i/ns +   89.59 deg)
        = -0.4715395 V * sin(3*2pi*i/ns) +  0.0033885 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0055219 V

07:10:58  Coil Rotation Frequency, Fcoil =  4.048518  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.048614 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00047750  -139.40   0.00002091   139.40
  2   0.00758365   -64.42   0.00033212    32.21
  3   0.47155175    89.59   0.02065099   -29.86
  4   0.00050731  -152.05   0.00002222    38.01
  5   0.00056888   -95.12   0.00002491    19.02
  6   0.00011544   173.45   0.00000506   -28.91
  7   0.00011889   -88.20   0.00000521    12.60
  8   0.00009708   113.09   0.00000425   -14.14
  9   0.00156899   -90.74   0.00006871    10.08
 10   0.00002257   179.70   0.00000099   -17.97
 11   0.00001657    12.10   0.00000073    -1.10
 12   0.00001716    37.70   0.00000075    -3.14
 13   0.00003254    -9.34   0.00000143     0.72
 14   0.00004776   132.27   0.00000209    -9.45
 15   0.00034159   -90.89   0.00001496     6.06
 16   0.00002198   165.16   0.00000096   -10.32

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00002  0.00000    132.11     4.37
  2   0.00033  0.00000     32.25     0.04
  3   0.02066  0.00001    -29.86     0.00
  4   0.00002  0.00000     38.18     0.32
  5   0.00003  0.00000     19.09     0.33
  6   0.00000  0.00000    -12.88    24.33
  7   0.00001  0.00000     12.41     0.65
  8   0.00000  0.00000    -14.19     2.47
  9   0.00007  0.00000     10.11     0.04
 10   0.00000  0.00000    -10.43     7.43
 11   0.00000  0.00000     -4.88     6.33
 12   0.00000  0.00000     -4.43     4.49
 13   0.00000  0.00000     -2.93     3.26
 14   0.00000  0.00000     -8.75     3.12
 15   0.00001  0.00000      6.05     0.32
 16   0.00000  0.00000     -5.20     5.04

07:10:58  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  2.065583E-02  +-  6.76829E-06  Tm
Integrated Sextupole Strength, SL =  20.50823  +-  6.719927E-03  T/m

07:10:59  Magnet Current, Imag =  100.6188  A

07:10:59  Magnet Current Ramping to  50  A...

07:11:49  Magnet Current, Imag =  50.62302  A

07:11:50  Magnet Current, Imag =  50.6267  A

07:11:52  Magnet Current, Imag =  50.6236  A

07:11:54  Magnet Current, Imag =  50.6246  A

07:11:56  Magnet Current, Imag =  50.62652  A

07:11:56  Average Magnet Current:
Imag =  50.62536  +-  1.305008E-03  A

07:11:59  Coil Rotation Frequency, Fcoil =  4.046247  Hz

07:12:03  Coil Rotation Frequency, Fcoil =  4.044961  Hz

07:12:32  Coil Voltage Measurement #  37  Made, Stored in RAWFILE

07:12:32  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2394879  V, Vp main =  89.59159  deg

07:12:32  Coil Voltage Fit: 
Vfit(i) =  0.2394879 V * cos(3*2pi*i/ns +   89.59 deg)
        = -0.2394819 V * sin(3*2pi*i/ns) +  0.0017070 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028250 V

07:12:36  Coil Rotation Frequency, Fcoil =  4.049289  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.046833 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00065503   126.56   0.00002870  -126.56
  2   0.00383712   -64.10   0.00016812    32.05
  3   0.23948793    89.59   0.01049268   -29.86
  4   0.00019850  -155.81   0.00000870    38.95
  5   0.00026902   -99.73   0.00001179    19.95
  6   0.00005447   138.93   0.00000239   -23.16
  7   0.00004244   -65.28   0.00000186     9.33
  8   0.00005252   111.66   0.00000230   -13.96
  9   0.00079001   -89.23   0.00003461     9.91
 10   0.00003193    34.16   0.00000140    -3.42
 11   0.00002969   -93.98   0.00000130     8.54
 12   0.00000930   140.36   0.00000041   -11.70
 13   0.00002502   -87.47   0.00000110     6.73
 14   0.00003749   134.55   0.00000164    -9.61
 15   0.00019563   -97.42   0.00000857     6.49
 16   0.00004475   132.42   0.00000196    -8.28

07:12:39  Coil Rotation Frequency, Fcoil =  4.048687  Hz

07:12:43  Coil Rotation Frequency, Fcoil =  4.045685  Hz

07:13:12  Coil Voltage Measurement #  38  Made, Stored in RAWFILE

07:13:12  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2394843  V, Vp main =  89.58711  deg

07:13:12  Coil Voltage Fit: 
Vfit(i) =  0.2394842 V * cos(3*2pi*i/ns +   89.59 deg)
        = -0.2394780 V * sin(3*2pi*i/ns) +  0.0017257 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0027927 V

07:13:16  Coil Rotation Frequency, Fcoil =  4.047808  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.047393 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00061185   127.12   0.00002680  -127.12
  2   0.00380461   -64.00   0.00016667    32.00
  3   0.23948430    89.59   0.01049107   -29.86
  4   0.00020285  -155.35   0.00000889    38.84
  5   0.00025571   -98.28   0.00001120    19.66
  6   0.00003010   145.38   0.00000132   -24.23
  7   0.00005352   -91.44   0.00000234    13.06
  8   0.00007769   128.61   0.00000340   -16.08
  9   0.00074178   -91.94   0.00003250    10.22
 10   0.00003164   164.92   0.00000139   -16.49
 11   0.00005274   135.77   0.00000231   -12.34
 12   0.00003426  -139.65   0.00000150    11.64
 13   0.00003980  -156.05   0.00000174    12.00
 14   0.00002825  -160.09   0.00000124    11.43
 15   0.00021564   -86.77   0.00000945     5.78
 16   0.00002109  -155.67   0.00000092     9.73

07:13:19  Coil Rotation Frequency, Fcoil =  4.048676  Hz

07:13:23  Coil Rotation Frequency, Fcoil =  4.048432  Hz

07:13:51  Coil Voltage Measurement #  39  Made, Stored in RAWFILE

07:13:51  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2394562  V, Vp main =  89.57973  deg

07:13:51  Coil Voltage Fit: 
Vfit(i) =  0.2394562 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.2394498 V * sin(3*2pi*i/ns) +  0.0017563 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028208 V

07:13:55  Coil Rotation Frequency, Fcoil =  4.048567  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.048559 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00061597   123.22   0.00002698  -123.22
  2   0.00383106   -65.31   0.00016778    32.65
  3   0.23945624    89.58   0.01048682   -29.86
  4   0.00023389  -152.80   0.00001024    38.20
  5   0.00023953   -90.52   0.00001049    18.10
  6   0.00007521   168.08   0.00000329   -28.01
  7   0.00006372   -57.21   0.00000279     8.17
  8   0.00002747  -156.31   0.00000120    19.54
  9   0.00081781   -89.31   0.00003582     9.92
 10   0.00002924   -60.14   0.00000128     6.01
 11   0.00002020    84.32   0.00000088    -7.67
 12   0.00009698   142.40   0.00000425   -11.87
 13   0.00009650    67.12   0.00000423    -5.16
 14   0.00006838   130.46   0.00000299    -9.32
 15   0.00013008   -99.00   0.00000570     6.60
 16   0.00002433   -87.71   0.00000107     5.48

07:13:59  Coil Rotation Frequency, Fcoil =  4.049031  Hz

07:14:03  Coil Rotation Frequency, Fcoil =  4.047978  Hz

07:14:31  Coil Voltage Measurement #  40  Made, Stored in RAWFILE

07:14:31  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .2393366  V, Vp main =  89.58202  deg

07:14:31  Coil Voltage Fit: 
Vfit(i) =  0.2393365 V * cos(3*2pi*i/ns +   89.58 deg)
        = -0.2393301 V * sin(3*2pi*i/ns) +  0.0017459 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0028327 V

07:14:35  Coil Rotation Frequency, Fcoil =  4.0475  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.04817 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00062787   123.85   0.00002750  -123.85
  2   0.00384063   -65.08   0.00016821    32.54
  3   0.23933658    89.58   0.01048258   -29.86
  4   0.00025512  -155.45   0.00001117    38.86
  5   0.00029284   -88.27   0.00001283    17.65
  6   0.00004667   130.32   0.00000204   -21.72
  7   0.00013778   -49.03   0.00000603     7.00
  8   0.00005401   140.36   0.00000237   -17.54
  9   0.00081897   -88.49   0.00003587     9.83
 10   0.00005558   131.91   0.00000243   -13.19
 11   0.00006445  -164.98   0.00000282    15.00
 12   0.00002063   142.09   0.00000090   -11.84
 13   0.00002886    73.25   0.00000126    -5.63
 14   0.00003762    -7.52   0.00000165     0.54
 15   0.00009960   -91.52   0.00000436     6.10
 16   0.00005593  -107.49   0.00000245     6.72

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00003  0.00000   -125.19     1.68
  2   0.00017  0.00000     32.31     0.29
  3   0.01049  0.00000    -29.86     0.00
  4   0.00001  0.00000     38.71     0.30
  5   0.00001  0.00000     18.84     0.98
  6   0.00000  0.00000    -24.28     2.33
  7   0.00000  0.00000      9.39     2.27
  8   0.00000  0.00000     -7.01    15.38
  9   0.00003  0.00000      9.97     0.15
 10   0.00000  0.00000     -6.77     8.81
 11   0.00000  0.00000      0.88    11.25
 12   0.00000  0.00000     -5.94    10.15
 13   0.00000  0.00000      1.98     7.62
 14   0.00000  0.00000     -1.74     8.63
 15   0.00001  0.00000      6.25     0.32
 16   0.00000  0.00000      3.41     6.92

07:14:35  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  1.048829E-02  +-  3.92738E-06  Tm
Integrated Sextupole Strength, SL =  10.41334  +-  3.899317E-03  T/m

07:14:37  Magnet Current, Imag =  50.62432  A

07:14:37  Magnet Current Ramping to  25  A...

07:15:20  Magnet Current, Imag =  25.63692  A

07:15:22  Magnet Current, Imag =  25.6332  A

07:15:23  Magnet Current, Imag =  25.63508  A

07:15:25  Magnet Current, Imag =  25.63846  A

07:15:27  Magnet Current, Imag =  25.6397  A

07:15:27  Average Magnet Current:
Imag =  25.63661  +-  2.595792E-03  A

07:15:30  Coil Rotation Frequency, Fcoil =  4.04409  Hz

07:15:34  Coil Rotation Frequency, Fcoil =  4.045881  Hz

07:16:03  Coil Voltage Measurement #  41  Made, Stored in RAWFILE

07:16:03  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .123449  V, Vp main =  89.569  deg

07:16:03  Coil Voltage Fit: 
Vfit(i) =  0.1234490 V * cos(3*2pi*i/ns +   89.57 deg)
        = -0.1234455 V * sin(3*2pi*i/ns) +  0.0009286 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015897 V

07:16:07  Coil Rotation Frequency, Fcoil =  4.047669  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.04588 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00098496   112.92   0.00004316  -112.92
  2   0.00195509   -66.57   0.00008568    33.29
  3   0.12344897    89.57   0.00540994   -29.86
  4   0.00015209  -128.90   0.00000667    32.22
  5   0.00005277   -89.17   0.00000231    17.83
  6   0.00006504  -124.59   0.00000285    20.76
  7   0.00002232    20.64   0.00000098    -2.95
  8   0.00001540  -176.58   0.00000067    22.07
  9   0.00042411   -86.27   0.00001859     9.59
 10   0.00002561   176.16   0.00000112   -17.62
 11   0.00003696   -84.97   0.00000162     7.72
 12   0.00004041  -168.11   0.00000177    14.01
 13   0.00003155   152.71   0.00000138   -11.75
 14   0.00002423    71.09   0.00000106    -5.08
 15   0.00007943  -105.82   0.00000348     7.05
 16   0.00003767   -48.23   0.00000165     3.01

07:16:10  Coil Rotation Frequency, Fcoil =  4.046837  Hz

07:16:14  Coil Rotation Frequency, Fcoil =  4.045893  Hz

07:16:43  Coil Voltage Measurement #  42  Made, Stored in RAWFILE

07:16:43  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1234097  V, Vp main =  89.54774  deg

07:16:43  Coil Voltage Fit: 
Vfit(i) =  0.1234097 V * cos(3*2pi*i/ns +   89.55 deg)
        = -0.1234059 V * sin(3*2pi*i/ns) +  0.0009741 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015782 V

07:16:47  Coil Rotation Frequency, Fcoil =  4.044179  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.045637 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00098354   112.02   0.00004310  -112.02
  2   0.00193762   -65.18   0.00008492    32.59
  3   0.12340975    89.55   0.00540855   -29.85
  4   0.00009163  -156.69   0.00000402    39.17
  5   0.00010481   -82.64   0.00000459    16.53
  6   0.00003505    11.56   0.00000154    -1.93
  7   0.00004713  -146.97   0.00000207    21.00
  8   0.00003579    28.51   0.00000157    -3.56
  9   0.00042167   -88.76   0.00001848     9.86
 10   0.00003988   -95.63   0.00000175     9.56
 11   0.00006366   -28.79   0.00000279     2.62
 12   0.00003327  -108.09   0.00000146     9.01
 13   0.00003088   122.38   0.00000135    -9.41
 14   0.00003400    40.48   0.00000149    -2.89
 15   0.00006879  -120.36   0.00000301     8.02
 16   0.00002796    45.77   0.00000123    -2.86

07:16:50  Coil Rotation Frequency, Fcoil =  4.045046  Hz

07:16:54  Coil Rotation Frequency, Fcoil =  4.046606  Hz

07:17:22  Coil Voltage Measurement #  43  Made, Stored in RAWFILE

07:17:23  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1234084  V, Vp main =  89.59233  deg

07:17:23  Coil Voltage Fit: 
Vfit(i) =  0.1234084 V * cos(3*2pi*i/ns +   89.59 deg)
        = -0.1234053 V * sin(3*2pi*i/ns) +  0.0008780 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015832 V

07:17:26  Coil Rotation Frequency, Fcoil =  4.046552  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.046068 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00101692   112.90   0.00004456  -112.90
  2   0.00193493   -66.12   0.00008479    33.06
  3   0.12340844    89.59   0.00540791   -29.86
  4   0.00010205  -150.56   0.00000447    37.64
  5   0.00013756  -101.44   0.00000603    20.29
  6   0.00001558    88.37   0.00000068   -14.73
  7   0.00004230   -70.65   0.00000185    10.09
  8   0.00000653   104.50   0.00000029   -13.06
  9   0.00040704   -96.26   0.00001784    10.70
 10   0.00001663   -64.50   0.00000073     6.45
 11   0.00004527  -156.09   0.00000198    14.19
 12   0.00002757   104.34   0.00000121    -8.69
 13   0.00005310  -120.35   0.00000233     9.26
 14   0.00007445   161.02   0.00000326   -11.50
 15   0.00010589  -110.99   0.00000464     7.40
 16   0.00003582   152.00   0.00000157    -9.50

07:17:30  Coil Rotation Frequency, Fcoil =  4.04595  Hz

07:17:34  Coil Rotation Frequency, Fcoil =  4.044922  Hz

07:18:02  Coil Voltage Measurement #  44  Made, Stored in RAWFILE

07:18:02  Coil Voltage Main Harmonic From FFT:
Nmain =  3 , Vm main =  .1233216  V, Vp main =  89.57367  deg

07:18:02  Coil Voltage Fit: 
Vfit(i) =  0.1233216 V * cos(3*2pi*i/ns +   89.57 deg)
        = -0.1233182 V * sin(3*2pi*i/ns) +  0.0009176 V * cos(3*2pi*i/ns)
RMS of the residuals =  0.0015655 V

07:18:06  Coil Rotation Frequency, Fcoil =  4.04671  Hz

                FIELD HARMONICS CALCULATION

Coil Radius, Rcoil =  .044882  m,  # Turns, Nturns =  20 
Coil Rotation Frequency, Fcoil =  4.045861 

 N       Vm         Vp        BLn       THspole
         (V)       (deg)      (Tm)       (deg) 
---  -----------  -------  -----------  -------
  1   0.00094828   113.72   0.00004156  -113.72
  2   0.00193894   -64.92   0.00008497    32.46
  3   0.12332162    89.57   0.00540438   -29.86
  4   0.00007684  -134.32   0.00000337    33.58
  5   0.00014046  -103.70   0.00000616    20.74
  6   0.00001008    67.08   0.00000044   -11.18
  7   0.00006002  -129.61   0.00000263    18.52
  8   0.00001119  -131.07   0.00000049    16.38
  9   0.00038609   -90.61   0.00001692    10.07
 10   0.00006585   -68.65   0.00000289     6.87
 11   0.00003565    30.44   0.00000156    -2.77
 12   0.00001355  -110.56   0.00000059     9.21
 13   0.00001682   155.20   0.00000074   -11.94
 14   0.00003357   117.71   0.00000147    -8.41
 15   0.00016925  -111.59   0.00000742     7.44
 16   0.00001861    43.77   0.00000082    -2.74

                          FIELD HARMONICS

Coil Radius, Rcoil =  .044882  m
Coil # Turns, Nturns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 

 N     BLn     sigBLn   THspole   sigTH  
       (Tm)     (Tm)     (deg)    (deg)  
---  --------+--------  --------+--------
  1   0.00004  0.00000   -112.89     0.60
  2   0.00009  0.00000     32.85     0.34
  3   0.00541  0.00000    -29.86     0.01
  4   0.00000  0.00000     35.65     2.85
  5   0.00000  0.00000     18.85     1.74
  6   0.00000  0.00000     -1.77    13.82
  7   0.00000  0.00000     11.66     9.35
  8   0.00000  0.00000      5.46    14.32
  9   0.00002  0.00000     10.05     0.41
 10   0.00000  0.00000      1.32    11.00
 11   0.00000  0.00000      5.44     6.27
 12   0.00000  0.00000      5.88     8.65
 13   0.00000  0.00000     -5.96     8.84
 14   0.00000  0.00000     -6.97     3.27
 15   0.00000  0.00000      7.48     0.35
 16   0.00000  0.00000     -3.02     4.43

07:18:06  Integrated Sextupole Strength Calculation:
Coil: Radius =  .044882  m, # Turns =  20 
Average, # Rotations/Measurement =  10 , # Measurements =  4 
Integrated Field Strength At Rcoil, BL3 =  5.407696E-03  +-  2.047338E-06  Tm
Integrated Sextupole Strength, SL =  5.369055  +-  2.032709E-03  T/m

07:18:08  Magnet Current, Imag =  25.63902  A

07:18:08  Magnet Current Ramping to  0  A...

07:18:51  Magnet Current, Imag =  .648068  A