B9V2 Septum Measurement Test Plan

Rev1-1/22/16

Logistic Info

| Person Responsible | Domenico Dell’Orco |
| --- | --- |
| Phone # | 650-926-8683 (cell. 510-219-0378) |
| Start Date | 2-1-2016 |
| Finish Date | 2-8-2016 |
| PA # for MagMeas/alignment | 14427-A8001 |

Magnet Designation and Type

| Project Name | Spear 3 B9V2 septum |
| --- | --- |
| Magnet Type | Focusing Quadrupole |
| Magnet Name/Number | B9V2 |
| Serial # / PC # | #1 |
| Trim Coils | No | Trim Types | Hollow copper water cooled |
| Magnet gap or diameter (mm) | 9 mm |

Alignment

| Precision (0.05 mm) |
| --- |
| Has the magnet been fiducialized | Yes (Z=0 is center of chamber length, Y=0 is center of chamber height, X=0 is the insert flat surface |
| If it has not been fiducialized, what is origin point of the magnet, what is its coordinate system and what surfaces should be used for alignment? |  |
| + Z direction of magnet (Please provide drawing) |  |

Special Alignment Tolerances

| X |  |
| --- | --- |
| Y |  |
| Pitch |  |
| Yaw |  |
| Roll |  |

Water and Power.

| Water Pressure | 100 psi DP (3 water circuits in parallel) | PSI |
| --- | --- | --- |
| Water Flow | ~1.3 GPM @ 100 psi DP | GPM |
| Maximum Current Main | 265 | Amp |
| Max Current Trims |  |  |
| Magnet resistance | ~100 mOhm at 40 C |  |

Polarity

| Main Coil Polarity. (Nearest North pole to Horizontal look in +z direction) | Power leads are marked. |
| --- | --- |
| 1st Trim Polarity (Nearest North pole to Horizontal look in +z direction) | N/A |
| 2nd Trim Polarity (Nearest North pole to Horizontal look in +z direction) | N/A |

Temperature Tests

| Temperature and Resistance Test | No, Protect magnet using thermostats |
| --- | --- |
| Areas to be measured |  |
| Currents (Amps) |  |
| Check water flow | Yes |

Standardization

| Magnet warm up. ? time (mins) @ ? current (Amps) | 98 A |
| --- | --- |
| Conditioning Standardization Cycles Performed before measurements: | YES |
| Number of Stdz cycles | 3 |
| Ramp Rate (A/s) | 4 A/s | Minimum Current (A) | 0 |
| Settle Time (sec) | 2 min | Maximum Current (A) | 265 |
| Ramp Type (Linear or Three Linear or Cosine | Linear |

Measurements

| Integrated Strength | Main | Yes | Trims | Yes |
| --- | --- | --- | --- | --- |
| Currents: | See attachment |  |
| Harmonics | Main | Yes | Trims | Yes |
| Currents: |  |  |

Harmonic Tolerances (as % of main, Main =100 %)

| Dipole n = 1 | Quadrupole n = 2 | Sextupole n = 3 | Octupole n =4 |
| --- | --- | --- | --- |

Field Map

| Type of map? (Transverse, axial, 3D, Locate Center) | N/A |
| --- | --- |
| Dimensions ( X, Y, Z) |  |
| Spacing between step (X, Y, Z) |  |

Notes and Additional Tests: