LCLS BFW WIRECARD ASSY

FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Venkat Srinivasan |
| Date: | Friday, May 09, 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 13 / WC - 13 |

Basic Procedure:

- Locate Bench and Bench CSY

- Install Top Portion of BFW

- Mount Wire Card and Center to Bench CSY

- 5 Cycles of Repeatability to Bench CSY of

  - Positions of Wire Card (Center, 2 Corners/Intersection Points)

  - 4 – BFW Fiducials (X,Y,Z locations)

- Create Wire Card CSY

- Transform to Wire Cross Hairs (Optical CMM Location Offset to Outer Datums of Card)

- Translate 4 – BFW Fiducials into Wire CSY

- Use 4X Screws to Secure the BFW in its Up or “In-Beam Position” for Transport and Girder Alignment

- Place BFW Chamber onto Support Stand, Set to Nominal Dimensions in X & Y.

- Place Top portion of BFW onto BFW Chamber and Support Stand

  - Tighten down per ANL Torque Sequence/Specs

  - Coordinate with MFD Vacuum for Pump Down

Coordinate System Setups

Bench CSY

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Wire CSY

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Shift this CSY using the Optical CMM Output for the exact offsets (file in Sharepoint SV-VS122108-Wire.xls per Serialized Wire Card.

Transform TB’s into Wire CSY for Fiducial Numbers

Repeatability Data

CSY: BENCH$CSY

Wire Card Data

|  | X-POS CARD | X-INTPT CARD(1) | Y-INTPT CARD(1) | X-INTPT CARD(2) | Y-INTPT CARD(2) | Y1 -Y2 |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |
| average |  |  |  |  |  |  |
| range |  |  |  |  |  |  |
| st dev |  |  |  |  |  |  |
| RMS |  |  |  |  |  |  |

Tooling Ball Repeatability

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |
| 4 |  |  |  |
| 5 |  |  |  |
| average |  |  |  |
| range |  |  |  |
| st dev |  |  |  |
| RMS |  |  |  |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |
| 4 |  |  |  |
| 5 |  |  |  |
| average |  |  |  |
| range |  |  |  |
| st dev |  |  |  |
| RMS |  |  |  |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |
| 4 |  |  |  |
| 5 |  |  |  |
| average |  |  |  |
| range |  |  |  |
| st dev |  |  |  |
| RMS |  |  |  |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |
| 4 |  |  |  |
| 5 |  |  |  |
| average |  |  |  |
| range |  |  |  |
| st dev |  |  |  |
| RMS |  |  |  |

Fiducial Data

CSY : Wire$CSY (Wire Crosshair)

| TB | Form | Diameter | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| 5 |  |  |  |  |  |
| 6 |  |  |  |  |  |
| 7 |  |  |  |  |  |
| 8 |  |  |  |  |  |

Checklist

Top of Form

Bottom of Form

# Text boxes

Z+

+Z

X+

Y+

+X

+Y

Transformation

Y+