BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Tuesday, July 21, 2009 |
| Work Order/Charge No.: | 09-3008 |
| Serial Number: | #6 (Formerly #01) |
| Stamped Drwg. #: | AD-234-309-80 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\AD-234-309-80 SN-6.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | n | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00024 | 0.25046 | 3.49242 | 5.45759 | 1.63957 | 0.00047 |
| TB 2 | 0.00012 | 0.25050 | 3.48810 | 5.45606 | -1.61569 | 0.00023 |
| TB 3 | 0.00019 | 0.25046 | -3.49419 | 5.45834 | -1.61656 | 0.00031 |
| TB 4 | 0.00025 | 0.25045 | -3.49551 | 5.45704 | 1.63662 | 0.00042 |
| TB 5 | 0.00071 | 0.25024 | -6.24374 | 0.00747 | 1.62757 | 0.00042 |
| TB 6 | 0.00015 | 0.25044 | -6.25000 | 0.00400 | -1.62405 | 0.00034 |

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.60065 | -1.125 | -1.375 |
| 2 | 0.60050 | 1.125 | -1.375 |
| 3 | 0.60026 | 0.000 | 0.000 |
| 4 | 0.59982 | -1.125 | 1.375 |
| 5 | 0.59945 | 1.125 | 1.375 |
| Avg. Gap | 0.60020 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X