BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Wednesday, July 22, 2009 |
| Work Order/Charge No.: | 09-3008 |
| Serial Number: | #7 (formerly #2) |
| Stamped Drwg. #: | AD-234-309-80 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\AD-234-309-80 SN-7.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | n | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00029 | 0.25052 | 3.50411 | 5.45670 | 1.61940 | 0.00051 |
| TB 2 | 0.00025 | 0.25046 | 3.49713 | 5.45792 | -1.64112 | 0.00030 |
| TB 3 | 0.00013 | 0.25043 | -3.49396 | 5.45843 | -1.64261 | 0.00010 |
| TB 4 | 0.00039 | 0.25039 | -3.49816 | 5.45765 | 1.60258 | 0.00062 |
| TB 5 | 0.00020 | 0.25055 | -6.24523 | 0.00362 | 1.62350 | 0.00029 |
| TB 6 | 0.00051 | 0.25022 | -6.24112 | 0.00558 | -1.63635 | 0.00043 |

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.59987 | -1.125 | -1.375 |
| 2 | 0.59923 | 1.125 | -1.375 |
| 3 | 0.59972 | 0.000 | 0.000 |
| 4 | 0.59933 | -1.125 | 1.375 |
| 5 | 0.59900 | 1.125 | 1.375 |
| Avg. Gap | 0.59953 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X