BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Tuesday, July 21, 2009 |
| Work Order/Charge No.: | 09-3008 |
| Serial Number: | #2 |
| Stamped Drwg. #: | AD-234-309-91 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\AD-234-309-91 SN-2.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | n | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00021 | 0.25041 | 3.48753 | 5.03816 | 1.63292 | 0.00016 |
| TB 2 | 0.00012 | 0.25045 | 3.48129 | 5.03834 | -1.63327 | 0.00018 |
| TB 3 | 0.00009 | 0.25045 | -3.50127 | 5.03839 | -1.60945 | 0.00020 |
| TB 4 | 0.00022 | 0.25045 | -3.50087 | 5.03813 | 1.64281 | 0.00044 |
| TB 5 | 0.00019 | 0.25045 | -6.24155 | -0.00101 | 1.63150 | 0.00024 |
| TB 6 | 0.00050 | 0.25036 | -6.24665 | -0.00068 | -1.62447 | 0.00034 |

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.59758 | -1.125 | -1.375 |
| 2 | 0.59758 | 1.125 | -1.375 |
| 3 | 0.59780 | 0.000 | 0.000 |
| 4 | 0.59807 | -1.125 | 1.375 |
| 5 | 0.59773 | 1.125 | 1.375 |
| Avg. Gap | 0.59777 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X