BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Thursday, August 06, 2009 |
| Work Order/Charge No.: | 09-3008 |
| Serial Number: | #3 |
| Stamped Drwg. #: | AD-234-309-91 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\AD-234-309-91 SN-3.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | n | X | Y | Z | b |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00129 | 0.24994 | 3.49657 | 5.03263 | 1.59981 | 0.00041 |
| TB 2 | 0.00162 | 0.24995 | 3.49181 | 5.03296 | -1.63728 | 0.00126 |
| TB 3 | 0.00060 | 0.25021 | -3.49882 | 5.03117 | -1.62038 | 0.00016 |
| TB 4 | 0.00183 | 0.24953 | -3.49583 | 5.03480 | 1.63424 | 0.00087 |
| TB 5 | 0.00105 | 0.25023 | -6.24679 | -0.00067 | 1.63110 | 0.00139 |
| TB 6 | 0.00396 | 0.24810 | -6.25338 | -0.00990 | -1.63429 | 0.00461 |

**Form of cylinder are out of round, .2500 deltronics pin fits through all, form relates to perpendicularity errors as well

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.59982 | -1.125 | -1.375 |
| 2 | 0.60046 | 1.125 | -1.375 |
| 3 | 0.60005 | 0.000 | 0.000 |
| 4 | 0.59987 | -1.125 | 1.375 |
| 5 | 0.60052 | 1.125 | 1.375 |
| Avg. Gap | 0.60008 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X