BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Friday, November 13, 2009 |
| Work Order/Charge No.: | 8540022 |
| Serial Number: | #08 |
| Stamped Drwg. #: | n/a |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\SN 08.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | Diameter | X | Y | Z | Perpendicularity |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00017 | 0.25037 | 3.50301 | 5.48693 | 1.61854 | 0.00071 |
| TB 2 | 0.00346 | 0.25010 | 3.49304 | 5.48667 | -1.64794 | 0.00205 |
| TB 3 | 0.00036 | 0.25035 | -3.49203 | 5.48397 | -1.63821 | 0.00031 |
| TB 4 | 0.00110 | 0.25022 | -3.49662 | 5.48720 | 1.61464 | 0.00045 |
| TB 5 | 0.00361 | 0.24870 | -6.25326 | -0.00328 | 1.63301 | 0.00213 |
| TB 6 | 0.00196 | 0.24898 | -6.25402 | -0.00253 | -1.62670 | 0.00057 |

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.60110 | -1.125 | -1.375 |
| 2 | 0.60013 | 1.125 | -1.375 |
| 3 | 0.60231 | 0.000 | 0.000 |
| 4 | 0.60094 | -1.125 | 1.375 |
| 5 | 0.60004 | 1.125 | 1.375 |
| Avg. Gap | 0.60066 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X