BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Wednesday, November 11, 2009 |
| Work Order/Charge No.: | 8540022 |
| Serial Number: | #09 |
| Stamped Drwg. #: | n/a |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\SN 09.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | Diameter | X | Y | Z | Perpendicularity |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00081 | 0.25031 | 3.48867 | 5.48663 | 1.61746 | 0.00065 |
| TB 2 | 0.00031 | 0.25037 | 3.48173 | 5.48593 | -1.64198 | 0.00039 |
| TB 3 | 0.00080 | 0.25033 | -3.50671 | 5.48645 | -1.61422 | 0.00054 |
| TB 4 | 0.00033 | 0.25031 | -3.49745 | 5.08930 | 1.64349 | 0.00034 |
| TB 5 | 0.00096 | 0.25003 | -6.24530 | 0.00633 | 1.63996 | 0.00021 |
| TB 6 | 0.00083 | 0.24975 | -6.25224 | -0.01640 | -1.62145 | 0.00059 |

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.60200 | -1.125 | -1.375 |
| 2 | 0.60179 | 1.125 | -1.375 |
| 3 | 0.60172 | 0.000 | 0.000 |
| 4 | 0.60162 | -1.125 | 1.375 |
| 5 | 0.60129 | 1.125 | 1.375 |
| Avg. Gap | 0.60169 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X