BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Thursday, November 12, 2009 |
| Work Order/Charge No.: | 8540022 |
| Serial Number: | #10 |
| Stamped Drwg. #: | n/a |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\SN 09.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | Diameter | X | Y | Z | Perpendicularity |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00191 | 0.24989 | 3.48850 | 5.49117 | 1.67276 | 0.00083 |
| TB 2 | 0.00201 | 0.24979 | 3.48256 | 5.49095 | -1.62493 | 0.00035 |
| TB 3 | 0.00196 | 0.25005 | -3.49841 | 5.48945 | -1.61661 | 0.00118 |
| TB 4 | 0.00029 | 0.25033 | -3.50128 | 5.48689 | 1.59043 | 0.00015 |
| TB 5 | 0.00173 | 0.24943 | -6.25154 | 0.00054 | 1.63830 | 0.00076 |
| TB 6 | 0.00216 | 0.24896 | -6.25264 | -0.01198 | -1.62027 | 0.00121 |

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.60245 | -1.125 | -1.375 |
| 2 | 0.60182 | 1.125 | -1.375 |
| 3 | 0.60253 | 0.000 | 0.000 |
| 4 | 0.60305 | -1.125 | 1.375 |
| 5 | 0.60248 | 1.125 | 1.375 |
| Avg. Gap | 0.60248 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X