BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Monday, November 16, 2009 |
| Work Order/Charge No.: | 8540022 |
| Serial Number: | #12 |
| Stamped Drwg. #: | n/a |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\SN 12.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | Diameter | X | Y | Z | Perpendicularity |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00261 | 0.24979 | 3.50526 | 5.48494 | 1.59664 | 0.00037 |
| TB 2 | 0.00041 | 0.25036 | 3.49844 | 5.48377 | -1.63925 | 0.00007 |
| TB 3 | 0.00101 | 0.25014 | -3.49171 | 5.48760 | -1.62827 | 0.00047 |
| TB 4 | 0.00161 | 0.25016 | -3.49407 | 5.48377 | 1.59280 | 0.00036 |
| TB 5 | 0.00350 | 0.24866 | -6.25184 | 0.00879 | 1.62251 | 0.00321 |
| TB 6 | 0.00117 | 0.24958 | -6.24651 | 0.00498 | -1.63527 | 0.00347 |

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.60289 | -1.125 | -1.375 |
| 2 | 0.60060 | 1.125 | -1.375 |
| 3 | 0.60213 | 0.000 | 0.000 |
| 4 | 0.60344 | -1.125 | 1.375 |
| 5 | 0.60119 | 1.125 | 1.375 |
| Avg. Gap | 0.60213 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X