BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Monday, November 16, 2009 |
| Work Order/Charge No.: | 8540022 |
| Serial Number: | #13 |
| Stamped Drwg. #: | n/a |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\SN 13.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | Diameter | X | Y | Z | Perpendicularity |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00048 | 0.25045 | 3.49330 | 5.48396 | 1.63665 | 0.00036 |
| TB 2 | 0.00026 | 0.25048 | 3.49557 | 5.48155 | -1.62336 | 0.00031 |
| TB 3 | 0.00022 | 0.25063 | -3.48616 | 5.48498 | -1.61738 | 0.00035 |
| TB 4 | 0.00015 | 0.25055 | -3.48892 | 5.48323 | 1.62553 | 0.00014 |
| TB 5 | 0.00060 | 0.24997 | -6.25036 | -0.00039 | 1.62714 | 0.00045 |
| TB 6 | 0.00104 | 0.25018 | -6.25272 | -0.00940 | -1.63330 | 0.00027 |

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.60204 | -1.125 | -1.375 |
| 2 | 0.60084 | 1.125 | -1.375 |
| 3 | 0.60239 | 0.000 | 0.000 |
| 4 | 0.60252 | -1.125 | 1.375 |
| 5 | 0.60255 | 1.125 | 1.375 |
| Avg. Gap | 0.60210 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X