BLUE DIPOLE - ECHO 7 EXP. (3D4 MAGNET)

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Customer: | Dieter Walz |
| Date: | Monday, November 16, 2009 |
| Work Order/Charge No.: | 8540022 |
| Serial Number: | #14 |
| Stamped Drwg. #: | n/a |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\BLUE-DIPOLE FFTB STEERING MAGNET\SN 14.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Plane along bottom pole plane.

Spatial Alignment

- Plane of +Z face of magnet

“Z” Zero

- Mid-Plane of the magnet. (see dashed planar alignment above)

“X” & “Y” Zero

- X zero is created by the symmetry point of the outer ends of the magnet where TB 5 & 6 are and opposite where the terminal strip is located.

- Symmetry plane of the pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

Projected cylinder into 1” offset plane

| Tooling Ball | Form | Diameter | X | Y | Z | Perpendicularity |
| --- | --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00040 | 0.25038 | 3.48903 | 5.48103 | 1.63282 | 0.00027 |
| TB 2 | 0.00406 | 0.24998 | 3.47966 | 5.48098 | -1.65031 | 0.00205 |
| TB 3 | 0.00181 | 0.24990 | -3.50476 | 5.48367 | -1.61475 | 0.00129 |
| TB 4 | 0.00096 | 0.25018 | -3.49789 | 5.48147 | 1.64960 | 0.00032 |
| TB 5 | 0.00228 | 0.24976 | -6.25032 | 0.00747 | 1.66379 | 0.00139 |
| TB 6 | 0.00127 | 0.24927 | -6.25441 | -0.00575 | -1.61969 | 0.00107 |

Pole Tip Distance/Gaps (at location X, Z)

| Station | Gap Distance | X | Z |
| --- | --- | --- | --- |
| 1 | 0.60295 | -1.125 | -1.375 |
| 2 | 0.60288 | 1.125 | -1.375 |
| 3 | 0.60294 | 0.000 | 0.000 |
| 4 | 0.60293 | -1.125 | 1.375 |
| 5 | 0.60285 | 1.125 | 1.375 |
| Avg. Gap | 0.60291 | - | - |

# Text boxes

+Y

+Z

+X

+Y

-Z

+Y

-X