AFT2 REFURBISHED SEXTUPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Cherrill Spencer |
| Date: | Wednesday, August 20, 2008 |
| Work Order/Charge No.: | 1111143 |
| Serial Number: | 02 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/CHERRILL SPENCER/AFT2-SEXTUPOLE-02.PDF |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet using 6 scans of each sextupole pole tip on each side (Terminal and Non Terminal sides) creating 2 circles on the pole tips.  One on each side where Positive Z is on the Terminal Side of the Magnet.

Planar Alignment

- Radial Pole tip #1’s center and the geometric center of all poles to create an axis on the Terminal Side of the Magnet.

“Z” Zero

- Mid-plane of the magnet (middle of Terminal and Non Terminal ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View (Looking from upstream side +Z) | Side View (looking from +X side) |
| --- | --- |

Tooling Ball Locations for SN 02

Used Standard ½” Tooling Balls w/ 1” extension

Magnet CSY (stated above)

| TB | FORM | DIA | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| 1 | 0.00031 | 0.49364 | 7.68954 | 0.44290 | 1.50230 |
| 2 | 0.00021 | 0.49862 | 0.03979 | 7.70093 | 1.51019 |
| 3 | 0.00018 | 0.49855 | 0.01412 | 7.70304 | -1.51232 |
| 4 | 0.00023 | 0.49817 | 7.68793 | 0.45463 | -1.51476 |

|  |  | Clocked to Pole 1 |  |  |
| --- | --- | --- | --- | --- |
| Terminal Side | Radial Distance (0.8125) | Actual Angle of Pole w.r.t CSY | Deviation Angle to Pole (act-nom) | Radians | Micro Radians | Pole Tip Distance (1.625) |
| Pole Tip 1 | 0.81098 | 89.99195 | -0.00805 | -0.00014 | 140 | 1.62236 |
| Pole Tip 2 | 0.81094 | 270.27162 | 0.27162 | 0.00474 | 4741 |  |
| Pole Tip 3 | 0.81075 | 30.00680 | 0.00680 | 0.00012 | 119 | 1.62635 |
| Pole Tip 4 | 0.81542 | 210.09029 | 0.09029 | 0.00158 | 1576 |  |
| Pole Tip 5 | 0.81471 | 330.20776 | 0.20776 | 0.00363 | 3626 | 1.62547 |
| Pole Tip 6 | 0.81138 | 150.10550 | 0.10550 | 0.00184 | 1841 |  |
| Non Terminal Side | Radial Distance (0.8125) | Actual Angle of Pole w.r.t CSY | Deviation Angle to Pole (act-nom) | Radians | Micro Radians | Pole Tip Distance (1.625) |
| Pole Tip 1 | 0.81141 | 90.03487 | 0.03487 | 0.00061 | 609 | 1.62356 |
| Pole Tip 2 | 0.81059 | 270.22009 | 0.22009 | 0.00384 | 3841 |  |
| Pole Tip 3 | 0.81109 | 30.01479 | 0.01479 | 0.00026 | 258 | 1.62666 |
| Pole Tip 4 | 0.81607 | 210.10301 | 0.10301 | 0.00180 | 1798 |  |
| Pole Tip 5 | 0.81538 | 330.14457 | 0.14457 | 0.00252 | 2523 | 1.62647 |
| Pole Tip 6 | 0.81174 | 150.13739 | 0.13739 | 0.00240 | 2398 |  |
|  |  | Gap Nominal (0.3378) | Terminal Side | Non Terminal Side |  |  |
|  |  | 3-5 | 0.33619 | 0.33751 |  |  |
|  |  | 4-6 | 0.33644 | 0.33774 |  |  |

|  | Clocked to Pole 3, rotated -30° nominally |  |
| --- | --- | --- |
| Terminal Side | Radial Distance (0.8125) | Actual Angle of Pole w.r.t CSY | Deviation Angle to Pole (act-nom) | Radians | Micro Radians | Pole Tip Distance (1.625) |
| Pole Tip 1 | 0.81098 | 89.98515 | -0.01485 | -0.00026 | 259 | 1.62236 |
| Pole Tip 2 | 0.81094 | 270.26483 | 0.26483 | 0.00462 | 4622 |  |
| Pole Tip 3 | 0.81075 | 30.00000 | 0.00000 | 0.00000 | 0 | 1.62635 |
| Pole Tip 4 | 0.81542 | 210.08349 | 0.08349 | 0.00146 | 1457 |  |
| Pole Tip 5 | 0.81471 | 330.20096 | 0.20096 | 0.00351 | 3507 | 1.62547 |
| Pole Tip 6 | 0.81138 | 150.09870 | 0.09870 | 0.00172 | 1723 |  |
| Non Terminal Side | Radial Distance (0.8125) | Actual Angle of Pole w.r.t CSY | Deviation Angle to Pole (act-nom) | Radians | Micro Radians | Pole Tip Distance (1.625) |
| Pole Tip 1 | 0.81141 | 90.02807 | 0.02807 | 0.00049 | 490 | 1.62356 |
| Pole Tip 2 | 0.81059 | 270.21329 | 0.21329 | 0.00372 | 3723 |  |
| Pole Tip 3 | 0.81109 | 30.00799 | 0.00799 | 0.00014 | 139 | 1.62666 |
| Pole Tip 4 | 0.81607 | 210.09621 | 0.09621 | 0.00168 | 1679 |  |
| Pole Tip 5 | 0.81538 | 330.13778 | 0.13778 | 0.00240 | 2405 | 1.62647 |
| Pole Tip 6 | 0.81174 | 150.13060 | 0.13060 | 0.00228 | 2279 |  |
|  |  | Gap Nominal (0.3378) | Terminal Side | Non Terminal Side |  |  |
|  |  | 3-5 | 0.33619 | 0.33751 |  |  |
|  |  | 4-6 | 0.33644 | 0.33774 |  |  |

# Text boxes

180°

90°

0°

+Y

270°

270°

+X

90°

0°

+Y

+Z

180°

+Y

+X

+X

270°

180°

90°

0°

+Y

+X

+Y