QC3 Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Cherrill Spencer |
| Date: | Wednesday, April 09, 2008 |
| Work Order/Charge No.: | 1111143 |
| Serial Number: | QC3 |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/CHERRILL SPENCER/QC3.PDF |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Top Plane (+Y) of the Magnet (Top most surface).

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Back View (Looking from upstream side –Z) | Side View (looking from –X side) |
| --- | --- |

Tooling Ball Locations

| Tooling Ball | X | Y | Z |
| --- | --- | --- | --- |
| TB 1 | -9.86913 | 1.58922 | -7.37043 |
| TB 2 | -9.87028 | 1.58966 | 7.35011 |
| TB 3 | -7.17313 | 5.08962 | 4.13867 |
| TB 4 | -7.16787 | 5.09117 | -4.18066 |
| TB 5 | -1.60260 | 9.87313 | -7.36915 |
| TB 6 | -1.60538 | 9.87194 | 7.34844 |
| TB 7 | 1.57893 | 9.87330 | 7.34911 |
| TB 8 | 1.58237 | 9.87250 | -7.36892 |
| TB 9 | 7.16487 | 5.08915 | -4.18049 |
| TB 10 | 7.16397 | 5.08932 | 4.15874 |
| TB 11 | 9.86642 | 1.59377 | 7.34863 |
| TB 12 | 9.86781 | 1.59381 | -7.37132 |

Pole Tip Additional Data

*Data looking from Downstream End (+Z End) **Revised correctly per C. Spencer 5/6/08)

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 1.96992 | 1.96906 | 0.85141 | 0.85105 | 0.85170 | 0.85079 |
| Upstream End (-Z) | 1.96933 | 1.96988 | 0.85130 | 0.85103 | 0.85176 | 0.85137 |

# Text boxes

+Y

+Z

+Y

+X

**Photo of QP2A, Not QC3