QP2A Quadrupole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Cherrill Spencer |
| Date: | Wednesday, April 09, 2008 |
| Work Order/Charge No.: | 1111143 |
| Serial Number: | QP2A |
| URL of Fiducial Report: | http://www-group.slac.stanford.edu/met/Quality/FIDUCIAL REPORTS/CHERRILL SPENCER/QP2A.PDF |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric axis of the poles of the magnet.

Planar Alignment

- Top Plane (+Y) of the Magnet (Top most surface).

“Z” Zero

- Mid-plane of the magnet (middle of upstream and downstream ends).

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Back View (Looking from upstream side –Z) | Side View (looking from –X side) |
| --- | --- |

Tooling Ball Locations

| Tooling Ball | X | Y | Z |
| --- | --- | --- | --- |
| TB 1 | -9.88008 | 1.64207 | -7.35267 |
| TB 2 | -9.87824 | 1.64368 | 7.36262 |
| TB 3 | -7.15722 | 5.13769 | 4.17136 |
| TB 4 | -7.12664 | 5.13582 | -4.15118 |
| TB 5 | -1.51839 | 9.86381 | -7.35722 |
| TB 6 | -1.51791 | 9.86547 | 7.35805 |
| TB 7 | 1.65478 | 9.86474 | 7.35772 |
| TB 8 | 1.65404 | 9.86857 | -7.35662 |
| TB 9 | 7.19454 | 5.04300 | -4.16831 |
| TB 10 | 7.18494 | 5.04085 | 4.16819 |
| TB 11 | 9.87808 | 1.53397 | 7.35481 |
| TB 12 | 9.87436 | 1.53186 | -7.35815 |

Pole Tip Additional Data

*Data looking from Downstream End (+Z End)

| Side | Pole Dist A-C | Pole Dist B-D | Gap 1 | Gap 2 | Gap 3 | Gap 4 |
| --- | --- | --- | --- | --- | --- | --- |
| Downstream End (+Z) | 1.96975 | 1.97028 | 0.84895 | 0.85155 | 0.85360 | 0.85062 |
| Upstream End (-Z) | 1.97016 | 1.96955 | 0.84858 | 0.85141 | 0.85334 | 0.85114 |

# Text boxes

+Y

+Z

+Y

+X