NLCTA Dipole Magnet

FIDUCIALIZATION REPORT

Inspector: 	Keith Caban

Engineer: 	Jim Spencer

Date: 		09/13/05

Charge No:	12-1410-1

Mag. S/N:	B

Fiducialization Coordinate System Set Up:

Magnet is set on 2 granite parallels as displayed in the photo below.

SIDE VIEW

Z zero is set by the mid-plane of these 2 surfaces.

(Distance width = 6.0085”)

“B” Exit View                                ZOOM “B” Exit View

X & Y zero shown, with X offset 1.000” in +X

off of “True Magnet Center”.

---- Dashed Green line is Mechanical Magnet Centerline

3-D VIEW

Tooling Ball Fiducials

- using ½” Diameter Tooling Balls w/ 1” Extension

Coordinates of Solid Green (Beam)

| TB | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00049 | 0.49793 | 5.04788 | 9.50555 | -2.50520 |
| TB 2 | 0.00047 | 0.49724 | -7.03506 | 9.50644 | -2.49774 |
| TB 3 | 0.00017 | 0.49926 | -7.01313 | 9.50743 | 2.47936 |
| TB 4 | 0.00025 | 0.49827 | 5.04212 | 9.50313 | 2.48223 |

ANGLE OF LARGE TRIANGLE = 37.24°

# Text boxes

TB 4

TB 3

TB 2

+Z

+Y

+X

+1.000” OFFSET +X

+Z

+X

+Y

+Y

TB 1

+Z

+X