NLCTA Dipole Magnet

FIDUCIALIZATION REPORT

Inspector: 	Keith Caban

Engineer: 	Jim Spencer

Date: 		09/13/05

Charge No:	12-1410-1

Mag. S/N:	B

Fiducialization Coordinate System Set Up:

Magnet is set on 2 granite parallels as displayed in the photo below.

SIDE VIEW

Z zero is set by the mid-plane of these 2 surfaces.

(Distance width = 6.0085”)

Back Exit View                           ZOOM Back/Exit View

X & Y zero shown, with X offset -1.000” in -X (Aisle Side)

off of “True Magnet Center”.

---- Dashed Green is Mechanical Centerline

3-D VIEW

Tooling Ball Fiducials

- using ½” Diameter Tooling Balls w/ 1” Extension

| TB | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00049 | 0.49793 | -5.04788 | 9.50555 | -2.50520 |
| TB 2 | 0.00047 | 0.49724 | 7.03506 | 9.50644 | -2.49774 |
| TB 3 | 0.00017 | 0.49926 | 7.01313 | 9.50743 | 2.47936 |
| TB 4 | 0.00025 | 0.49827 | -5.04212 | 9.50313 | 2.48223 |

ANGLE OF LARGE TRIANGLE = 37.24°

# Text boxes

TB 3

TB 4

TB 1

+Z

+Y

+X

-1.000” OFFSET –X

(Solid Green)

+Z

+X

+Y

+Y

TB 2

+Z

+X