E163 Gun Spectrometer

FIDUCIALIZATION REPORT

Inspector: 	Keith Caban

Engineer: 	Jim Spencer

Date: 		06/10/05

Charge No:	12-1410-1

Mag. S/N:	N/A

Fiducialization Coordinate System Set Up:

Magnet is set on 2 granite parallels as displayed in the photo below.

SIDE VIEW

Z zero is set by the mid-plane of these 2 surfaces.

(Distance width = 6.2552”)

FRONT

X zero is set by the mid-plane of these 2 surfaces.

(Distance between = 1.5740”)

ZOOM FRONT VIEW

Y zero is the bottom of Triangular plates (2 ea) plane shifted up (green line) 1.500”.  (Dist from Green Line to bottom where Granite Parallels = 3.060”)

3-D VIEW

Tooling Ball Fiducials

- using ½” Diameter Tooling Balls w/ 1” Extension

TB’S A - D

TB C & D ON OPPOSITE SIDE

| TB | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00030 | 0.49708 | -5.50796 | -2.80649 | -2.24880 |
| TB B | 0.00038 | 0.49731 | -5.50348 | -2.77013 | 2.27880 |
| TB C | 0.00048 | 0.49797 | 5.50324 | -2.41333 | 2.44159 |
| TB D | 0.00021 | 0.49870 | 5.49870 | -2.31543 | -2.26850 |

TB’S E - H

| TB | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB E | 0.00053 | 0.49804 | 3.43368 | 8.45147 | -2.07726 |
| TB F | 0.00029 | 0.49977 | 3.37223 | 8.45125 | 2.11399 |
| TB G | 0.00054 | 0.49777 | -3.25546 | 8.44859 | 2.53822 |
| TB H | 0.00056 | 0.49726 | -3.35994 | 8.45149 | -2.60550 |

# Text boxes

+Z

-X

+Y

+Z