Fiducialization of Big Green Magnets

Spatial Alignment – Plane taken from 4 points at the outer corners of the bottom surface of the lower inner surface. Determines the direction of the Y axis

Planar Alignment – From an axis taken on the outside of the lower half of the magnet below the parting line. Determines the direction of the Z axis

Origin in Z – Symmetry point between the ends of the magnet.

Origin in Y - Symmetry plane between the top and bottom inner surfaces.

Origin in X – Symmetry point between two points on the outside of the lower half of the magnet.

Aperture width measurements – The reported aperture opening widths are reported normal to the bottom inner surface which is the spatial alignment for the reference coordinate system.

Magnet 15-D-12

X		Y		Z		WIDTH

Tooling Ball  		8.9940		7.5637		-14.4875

Tooling Ball B	9.0046		7.5638		15.4813

Tooling Ball C	-8.9850	7.5616		-14.4814

Tooling Ball D	-8.9745	7.5594		15.4892

Width near A		3.0018				-17.5590	3.0018

Width near B		3.3216				18.1195	3.0028

Width near C 		-4.2014			-18.0185	3.0016

Width near D		-3.6460			18.1136	3.0032