LCLS Accelerator Support Structure

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Jose Chan |
| Date: | Wednesday, July 12, 2006 |
| Work Order/Charge No.: | 92-4215-4 |
| Serial Number | not yet assembled |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Lid of base

Spatial Alignment

- A line on the top part of the base

  - +X goes towards TB 1 side

“X” & “Y” Zero

- ID Cylinder of stainless diameter

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00100 | 0.49660 | 2.77731 | 3.86759 | -1.01765 |
| TB 2 | 0.00041 | 0.49768 | -2.77191 | 3.86536 | -1.04685 |

# Text boxes

TB 1

TB 2

TB 3

TB 4

X+

+Z

+X

A

B

C

D

View From +Z

Y+