LCLS Accelerator Support Structure

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Jose Chan |
| Date: | Thursday, August 03, 2006 |
| Work Order/Charge No.: | 92-4215-4 |
| Serial Number | 591 |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of Both End Flanges

Spatial Alignment

- A line on the inside right rectangle flange. (TB 1 SIDE)

  - +Y goes towards TB 1 side

“X” & “Y” Zero

- OD of End Flanges, 2 circles create beamline axis.

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.0005 | 0.4973 | 2.7613 | 3.8673 | 58.4971 |
| TB 2 | 0.0002 | 0.4990 | -2.7881 | 3.8671 | 58.5516 |

Additional Measurements

Overall Length: 123.0739

Parallelism between end flanges: 0.0130

Overall Straightness of accelerator sections (5 – 84): 0.0823

| Accelerator Sections | Straightness |
| --- | --- |
| 5-10 | 0.0035 |
| 11-20 | 0.0046 |
| 21-30 | 0.0065 |
| 31-40 | 0.0107 |
| 41-50 | 0.0059 |
| 51-60 | 0.0042 |
| 61-70 | 0.0091 |
| 71-80 | 0.0086 |
| 81-84 | 0.0027 |

# Text boxes

TB 1

TB 2

X+

+Z

+X

Y+