LCLS BC 1 Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Jose Chan |
| Date: | Wednesday, August 30, 2006 |
| Work Order/Charge No.: | 92-4223-2 |
| Serial Number: | 001078 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS BC1 MAGNETS\LCLS BC1 001078.pdf |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the magnet

Spatial Alignment

  - Top of magnet where label is.

“Z” Zero

- Mid-Plane of the magnet.

“X” & “Y” Zero

- X zero is created by the symmetry point of the inner stainless steel where coils lie.

    - Both ends of both sides.

      - Create lines which is y axis.

        - This Creates X- zero

- Symmetry of pole planes

  - This creates Y- zero

Tooling Ball Measurements/Locations

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00136 | 0.49453 | 6.04552 | 5.67027 | 2.52974 |
| TB 2 | 0.00075 | 0.49736 | 6.04751 | 5.67027 | -2.52954 |
| TB 3 | 0.00154 | 0.49442 | -6.02812 | 5.67595 | -2.53652 |
| TB 4 | 0.00433 | 0.49035 | -6.03246 | 5.67745 | 2.52710 |

# Text boxes

+Z

+X

+Y

+Y

+Z

+X