LCLS BFW WIRECARD ASSY

INSPECTION/FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Don Schafer |
| Date: | Thursday, September 25, 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 03 / VC – 03 / WC – 03 / BASE – 06 |
| Units of Measure: | Metric – Millimeters (mm.) |
| URL | http://www-group/met/Quality/FIDUCIAL%20REPORTS/LCLS%20BFW/BFW-03_VC-03_WC-03_BAS-06.pdf |

Coordinate System Setups

Bench CSY (BENCH$CSY)

(The only CSY in Both States of measurement - out and under vacuum)

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Bench Tooling Ball CSY (BTB$CSY)

- Create a plane using Tooling Balls 1, 2, & 3

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 2 to 1 (+X)

  - This is the planar alignment

- TB 2 is a single point that sets zero in X, Y, Z.

BFW Tooling Ball CSY (BFWTB$CSY)

- Create a plane using Tooling Balls 5, 6, & 7

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 6 to 5 (+X)

  - This is the planar alignment

- TB 6 is a single point that sets zero in X, Y, Z.

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

Wire CSY (WIRE$CSY)

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Wire offset from Edges per T. Nakashima’s Optical Measurement

| Wire | Wire Location | Wire Diameter |
| --- | --- | --- |
| Vertical Wire (X Location from Card) | 39.6287 | 0.0383 |
| Horizontal Wire (Y Location from Card) | 37.0203 | 0.0376 |

Support Stand CSY (BASE$CSY)

- A plane on Torque Fixture sets Zero in Y and is the Spatial Alignment

- The symmetry of the outer surfaces where “X” fine adjustments are sets zero in X.

- A line where the Torque Fixture 2X Dowel pins sets zero in Z and is the Planar Alignment.

Beamline CSY (BEAMLINE$CSY)

- Use the BENCH$CSY setup except use the Torque Fixture plate to set zero in Y and the Spatial Alignment, transform +258.67 in Y to replicate Theoretical Beamline Center

- This coordinate system will tell us where the Wire Crosshairs are to a theoretical Beam Centerline.

- The wires should be offset ~ -0.400 in X, -0.200 in Y.

Statistical Data (mm.)

Out of Vacuum

10 Cycles (10 recordings)

Card Locations  
CSY = BENCH$CSY

| STATS | X-POS CARD | X-INTPT CARD | Y-INTPT CARD |
| --- | --- | --- | --- |
| AVG. | 0.01326 | -40.11954 | -95.13720 |
| Range | 0.04735 | 0.05499 | 0.00608 |
| St. Dev. | 0.01757 | 0.02048 | 0.00181 |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.40989 | -0.21438 |
| Range | 0.04713 | 0.00765 |
| St. Dev. | 0.01751 | 0.00243 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.40989 | -58.21438 | -2.89980 | -0.12745 | 89.78871 | 90.01833 |
| Range | 0.04713 | 0.00765 | 0.02342 | 0.01166 | 0.00722 | 0.00300 |
| St. Dev. | 0.01751 | 0.00243 | 0.00845 | 0.00460 | 0.00242 | 0.00096 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Transformation WIRE$CSY to BFWTB$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | 94.67784 | -160.26242 | 35.96923 | 0.11984 | 89.69677 | 90.09755 |
| Range | 0.00108 | 0.00073 | 0.00495 | 0.00054 | 0.00176 | 0.00171 |
| St. Dev. | 0.00030 | 0.00022 | 0.00137 | 0.00019 | 0.00062 | 0.00053 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Under Vacuum

10 Cycles (10 recordings)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 94.27405 | 101.62454 | -38.78624 |
| Range | 0.00511 | 0.00622 | 0.00280 |
| St. Dev. | 0.00172 | 0.00209 | 0.00097 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.60207 | 102.41988 | -38.08367 |
| Range | 0.00488 | 0.00589 | 0.00300 |
| St. Dev. | 0.00175 | 0.00202 | 0.00103 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -51.09174 | 102.33596 | 67.57591 |
| Range | 0.00396 | 0.00329 | 0.00193 |
| St. Dev. | 0.00135 | 0.00105 | 0.00074 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 51.49622 | 101.92488 | 67.21906 |
| Range | 0.00480 | 0.00335 | 0.00283 |
| St. Dev. | 0.00161 | 0.00131 | 0.00093 |
| RMS Tol | 0.06500 | 0.03000 | - |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.46754 | -0.27058 |
| Range | 0.01222 | 0.00148 |
| St. Dev. | 0.00494 | 0.00044 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.46591 | -58.20675 | -2.31692 | -0.12148 | 89.64268 | 89.88341 |
| Range | 0.01222 | 0.00148 | 0.00149 | 0.00293 | 0.00037 | 0.00149 |
| St. Dev. | 0.00494 | 0.00044 | 0.00042 | 0.00121 | 0.00012 | 0.00054 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Locations of ¼-20 Jo-Plugs Cylinders Intersected into Plane projected 12.7mm away from surface replicating a ½” (12.7mm) offset to center of Tooling Ball.

CSY = BEAMLINE$CSY

| INTPT | X | Y | Z |
| --- | --- | --- | --- |
| 1 | -26.84823 | 227.58876 | 68.58090 |
| 2 | 27.16408 | 227.57033 | 68.44907 |
| 3 | 79.61346 | 180.07157 | -68.67904 |
| 4 | -80.01894 | 180.14357 | -68.28114 |

# Text boxes

Y+

+Z

Z+

Y+

+X

+Y

X+

Transformation