LCLS BFW WIRECARD ASSY

INSPECTION/FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Don Schafer |
| Date: | Friday, August 15, 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 08 / VC – 08 / WC – 08 / BASE – 28 |
| Units of Measure: | Metric – Millimeters (mm.) |
| URL | http://www-group/met/Quality/FIDUCIAL%20REPORTS/LCLS%20BFW/BFW-08_VC-08_WC-08_BAS-28.pdf |

Coordinate System Setups

Bench CSY (BENCH$CSY)

(The only CSY in Both States of measurement - out and under vacuum)

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Bench Tooling Ball CSY (BTB$CSY)

- Create a plane using Tooling Balls 1, 2, & 3

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 2 to 1 (+X)

  - This is the planar alignment

- TB 2 is a single point that sets zero in X, Y, Z.

BFW Tooling Ball CSY (BFWTB$CSY)

- Create a plane using Tooling Balls 5, 6, & 7

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 6 to 5 (+X)

  - This is the planar alignment

- TB 6 is a single point that sets zero in X, Y, Z.

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

Wire CSY (WIRE$CSY)

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Wire offset from Edges per T. Nakashima’s Optical Measurement

| Wire | Wire Location | Wire Diameter |
| --- | --- | --- |
| Vertical Wire (X Location from Card) | 39.6111 | 0.0372 |
| Horizontal Wire (Y Location from Card) | 37.0048 | 0.0403 |

Support Stand CSY (BASE$CSY)

- A plane on Torque Fixture sets Zero in Y and is the Spatial Alignment

- The symmetry of the outer surfaces where “X” fine adjustments are sets zero in X.

- A line where the Torque Fixture 2X Dowel pins sets zero in Z and is the Planar Alignment.

Beamline CSY (BEAMLINE$CSY)

- Use the BENCH$CSY setup except use the Torque Fixture plate to set zero in Y and the Spatial Alignment, transform +258.67 in Y to replicate Theoretical Beamline Center

- This coordinate system will tell us where the Wire Crosshairs are to a theoretical Beam Centerline.

- The wires should be offset ~ -0.400 in X, -0.200 in Y.

Statistical Data (mm.)

Out of Vacuum

10 Cycles (10 recordings)

Card Locations  
CSY = BENCH$CSY

| STATS | X-POS CARD | X-INTPT CARD | Y-INTPT CARD |
| --- | --- | --- | --- |
| AVG. | -0.02551 | -40.05650 | -95.17795 |
| Range | 0.00515 | 0.00643 | 0.00300 |
| St. Dev. | 0.00154 | 0.00202 | 0.00113 |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.44746 | -0.18284 |
| Range | 0.00499 | 0.00250 |
| St. Dev. | 0.00150 | 0.00076 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.44746 | -58.18284 | -2.85268 | 0.00249 | 89.92657 | 89.92548 |
| Range | 0.00499 | 0.00250 | 0.01220 | 0.00235 | 0.00280 | 0.00567 |
| St. Dev. | 0.00150 | 0.00076 | 0.00366 | 0.00087 | 0.00095 | 0.00175 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Transformation WIRE$CSY to BFWTB$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | 94.61596 | -160.33683 | 35.79886 | 0.01711 | 89.71551 | 89.83942 |
| Range | 0.00520 | 0.00114 | 0.00453 | 0.00150 | 0.00150 | 0.00242 |
| St. Dev. | 0.00200 | 0.00037 | 0.00159 | 0.00054 | 0.00055 | 0.00072 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Under Vacuum

10 Cycles (10 recordings)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 93.90808 | 102.13841 | -37.97516 |
| Range | 0.00578 | 0.00395 | 0.00751 |
| St. Dev. | 0.00201 | 0.00145 | 0.00269 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.97127 | 102.13761 | -38.09542 |
| Range | 0.00573 | 0.00320 | 0.00764 |
| St. Dev. | 0.00200 | 0.00114 | 0.00250 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -51.93104 | 102.01792 | 67.76990 |
| Range | 0.00270 | 0.00191 | 0.00434 |
| St. Dev. | 0.00088 | 0.00066 | 0.00143 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 50.67392 | 102.02228 | 67.83741 |
| Range | 0.00384 | 0.00422 | 0.00377 |
| St. Dev. | 0.00115 | 0.00139 | 0.00142 |
| RMS Tol | 0.06500 | 0.03000 | - |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.36487 | -0.24978 |
| Range | 0.00339 | 0.00189 |
| St. Dev. | 0.00097 | 0.00064 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.37476 | -58.23975 | -2.41576 | 0.01797 | 89.77951 | 89.87671 |
| Range | 0.00338 | 0.00189 | 0.00265 | 0.00217 | 0.00096 | 0.00449 |
| St. Dev. | 0.00097 | 0.00064 | 0.00073 | 0.00064 | 0.00028 | 0.00157 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Locations of ¼-20 Jo-Plugs Cylinders Intersected into Plane projected 12.7mm away from surface replicating a ½” (12.7mm) offset to center of Tooling Ball.

CSY = BEAMLINE$CSY

| INTPT | X | Y | Z |
| --- | --- | --- | --- |
| 1 | -26.94432 | 227.50002 | 68.60144 |
| 2 | 27.03304 | 227.48825 | 68.55532 |
| 3 | 79.73340 | 180.23831 | -68.53984 |
| 4 | -79.96120 | 180.29532 | -68.39897 |

# Text boxes

Y+

+Z

Z+

Y+

+X

+Y

X+

Transformation