LCLS BFW WIRECARD ASSY

INSPECTION/FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Venkat Srinivasan |
| Date: | Friday, June 13 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 12 / VC – 12 / WC – 12 / BASE – 17 |
| Units of Measure: | Metric – Millimeters (mm.) |
| URL | http://www-group/met/Quality/FIDUCIAL%20REPORTS/LCLS%20BFW/BFW-12_VC-12_WC-12_BAS-17.pdf |

Coordinate System Setups

Bench CSY (BENCH$CSY)

(The only CSY in Both States of measurement - out and under vacuum)

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Bench Tooling Ball CSY (BTB$CSY)

- Create a plane using Tooling Balls 1, 2, & 3

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 2 to 1 (+X)

  - This is the planar alignment

- TB 2 is a single point that sets zero in X, Y, Z.

BFW Tooling Ball CSY (BFWTB$CSY)

- Create a plane using Tooling Balls 5, 6, & 7

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 6 to 5 (+X)

  - This is the planar alignment

- TB 6 is a single point that sets zero in X, Y, Z.

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

Wire CSY (WIRE$CSY)

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Wire offset from Edges per T. Nakashima’s Optical Measurement

| Wire | Wire Location | Wire Diameter |
| --- | --- | --- |
| Vertical Wire (X Location from Card) | 39.5963 | 0.0376 |
| Horizontal Wire (Y Location from Card) | 36.9908 | 0.0413 |

Support Stand CSY (BASE$CSY)

- A plane on Torque Fixture sets Zero in Y and is the Spatial Alignment

- The symmetry of the outer surfaces where “X” fine adjustments are sets zero in X.

- A line where the Torque Fixture 2X Dowel pins sets zero in Z and is the Planar Alignment.

Beamline CSY (BEAMLINE$CSY)

- Use the BENCH$CSY setup except use the Torque Fixture plate to set zero in Y and the Spatial Alignment, transform +258.67 in Y to replicate Theoretical Beamline Center

- This coordinate system will tell us where the Wire Crosshairs are to a theoretical Beam Centerline.

- The wires should be offset ~ -0.400 in X, -0.200 in Y.

Statistical Data (mm.)

Out of Vacuum

10 Cycles (10 recordings)

Date: 06/02/08

Card Locations  
CSY = BENCH$CSY

| STATS | X-POS CARD | X-INTPT CARD | Y-INTPT CARD |
| --- | --- | --- | --- |
| AVG. | 0.01668 | -40.16612 | -95.40390 |
| Range | 0.01713 | 0.02422 | 0.00779 |
| St. Dev. | 0.00601 | 0.00726 | 0.00254 |

Wire Location

NOTE: Device was not cycled 10 times prior to vacuum. This measurement method was added on all devices after BFW #12 (Count #5). This does not affect the functionality of the device since BFW translation data is accurately recorded before vacuum, and BFW position and repeatability data are recorded after vacuum

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.42173 | -58.61506 | -3.03308 | -0.28261 | 90.02656 | 89.60155 |
| Range | 0.01717 | 0.00917 | 0.04540 | 0.00914 | 0.01114 | 0.00423 |
| St. Dev. | 0.00596 | 0.00303 | 0.01404 | 0.00284 | 0.00341 | 0.00123 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Transformation WIRE$CSY to BFWTB$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | 94.38934 | -160.79138 | 35.62403 | -0.13668 | 89.83456 | 89.82401 |
| Range | 0.00595 | 0.00611 | 0.02598 | 0.00475 | 0.00623 | 0.00292 |
| St. Dev. | 0.00168 | 0.00199 | 0.00756 | 0.00132 | 0.00179 | 0.00086 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Under Vacuum

200 Cycles (14 recordings)

Date: 06/03/08 (Did not pass RMS)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 94.38209 | 102.09440 | -38.37162 |
| Range | 0.10018 | 0.19281 | 0.05689 |
| St. Dev. | 0.03272 | 0.07647 | 0.01984 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.49539 | 102.33838 | -37.55954 |
| Range | 0.09997 | 0.13242 | 0.02661 |
| St. Dev. | 0.03272 | 0.05230 | 0.00751 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -50.90705 | 102.23077 | 68.09083 |
| Range | 0.10472 | 0.03820 | 0.02603 |
| St. Dev. | 0.04092 | 0.01486 | 0.00724 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 51.66240 | 102.10535 | 67.64517 |
| Range | 0.10416 | 0.13559 | 0.03968 |
| St. Dev. | 0.04084 | 0.05455 | 0.01515 |
| RMS Tol | 0.06500 | 0.03000 | - |

Wire Location

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.16137 | -58.59492 | -2.40223 | -0.21368 | 89.85858 | 89.57545 |
| Range | 0.37711 | 0.03681 | 0.01153 | 0.09862 | 0.01233 | 0.02012 |
| St. Dev. | 0.14489 | 0.01465 | 0.00345 | 0.03904 | 0.00456 | 0.00652 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Note: After this test the device was put on hold per Venkat Srinivasan.  It was decided not to do the 200 rigorous cycles, therefore, changing our cycle testing format.

New Vacuum Testing Format

- 10 Continuous cycles and Record Data.

- After each cycle to the “Down Position,” wait 1 minute before cycling the device to take another reading.

- This has been ratified by LCLS Physics. Actual usage in the field will tend to be sporadic. As per Heinz-Dieter Nuhn, a single BFW may be used as little as once a week. This suggests that repeated pounding with cycling time of less than 1 second may not correspond with accurate simulation of actual usage patterns. Further, the device has shown degraded performance under such repeated fast cycling conditions. For further explanations, contact Venkat Srinivasan (SLAC, 650-926-2631) or Jim Bailey (Argonne, 630-252-5306)

Under Vacuum (New Vacuum Testing Format)

10 Cycles (10 recordings)

Date: 06/06/08 (Passes RMS)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 94.33196 | 102.38456 | -38.32288 |
| Range | 0.05302 | 0.06716 | 0.03526 |
| St. Dev. | 0.01849 | 0.02199 | 0.01159 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.54507 | 102.87021 | -37.44166 |
| Range | 0.05268 | 0.04891 | 0.03780 |
| St. Dev. | 0.01835 | 0.01565 | 0.01444 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -50.91331 | 102.68316 | 68.19318 |
| Range | 0.03940 | 0.01828 | 0.02349 |
| St. Dev. | 0.01132 | 0.00561 | 0.00887 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 51.65781 | 102.43699 | 67.70747 |
| Range | 0.03953 | 0.04645 | 0.02118 |
| St. Dev. | 0.01136 | 0.01510 | 0.00627 |
| RMS Tol | 0.06500 | 0.03000 | - |

Under Vacuum (New Vacuum Testing Format) Cont…

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.40433 | -0.18282 |
| Range | 0.11261 | 0.00886 |
| St. Dev. | 0.03133 | 0.00259 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Locations of ¼-20 Jo-Plugs Cylinders Intersected into Plane projected 12.7mm away from surface replicating a ½” (12.7mm) offset to center of Tooling Ball.

CSY = BEAMLINE$CSY

| INTPT | X | Y | Z |
| --- | --- | --- | --- |
| 1 | -27.10957 | 227.52515 | 68.78973 |
| 2 | 26.92714 | 227.53492 | 68.74626 |
| 3 | 79.70496 | 180.44321 | -68.40215 |
| 4 | -79.98042 | 180.33467 | -68.26046 |

# Text boxes

Y+

+Z

Z+

Y+

+X

+Y

X+

Transformation