LCLS BFW WIRECARD ASSY

INSPECTION/FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Venkat Srinivasan |
| Date: | Monday, July 07, 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 17 / VC – 17 / WC – 17 / BASE – 20 |
| Units of Measure: | Metric – Millimeters (mm.) |
| URL | http://www-group/met/Quality/FIDUCIAL%20REPORTS/LCLS%20BFW/BFW-17_VC-17_WC-17_BAS-20.pdf |

Coordinate System Setups

Bench CSY (BENCH$CSY)

(The only CSY in Both States of measurement - out and under vacuum)

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Bench Tooling Ball CSY (BTB$CSY)

- Create a plane using Tooling Balls 1, 2, & 3

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 2 to 1 (+X)

  - This is the planar alignment

- TB 2 is a single point that sets zero in X, Y, Z.

BFW Tooling Ball CSY (BFWTB$CSY)

- Create a plane using Tooling Balls 5, 6, & 7

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 6 to 5 (+X)

  - This is the planar alignment

- TB 6 is a single point that sets zero in X, Y, Z.

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

Wire CSY (WIRE$CSY)

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Wire offset from Edges per T. Nakashima’s Optical Measurement

| Wire | Wire Location | Wire Diameter |
| --- | --- | --- |
| Vertical Wire (X Location from Card) | 39.6090 | 0.0345 |
| Horizontal Wire (Y Location from Card) | 37.0163 | 0.0390 |

Support Stand CSY (BASE$CSY)

- A plane on Torque Fixture sets Zero in Y and is the Spatial Alignment

- The symmetry of the outer surfaces where “X” fine adjustments are sets zero in X.

- A line where the Torque Fixture 2X Dowel pins sets zero in Z and is the Planar Alignment.

Beamline CSY (BEAMLINE$CSY)

- Use the BENCH$CSY setup except use the Torque Fixture plate to set zero in Y and the Spatial Alignment, transform +258.67 in Y to replicate Theoretical Beamline Center

- This coordinate system will tell us where the Wire Crosshairs are to a theoretical Beam Centerline.

- The wires should be offset ~ -0.400 in X, -0.200 in Y.

Statistical Data (mm.)

Out of Vacuum

10 Cycles (10 recordings)

Card Locations  
CSY = BENCH$CSY

| STATS | X-POS CARD | X-INTPT CARD | Y-INTPT CARD |
| --- | --- | --- | --- |
| AVG. | 0.05958 | -40.04379 | -95.16616 |
| Range | 0.00314 | 0.00491 | 0.00266 |
| St. Dev. | 0.00108 | 0.00189 | 0.00084 |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.37419 | -0.23541 |
| Range | 0.00323 | 0.00159 |
| St. Dev. | 0.00117 | 0.00050 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.37419 | -58.23541 | -2.42617 | -0.10720 | 89.81564 | 89.85133 |
| Range | 0.00323 | 0.00159 | 0.00299 | 0.00194 | 0.00975 | 0.00420 |
| St. Dev. | 0.00117 | 0.00050 | 0.00073 | 0.00064 | 0.00309 | 0.00116 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Transformation WIRE$CSY to BFWTB$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | 94.02384 | -160.48165 | 35.74591 | -0.12745 | 89.75476 | 89.96513 |
| Range | 0.00243 | 0.00163 | 0.00693 | 0.00213 | 0.01001 | 0.00353 |
| St. Dev. | 0.00067 | 0.00060 | 0.00192 | 0.00072 | 0.00323 | 0.00102 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Under Vacuum

10 Cycles (10 recordings)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 94.33756 | 102.32898 | -38.31896 |
| Range | 0.00827 | 0.01670 | 0.01946 |
| St. Dev. | 0.00244 | 0.00543 | 0.00613 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.54142 | 102.25380 | -37.89133 |
| Range | 0.00752 | 0.00908 | 0.13721 |
| St. Dev. | 0.00222 | 0.00245 | 0.04278 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -51.18543 | 102.25431 | 67.85645 |
| Range | 0.07893 | 0.08782 | 0.10230 |
| St. Dev. | 0.02494 | 0.02748 | 0.03192 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 51.40404 | 102.29719 | 67.61674 |
| Range | 0.07823 | 0.08463 | 0.01958 |
| St. Dev. | 0.02472 | 0.02605 | 0.00600 |
| RMS Tol | 0.06500 | 0.03000 | - |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.38864 | -0.16323 |
| Range | 0.01813 | 0.00950 |
| St. Dev. | 0.00573 | 0.00298 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.37345 | -58.19657 | -2.38341 | -0.10511 | 89.76557 | 89.83373 |
| Range | 0.02880 | 0.02079 | 0.08992 | 0.00294 | 0.05330 | 0.04737 |
| St. Dev. | 0.00967 | 0.00648 | 0.02781 | 0.00107 | 0.01650 | 0.01482 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Locations of ¼-20 Jo-Plugs Cylinders Intersected into Plane projected 12.7mm away from surface replicating a ½” (12.7mm) offset to center of Tooling Ball.

CSY = BEAMLINE$CSY

| INTPT | X | Y | Z |
| --- | --- | --- | --- |
| 1 | -26.97780 | 227.55583 | 68.57593 |
| 2 | 27.01996 | 227.54609 | 68.51281 |
| 3 | 79.70427 | 180.36654 | -68.58627 |
| 4 | -80.02980 | 180.34162 | -68.39091 |

# Text boxes

Y+

+Z

Z+

Y+

+X

+Y

X+

Transformation