LCLS BFW WIRECARD ASSY

INSPECTION/FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Don Schafer |
| Date: | Tuesday, July 29, 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 19 / VC – 19 / WC – 19 / BASE – 03 |
| Units of Measure: | Metric – Millimeters (mm.) |
| URL | http://www-group/met/Quality/FIDUCIAL%20REPORTS/LCLS%20BFW/BFW-19_VC-19_WC-19_BAS-03.pdf |

Coordinate System Setups

Bench CSY (BENCH$CSY)

(The only CSY in Both States of measurement - out and under vacuum)

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Bench Tooling Ball CSY (BTB$CSY)

- Create a plane using Tooling Balls 1, 2, & 3

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 2 to 1 (+X)

  - This is the planar alignment

- TB 2 is a single point that sets zero in X, Y, Z.

BFW Tooling Ball CSY (BFWTB$CSY)

- Create a plane using Tooling Balls 5, 6, & 7

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 6 to 5 (+X)

  - This is the planar alignment

- TB 6 is a single point that sets zero in X, Y, Z.

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

Wire CSY (WIRE$CSY)

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Wire offset from Edges per T. Nakashima’s Optical Measurement

| Wire | Wire Location | Wire Diameter |
| --- | --- | --- |
| Vertical Wire (X Location from Card) | 39.6009 | 0.0372 |
| Horizontal Wire (Y Location from Card) | 37.0069 | 0.0382 |

Support Stand CSY (BASE$CSY)

- A plane on Torque Fixture sets Zero in Y and is the Spatial Alignment

- The symmetry of the outer surfaces where “X” fine adjustments are sets zero in X.

- A line where the Torque Fixture 2X Dowel pins sets zero in Z and is the Planar Alignment.

Beamline CSY (BEAMLINE$CSY)

- Use the BENCH$CSY setup except use the Torque Fixture plate to set zero in Y and the Spatial Alignment, transform +258.67 in Y to replicate Theoretical Beamline Center

- This coordinate system will tell us where the Wire Crosshairs are to a theoretical Beam Centerline.

- The wires should be offset ~ -0.400 in X, -0.200 in Y.

Statistical Data (mm.)

Out of Vacuum

10 Cycles (10 recordings)

Card Locations  
CSY = BENCH$CSY

| STATS | X-POS CARD | X-INTPT CARD | Y-INTPT CARD |
| --- | --- | --- | --- |
| AVG. | 0.04666 | -40.15629 | -95.03599 |
| Range | 0.05641 | 0.08606 | 0.03026 |
| St. Dev. | 0.01558 | 0.02379 | 0.00920 |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.38210 | -0.23046 |
| Range | 0.05633 | 0.05473 |
| St. Dev. | 0.01556 | 0.01765 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.38210 | -58.23046 | -2.83327 | -0.27155 | 89.77791 | 89.82681 |
| Range | 0.05633 | 0.05473 | 0.12148 | 0.04474 | 0.09001 | 0.01399 |
| St. Dev. | 0.01556 | 0.01765 | 0.04399 | 0.01437 | 0.03130 | 0.00498 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Transformation WIRE$CSY to BFWTB$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | 94.82346 | -160.59171 | 35.98869 | 0.05633 | 89.65418 | 89.97070 |
| Range | 0.00269 | 0.00058 | 0.00191 | 0.00060 | 0.00118 | 0.00587 |
| St. Dev. | 0.00073 | 0.00018 | 0.00059 | 0.00017 | 0.00044 | 0.00182 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Under Vacuum

10 Cycles (10 recordings)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 94.39393 | 101.85985 | -38.65849 |
| Range | 0.01058 | 0.00690 | 0.01383 |
| St. Dev. | 0.00401 | 0.00209 | 0.00431 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.45293 | 102.90466 | -38.29262 |
| Range | 0.00978 | 0.00800 | 0.01455 |
| St. Dev. | 0.00356 | 0.00248 | 0.00559 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -51.15066 | 102.75271 | 67.44710 |
| Range | 0.00514 | 0.01212 | 0.01948 |
| St. Dev. | 0.00191 | 0.00364 | 0.00570 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 51.44829 | 102.15119 | 67.25690 |
| Range | 0.00506 | 0.01016 | 0.02350 |
| St. Dev. | 0.00187 | 0.00309 | 0.00709 |
| RMS Tol | 0.06500 | 0.03000 | - |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.44968 | -0.27661 |
| Range | 0.00365 | 0.00894 |
| St. Dev. | 0.00103 | 0.00256 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.44986 | -58.17968 | -2.35526 | -0.26105 | 89.60782 | 89.85737 |
| Range | 0.00365 | 0.00895 | 0.00257 | 0.00167 | 0.00236 | 0.00818 |
| St. Dev. | 0.00103 | 0.00256 | 0.00092 | 0.00055 | 0.00076 | 0.00281 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Locations of ¼-20 Jo-Plugs Cylinders Intersected into Plane projected 12.7mm away from surface replicating a ½” (12.7mm) offset to center of Tooling Ball.

CSY = BEAMLINE$CSY

| INTPT | X | Y | Z |
| --- | --- | --- | --- |
| 1 | -26.98472 | 227.63490 | 68.22628 |
| 2 | 27.04411 | 227.61757 | 68.22777 |
| 3 | 79.90804 | 180.10427 | -68.73710 |
| 4 | -79.80949 | 180.07941 | -68.73539 |

# Text boxes

Y+

+Z

Z+

Y+

+X

+Y

X+

Transformation