LCLS BFW WIRECARD ASSY

INSPECTION/FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Venkat Srinivasan |
| Date: | Thursday, July 17, 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 28 / VC – 28 / WC – 28 / BASE – 08 |
| Units of Measure: | Metric – Millimeters (mm.) |
| URL | http://www-group/met/Quality/FIDUCIAL%20REPORTS/LCLS%20BFW/BFW-28_VC-28_WC-28_BAS-08.pdf |

Coordinate System Setups

Bench CSY (BENCH$CSY)

(The only CSY in Both States of measurement - out and under vacuum)

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Bench Tooling Ball CSY (BTB$CSY)

- Create a plane using Tooling Balls 1, 2, & 3

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 2 to 1 (+X)

  - This is the planar alignment

- TB 2 is a single point that sets zero in X, Y, Z.

BFW Tooling Ball CSY (BFWTB$CSY)

- Create a plane using Tooling Balls 5, 6, & 7

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 6 to 5 (+X)

  - This is the planar alignment

- TB 6 is a single point that sets zero in X, Y, Z.

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

Wire CSY (WIRE$CSY)

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Wire offset from Edges per T. Nakashima’s Optical Measurement

| Wire | Wire Location | Wire Diameter |
| --- | --- | --- |
| Vertical Wire (X Location from Card) | 39.6076 | 0.0384 |
| Horizontal Wire (Y Location from Card) | 37.0027 | 0.0393 |

Support Stand CSY (BASE$CSY)

- A plane on Torque Fixture sets Zero in Y and is the Spatial Alignment

- The symmetry of the outer surfaces where “X” fine adjustments are sets zero in X.

- A line where the Torque Fixture 2X Dowel pins sets zero in Z and is the Planar Alignment.

Beamline CSY (BEAMLINE$CSY)

- Use the BENCH$CSY setup except use the Torque Fixture plate to set zero in Y and the Spatial Alignment, transform +258.67 in Y to replicate Theoretical Beamline Center

- This coordinate system will tell us where the Wire Crosshairs are to a theoretical Beam Centerline.

- The wires should be offset ~ -0.400 in X, -0.200 in Y.

Statistical Data (mm.)

Out of Vacuum

10 Cycles (10 recordings)

Card Locations  
CSY = BENCH$CSY

| STATS | X-POS CARD | X-INTPT CARD | Y-INTPT CARD |
| --- | --- | --- | --- |
| AVG. | 0.07504 | -39.84196 | -95.36475 |
| Range | 0.00652 | 0.00816 | 0.00334 |
| St. Dev. | 0.00172 | 0.00212 | 0.00112 |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.34866 | -0.25640 |
| Range | 0.00638 | 0.00250 |
| St. Dev. | 0.00168 | 0.00094 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.34866 | -58.25640 | -2.52010 | 0.17183 | 89.36093 | 89.99125 |
| Range | 0.00638 | 0.00250 | 0.00423 | 0.00195 | 0.00214 | 0.00073 |
| St. Dev. | 0.00168 | 0.00094 | 0.00125 | 0.00057 | 0.00058 | 0.00021 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Transformation WIRE$CSY to BFWTB$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | 94.42704 | -161.20821 | 36.55457 | 0.19718 | 89.24011 | 90.12771 |
| Range | 0.00240 | 0.00230 | 0.01359 | 0.00143 | 0.00510 | 0.00059 |
| St. Dev. | 0.00094 | 0.00069 | 0.00393 | 0.00051 | 0.00144 | 0.00020 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Under Vacuum

10 Cycles (10 recordings)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 93.99508 | 102.99947 | -39.01716 |
| Range | 0.01584 | 0.02047 | 0.00356 |
| St. Dev. | 0.00515 | 0.00675 | 0.00122 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.86683 | 103.20170 | -38.35431 |
| Range | 0.01539 | 0.01311 | 0.00996 |
| St. Dev. | 0.00511 | 0.00464 | 0.00320 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -51.39251 | 103.06775 | 67.32547 |
| Range | 0.00860 | 0.00358 | 0.00671 |
| St. Dev. | 0.00296 | 0.00113 | 0.00214 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 51.20398 | 102.96899 | 66.96732 |
| Range | 0.00854 | 0.01508 | 0.00134 |
| St. Dev. | 0.00295 | 0.00504 | 0.00040 |
| RMS Tol | 0.06500 | 0.03000 | - |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.45881 | -0.23662 |
| Range | 0.04154 | 0.00460 |
| St. Dev. | 0.01400 | 0.00145 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.48390 | -58.13814 | -2.26243 | 0.13618 | 89.28692 | 89.92567 |
| Range | 0.04154 | 0.00459 | 0.00275 | 0.01019 | 0.00211 | 0.00418 |
| St. Dev. | 0.01400 | 0.00145 | 0.00085 | 0.00345 | 0.00062 | 0.00136 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Locations of ¼-20 Jo-Plugs Cylinders Intersected into Plane projected 12.7mm away from surface replicating a ½” (12.7mm) offset to center of Tooling Ball.

CSY = BEAMLINE$CSY

| INTPT | X | Y | Z |
| --- | --- | --- | --- |
| 1 | -26.85977 | 227.58328 | 68.33409 |
| 2 | 27.13514 | 227.61846 | 68.28566 |
| 3 | 79.87020 | 180.13820 | -68.72376 |
| 4 | -79.79931 | 180.11787 | -68.57121 |

# Text boxes

Y+

+Z

Z+

Y+

+X

+Y

X+

Transformation