LCLS BFW WIRECARD ASSY

INSPECTION/FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Venkat Srinivasan |
| Date: | Tuesday, July 08, 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 31 / VC – 31 / WC – 31 / BASE – 30 |
| Units of Measure: | Metric – Millimeters (mm.) |
| URL | http://www-group/met/Quality/FIDUCIAL%20REPORTS/LCLS%20BFW/BFW-31_VC-31_WC-31_BAS-30.pdf |

Coordinate System Setups

Bench CSY (BENCH$CSY)

(The only CSY in Both States of measurement - out and under vacuum)

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Bench Tooling Ball CSY (BTB$CSY)

- Create a plane using Tooling Balls 1, 2, & 3

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 2 to 1 (+X)

  - This is the planar alignment

- TB 2 is a single point that sets zero in X, Y, Z.

BFW Tooling Ball CSY (BFWTB$CSY)

- Create a plane using Tooling Balls 5, 6, & 7

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 6 to 5 (+X)

  - This is the planar alignment

- TB 6 is a single point that sets zero in X, Y, Z.

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

Wire CSY (WIRE$CSY)

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Wire offset from Edges per T. Nakashima’s Optical Measurement

| Wire | Wire Location | Wire Diameter |
| --- | --- | --- |
| Vertical Wire (X Location from Card) | 39.6029 | 0.0373 |
| Horizontal Wire (Y Location from Card) | 37.0126 | 0.0374 |

Support Stand CSY (BASE$CSY)

- A plane on Torque Fixture sets Zero in Y and is the Spatial Alignment

- The symmetry of the outer surfaces where “X” fine adjustments are sets zero in X.

- A line where the Torque Fixture 2X Dowel pins sets zero in Z and is the Planar Alignment.

Beamline CSY (BEAMLINE$CSY)

- Use the BENCH$CSY setup except use the Torque Fixture plate to set zero in Y and the Spatial Alignment, transform +258.67 in Y to replicate Theoretical Beamline Center

- This coordinate system will tell us where the Wire Crosshairs are to a theoretical Beam Centerline.

- The wires should be offset ~ -0.400 in X, -0.200 in Y.

Statistical Data (mm.)

Out of Vacuum

10 Cycles (10 recordings)

Card Locations  
CSY = BENCH$CSY

| STATS | X-POS CARD | X-INTPT CARD | Y-INTPT CARD |
| --- | --- | --- | --- |
| AVG. | 0.04261 | -40.06974 | -95.12375 |
| Range | 0.00334 | 0.00508 | 0.01249 |
| St. Dev. | 0.00114 | 0.00159 | 0.00363 |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.39333 | -0.20073 |
| Range | 0.00331 | 0.01131 |
| St. Dev. | 0.00113 | 0.00346 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.39333 | -58.20073 | -2.76069 | -0.11525 | 89.95929 | 89.77612 |
| Range | 0.00331 | 0.01131 | 0.02167 | 0.00261 | 0.00685 | 0.00468 |
| St. Dev. | 0.00113 | 0.00346 | 0.00774 | 0.00070 | 0.00253 | 0.00124 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Transformation WIRE$CSY to BFWTB$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | 94.55541 | -160.81241 | 35.77320 | -0.07649 | 89.81102 | 89.97500 |
| Range | 0.00486 | 0.01278 | 0.01242 | 0.00336 | 0.00504 | 0.00474 |
| St. Dev. | 0.00140 | 0.00439 | 0.00330 | 0.00091 | 0.00133 | 0.00122 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Under Vacuum

10 Cycles (10 recordings)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 93.98741 | 102.56763 | -38.35804 |
| Range | 0.00146 | 0.00344 | 0.00468 |
| St. Dev. | 0.00044 | 0.00133 | 0.00134 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.89700 | 102.66781 | -37.82369 |
| Range | 0.00113 | 0.00307 | 0.00552 |
| St. Dev. | 0.00041 | 0.00111 | 0.00167 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -51.48802 | 102.55052 | 67.89985 |
| Range | 0.00141 | 0.00219 | 0.00454 |
| St. Dev. | 0.00042 | 0.00061 | 0.00130 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 51.10289 | 102.49178 | 67.61355 |
| Range | 0.00156 | 0.00384 | 0.00499 |
| St. Dev. | 0.00046 | 0.00117 | 0.00141 |
| RMS Tol | 0.06500 | 0.03000 | - |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.31403 | -0.20897 |
| Range | 0.00493 | 0.00203 |
| St. Dev. | 0.00153 | 0.00072 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.32541 | -58.23329 | -2.45966 | -0.10665 | 89.86151 | 89.81295 |
| Range | 0.00494 | 0.00235 | 0.00850 | 0.00140 | 0.00158 | 0.00059 |
| St. Dev. | 0.00153 | 0.00084 | 0.00240 | 0.00042 | 0.00054 | 0.00019 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Locations of ¼-20 Jo-Plugs Cylinders Intersected into Plane projected 12.7mm away from surface replicating a ½” (12.7mm) offset to center of Tooling Ball.

CSY = BEAMLINE$CSY

| INTPT | X | Y | Z |
| --- | --- | --- | --- |
| 1 | -26.91662 | 227.56425 | 68.41841 |
| 2 | 27.07897 | 227.60526 | 68.41435 |
| 3 | 79.93328 | 180.28350 | -68.59785 |
| 4 | -79.78550 | 180.21806 | -68.56999 |

# Text boxes

Y+

+Z

Z+

Y+

+X

+Y

X+

Transformation