LCLS BFW WIRECARD ASSY

INSPECTION/FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Don Schafer |
| Date: | Friday, August 22, 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 34 / VC – 34 / WC – 00 / BASE – 37 |
| Units of Measure: | Metric – Millimeters (mm.) |
| URL | http://www-group/met/Quality/FIDUCIAL%20REPORTS/LCLS%20BFW/BFW-34_VC-34_WC-00_BAS-37.pdf |

Coordinate System Setups

Bench CSY (BENCH$CSY)

(The only CSY in Both States of measurement - out and under vacuum)

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Bench Tooling Ball CSY (BTB$CSY)

- Create a plane using Tooling Balls 1, 2, & 3

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 2 to 1 (+X)

  - This is the planar alignment

- TB 2 is a single point that sets zero in X, Y, Z.

BFW Tooling Ball CSY (BFWTB$CSY)

- Create a plane using Tooling Balls 5, 6, & 7

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 6 to 5 (+X)

  - This is the planar alignment

- TB 6 is a single point that sets zero in X, Y, Z.

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

Wire CSY (WIRE$CSY)

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Wire offset from Edges per T. Nakashima’s Optical Measurement

| Wire | Wire Location | Wire Diameter |
| --- | --- | --- |
| Vertical Wire (X Location from Card) | 39.6238 | 0.0368 |
| Horizontal Wire (Y Location from Card) | 36.9711 | 0.0359 |

Support Stand CSY (BASE$CSY)

- A plane on Torque Fixture sets Zero in Y and is the Spatial Alignment

- The symmetry of the outer surfaces where “X” fine adjustments are sets zero in X.

- A line where the Torque Fixture 2X Dowel pins sets zero in Z and is the Planar Alignment.

Beamline CSY (BEAMLINE$CSY)

- Use the BENCH$CSY setup except use the Torque Fixture plate to set zero in Y and the Spatial Alignment, transform +258.67 in Y to replicate Theoretical Beamline Center

- This coordinate system will tell us where the Wire Crosshairs are to a theoretical Beam Centerline.

- The wires should be offset ~ -0.400 in X, -0.200 in Y.

Statistical Data (mm.)

Out of Vacuum

10 Cycles (10 recordings)

Card Locations  
CSY = BENCH$CSY

| STATS | X-POS CARD | X-INTPT CARD | Y-INTPT CARD |
| --- | --- | --- | --- |
| AVG. | -0.03956 | -40.12732 | -95.04849 |
| Range | 0.04022 | 0.04210 | 0.00184 |
| St. Dev. | 0.01299 | 0.01453 | 0.00067 |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.45994 | -0.18758 |
| Range | 0.04037 | 0.00792 |
| St. Dev. | 0.01302 | 0.00236 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.45994 | -58.18758 | -2.98206 | -0.14325 | 89.96519 | 89.88207 |
| Range | 0.04037 | 0.00792 | 0.02421 | 0.00892 | 0.00496 | 0.00638 |
| St. Dev. | 0.01302 | 0.00236 | 0.00767 | 0.00297 | 0.00162 | 0.00172 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Transformation WIRE$CSY to BFWTB$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | 94.29371 | -160.74525 | 35.95042 | -0.07858 | 89.76249 | 90.05264 |
| Range | 0.00293 | 0.00091 | 0.00762 | 0.00186 | 0.00335 | 0.00277 |
| St. Dev. | 0.00094 | 0.00029 | 0.00264 | 0.00057 | 0.00109 | 0.00077 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Under Vacuum

10 Cycles (10 recordings)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 94.20000 | 102.49654 | -38.61772 |
| Range | 0.02639 | 0.00487 | 0.02968 |
| St. Dev. | 0.00856 | 0.00151 | 0.01030 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.66877 | 102.65707 | -38.05758 |
| Range | 0.02637 | 0.00332 | 0.03376 |
| St. Dev. | 0.00844 | 0.00116 | 0.01138 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -51.22881 | 102.67404 | 67.66477 |
| Range | 0.01850 | 0.00686 | 0.02669 |
| St. Dev. | 0.00558 | 0.00189 | 0.00782 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 51.34748 | 102.60014 | 67.34950 |
| Range | 0.01822 | 0.00409 | 0.02366 |
| St. Dev. | 0.00532 | 0.00119 | 0.00677 |
| RMS Tol | 0.06500 | 0.03000 | - |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.40584 | -0.21629 |
| Range | 0.01832 | 0.00154 |
| St. Dev. | 0.00540 | 0.00041 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.40682 | -58.15006 | -2.30482 | -0.12810 | 89.73308 | 89.88223 |
| Range | 0.01832 | 0.00154 | 0.00854 | 0.00173 | 0.00417 | 0.01845 |
| St. Dev. | 0.00540 | 0.00040 | 0.00262 | 0.00059 | 0.00124 | 0.00577 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Locations of ¼-20 Jo-Plugs Cylinders Intersected into Plane projected 12.7mm away from surface replicating a ½” (12.7mm) offset to center of Tooling Ball.

CSY = BEAMLINE$CSY

| INTPT | X | Y | Z |
| --- | --- | --- | --- |
| 1 | -27.03676 | 227.41543 | 68.34449 |
| 2 | 26.98208 | 227.39789 | 68.30147 |
| 3 | 79.71728 | 180.04599 | -68.74492 |
| 4 | -79.98268 | 179.97547 | -68.62185 |

# Text boxes

Y+

+Z

Z+

Y+

+X

+Y

X+

Transformation