LCLS BFW WIRECARD ASSY

INSPECTION/FIDUCIAL REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Don Schafer |
| Date: | Monday, September 08, 2008 |
| Work Order/Charge No.: | 23800-1 |
| Serial Number: | BFW – 37 / VC – 37 / WC – 37 / BASE – 29 |
| Units of Measure: | Metric – Millimeters (mm.) |
| URL | http://www-group/met/Quality/FIDUCIAL%20REPORTS/LCLS%20BFW/BFW-37_VC-37_WC-37_BAS-29.pdf |

Coordinate System Setups

Bench CSY (BENCH$CSY)

(The only CSY in Both States of measurement - out and under vacuum)

- Plane measurement on top of Bench to set zero in Y and is the Spatial Alignment.

- Measure Pin and Diamond Pin to get centers, create a line between the two center points and this sets zero in Z and is the Planar Alignment.

- Take the symmetry point of the two pins this sets zero in X.

Bench Tooling Ball CSY (BTB$CSY)

- Create a plane using Tooling Balls 1, 2, & 3

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 2 to 1 (+X)

  - This is the planar alignment

- TB 2 is a single point that sets zero in X, Y, Z.

BFW Tooling Ball CSY (BFWTB$CSY)

- Create a plane using Tooling Balls 5, 6, & 7

  - This sets Zero in Y and is the spatial alignment

- Create an axis/line using TB’s 6 to 5 (+X)

  - This is the planar alignment

- TB 6 is a single point that sets zero in X, Y, Z.

| View from Z+ or Downstream | View from X+ Side |
| --- | --- |

Wire CSY (WIRE$CSY)

- Back Plane (-Z) Side sets Zero in Z and is the Spatial Alignment

- Looking from +Z Side, Bottom of Card Sets Zero is the Planar Alignment

- The Intersection of the Left Side of the Card and the Bottom, sets Zero in X & Y

Wire offset from Edges per T. Nakashima’s Optical Measurement

| Wire | Wire Location | Wire Diameter |
| --- | --- | --- |
| Vertical Wire (X Location from Card) | 39.6078 | 0.0401 |
| Horizontal Wire (Y Location from Card) | 37.0084 | 0.0353 |

Support Stand CSY (BASE$CSY)

- A plane on Torque Fixture sets Zero in Y and is the Spatial Alignment

- The symmetry of the outer surfaces where “X” fine adjustments are sets zero in X.

- A line where the Torque Fixture 2X Dowel pins sets zero in Z and is the Planar Alignment.

Beamline CSY (BEAMLINE$CSY)

- Use the BENCH$CSY setup except use the Torque Fixture plate to set zero in Y and the Spatial Alignment, transform +258.67 in Y to replicate Theoretical Beamline Center

- This coordinate system will tell us where the Wire Crosshairs are to a theoretical Beam Centerline.

- The wires should be offset ~ -0.400 in X, -0.200 in Y.

Statistical Data (mm.)

Out of Vacuum

10 Cycles (10 recordings)

Card Locations  
CSY = BENCH$CSY

| STATS | X-POS CARD | X-INTPT CARD | Y-INTPT CARD |
| --- | --- | --- | --- |
| AVG. | -0.04260 | -40.25754 | -95.02282 |
| Range | 0.03737 | 0.04413 | 0.01097 |
| St. Dev. | 0.01100 | 0.01304 | 0.00420 |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.47018 | -0.21565 |
| Range | 0.03735 | 0.01054 |
| St. Dev. | 0.01100 | 0.00385 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.47018 | -58.21565 | -3.12222 | -0.27947 | 89.98436 | 89.85369 |
| Range | 0.03735 | 0.01054 | 0.03485 | 0.01169 | 0.00851 | 0.00524 |
| St. Dev. | 0.01100 | 0.00385 | 0.01081 | 0.00353 | 0.00264 | 0.00187 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Transformation WIRE$CSY to BFWTB$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | 94.87178 | -160.63158 | 35.55397 | 0.05330 | 89.85125 | 89.82896 |
| Range | 0.00172 | 0.00041 | 0.00171 | 0.00080 | 0.00089 | 0.00103 |
| St. Dev. | 0.00053 | 0.00014 | 0.00059 | 0.00027 | 0.00029 | 0.00037 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Under Vacuum

10 Cycles (10 recordings)

TB 5-8 Locations

CSY = BENCH$CSY

| TB 5 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 94.48866 | 101.88910 | -37.91963 |
| Range | 0.00235 | 0.00537 | 0.00308 |
| St. Dev. | 0.00093 | 0.00172 | 0.00098 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 6 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -94.37790 | 103.00359 | -37.76597 |
| Range | 0.00259 | 0.01799 | 0.00251 |
| St. Dev. | 0.00095 | 0.00675 | 0.00072 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 7 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | -51.18104 | 102.92209 | 68.03166 |
| Range | 0.00375 | 0.01081 | 0.00166 |
| St. Dev. | 0.00108 | 0.00343 | 0.00060 |
| RMS Tol | 0.06500 | 0.03000 | - |

| TB 8 | X | Y | Z |
| --- | --- | --- | --- |
| AVG. | 51.41697 | 102.31901 | 67.95142 |
| Range | 0.00335 | 0.00687 | 0.00257 |
| St. Dev. | 0.00103 | 0.00242 | 0.00078 |
| RMS Tol | 0.06500 | 0.03000 | - |

Wire Location

CSY = BEAMLINE$CSY

| Stats | X | Y |
| --- | --- | --- |
| AVG. | -0.43280 | -0.24144 |
| Range | 0.01421 | 0.00997 |
| St. Dev. | 0.00617 | 0.00299 |
| Nom. | -0.40000 | -0.20000 |
| RMS Tol | 0.06500 | 0.03000 |

Transformation WIRE$CSY TO BENCH$CSY

| Stats | X | Y | Z | APA_PXPY | PA_PYPZ | PA_PXPZ |
| --- | --- | --- | --- | --- | --- | --- |
| AVG. | -0.42693 | -58.12678 | -2.02530 | -0.28496 | 89.75828 | 89.78078 |
| Range | 0.01421 | 0.00998 | 0.00956 | 0.00480 | 0.00322 | 0.00105 |
| St. Dev. | 0.00617 | 0.00299 | 0.00428 | 0.00207 | 0.00133 | 0.00034 |
| RMS Tol | 0.06500 | 0.03000 | - | - | - | - |

Locations of ¼-20 Jo-Plugs Cylinders Intersected into Plane projected 12.7mm away from surface replicating a ½” (12.7mm) offset to center of Tooling Ball.

CSY = BEAMLINE$CSY

| INTPT | X | Y | Z |
| --- | --- | --- | --- |
| 1 | -26.75555 | 227.43967 | 68.45431 |
| 2 | 27.22609 | 227.42651 | 68.44453 |
| 3 | 80.02072 | 180.13270 | -68.62338 |
| 4 | -79.60120 | 180.18158 | -68.58850 |

# Text boxes

Y+

+Z

Z+

Y+

+X

+Y

X+

Transformation