LCLS BX3 DIPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Ed Reese |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Wednesday, February 14, 2007 |
| Work Order/Charge No.: | 21698-1 |
| Serial Number | 000241 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS BX3 DIPOLE\000241.PDF |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Symmetry Axis between inner side plates of housing

Spatial Alignment

- Symmetry Plane between upper and lower poles

“Z” Zero

- Symmetry Point between faces perpendicular to beam

“X” Zero

- Symmetry Axis between Inner side plate of housing

“Y” Zero

- Symmetry Plane between upper and lower poles

Tooling Ball Measurements/Locations

Top Tooling Ball Sockets

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00036 | 0.49763 | 4.30566 | 4.63857 | -45.15252 |
| TB 2 | 0.00044 | 0.49661 | -4.33228 | 4.63909 | -45.17474 |
| TB 3 | 0.00030 | 0.49682 | 4.40152 | 4.63892 | 45.14911 |
| TB 4 | 0.00097 | 0.49764 | -4.31995 | 4.64642 | 45.15378 |

Side Optical/Magnetic Precision Sphere Holder

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| A | 0.00001 | 1.50003 | 6.63787 | 2.09729 | -31.36457 |
| B | 0.00001 | 1.50000 | 6.63426 | 2.12659 | 31.36137 |
| C | 0.00003 | 1.50001 | 6.63735 | -1.85395 | -31.37030 |
| D | 0.00003 | 1.50004 | 6.62845 | -2.09760 | 31.37185 |

Additional Requested Measurements

| LOCATION | POLE DISTANCE |
| --- | --- |
| -X/-Z | 0.90647 |
| +X/-Z | 0.90565 |
| -X/+Z | 0.91433 |
| +X/+Z | 0.91102 |