LCLS BX3 DIPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Ed Reese |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Thursday, March 1, 2007 |
| Work Order/Charge No.: | 21698-1 |
| Serial Number | 000309 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS BX3 DIPOLE\000309.PDF |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Symmetry Axis between inner side plates of housing

Spatial Alignment

- Symmetry Plane between upper and lower poles

“Z” Zero

- Symmetry Point between faces perpendicular to beam

“X” Zero

- Symmetry Axis between Inner side plate of housing

“Y” Zero

- Symmetry Plane between upper and lower poles

Tooling Ball Measurements/Locations

Top Tooling Ball Sockets

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00072 | 0.49762 | 4.24567 | 4.64831 | -45.15880 |
| TB 2 | 0.00032 | 0.49794 | -4.29794 | 4.64282 | -45.18815 |
| TB 3 | 0.00023 | 0.49803 | 4.29070 | 4.65325 | 45.12867 |
| TB 4 | 0.00016 | 0.49696 | -4.31244 | 4.64931 | 45.14202 |

Side Optical/Magnetic Precision Sphere Holder

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| A | 0.00001 | 1.50003 | 6.62589 | 2.16619 | -31.47583 |
| B | 0.00005 | 1.50005 | 6.66370 | -2.08982 | -31.48549 |
| C | 0.00002 | 1.50009 | 6.62173 | 2.15660 | 31.31972 |
| D | 0.00001 | 1.50006 | 6.61656 | -2.14863 | 31.30905 |

Additional Requested Measurements

| LOCATION | POLE DISTANCE |
| --- | --- |
| -X/-Z | 0.93418 |
| +X/-Z | 0.91705 |
| -X/+Z | 0.90417 |
| +X/+Z | 0.90415 |