LCLS BX3 DIPOLE MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Ed Reese |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Wednesday, February 28, 2007 |
| Work Order/Charge No.: | 21698-1 |
| Serial Number | 000324 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS BX3 DIPOLE\000324.PDF |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Symmetry Axis between inner side plates of housing

Spatial Alignment

- Symmetry Plane between upper and lower poles

“Z” Zero

- Symmetry Point between faces perpendicular to beam

“X” Zero

- Symmetry Axis between Inner side plate of housing

“Y” Zero

- Symmetry Plane between upper and lower poles

Tooling Ball Measurements/Locations

Top Tooling Ball Sockets

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00004 | 0.49716 | 4.31466 | 4.64516 | -45.16716 |
| TB 2 | 0.00001 | 0.49620 | -4.32652 | 4.64494 | -45.18730 |
| TB 3 | 0.00004 | 0.49503 | 4.29690 | 4.64534 | 45.14764 |
| TB 4 | 0.00004 | 0.49667 | -4.11248 | 4.64778 | 45.16518 |

Side Optical/Magnetic Precision Sphere Holder

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| A | 0.00004 | 1.50015 | 6.62089 | 2.14091 | -31.39265 |
| B | 0.00006 | 1.50013 | 6.61203 | 2.15606 | 31.31260 |
| C | 0.00005 | 1.50014 | 6.63972 | -2.17013 | -31.37837 |
| D | 0.00007 | 1.50018 | 6.62863 | -2.15091 | 31.30864 |

Additional Requested Measurements

| LOCATION | POLE DISTANCE |
| --- | --- |
| -X/-Z | 0.90781 |
| +X/-Z | 0.90790 |
| -X/+Z | 0.90641 |
| +X/+Z | 0.90647 |