LCLS BXG Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Tom Borden |
| Date: | Wednesday, January 3, 2007 |
| Work Order/Charge No.: | 92-4264-2 |
| Serial Number: | 002012 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS BXG MAGNET\002012.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric horizontal symmetry plane of the poles of the magnet.

Planar Alignment

- Mid-Plane of the angled ends (stainless steel) of the Magnet

“Z” Zero

- Mid-Plane of the magnet

“Y” Zero

- Mid-plane of the horizontal pole planes of the magnet

“X” Zero

- Symmetry axis of the angled pole planes on the lower half of the magnet.

Tooling Ball Measurements/Locations

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB A | 0.00038 | 0.49828 | 0.00668 | 11.11454 | 2.46776 |
| TB B | 0.00044 | 0.49839 | 0.00146 | 11.11440 | -2.46521 |
| TB C | 0.00005 | 0.49996 | -9.03836 | 11.11447 | -2.47805 |
| TB D | 0.00022 | 0.49892 | -9.05192 | 11.11476 | 2.44593 |

Pole Distances

| GAP | GAP DIST (Y) | X location | Z location |
| --- | --- | --- | --- |
| 1 | 1.69261 | 3.15700 | -4.64537 |
| 2 | 1.69276 | -3.17684 | -2.89452 |
| 3 | 1.69284 | -0.26888 | -1.15293 |
| 4 | 1.69305 | 3.15675 | 4.61483 |
| 5 | 1.69325 | -3.17699 | 2.86396 |
| 6 | 1.69303 | -0.26907 | 1.12234 |