LCLS BXKIK MAGNET

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Monday, November 05, 2007 |
| Work Order/Charge No.: | 23306-1 |
| Serial Number: | None given (PART #: SA-380-330-01) |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS BXKIK MAGNET\23306-1.PDF |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Mid-plane of upper and lower split planes (g-10)

Planar Alignment

- Symetry line of the lower half section (even TB numbers)

“Z” Zero

- Mid-plane of lower half section in the long direction.

“X” & “Y” Zero

- Geometric axis of the poles of the magnet.

| Front View | Side View |
| --- | --- |

Tooling Ball Measurements/Locations

Looking from –X side

Looking from +X side

Tooling Balls Measured with ½” Tooling Ball Socket & 1” Extension

| Tooling Ball | FORM | Sph. Dia. | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00007 | 0.49984 | 3.54735 | 0.31793 | 19.08222 |
| TB 2 | 0.00023 | 0.49730 | 3.56770 | -0.25679 | 19.08810 |
| TB 3 | 0.00002 | 0.49989 | 3.54005 | 0.27789 | -0.00999 |
| TB 4 | 0.00005 | 0.49973 | 3.56750 | -0.29329 | -0.00084 |
| TB 5 | 0.00011 | 0.49933 | 3.53656 | 0.26982 | -19.09116 |
| TB 6 | 0.00016 | 0.49985 | 3.55664 | -0.30683 | -19.07853 |
| TB 7 | 0.00020 | 0.49907 | -3.56199 | 0.27136 | -19.16259 |
| TB 8 | 0.00031 | 0.49966 | -3.54925 | -0.28586 | -19.16764 |
| TB 9 | 0.00007 | 0.49993 | -3.55868 | 0.26449 | -0.08056 |
| TB 10 | 0.00007 | 0.49988 | -3.56632 | -0.31086 | -0.09115 |
| TB 11 | 0.00006 | 0.49940 | -3.55553 | 0.21856 | 18.98555 |
| TB 12 | 0.00005 | 0.49993 | -3.56264 | -0.29745 | 18.99311 |

# Text boxes

+Y

+Z

+Y

+X

+Z

+Y

+Z

+Y