LCLS BXS Spectrometer Dipole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Ed Reese/Keith Caban |
| --- | --- |
| Responsible Engineer: | Tom Borden |
| Date: | Wednesday, November 29, 2006 |
| Work Order/Charge No.: | 92-4264-2 |
| Serial Number: | 002005 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS BXS DIPOLE\002005.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Geometric horizontal symmetry plane of the poles of the magnet.

Planar Alignment

- Mid-Plane of the angled ends (stainless steel) of the Magnet

“Z” Zero

- Mid-Plane of the magnet

“Y” Zero

- Mid-plane of the horizontal pole planes of the magnet

“X” Zero

- Symmetry axis of the angled pole planes on the lower half of the magnet.

Tooling Ball Measurements/Locations

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.0005 | 0.4969 | -10.5452 | 8.6664 | -9.0839 |
| TB 2 | 0.0005 | 0.4961 | 8.7113 | 8.6667 | -7.3582 |
| TB 3 | 0.0006 | 0.4968 | 8.6851 | 8.6655 | 7.3498 |
| TB 4 | 0.0002 | 0.4981 | -10.5553 | 8.6658 | 9.0841 |

Pole Distances

| GAP | GAP DIST (Y) | X location | Z location |
| --- | --- | --- | --- |
| 1 | 1.3388 | 3.3121 | 7.9563 |
| 2 | 1.3390 | -3.4311 | 8.7110 |
| 3 | 1.3397 | 3.4273 | -7.9564 |
| 4 | 1.3396 | -3.0787 | -8.8520 |