LCLS type 1g Corrector Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | T. Borden |
| Date: | Friday, January 12, 2007 |
| Work Order/Charge No.: | 92-4216-9 |
| Serial Number: | 002408 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS Corrector Magnets\002408.pdf |

Part Set-up – Coordinate System Set-up

Spatial Alignment

- Inner Center line created below (x,y zero setup)

Planar Alignment

- 4 intersection points of the inner planes in the horizontal plane.

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- Inner planes intersect with each end to create 4 diagonal axis

  - 4 Diagonal Axis intersect to create 4 points on each side.

  - Use radius side intersection points to create X axis

  - Use top and bottom intersection points to create Y axis

  - Intersect x,y axis’ on both sides to get center points

  - These center points collected create a line which is the center of the magnet and x,y zero and Spatial Alignment

Front View from Z+	                            	Side View from X+

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00052 | 0.49758 | 2.68859 | 1.50484 | 0.75188 |
| TB 2 | 0.00079 | 0.49792 | 2.68810 | 1.50427 | -0.74822 |
| TB 3 | 0.00142 | 0.49601 | -2.68527 | 1.50468 | -0.75053 |
| TB 4 | 0.00108 | 0.49549 | -2.68653 | 1.50421 | 0.74926 |

# Text boxes

TB 2

TB 3

TB 4

TB 1

Z+

+Z

+X

A

B

C

D

Y+

X+

Y+