LCLS Dipole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Ed Reese |
| --- | --- |
| Responsible Engineer: | Carl Rago |
| Date: | Monday, February 12, 2007 |
| Work Order/Charge No.: | 21697-1 |
| Serial Number | 000353 |
| URL of Fiducial Report: | \\Web002\www-group\met\Quality\FIDUCIAL REPORTS\LCLS DIPOLE\000353.PDF |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Symmetry Axis between inner side plates of housing

Spatial Alignment

- Symmetry Plane between upper and lower poles

“Z” Zero

- Symmetry Point between faces perpendicular to beam

“X” Zero

- Symmetry Axis between Inner side plate of housing

“Y” Zero

- Symmetry Plane between upper and lower poles

-Z End View

Tooling Ball Measurements/Locations

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00108 | 0.49657 | 4.01339 | 5.16433 | -17.01042 |
| TB 2 | 0.00017 | 0.49917 | -3.86069 | 5.16223 | -16.95661 |
| TB 3 | 0.00004 | 0.49972 | 3.88023 | 5.16239 | 17.02284 |
| TB 4 | 0.00000 | 0.49809 | -3.88433 | 5.16311 | 17.03344 |

Additional Requested Measurements

| LOCATION | POLE DISTANCE |
| --- | --- |
| -X/-Z | 1.37802 |
| +X/-Z | 1.37754 |
| -X/+Z | 1.37886 |
| +X/+Z | 1.37817 |

# Text boxes

TB 1

TB 2

TB 3

TB 4

Z+

+Z

+X

A

B

C

D

View From +Z

+Y

TB1

TB2

TB3

+X

+Y

TB4