LCLS Injector Dogleg Dipole Magnet

FIDUCIALIZATION REPORT

| Inspector: | Keith Caban |
| --- | --- |
| Responsible Engineer: | Roger Carr |
| Date: | Tuesday, May 16, 2006 |
| Work Order/Charge No.: | 92-4217-3 |
| Serial Number | 000438 |

Part Set-up – Coordinate System Set-up

Planar Alignment

- Mid-Plane of the magnet

Spatial Alignment

- Bottom pole plane

  - -Y plane

“Z” Zero

- Mid-Plane of the magnet

“X” & “Y” Zero

- X zero is created by the symmetry point of the inner stainless steel where coils lie.

    - Both ends of both sides.

      - Create lines which is y axis.

        - This Creates X- zero

- Symmetry of pole planes

  - This creates Y- zero

| ISO | BACK VIEW |
| --- | --- |

Tooling Ball Measurements/Locations

Top of magnet; view from “+Y”

| Tooling Ball | FORM | DIAMETER | X | Y | Z |
| --- | --- | --- | --- | --- | --- |
| TB 1 | 0.00043 | 0.49840 | 7.32590 | 7.76271 | 2.92288 |
| TB 2 | 0.00005 | 0.50002 | 7.32321 | 7.76461 | -2.88267 |
| TB 3 | 0.00042 | 0.49777 | -7.31142 | 7.76647 | -2.87136 |
| TB 4 | 0.00038 | 0.49909 | -7.30865 | 7.76285 | 2.93523 |

Additional Requested Measurements

Parallelism of pole planes

// = 0.00057

# Text boxes

TB 1

TB 2

TB 3

TB 4

Z+

+Z

+X

A

B

C

D

View From +Z

+Y

+Z

+Y

+X

+X

+Z